## Slide 1: CEPC Injection
Cui Xiaohao, Bian Tianjian, Zhang Chuang
2017/11/07

## Slide 2: Contents
1. Injection Systems
2. requirement
3. Injection Process
4. Summary

## Slide 3: 1. Injection Systems
10 GeV
Linac
Transport line
From Linac
To booster
100 km booster
10 GeV -> 120 GeV
Transport line
From booster
To collider
Booster Dipole field at low energy is only 30 Gauss, Low field Magnet R&D is needed

## Slide 4: Geometrical Arrangement
Booster
Collider
1.5 m
Linac on the ground level
Booster and collider in the same tunnel about 100 m deep
Booster is 1.5 m above the collider

## Slide 5: Transport lines: Linac to booster
Geometry of the Transport line
Guiding the beam from Linac to the booster
Beam Energy: 10 GeV
Beam emittance: 300 nm.rad
horizontal bending section and one vertical bending section
Vertical bending section matches the 100m height
Efficiency: > 99%
Linac
Separation
Vertical slope
Horizontal bending

## Slide 6: Transport lines: booster to collider
Horizontal Extraction
Horizontal Injection
Vertical Slope
Geometry of the Transport line
Guiding the beam from the booster to collider ring
Beam Energy: 120/80/45 GeV
Beam emittance: 3.1/1.56/0.51 nm.rad
horizontal bending section and one vertical bending section
Vertical bending section matches the 1.5 m height
Efficiency: > 99%

## Slide 7: Machine Functions of Two Transport lines

## Slide 8: 2. requirement
 | Higgs | W | Z
Energy | 120 | 80 | 45.5
Bunch number | 286 | 5220 | 10900
Beam current (mA) | 17.7 | 90.3 | 83.8
Collider Lifetime | 20 min | 3.5 Hr | 7.4 Hr
3% decay time (sec) | 37 | 383 | 811
3% current (mA) | 0.531 | 2.709 | 2.514
Some parameters of the Collider ring
Due to the short lifetime, a Top-up injection is needed and the injection time must be less than that listed above.

## Slide 9: Booster current
The current in the booster is limited by the instabilities. For aluminium vacuum chamber, the TMCI current threshold is 0.803 mA. In W, and Z mode, It takes the booster 5 cycles to fill all bunches.

## Slide 10: Acceptance
For booster injection: the beam emittance from linac is 300 nm.rad in both x, and y direction. The booster physical aperture is 3 sigma + 5mm.
For collider injection: the beam emittance from booster is 3.1 nm.rad in x, and 1% coupling. The collider dynamic aperture is more than 16 sigma in x, and 6 sigma in y for higgs injection.

## Slide 11: Beam parameters from Linac
Parameter | Value | Unit
Beam Energy | 10 | GeV
Repetition rate | 100 | Hz
Bunch Charge | >1 | nC
Energy Spread | <2E-3 | 
Emittance | < 0.3 | mm.rad
Emittance is required by the vacuum chamber in the booster.
Bunch charge is required by the injection current in Higgs mode.

## Slide 12: Beam parameters from booster
Parameter | H | W | Z | Unit
Bunch Charge | 0.62 | 0.18 | 0.077 | nC
Ramping Cycle | 10 | 6 | 2 | s
Beam Current | 0.532 | 0.542 | 0.504 | mA
Emittance x | 3.1 | 1.56 | 0.51 | nm.rad
Energy Spread | 0.0966 | 0.064 | 0.037 | %
Efficiency | 92 % |  |  | 

## Slide 13: 3. Injection process
Injection from Linac to booster
Booster ramping to High Energy
Inject from booster to collider
Booster ramping to Low Energy
repeat

## Slide 14: Injection Time Structure:
In W, and Z mode, It takes the booster 5 cycles to fill all bunches
For Z injection, the booster needs 8s at the high energy for beam damping.

## Slide 15: Booster injection and Extraction:
On axis injection
One septum and one kicker is needed
Extraction is just the oppsite
Injecting beam
Septum
X’
X
Injected beam

## Slide 16: Kickers and Septums:
Component | Length (m) | Waveform | Deflection angle (mrad) | Field (T) | Beam-Stay-clear | 
 |  |  |  |  | H(mm) | V(mm)
Septum | 2 | DC | 9.1 | 0.152 | 63 | 63
Kicker | 0.5 | Half_sin | 0.5 | 0.034 | 63 | 63
Component | Length (m) | Waveform | Deflection angle (mrad) | Field (T) | Beam-Stay-clear | 
 |  |  |  |  | H(mm) | V(mm)
Septum | 10 | DC | 10.4 | 0.41 | 20 | 20
Kicker | 2 | Half_sin | 0.2 | 0.04 | 20 | 20
Booster Injection
Booster Extraction

## Slide 17
Bumped
Stored beam
Injected beam
Septum
2mm
X’
X
Acceptance >4sxc + 8sxi + S
Bump Height
Collider Injection:
For Higgs:
e_x = 1.21 nm.rad; e_inject = 3.1 nm.rad
sx = 0.47 mm, s_inject = 0.45 mm
Septum = 2 mm
Acceptance > 16 s
For Z:
e_x = 0.17 nm.rad; e_inject = 0.51 nm.rad
sx = 0.18 mm, s_inject = 0.16 mm
Septum = 2 mm
Acceptance > 23 s

## Slide 18: Injection Simulation:
Performed simulations of the injected beam dynamics
Beam distribution in X-X’ phase-space is tracked after injection
Blue distribution: Beam before injection
Green distribution: Beam of the first 10 turns after injection
Dotted line is the acceptance

## Slide 19: Kickers and Septums:
Bump height 20mm,kicker length 2m,then the strength of the kickers are about 200 Gauss
Kicker strength
Septum strength
If the Septum is 35m, the strength needed is much higher.
As a result, we tried to use 4 separate septum instead of a single one.
Their magnet strength are: 0.64T, 0.32T, 0.16T, 0.08T and their thickness are 16mm,8mm,4mm,2mm separately.

## Slide 20: Booster parameters and filling time
Mode | Higgs | W | Z
Injection Energy (GeV) | 120 | 80 | 45.5
Bunch number | 286 | 1044 | 2180
Bunch Charge (nC) | 0.62 | 0.173 | 0.077
Beam Current (mA) | 0.532 | 0.542 | 0.504
Current threshold due to TMCI | 0.803 | 0.803 | 0.803
Number of Cycles | 1 | 5 | 5
Current decay | 3% | 3% | 3%
Ramping Cycle (sec) | 10 | 6 | 2
Filling time (sec) | 28 | 185 | 318
Injection frequency (sec) | 37 | 383 | 811

## Slide 21: 4. Summary
A baseline design of the injection systems of CEPC is presented in this talk
The total transmission efficiency of the system is larger than 90% (99%*92%*99%)
It satisfies the Top-Up injection requirements for both Higgs, W, and Z mode.
It also has the ability to fill the collider from empty in a reasonable time.

## Slide 22: Thank you!