## Slide 1: SPPC CDR - Status
Jingyu Tang
for the SPPC study group
International Workshop on CEPC, Nov. 6-8, 2017, IHEP

## Slide 2: Main topics
About the SPPC CDR study
Collider accelerator physics
Technical issues
Design concepts on the injector chain
Plan for CDR writing
Summary

## Slide 3: From CEPC to SPPC
SPPC is the second phase of the project, differing by 10-15 years
Use the same CEPC tunnel to build SPPC, exploring new physics beyond SM and also precision Higgs
Center-of-Mass energy larger than 70 TeV with possible energy upgrade
Keep the e-/e+ rings when adding the SPPC
Collisions possible: pp, e-/e+, ep, pA, eA, AA
Build a new injector chain for SPPC (proton and ions)
Independent physics programs for the accelerators of the injector chain

## Slide 4
Parameter | Unit | Value |  | 
 |  | PreCDR | CDR | Ultimate
Circumference | km | 54.4 | 100 | 100
C.M. energy | TeV | 70.6 | 75 | 125-150
Dipole field | T | 20 | 12 | 20-24
Injection energy | TeV | 2.1 | 2.1 | 4.2
Number of IPs |  | 2 | 2 | 2
Nominal luminosity per IP | cm-2s-1 | 1.2e35 | 1.0e35 | -
Beta function at collision | m | 0.75 | 0.75 | -
Circulating beam current | A | 1.0 | 0.7 | -
Bunch separation | ns | 25 | 25 | -
Bunch population |  | 2.0e11 | 1.5e11 | -
SR power per beam | MW | 2.1 | 1.1 | -
SR heat load per aperture @arc | W/m | 45 | 13 | -
SPPC main parameters (updated)

## Slide 5
Tunnel cross-section
More space required for CEPC double-ring scheme

## Slide 6: CDR Study objectives
SPPC study is focusing on
  Describing what a future proton-proton collider looks like, physics performance
  Following the CEPC project, try to avoid what will hinder the future upgrading to SPPC, e.g. tunnel circumference and layout
  Studying key accelerator physics issues of that scale accelerators, which is also a contribution to the accelerator community, e.g. collimation, beam-beam effects
  Identifying key technical challenges, for some of them needing long-term R&D efforts, we should start them as early as possible, e.g. high-field superconducting magnets, beam screen

## Slide 7: Considerations on layout
Layout consideration
  8 arcs and long straight sections (accepted by CEPC)
  Arcs will be traditional FODO based, 6-8 long SC dipoles per half cell, missing dipoles for dispersion suppression
  Long straight sections (LSS) are important for pp colliders, here, two IPs, injection, extraction, collimation and RF stations
  [Two very long LSSs for collimation and extraction
  Perhaps one IP more for A-A and one for e-p]
Detouring detectors: quite challenging, CEPC rings and ee detectors to bypass the SPPC rings and pp detectors, how about AA and ep detectors

## Slide 8: Compatibility between CEPC and SPPC
CEPC first to be built, with potential to add SPPC later
Three machines in one tunnel: e booster, ee double-ring collider, pp double-ring collider
Allow ep collision in the future, to solve the problem in circumference difference (CEPC outside of SPPC)
Layout: 8 long straights and arcs, LHC-like DS lattice, lengths for LSSs
Several rounds of interactions between CEPC and SPPC design teams, tbc
SPPC layout- 100km
CEPC double-ring layout- 100km

## Slide 9: Lattice design
Different lattice designs
  Different schemes (100 TeV and 75 TeV @100 km)
  Lattice at injection and collision
  Compatibility between CEPC and SPPC
  Arc cells, Dispersion suppressors, insertions
For supporting other studies, e.g. magnets, collimation, dynamic aperture, …
IP: at collision
IP: at injection
Yukai Chen, Feng Su, Linhao Zhang
Details by Y.K. Chen on SPPC IV

## Slide 10: Dynamic aperture study
At collision energy
At injection energy
(Sixtrack code)
For the moment, it is ok, with iterations with magnet design
Yukai Chen, Feng Su, collaborating with F. Schmidt

## Slide 11: Longitudinal beam dynamics
Concerns:
  Bunch filling schemes
  Luminosity leveling schemes
  Instabilities
  Requirement to the RF systems
  Global study with the injector accelerators
Different factors:
  IBS effect
  Emittance control (shrinking and blow-up)
  Bunch preparation in the injector chain
Linhao Zhang
Limitation by Transverse Mode Coupling Instability
@Injection
@Extraction
Details by L.H. Zhang on SPPC IV

## Slide 12: Bunch filling schemes
100 km - 75 TeV -25 ns (also for different SPPC designs)
Bunching filling factor: ~76%

## Slide 13: Beam-beam effects
Beam-beam effect has direct impact to the luminosity
Studying different effects (ongoing)
  Head-on interaction
  Long-range interaction
  Pacman effects
  Orbit effects
  Coherent beam effects
  BB compensation methods (Electron lens, Compensation wires)
Lijiao Wang, collaborating with K. Ohmi and T. Sen
New results will be presented by K. Ohmi on SPPC IV

## Slide 14: Luminosity Leveling
Increasing the average luminosity by programing the beam collision scenario (controlled emittance shrinking, turnaround time, beta*, B-B parameter, bunch spacing)
Turnaround:
0.8 hrs (min),
2.4 hrs (ave)
Q: 0.03 (max)
Spacing:
25, 10, 5 ns
Beta*:
0.75 m
0.75->0.25m

## Slide 15: Goals
Requirements
  SC magnet quench prevention:
  Halo particles cleaning
  Machine protection: prevent damaging radiation-sensitive devices
  Radiation losses concentration: hands-on maintenance
  Cleaning physics debris: collision products
  Optimizing background: in the experiments
    halo diagnostics
Rq: ~106 protons/m/s
： 1.5×1015
： 0.2 h (10s) /5 h
Collimation study
Ye Zou, Jianquan Yang, collaborating with LAL and LHC
Huge stored energy: 9.1 GJ/beam
Details by J.Q. Yang on SPPC IV

## Slide 16
Further developing the concept of combining betatron and momentum collimations in a same long straight section (4.3km)
Recently a new design for the transverse collimation section, by introducing protected large-aperture superconducting magnets and add an additional collimation stage
  Simulations show good effect in collimation efficiency
  Protection-aid low-field SC quadrupoles workable
With RT magnets in beta-collimation
With SC magnets in beta-collimation

## Slide 17
Other undergoing studies
  Instabilities: Liu Yudong continues to work on different instabilities, especially EC effects
  Injection/extraction: Yang Ye and Li Guangrui continues to work on the topic

## Slide 18: Technical challenges and R&D requirements -High field SC magnets
Following the new SPPC design scope
  Phase I: 12 T, all-HTS (iron-based conductors)
  Phase II: 20-24 T, all-HTS
New magnet design for 12-T dipoles
R&D effort in 2016-2018
  Cables, infrastructure
  Development of a 12-T Nb3Sn-based twin-aperture magnets (alone, with NbTi, with HTS)
Collaboration
  Domestic collaboration frame on HTS (material and applications) formed in October 2016
  CERN-IHEP collaboration on HiLumi LHC magnets
Details by Q.J. Xu in plenary and also on SPPC II

## Slide 19
Design of 12-T Fe-based Dipole Magnet
Yoke OD
500mm
Table 1: Main parameters of the cables
Table 2: Main parameters of the strand
Cable | Hight | Width-i | Width-o | Ns | Strand | Filament | Insulation
IRONBASED1 | 8 | 1.5 | 1.5 | 20 | IRON-BASED | FE-BASED | 0.15
IRONBASED2 | 5.6 | 1.5 | 1.5 | 14 | IRON-BASED | FE-BASED | 0.15
IRONBASED3 | 5 | 1.5 | 1.5 | 12 | IRON-BASED | FE-BASED | 0.15
Strand | diam. | cu/sc | RRR | Tref | Bref | Jc@ BrTr | dJc/dB
IRON-BASED | 0.802 | 1 | 200 | 4.2 | 10 | 4000 | 111
For per meter of such magnet, the required length of the iron-based strand: 6.08 Km
C. Wang, E. Kong (USTC), Q. Xu et al.

## Slide 20: Beam screen study
With the new design scope, SR power decreases from 45 W/m to 12.8 W/m, but still very important, and beam screen still a critical issue
Different effects combined: impedance, electron cloud, vacuum, magnet quenches, cooling etc.
Recent work focused on: structure, HTS coating, working temperature, impedance, cooling method
Kun Zhu, Pingping Gan
Details by K. Zhu on SPPC III

## Slide 21
Collimation system: new materials to reduce impedance and tolerate more heat deposit
Very large scale cryogenics system: SC magnets, SRF, beam screens
Sophisticated beam feedback system: to control the emittance heat-up and suppress beam instabilities
Machine protection system: fast detection of abnormal function, reliable beam abort (kickers and septa)
There are also many technical challenges in building high-power injector chain: e.g. RF systems for p-RCS and MSS, fast ramping for SS
Other important technical challenges

## Slide 22: Injector chain (for proton beam)
p-Linac: proton superconducting linac
p-RCS: proton rapid cycling synchrotron
MSS: Medium-Stage Synchrotron
SS: Super Synchrotron
Ion beams have dedicated linac (I-Linac) and RCS (I-RCS)
Details by Y.R. Lu on SPPC III

## Slide 23: Preliminary design of the injector chain
Accelerator schemes and parameter lists
Preparation of the beam for injection into SPPC: energy, intensity, emittance, bunch pattern, turnaround time
Maximize the performance with modest cost for each accelerator (different settings from service to SPPC)
Pre-conceptual design on each stage:
  p-Linac/i-Linac: Yuanrong Lu, Haifeng Li (RFQ, DTL, SC cavities)
  p-RCS/i-RCS: Linhao Zhang, Jingyu Tang (parameter design)
  MSS: Yang Hong (parameter design, lattice)
  SS: Xiangqi Wang, Tao Liu (parameters, lattice, injection/extraction, acceleration)

## Slide 24: Major parameters for the injector chain
 | Value | Unit |  | Value | Unit
p-Linac |  |  | MSS |  | 
Energy | 1.2 | GeV | Energy | 180 | GeV
Average current | 1.4 | mA | Average current | 20 | uA
Length | ~300 | m | Circumference | 3500 | m
RF frequency | 325/650 | MHz | RF frequency | 40 | MHz
Repetition rate | 50 | Hz | Repetition rate | 0.5 | Hz
Beam power | 1.6 | MW | Beam power | 3.7 | MW
p-RCS |  |  | SS |  | 
Energy | 10 | GeV | Energy | 2.1 | TeV
Average current | 0.34 | mA | Accum. protons | 1.0E14 | 
Circumference | 970 | m | Circumference | 7200 | m
RF frequency | 36-40 | MHz | RF frequency | 200 | MHz
Repetition rate | 25 | Hz | Repetition period | 30 | s
Beam power | 3.4 | MW | Protons per bunch | 1.5E11 | 
 |  |  | Dipole field | 8.3 | T

## Slide 25: More about the Injector Chain
Injector chain by itself is a very complicated and powerful accelerator system, large enough by a single stage
  Totally new, different from LHC or Tevatron (building-up by steps)
  No close reference accelerators (scaled up by large factors)
  Should be built earlier than SPPC by a few years to allow relatively long-time commissioning stage by stage
Rich physics programs for each stage, e.g.:
  p-Linac: producing intense neutrons and muons and rare isotopes for wide research areas
  p-RCS and MSS: producing very powerful neutrino beams for neutrino oscillation experiments
Key technical challenges should be identified, so needed R&D program can be pursued (e.g. high-Q ferrite-loaded RF cavities)

## Slide 26: Plan on the SPPC chapter in the CDR
Subsection material preparation assignment: November 2017
Material collection will be finished by December 2017 (Jingyu Tang)
First version to the editor: mid-January 2018
Second version to the editor : end-January 2018
Final version to the editor: mid-February

## Slide 27: Summary
SPPC - the second phase of CEPC-SPPC, a pre-conceptual design for a 75-TeV pp collider is ongoing, to explore new physics in energy frontier
SPPC will provide wide physics programs, including the collider and the beams from the injector accelerators
Study focusing on a few key accelerator physics issues: lattice, collimation, b-b effects, longitudinal dynamics, instabilities, injection/extraction
Identifying technical challenges to be solved in the next two decades, besides high-field SC magnets and beam screen
Pre-conceptual study on the injector chain is also under way
SPPC chapter writing in the CDR is in progress, first version in January 2018

## Slide 28: Thank you for attention!