## Slide 1: High Energy CEPC Injector Based on Plasma Wakefield Accelerator
Wei Lu
Tsinghua University
International Workshop on High Energy Circular Electron-Positron Collider
Nov 6-8, IHEP, Beijing, China

## Slide 2: AARG A joint effort of IHEP and Tsinghua
IHEP
Jie Gao, Yongsheng Huang, Dazhang Li, Dou Wang, Cai Meng, Tianjian Bian, Zhenchao Liu, Yiwei Wang
Tsinghua
Wei Lu, Shiyu Zhou, Yue Ma, Jianfei Hua, Chi-hao Pai, Shuang Liu

## Slide 3: Outline
Plasma based wakefield accelerator (PBA)
Key accelerator physics for PBA
Plasma based injector for CEPC
Boundary conditions
Overall concept design
Preliminary design parameters

## Slide 4
Plasma Based Wakefield Acceleration
Huge gradient (~100GV/m) + Tiny structures (~10-100um)
T.Tajima and J.M. Dawson PRL (1979) LWFA
P.Chen, J.M. Dawson et.al. PRL (1983) PWFA
Laser or beam Pulse
Wake
Trailing beam

## Slide 5
Important progress in past decade

## Slide 6
Key physics issues for a plasma accelerator
The structure issue:
Wake excitation for given drivers ……
The energy spread and efficiency issue:
Beam loading, pulse shaping, transformer ratio ……
The stability issue:
Driver evolution, matching, guiding, instabilities ……
The injector issue:
Self-injection, wave breaking, controlled injection ….
The overall design and staging issue:
Parameter optimization for a plasma based accelerator to match the requirements of beam parameters,staging,external injection ….

## Slide 7
Beam loading efficiency and energy spread
High efficiency (near 100%) + Uniform acceleration
M. Tzoufras,W. Lu et al., PRL (2008), PoP [invited] (2009)

## Slide 8: Verified through Experiment
30-50% energy conversion efficiency

## Slide 9: High Transformer Ratio PWFA
E-
E+
Transformer ratio: R = E+/E-
Lower Drive Beam Energy
High efficiency
TR=5
1% energy spread
Parameters | Value
Peak current | 6.3 kA
Beam length | ~200 fs
Initial energy | 1.5 GeV
Lu et al., PAC 2009, Huang et al., IPAC17

## Slide 10: Plasma Based Injector for CEPC
The boundary condition
Overall concept design
Driver/trailer beam generation through Photo-injector
HTR PWFA with good stability (single stage TR=3-4, Cascaded stage 6-12, high efficiency)
Positron generation and acceleration in an electron beam driven PWFA using hollow plasma channel (TR=1)

## Slide 11
Parameter | Symbol | Unit | Pre-CDR | CDR
e- /e+ beam energy | Ee-/Ee+ | GeV | 6 | 10
Repetition rate | frep | Hz | 50 | 50
e- /e+ bunch population | Ne-/Ne+ |  | 2×1010 | 6.25×109
 |  | nC | 3.2 | 1.0
Energy spread (e- /e+ ) | σE |  | <1×10-3 | <2×10-3
Emittance (e- /e+ ) | εr | mm mrad | <0.3 | <0.3
e- beam energy on Target |  | GeV | 4 | 4 (2)
e- bunch charge on Target |  | nC | 10 | 10
CEPC Pre-CDR/CDR Linac Requirement

## Slide 12: Boundary Conditions
Beam average power (kW 100Hz)
Beam charge per-bunch ( nC)
Beam energy spread (0.2%)
Beam geometric emittance (<0.3mm mrad)
Positron generation and acceleration

## Slide 13: Overall Concept Design based on single stage HTR PWFA (TR=3.5)
By Cai Meng et al.

## Slide 14: HTR PWFA parameter design (TR=3.55)
Input parameters | 
Plasma density | 
Driver charge | 
Driver energy | 
Driver length | 
Driver RMS size | 
Driver normalized emittance | 
Trailor charge | 
Trailor energy | 
Trailor length | 
Trailor RMS size | 
Trailor normalized emittance | 
Input parameters | 
By Shiyu Zhou

## Slide 15: HTR PWFA simulation (TR=3.55)
Output parameters | 
Trailor energy | 
Trailor normalized emittance | 
TR | 
Energy spread | 
Efficiency (driver -> trailor) | 
Output parameters | 
TR | 
Efficiency (driver -> trailor) | 
Plasma length

## Slide 16: 7nC Shaped bunch by S-band photo-injector and LINAC
Simulation data by Zhen Wang of SINAP
0.28
-0.98

## Slide 17: Positron generation
Damping ring | DR V1.0
Energy (MeV) | 240
Circumference （m） | 20
Bending radius (m) | 1.7
B0 (T) | 0.47
U0 (keV/turn) | 0.17
Damping time x/y/z (ms) | 185/185/93
0 (%) | 0.016
0 (mm.mrad) | 6
Nature z (mm) | 3
Extract z (mm) | 1.8
inj (mm.mrad) | 2400
ext x/y (mm.mrad) | 819/815
inj /ext (%) | 1 /0.13
Storage time (ms) | 100
Lattice parameters | 
FODO length (m) | 1.2
Phase per cell | 60
Dipole length (m) | 0.46
Dipole strength (T) | 0.47
Quadrupole length (m) | 0.11
Quadrupole strength (m-2) | 15
RF parameters | 
RF frequency (MHz) | 500
RF voltage (MV) | 0.8
Energy acceptance by RF(%) | 1.8
harmonic | 33
By Dou Wang

## Slide 18: Positron compression
 | BC I | BC II | BC III
Initial energy (MeV) | 240 | 240 | 1300
inj (%) | 0.13 | 1.95 | 1.58
Initial z (um) | 1800 | 220 | 50
fRF (MHz) | 2856 | 2856 | 5712
Voltage(GV) | 0.14 | 5.0 | 36
RF (度) | 90 | 77.8 | 86.6
R56 (mm) | 92 | 13.9 | 2.5
Final energy(MeV) | 240 | 1300 | 3400
ext (%) | 1.95 | 1.58 | 2.0
final z (um) | 220 | 50 | 15
Compression ratio：
BCI：8.2
BCII：4.4
BCIII: 3.3

## Slide 19: Positron Acceleration Uniform acceleration + High efficiency + TR=1
electrons
positrons
By Shiyu Zhou

## Slide 20
Input parameters | 
Plasma density | 
Channel inner radius | 
Channel out radius | 
Bunches | 
Driver charge | 
Driver energy | 
Driver length | 
Driver RMS size | 
Driver normalized emittance | 
Trailor charge | 
Trailor energy | 
Trailor length | 
Trailor RMS size | 
Trailor normalized emittance | 
Input parameters | 
Bunches | 
Output parameters | 
Trailor energy | 
Trailor normalized emittance | 
TR | 
Energy spread | 
Efficiency (driver -> trailor) | 
Output parameters | 
TR | 
Efficiency (driver -> trailor) | 
Plasma length

## Slide 21
Fields Structure

## Slide 22: Electron driver/trailer parameters for e+ acceleration
Input parameters | 
Plasma density | 
Driver charge | 
Driver energy | 
Driver length | 
Driver RMS size | 
Driver normalized emittance | 
Trailor charge | 
Trailor energy | 
Trailor length | 
Trailor RMS size | 
Trailor normalized emittance | 
Input parameters | 
TR~3.5

## Slide 23: Cascaded HTR PWFA
The 1st stage
Two shaped bunches (5ps 25nC, 1ps 5nC)
TR=2 or 3
Efficiency (60%)
The 2nd stage
Controlled injection for e (200fs 1nC or 2nC)
TR=2 or 3
Single stage efficiency (60%)
Overall TR=(1+TR1)*TR2
Overall efficiency Q3(1+TR1)*TR2/(Q1+Q2)=40%
The positron stage
Combining e+ with e- (200fs 1nC )
TR=1 Single stage efficiency (~50%)
Overall efficiency for positron 20%

## Slide 24
Driver pulse | 5ps
Driver charge Q1 | 25nC
Driver energy | 2GeV
Trailer pulse | 0.5ps
Trailor charge Q2 | 5nC
Trailor energy | 2GeV
Final energy | 8GeV
Average TR | 3
Efficiency | ~60%
Parameters of Stage I
Electron Acceleration Stage ( I and II)
Notes: 补了一张颜色比较深的图~

## Slide 25
Thank you for your attention!