## Slide 1: CEPC SRF Parameters (100 km Main Ring)
Jiyuan Zhai
IHEP
2016-11-30

## Slide 2: CEPC 100 km & FCC-ee (w/o tt) Machine Top Parameters
CEPC-WD161123; FCC-V3 | C-H-HV | C-H-LP | C-H-HL | C-W | C-Z-LL | C-Z-HL | F-H | F-W | F-Z-HL | F-Z-LL
Luminosity / IP [1034 cm-2s-1] | 2 |  | 3 | 4.5 | 1.2 | 70 | 5 | 19 | 207 | 90
Beam energy [GeV] | 120 |  |  | 80 | 45.5 |  | 120 | 80 | 45.6 | 
SR power / beam [MW] | 33 |  | 50 | 18.3 | 0.84 | 50 | 50 |  |  | 
Beam current / beam [mA] | 20 |  | 30 | 56 | 24 | 1450 | 30 | 152 | 1450 | 
Bunches / beam | 1006 | 425 | 644 | 1100 | 1100 | 65716 | 780 | 5260 | 30180 | 91500
Bunch spacing [ns] APDR / DR | 20 / 166 | 47 / 391 | 31 / 257 | 17 / 151 | 17 / 151 | NA / 1.5 | 400 | 50 | 7.5 | 2.5
Bunch population [1011] | 0.41 | 0.97 |  | 1.05 | 0.46 |  | 0.8 | 0.6 | 1 | 0.33
Horizontal emittance εx [nm] Vertical emittance εy [pm] | 0.88 2.7 | 1.56 4.7 |  | 2.68 8 | 0.93 4.9 |  | 0.61 1.2 | 0.26 1 | 0.2 1 | 0.09 1
Momentum compaction [10-5] | 0.87 | 1.3 |  | 3.1 | 3.3 |  | 0.7 |  |  | 
Betatron function at IP βx* [m] βy* [mm] | 0.08 2 | 0.14 2 |  | 0.1 1 | 0.12 1 |  | 1 2 | 1 2 | 0.5 1 | 1 2
Horizontal beam size σx* [μm] σy* [nm] | 8.46 73 | 15 97 |  | 16.4 90 | 10.5 70 |  | 25 49 | 16 45 | 10 32 | 9.5 45
Energy spread [%] SR Total | 0.1 1.95 | 0.1 1.5 |  | 0.07 ? | 0.04 ? |  | 0.10 0.12 | 0.07 0.10 | 0.04 0.22 | 0.04 0.09
Bunch length [mm] SR Total | 1.53 1.63 | 2.72 2.9 |  | 3.8 3.9 | 3.93 4.0 |  | 2.0 2.4 | 2.0 3.1 | 1.2 6.7 | 1.6 3.8
Energy loss / turn [GeV] | 1.67 |  |  | 0.33 | 0.03 |  | 1.67 | 0.33 | 0.03 | 0.03
Total RF voltage [GV] | 3.56 | 2.22 |  | 0.63 | 0.11 |  | 3 | 0.8 | 0.4 | 0.2
RF frequency [MHz] | 650 |  |  |  |  |  | 400 |  |  | 
Energy acceptance / RF [%] | 1.95 / 6 | 1.5 / 2.2 |  | 1 / 1.5 | 1 / 1.1 | 1 / 1.1 | 2 / 7 | 2 / 5.5 | 1 / 7.2 | 1 / 4.7
Hourglass factor | 0.98 | 0.95 |  | 0.84 | 0.91 | 0.91 | 0.92 | 0.95 | 0.92 | 0.98
Beam-beam parameter ξx ξy | 0.009 0.083 | 0.013 0.083 |  | 0.008 0.055 | 0.008 0.054 |  | 0.08 0.14 | 0.07 0.16 | 0.025 0.16 | 0.05 0.13
Lifetime [min] BS or BB | 52 | 25? |  | 144 | 238 | 238 | 67 | 90 | 94 | 185
circumference 100 km, bending radius 11 km, crossing angle 30 mrad, two IPs

## Slide 3: Constraints for SRF Parameter Choice
Common cavity for DR, RF sections NRF-DR-CC = 2 , half ring bucket filled; common cavity for (A)PDR, RF sections NRF-PDR-CC = 8, 2 half sections each
Total bunch train length per beam Tt /T0 < 6 % of the circumference ((A)PDR)
Cavity operation gradient Eacc < 20 MV/m ( < 16 MV/m if use beat cavity)
HOM power / cavity PHOM < 1 kW (HOM coupler limit including pulsed HOM power of (A)PDR; not for HL-Z)
Input power / cavity PCPL< 300 kW (only consider one coupler per cavity, variable input coupler, otherwise large extra power of mismatching; not for HL-Z)
Cavity operation Q0 < 2E10 at 2 K (magnetic shielding and field emission limit, long-term cavity performance degradation)
Cryogenic heat load of total cavity wall loss at 4.5 K eq. WCAV < 30 kW
Detuning frequency Δf < 3 kHz (revolution frequency; not for HL-Z)
Max phase shift of bunch train Δφmax < 5 deg (lifetime, luminosity, instability)
Cryomodule length LCM < 12 m

## Slide 4: Considerations for SRF Parameter Choice
Higgs and W share the same cavities, coupler mismatching if fixed coupling
HL-Z should use independent SRF cavity system (e.g. KEKB/BEPCII type)
Higgs cavities on-line detuned or off-line during W run
Higgs (and W) cavities off-line during Z run
Less cell number for easy HOM damping, cavity handling and processing
Klystron output power (< 1.2 MW) and distribution (even cavity number per klystron), could have two types of klystron with different power level
Input coupler must be assembled with cavity in Class 10 cleanroom, and should have small static and dynamic heat load
Two or even more input couplers per cavity should be considered especially for HL-Z
Instability feedback for large detuning of HL-Z
Phase shift correction with beat cavity for (A) PDR

## Slide 5
WD161123, Zhai161130 | H-HV | H-LP | H-HL | W | Z-LL | Z-HL
Luminosity [1034 cm-2s-1] | 2 |  | 3 | 4.5 | 1.2 | 70
SR power / beam [MW] | 33 |  | 50 | 18.3 | 0.84 | 50
Beam current / beam [mA] | 20 |  | 30 | 56 | 24 | 1450
Bunches / beam | 1006 | 425 | 644 | 1100 | 1100 | 65716
Bunch spacing [ns] APDR / DR | 20 / 166 | 47 / 391 | 31 / 257 | 17 / 151 | 17 / 151 | NA / 1.5
Bunch charge / length [nC / mm] | 6.6 / 1.6 | 15.5 / 2.9 | 15.5 / 2.9 | 16.8 / 3.9 | 7.4 / 4.0 | 7.4 / 4.0
RF voltage [GV] (w/ para. loss) | 3.57 | 2.24 |  | 0.65 | 0.12 | 
Synchrotron phase [deg] (from low zero) | 152.1 | 131.3 |  | 148.5 | 161.7 | 
Number of cells in a cavity | 2 |  |  |  |  | 1
Number of 650 MHz cavities | 384 | 240 | 384 | 128 | 16 | 64
Number of cryomodules / cavity per module | 64 / 6 | 48 / 5 | 64 / 6 | 32 / 4 | 16 / 1 | 64 / 1
Cavity operating gradient [MV/m] (< 20) | 20 | 20 | 12.6 | 11.0 | 16.7 | 8.4
Q0 at operating gradient @ 2 K (< 2E10) | 2.0E+10 | 1.2E+10 | 8.0E+09 | 8.0E+09 | 8.0E+09 | 8.0E+09
Input power / cavity (match) [kW] (< 300) | 173 | 277 | 263 | 295 | 117 | 1757
HOM power / cavity [kW] (< 1) | 0.25 | 0.42 | 0.63 | 1.04 | 0.20 | 5.84
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 28.7 | 30.0 | 28.2 | 7.1 | 2.1 | 1.0
QL (match) | 2.4E+06 | 1.5E+06 | 6.3E+05 | 4.3E+05 | 2.5E+06 | 2.1E+04
Cavity bandwidth / fill time [kHz / μs] | 0.3 / 1196 | 0.4 / 747 | 1.0 / 308 | 1.5 / 209 | 0.3 / 1207 | 31.4 / 10
Detuning frequency [kHz] (< 3) | -0.25 | -0.19 | -0.45 | -1.24 | -0.40 | -47.62
Cavity stored energy [J] | 103.2 | 103.4 | 40.5 | 30.8 | 70.8 | 8.9
Max voltage drop (4 trains / beam) [%] | 7 | 7 | 16 | 34 | 10 | decelerate
Max phase shift (4 trains / beam) [deg] | 4.3 | 5.8 | 14.1 | 23.0 | 6.0 | decelerate
CEPC 100 km SRF Parameters (DR and 4+4 APDR)

## Slide 6
Higgs-HV Cell Number Comparison
WD161123, Zhai161130 | H-HV 2-cell | H-HV 3-cell | H-HV 4-cell | H-HV 5-cell
Luminosity [1034 cm-2s-1] | 2 |  |  | 
SR power / beam [MW] | 33 |  |  | 
RF voltage [GV] (w/ para. loss) | 3.57 |  |  | 
Number of cells in a cavity | 2 | 3 | 4 | 5
Number of 650 MHz cavities | 384 | 320 | 256 | 256
Number of cryomodules / cavity per module | 64 / 6 | 64 / 5 | 64 / 4 | 64 / 4
Cavity operating gradient [MV/m] (< 20) | 20 | 16.2 | 15.1 | 12.1
Q0 at operating gradient @ 2 K (< 2E10) | 2.0E+10 | 1.5E+10 | 1.5E+10 | 1.2E+10
Input power / cavity (match) [kW] (< 300) | 173 | 207 | 259 | 259
HOM power / cavity [kW] (< 1) | 0.25 | 0.38 | 0.51 | 0.63
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 28.7 | 30.7 | 28.8 | 28.8
QL (match) | 2.4E+06 | 2.0E+06 | 1.8E+06 | 1.5E+06
Cavity bandwidth / fill time [kHz / μs] | 0.3 / 1196 | 0.3 / 957 | 0.4 / 897 | 0.4 / 718
Detuning frequency [kHz] (< 3) | -0.25 | -0.31 | -0.33 | -0.42
Cavity stored energy [J] | 103.2 | 99.2 | 116.2 | 93.1
Max voltage drop (4 trains / beam) [%] | 7 | 8 | 9 | 11
Max phase shift (4 trains / beam) [deg] | 4.3 | 5.4 | 5.8 | 7.2

## Slide 7
Higgs-LP Cell Number Comparison
WD161123, Zhai161130 | H-LP 2-cell | H-LP 3-cell | H-LP 4-cell | H-LP 5-cell
Luminosity [1034 cm-2s-1] | 2 |  |  | 
SR power / beam [MW] | 33 |  |  | 
RF voltage [GV] (w/ para. loss) | 2.24 |  |  | 
Number of cells in a cavity | 2 | 3 | 4 | 5
Number of 650 MHz cavities | 240 |  |  | 
Number of cryomodules / cavity per module | 48 / 5 | 48 / 5 | 48 / 5 | 48 / 5
Cavity operating gradient [MV/m] (< 20) | 20.2 | 13.5 | 10.1 | 8.1
Q0 at operating gradient @ 2 K (< 2E10) | 1.2E+10 | 8.0E+09 | 6.0E+09 | 5.0E+09
Input power / cavity (match) [kW] (< 300) | 277 |  |  | 
HOM power / cavity [kW] (< 1) | 0.42 | 0.63 | 0.83 | 1.04
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 30.0 | 30.0 | 30.1 | 28.9
QL (match) | 1.5E+06 | 1.0E+06 | 7.6E+05 | 6.1E+05
Cavity bandwidth / fill time [kHz / μs] | 0.4 / 747 | 0.6 / 498 | 0.9 / 374 | 1.1 / 299
Detuning frequency [kHz] (< 3) | -0.19 | -0.28 | -0.37 | -0.47
Cavity stored energy [J] | 103.4 | 69.0 | 51.9 | 41.6
Max voltage drop (4 trains / beam) [%] | 7 | 10 | 13 | 17
Max phase shift (4 trains / beam) [deg] | 5.8 | 8.7 | 11.6 | 14.5

## Slide 8
Higgs-HL Cell Number Comparison
WD161123, Zhai161130 | H-HL 2-cell | H-HL 3-cell | H-HL 4-cell | H-HL 5-cell
Luminosity [1034 cm-2s-1] | 3 |  |  | 
SR power / beam [MW] | 50 |  |  | 
RF voltage [GV] (w/ para. loss) | 2.24 |  |  | 
Number of cells in a cavity | 2 | 3 | 4 | 5
Number of 650 MHz cavities | 384 |  |  | 
Number of cryomodules / cavity per module | 64 / 6 | 64 / 6 | 64 / 6 | 64 / 6
Cavity operating gradient [MV/m] (< 20) | 12.6 | 8.4 | 6.3 | 5.1
Q0 at operating gradient @ 2 K (< 2E10) | 8.0E+09 | 5.0E+09 | 4.0E+09 | 3.0E+09
Input power / cavity (match) [kW] (< 300) | 263 |  |  | 
HOM power / cavity [kW] (< 1) | 0.63 | 0.95 | 1.26 | 1.58
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 28.2 | 30.1 | 28.3 | 30.3
QL (match) | 6.3E+05 | 4.2E+05 | 3.2E+05 | 2.5E+05
Cavity bandwidth / fill time [kHz / μs] | 1 / 308 | 1.5 / 206 | 2.1 / 155 | 2.6 / 124
Detuning frequency [kHz] (< 3) | -0.45 | -0.68 | -0.90 | -1.13
Cavity stored energy [J] | 40.5 | 27.1 | 20.4 | 16.3
Max voltage drop (4 trains / beam) [%] | 16 | 24 | 32 | 40
Max phase shift (4 trains / beam) [deg] | 14 | 21 | 28 | 35

## Slide 9
W Cell Number Comparison
WD161123, Zhai161130 | W 2-cell | W 3-cell | W 4-cell | W 5-cell
Luminosity [1034 cm-2s-1] | 4.5 |  |  | 
SR power / beam [MW] | 18.3 |  |  | 
Total RF voltage [GV] (w/ para. loss) | 0.65 |  |  | 
Number of cells in a cavity | 2 | 3 | 4 | 5
Number of 650 MHz cavities | 128 |  |  | 
Number of cryomodules / cavity per module | 32 / 4 | 32 / 4 | 32 / 4 | 32 / 4
Cavity operating gradient [MV/m] (< 20) | 11.0 | 7.4 | 5.5 | 4.4
Q0 at operating gradient @ 2 K (< 2E10) | 8.0E+09 | 8.0E+09 | 8.0E+09 | 8.0E+09
Input power / cavity (match) [kW] (< 300) | 295 |  |  | 
HOM power / cavity [kW] (< 1) | 1.0 | 1.6 | 2.1 | 2.6
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 7.1 | 4.8 | 3.6 | 2.9
QL (match) | 4.3E+05 | 2.9E+05 | 2.1E+05 | 1.7E+05
Cavity bandwidth / fill time [kHz / μs] | 1.5 / 209 | 2.3 / 140 | 3 / 105 | 3.8 / 84
Detuning frequency [kHz] (< 3) | -1.24 | -1.86 | -2.47 | -3.08
Cavity stored energy [J] | 30.8 | 20.6 | 15.5 | 12.5
Max voltage drop (4 trains / beam) [%] | 23 | 34 | 46 | 57
Max phase shift (4 trains / beam) [deg] | 34 | 51 | 68 | 85

## Slide 10: FCC 100 km SRF Parameters
Erk Jensen, FCC Week 2016