## Slide 1: CEPC parameter optimization and lattice design
Dou Wang, Jie Gao, Yuan Zhang, Yiwei Wang, Feng Su, Huiping Geng, Cai Meng, Jiyuan Zhai, Zhenchao Liu, Bai Sha, Tianjian Bian, Na Wang
CEPC AP meeting, 2016.10.21

## Slide 2: parameter for CEPC partial double ring （wangdou20161012）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 52.0
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 3.2
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 0.59
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 3.44

## Slide 3: parameter for CEPC –larger y* （wangdou20161017）
 | Pre-CDR | H-high lumi. | H-low power | H-large y | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 2.596 | 4.11 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.4 | 0.85 | 0.6
Bunch number | 50 | 107 | 70 | 153 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 16.9 | 26.8 | 52.0
SR power /beam (MW) | 51.7 | 50 | 32.5 | 50 | 15.7 | 3.2
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 1.48 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.139/0.0023 | 0.16/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 2.05/0.0062 | 0.93/0.003 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 16.9/0.12 | 12.2/0.056 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.017 | 0.0145 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.084 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 3.51 | 0.7 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.68 | 3.23 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 2.91 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.52 | 0.47 | 0.59
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 2.4 | 1.3 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.34 | 0.28 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.95 | 0.89 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 2.03 | 3.5 | 3.44

## Slide 4: New Z parameter for higher luminosity （wangdou20161018）
 | Pre-CDR | H-high lumi. | H-low power | W | Z-high lumi. | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 2.36 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 2.0 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100 | 3200
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 173 | 151.3
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 10.6 | 9.26
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 10.9 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.09/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 7.2/0.038 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 25.5/0.19 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.021 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.079 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 3.7 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.86 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 6.51 | 1.7
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.6 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.32 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.75 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 10.1 | 10.0

## Slide 5
bypass (pp)
bypass (pp)
Advantage:
Avoid pretzel orbit
Accommodate more bunches at Z/W energy
Reduce beam power with crab waist collision

## Slide 6: CEPC damping ring requirement
Energy: 1.1GeV
Storage time: 20ms
Injected emittance (normalized): 3500 mm-mrad, injected energy spread ~ 0.25%
Extracted energy spread <1×10-3
No strong requirement for the extracted emittance (<0.5inj)!
Transverse acceptance > 3*injection beam size

## Slide 7: CEPC DR design
 | DR V1.0
Energy (GeV) | 1.1
circumference | 58.5
Bending radius (m) | 3.6
B0 (T) | 1.01
U0 (keV/turn) | 35.8
Damping time x/y/z (ms) | 12/12/6 (61538 turns)
0 (%) | 0.049
0 (mm.mrad) | 302
Nature z (mm) | 7 (23ps)
Extract z (mm) | ~7 (23ps)
inj (mm.mrad) | 3500
ext x/y (mm.mrad) | 434/145
inj /ext (%) | 0.25 /0.05
Energy acceptance by RF(%) | 1.0
fRF=650MHz
VRF=1.8MV
Bunch compressor

## Slide 8: DR lattice design
FODO length (m) | 2.4
Phase per cell | 60
Dipole length (m) | 0.71
Dipole strength (T) | 1.0
Quadrupole length (m) | 0.2
Quadrupole strength (m-2) | 4.1
Sextupole length (m) | 0.06

## Slide 9: DA
inj / 0=11.6
inj / 0=3.4
inj,max=sqrt(1.626um*4m)
= 2.55mm
Tracking 240000turns （4 damping time）
5 times of injection beam size

## Slide 10: Status of damping ring design
 | unit | CDR | Now
Ext bunch length | ps | < 30 | 23
Ext energy spread | % | < 0.1 | 0.05
Ext emittace | mm.mrad | 1500 | 434/145
Energy acceptance | % |  1 | 1
DA |  | > 10x/10y | 150x/110y (on momentum) 30x/60y (0.75%)
Damping time | ms | < 20 | 12/12/6

## Slide 11: Primary design for bunch compressor
Dispersive section
RF structure
E0
E1

## Slide 12: Parameter design
入口：0=7mm， 0=0.05%， E0=1.1 GeV
出口：1<3mm， 1=??(0.1%)， E1=??

## Slide 13: Parameters of CEPC bunch compressor
 | BC (case I) | BC (case II)
初始能量 (GeV) | 1.1 | 1.1
初始能散 (%) | 0.05 | 0.05
初始束长 (mm) | 7 | 7
高频频率 (MHz) | 2856 | 2856
高频腔压 (MV) | 14.5 | 19.3
加速相位 (度) | 86 | 87
R56 (m) | -4 | -3
出口能量 (GeV) | 1.101 | 1.101
出口能散 (%) | 0.17 | 0.23
出口束长 (mm) | 2 (6.7ps) | 1.5 (5ps)
束长压缩比：3.5~4.7
束长压缩比可调

## Slide 14: BC energy spread and VRF vs. bunch length

## Slide 15: Check Yiwei’s lattice
z=2.92mm

## Slide 16: Check Yiwei’s lattice （ shorter bunch ）
Bunch length in parameter table: 2.7 mm
Plan:
- Re-optimize with 2.7mm bunch length
- Further optimization with MODE
- add additional sextupoles in IR

## Slide 17
synchrotron radiation of IR
IP
FT
CCX
CCY
MT
L*= 1.5m
x*= 0.22mm
y*= 1mm
GQD0= -200T/m
GQF1= 200T/m
LQD0=1.69m
LQF1=0.90m
565 kev
1952 kev
126kev
434kev
126kev
203kev
374kev
472kev
472kev

## Slide 18
synchrotron radiation of PDR (w/o IR)
Feng Su, Yiwei Wang
BSEP1：1631kev
BSEP3：1496kev
QBQ1：985kev

## Slide 19: synchrotron radiation spectrum of CEPC dipoles
Critical energy:
Energy spectrum:
Angular distribution:

## Slide 20: Arc dipole

## Slide 21: IP dipole

## Slide 22: septum

## Slide 23: Electric seperator