## Slide 1: CEPC Partial Double Ring Lattice Design and DA Study
SU Feng GAO Jie WANG Dou WANG Yiwei Li Yongjun BAI Sha
BIAN Tianjian GENG Huiping ZHANG Yuan
Institute of High Energy Physics
2016.10.28

## Slide 2: Outline
Design Goal
CEPC PDR lattice设计和DA优化
CEPC APDR lattice设计和DA优化
CEPC DR lattice设计和DA优化

## Slide 3
Design Goal
Outline

## Slide 4: Parameter for CEPC partial double ring （wangdou20160918）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 5.2 | 6.4
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.16 | 0.78
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 36.5 | 67.6
SR power /beam (MW) | 51.7 | 50 | 32.5 | 21.3 | 4.1
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.44 | 2.9
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.0078 | 0.88/0.008
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 9.7/0.088 | 9.4/0.089
x/IP | 0.118 | 0.041 | 0.042 | 0.013 | 0.01
y/IP | 0.083 | 0.11 | 0.11 | 0.073 | 0.072
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.74 | 0.11
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.95 | 3.78
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.88 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.7 | 1.2
n | 0.23 | 0.35 | 0.34 | 0.49 | 0.34
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.92 | 0.93
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 4.3 | 4.48

## Slide 5: Design goals of main ring
*assumming coupling factor =5% for injection beam,
x,r=200 m, x,i=60 m, ws = 4 mm, nr = 5, ns = 5
Parameter | Symbol | Unit | Value
Luminosity per IP | Lmax | 1034cm-2s-1 | 2.01
Main ring emittance | x/y | nmrad | 2.05 /0.0062
Injection emittance | x/y | nmrad | 3.5 / 0.17
Transvers acceptance* | Ax/Ay | nmrad | 787 / 4.17
DA requirement from beam-beam (inclu. errors and beam-beam effect) | DAx/DAy |  | 20 / 40 (dp/p=0) 5 / 10 (dp/p=2%)
DA requirement from injection (inclu. errors and beam-beam effect) | DAx/DAy |  | 20 / 26 (dp/p=0 and dp/p=0.5%)

## Slide 6
2. CEPC PDR Parameter and Lattice Layout
Outline

## Slide 7
CEPC Partial Double Ring Layout
SU Feng
2016.9.15
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3.7Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 3.7Km
IP2_pp/IP4_pp, 1132.8m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 944m
2 Short ARC, 24*FODO, 1132.8m
4 Medium ARC, 112*FODO, 5286.4m
4 Long ARC, 124*FODO, 5852.8m
C=61km
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
Bypass
about 42m

## Slide 8
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 5.2 | 6.4
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.16 | 0.78
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 36.5 | 67.6
SR power /beam (MW) | 51.7 | 50 | 32.5 | 21.3 | 4.1
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.44 | 2.9
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.0078 | 0.88/0.008
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 9.7/0.088 | 9.4/0.089
x/IP | 0.118 | 0.041 | 0.042 | 0.013 | 0.01
y/IP | 0.083 | 0.11 | 0.11 | 0.073 | 0.072
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.74 | 0.11
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.95 | 3.78
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.88 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.7 | 1.2
n | 0.23 | 0.35 | 0.34 | 0.49 | 0.34
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.92 | 0.93
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 4.3 | 4.48
Parameter for CEPC partial double ring （wangdou20160918）

## Slide 9
For CEPC 120GeV beam:
Max. deflection per separator is 66μrad.
CEPC Partial Double Ring Layout
B1
B2
B3
B4
15mrad
Full crossing angle 30mrad
Separator
Version 1.0
sufeng
2016.9.15
1851.733m
12
62.5urad
4.5m
IP
567.1m
614.4m
307.2m
7.852m
65m
357.5m

## Slide 10
Chart: 
CEPC PDR1.0.3 noFFS

## Slide 12
Emittance Increase (2.06nm->2.1668nm)
Notes: Integration radius

## Slide 13
Detail of CEPC PDR1.0.3 noFFS

## Slide 14
Parameters of Separators sufeng201605 |  |  |  | 
Separator length | 4.5 | m |  | 
Electrode length | 4 | m |  | 
Maximum operating field strength | 1.875 | MV/m | 上限2MV/m | 
Beam energy | 120 | GeV |  | 
Maximum deflection per separator at 120GeV | 62.5 | urad | 微弧度 | 
Number of separators per collision point | 12*2=24 |  |  | 
Total number of separators (PDR) | 24*2=48 |  |  | 
Total number of separators (APDR6) | 24*6=144 |  |  | 
Total number of separators (APDR8) | 24*8=192 |  |  | 
Notes: Maximum operating field strength

## Slide 15
According to CEPC Pre-CDR Magnet Parameter
Dipole magnets | 
Quantity | 1984
Maximum field strength(T) | 0.07
Magnetic gap (mm) | 80
Bending angle (mrad) | 3.17
Magnetic Length (m) | 18
Bending radius (m) | 6094
Good field region (mm) | 100
Core cross section (W*H) (mm) | 450*400
CEPC MQ | 
Quantity | 2304
Bore diameter (mm) | 100
Field Gradient (T/m) | 10
Magnetic Length (m) | 2.0
Core width and height (mm) | 700*700
Core length (mm) | 1960
Super Conducting Q in CEPC IR | QF | QD
Field Gradient (T/m) | 304 | 309
Magnetic Length (m) | 1.25 | 0.72
Peak field in coil (T) | 7.2 | 7.1
Coil inner diameter (mm) | 40 | 40
Coil out diameter (mm) | 74 | 74
Cryostat diameter (mm) | 400 | 400
Coil mechanical length (mm) | 1500 | 950
CEPC MS | SD | SF
Quantity | 992 | 992
Aperture diameter (mm) | 120 | 120
Good field region (mm) | 100 | 100
Strength of sextupole field (T/m^2) | 180 | 180
Magnetic Length (m) | 700 | 400
Core width and height (mm) | 520 | 520
Length of iron core (mm) | 670 | 370

## Slide 16
Dipole Strength PDR1.0.3 without FFS
 | Angle(mrad) | L(m) | Rho(m) | Brho(E0/c)(T/m) | B(T) | Ek(KeV) | KeV/m
B0 | 3.205 | 19.6 | 6115.44 | 400 | 0.06541 | 626.349 | 31.956
BSepL | -0.0625 | 4.5 | -72000 | 400 | -0.00556 | 53.2 | 11.822
BMatch1L | -8.344 | 19.6 | -2348.99 | 400 | -0.1702 | 1630.66 | 83.1967
BMatch2L | 1.997 | 19.6 | 9814.72 | 400 | 0.0407 | 390.271 | 19.9118
BMatch3L | -7.653 | 19.6 | -2561.09 | 400 | -0.1562 | 1495.61 | 76.3069
B2 | 2.1428 | 19.6 | 9146.91 | 400 | 0.04373 | 418.764 | 21.3655
B3 | -2.1428 | 19.6 | -9146.91 | 400 | -0.04373 | 418.764 | 21.3655
BMatch3R | 7.653 | 19.6 | 2561.09 | 400 | 0.1562 | 1495.61 | 76.3069
BMatch2R | -1.997 | 19.6 | -9814.72 | 400 | -0.0407 | 390.271 | 19.9118
BMatch1R | 8.344 | 19.6 | 2348.99 | 400 | 0.1702 | 1630.66 | 83.1967
BSepR | 0.0625 | 4.5 | 72000 | 400 | 0.00556 | 53.2 | 11.822

## Slide 17
CEPC PDR1.0.3 with FFS (Yiwei20160817)
Chart: 

## Slide 18
CEPC ARC+PDR_FFS

## Slide 19
Emittance Increase (2.06nm->2.147368nm)
Notes: Integration radius

## Slide 20: DA result
Dynamic aperture result
  W/O error of the magnets
  Synchrotron motion included, w/ damping
  Tracking with 100 turns
  Coupling factor =0.003 for y
  Working point (0.08, 0.22)
DAx
DAy

## Slide 21
18 45

## Slide 22
  full_ring240 half_ring480 full_ring480

## Slide 23
  CEPC_ARC_PDR_IR_96fam_damp ( Wang Yiwei) 100圈
0.8mm
5um
21.731um
0.08026um
37 SigmaX
63 SigmaY

## Slide 24
  CEPC_ARC_PDR_IR_96fam_damp 100圈优化 100代

## Slide 25
3. CEPC APDR lattice设计和DA优化
Notes: Integration radius

## Slide 26
New idea：Advanced PDR （APDR）
To solve the big problem of RF system

## Slide 27
ARC
CEPC Advanced Partial Double Ring Option II
SU Feng
2016.9.30
IP1_ee
IP3_ee
3.7Km
RF
RF
RF
RF
IP1_ee/IP3_ee, 3703.46m
IP2_pp/IP4_pp, 1132.8m
APDR, 1426m
RF Station, 188.8m
ARC1, 6041.6m
ARC1, 4902.87m
C=65640.2m
RF
RF
RF
RF
APDR
APDR
APDR
APDR
APDR
APDR

## Slide 28
PDR1
APDR
APDR
APDR
APDR
APDR
PDR3
APDR
CEPC Advanced Partial Double Ring Optics II

## Slide 29
DA of CEPC Advanced Partial Double Ring Optics II
2 groups sextupoles

## Slide 30
DA of CEPC Advanced Partial Double Ring Optics II
2 groups sextupoles

## Slide 31
APDR Part
1426m
Need update!!
Chart: 

## Slide 32
APDR Part
1426m
New!!
Chart: 

## Slide 33
Cell length=47.2m
Bypass Part at IP2/4
566.4m
s
12Lc
12Lc
24Lc
12Lc
12Lc
12Lc
12Lc
566.4m
566.4m
566.4m
L=42m

## Slide 34
PDR Part

## Slide 35
4. CEPC DR lattice设计和DA优化

## Slide 36
RF station
RF station

## Slide 37
e-ring
IP3
IP1
Double Ring Scheme

## Slide 38
IP3
IP1
Double Ring Scheme

## Slide 39
IP3
IP1
Double Ring Scheme

## Slide 40
DA of Double Ring

## Slide 41
DA of Double Ring
2 groups sextupoles

## Slide 42
Backup

## Slide 43
CEPC Advanced Partial Double Ring Option I
SU Feng
2016.5.23
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 1132.8m
4 ARC1, 124*FODO, 5852.8m
4 ARC2, 24*FODO, 1132.8m
4 ARC3, 79*FODO, 3728.8m
2 ARC4, 24*FODO, 1132.8m
C=62967.86m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
ARC1
ARC3
ARC2
ARC3
ARC2
ARC4
ARC1
APDR
APDR
APDR
APDR
C=65km

## Slide 44
CEPC Advanced Partial Double Ring Optics I
PDR1
PDR3
APDR
APDR
APDR
APDR
Bypass2
Bypass4

## Slide 45
Nonlinear Driving Term (ARC)
Betx：80.992367
bety：14.172123
2nm
Sizmax：402.47um
Sigmay：9.22um
X：60 Sigma
Y：813 Sigma
2 groups

## Slide 47
Nonlinear Driving Term (ARC_PDR_20160630)
Betx：80.992367
bety：14.172123
2nm
Sizmax：402.47um
Sigmay：9.22um
X：45 Sigma
Y：780 Sigma
2 groups

## Slide 48
Nonlinear Driving Term (ARC_PDR_FFS_2016.08.29)
Betx：0.219915m
bety：0.001m
2.147368nm
Sizmax：21.731um
Sigmay：0.08026um
2 groups
X：46 Sigma
Y：37 Sigma

## Slide 49
  CEPC_ARC_PDR_IR_96fam_damp 20160929
0.8mm
5um
21.731um
0.08026um
37 SigmaX
63 SigmaY