## Slide 1: CEPC parameter and DA optimization
Dou Wang, Jie Gao, Yuan Zhang, Yiwei Wang, Feng Su, Huiping Geng, Cai Meng, Bai Sha, Tianjian Bian, Na Wang
CEPC AP meeting, 2016.10.28

## Slide 2: Difficulties of CEPC single ring scheme
 | H |  | Z | 
 | Pre-CDR | Low-HOM |  | 
Number of IPs | 2 | 2 | 2 | 
Energy (GeV) | 120 | 120 | 45.5 | 
Circumference (km) | 54 | 54 | 54 | 
SR loss/turn (GeV) | 3.1 | 3.1 | 0.062 | 
Ne/bunch (1011) | 3.79 | 1.0 | 0.13 | 
Bunch number | 50 | 187 | 4800 | 100
Beam current (mA) | 16.6 | 16.6 | 55.5 | 1.1
SR power /beam (MW) | 51.7 | 50 | 3.45 | 0.072
Bending radius (km) | 6.1 | 6.1 | 6.1 | 
Momentum compaction (10-5) | 3.4 | 3.4 | 3.4 | 
IP x/y (m) | 0.8/0.0012 | 0.06/0.001 | 0.4/0.0012 | 
Emittance x/y (nm) | 6.12/0.018 | 6.13/0.018 | 0.9/0.018 | 
Transverse IP (um) | 69.97/0.15 | 19.2/0.13 | 18.9/0.15 | 
x/IP | 0.118 | 0.031 | 0.072 | 
y/IP | 0.083 | 0.074 | 0.028 | 
VRF (GV) | 6.87 | 6.87 | 0.68 | 
f RF (MHz) | 650 | 650 | 650 | 
Nature z (mm) | 2.14 | 2.13 | 1.5 | 
Total z (mm) | 2.65 | 2.4 | 1.5 | 
HOM power/cavity (kw) | 3.6 | 1.0 | 0.55 | 0.01
Energy spread (%) | 0.13 | 0.13 | 0.05 | 
Energy acceptance (%) | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 6.1 | 4.5 | 
n | 0.23 | 0.21 | 0.028 | 
Life time due to beamstrahlung_cal (minute) | 47 | 46 |  | 
F (hour glass) | 0.68 | 0.66 | 0.82 | 
Lmax/IP (1034cm-2s-1) | 2.04 | 2.1 | 1.04 | 0.022

## Slide 3
bypass (pp)
bypass (pp)
Advantage:
Avoid pretzel orbit
Accommodate more bunches at Z/W energy
Reduce beam power with crab waist collision

## Slide 4: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance (DA)
Phase advance per cell (FODO)

## Slide 5: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 6: parameter for CEPC partial double ring （wangdou20160325-54km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 8.5/7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.005/0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.084/0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.27/0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.61/3.09

## Slide 7: parameter for CEPC partial double ring （wangdou20161012-61km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 52.0
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 3.2
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 0.59
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 3.44

## Slide 8: parameter for CEPC –larger y* （wangdou20161017-61km）
 | Pre-CDR | H-high lumi. | H-low power | H-large y | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 2.596 | 4.11 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.4 | 0.85 | 0.6
Bunch number | 50 | 107 | 70 | 153 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 16.9 | 26.8 | 52.0
SR power /beam (MW) | 51.7 | 50 | 32.5 | 50 | 15.7 | 3.2
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 1.48 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.139/0.0023 | 0.16/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 2.05/0.0062 | 0.93/0.003 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 16.9/0.12 | 12.2/0.056 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.017 | 0.0145 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.11 | 0.084 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 3.51 | 0.7 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.68 | 3.23 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 2.91 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.52 | 0.47 | 0.59
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 2.4 | 1.3 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.34 | 0.28 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.95 | 0.89 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 2.03 | 3.5 | 3.44

## Slide 9: New Z parameter for higher luminosity （wangdou20161018-61km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z-high lumi. | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 5.86 | 5.86
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 0.6 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100 | 3200
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 52.0 | 151.3
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 3.2 | 9.26
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 3.1 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 0.87/0.0046 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 10.2/0.068 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.0098 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.073 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 0.12 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.9 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 0.59 | 1.7
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.1 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.24 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.92 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 3.44 | 10.0

## Slide 10: Beam-beam simulation-54km
Case: H-low power
Lifetime: 97 min(16)
Case Z
IBB: Strong-Strong Beam-Beam Code with Beamstrahlung effect
Developed by Y. Zhang@IHEP
Case: Pre-CDR
Lifetime: 108 min(16)
Lifetime: 118 min(16)
Case: H-high lum

## Slide 11: Beam-beam simulation-61km
Case: H-low power
Lifetime: 260 min
IBB: Strong-Strong Beam-Beam Code with Beamstrahlung effect
Developed by Y. Zhang@IHEP
Case: w

## Slide 12: CEPC Higgs luminosity vs. crossing angle
54 km ring

## Slide 13: CEPC Higgs Luminosity vs beam power
54 km ring

## Slide 14: CEPC PDR Luminosity vs circumference
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 15: 100km CEPC PDR vs Fcc-ee
PHOM,CEPC=11.3 kw
The large difference of Z is due to the constraint for RF HOM power.
* Fabiola Gianotti, Future Circular ColliderDesign Study, ICFA meeting, J-PARC, 25-2-2016.

## Slide 16: Parameter for single ring-61km （wangdou20160923）
 | Pre-CDR | New-61km
Number of IPs | 2 | 2
Energy (GeV) | 120 | 120
Circumference (km) | 54 | 61
SR loss/turn (GeV) | 3.1 | 3.0
Ne/bunch (1011) | 3.79 | 3.91
Bunch number | 50 | 54
Beam current (mA) | 16.6 | 16.6
SR power /beam (MW) | 51.7 | 50
Bending radius (km) | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 3.25
IP x/y (m) | 0.8/0.0012 | 0.43/0.00105
Emittance x/y (nm) | 6.12/0.018 | 6.28/0.04
Transverse IP (um) | 69.97/0.15 | 51.7/0.2
x/IP | 0.118 | 0.118
y/IP | 0.083 | 0.074
VRF (GV) | 6.87 | 6.99
f RF (MHz) | 650 | 650
Nature z (mm) | 2.14 | 2.19
Total z (mm) | 2.65 | 2.47
HOM power/cavity (kw) | 3.6 | 3.9
Energy spread (%) | 0.13 | 0.13
Energy acceptance (%) | 2 | 2.1
Energy acceptance by RF (%) | 6 | 6
n | 0.23 | 0.31
Life time due to beamstrahlung_cal (minute) | 47 | 34
F (hour glass) | 0.68 | 0.66
Lmax/IP (1034cm-2s-1) | 2.04 | 2.02

## Slide 17: Non-interleave sextupoles in arc (90/90 FODO)

## Slide 18: Partial double ring FFS design with crab sextupoles
Crab sextupole
Critical energy: Ec=190 keV
Dipole strength: B=0.019 T
Betax=0.25m
Betay=0.00136m
K2hs=26.8 m-3
K2vs=32.2 m-3
IP
The second FFS sextupoles of the CCS-Y section work as the crab sextupoles.

## Slide 19: CEPC IR sextupole strength
Ec=190keV
Ec=190keV
Ec=100keV

## Slide 20: Combine with partial double ring lattice
30 mrad
10 m

## Slide 21: DA bandwidth optimization with MODE (knob arc sextupoles)
test16 from Zhang Yuan@IHEP
Bandwidth = 1.4%.
DA (on-momentum): 32x  60y
Next step:
- Combine arc sextupoles with IR sextupoles.
- Add symmetry in arc
Crab sextupoles – off
Damping -off

## Slide 22
CEPC Advanced Partial Double Ring Layout I
SU Feng
2016.5.23
IP1_ee
IP3_ee
IP2_pp
IP4_pp
3Km
RF
1/2RF
1/2RF
1/2RF
RF
RF
RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 141.6m
4 Medium Straights, 566.4m
4 Long Straights, 1132.8m
4 ARC1, 124*FODO, 5852.8m
4 ARC2, 24*FODO, 1132.8m
4 ARC3, 79*FODO, 3728.8m
2 ARC4, 24*FODO, 1132.8m
C=62967.86m
1/2RF
1/2RF
1/2RF
1/2RF
Bypass
about 42m
ARC1
ARC3
ARC2
ARC3
ARC2
ARC4
ARC1
APDR
APDR
APDR
APDR

## Slide 23
ARC
CEPC Advanced Partial Double Ring Layout II
SU Feng
2016.6.2
IP1_ee
IP3_ee
3Km
1/2RF
1/2RF
1/2RF
1/2RF
IP1_ee/IP3_ee, 2.968Km
IP2_pp/IP4_pp, 1132.8m
APDR, 1052.87m
4 Short Straights, 94.4m
12 Long Straights, 566.4m
4 Long ARC, 124*FODO, 5852.8m
4 Medium ARC, 104*FODO, 4908.8m
4 Short ARC, 14*FODO, 660.8m
C=65640.2m
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
1/2RF
APDR
APDR
APDR
APDR
APDR
APDR

## Slide 24: Bunch length error with RF phase adjustment
H-high lum
H-low power
Z
For Z, error of bunch length: ~-1.5% (8 ring)
For H-high lum., error of bunch length: ~-3% (8 ring)
For H-low power, error of bunch length: ~-4% (6 ring), ~-3% (8 ring)

## Slide 25: Luminosity change with RF phase adjustment
H-high lum
H-low power
Z
For H-high lum., error of luminosity: ~3% (8 ring)
For H-low power, error of luminosity: ~ 3.5% (6 ring), ~2.4% (8 ring)
For Z, error of luminosity: ~1.7% (8 ring)

## Slide 26: RF voltage change with RF phase adjustment
H-high lum
H-low power
Z
For Z, error of VRF: ~ 2.6% (8 ring)
For H-high lum., error of VRF: ~ 2.6% (8 ring)
For H-low power, error of RF acceptance: ~ 2.8% (6 ring), ~ 2% (8 ring)
RF efficiency will be a little lower than 100%.

## Slide 27: BS life time with RF phase adjustment
For H-high lum., error of BS life time: ~-36% (8 ring)
For H-low power, error of BS life time: ~-37% (6 ring), ~-30% (8 ring)
H-high lum
H-low power
BS life time will be lower than the requirement!!

## Slide 28
synchrotron radiation of IR
(lattice: CEPC_ARC_PDR_IR_96fam_damp-new.sad)
IP
FT
CCX
CCY
MT
L*= 1.5m
x*= 0.22mm
y*= 1mm
GQD0= -200T/m
GQF1= 200T/m
LQD0=1.69m
LQF1=0.90m
565 kev
1952 kev
126kev
434kev
126kev
203kev
374kev
472kev
472kev
Yiwei Wang

## Slide 29
synchrotron radiation of PDR (w/o IR)
Feng Su, Yiwei Wang
BSEP1：1631kev
BSEP3：1496kev
QBQ1：985kev

## Slide 30: DA optimization with Yiwei’s lattice (code: MODE- zhangy@ihep.ac.cn)
Bunch length in parameter table: 2.7 mm
Plan:
- Re-optimize with 2.7mm bunch length
- Further optimization with MODE
- add additional sextupoles in IR
Damping effect - open

## Slide 31: Initial
0%: 18x/-19 x
+2%: 8x/-6 x
-2%: 1x/-7 x

## Slide 32: 91
initial

## Slide 33
0%: 18x/-19 x
+2%: 6x/-4 x
-2%: 1x/-6 x
Intial
122 generation
DA [x]
DA [x]
0%: 18x/-19 x
+2%: 17x/-4 x
-2%: 2x/-4 x

## Slide 34: 127

## Slide 35: 150

## Slide 36: 165

## Slide 37: CEPC damping ring requirement
Energy: 1.1GeV
Storage time: 20ms
Injected emittance (normalized): 3500 mm-mrad, injected energy spread ~ 0.25%
Extracted energy spread <1×10-3
No strong requirement for the extracted emittance (<0.5inj)!
Transverse acceptance > 3*injection beam size

## Slide 38: CEPC DR design
 | DR V1.0
Energy (GeV) | 1.1
circumference | 58.5
Bending radius (m) | 3.6
B0 (T) | 1.01
U0 (keV/turn) | 35.8
Damping time x/y/z (ms) | 12/12/6 (61538 turns)
0 (%) | 0.049
0 (mm.mrad) | 302
Nature z (mm) | 7 (23ps)
Extract z (mm) | ~7 (23ps)
inj (mm.mrad) | 3500
ext x/y (mm.mrad) | 434/145
inj /ext (%) | 0.25 /0.05
Energy acceptance by RF(%) | 1.0
fRF=650MHz
VRF=1.8MV
Bunch compressor

## Slide 39: DR lattice design
FODO length (m) | 2.4
Phase per cell | 60
Dipole length (m) | 0.71
Dipole strength (T) | 1.0
Quadrupole length (m) | 0.2
Quadrupole strength (m-2) | 4.1
Sextupole length (m) | 0.06

## Slide 40: DA
inj / 0=11.6
inj / 0=3.4
inj,max=sqrt(1.626um*4m)
= 2.55mm
Tracking 240000turns （4 damping time）
5 times of injection beam size

## Slide 41: Primary design for bunch compressor
Dispersive section
RF structure
E0
E1

## Slide 42: Parameter design
入口：0=7mm， 0=0.05%， E0=1.1 GeV
出口：1<3mm， 1=??(0.1%)， E1=1.1 GeV

## Slide 43: Parameters of CEPC bunch compressor
 | BC (case I) | BC (case II)
初始能量 (GeV) | 1.1 | 1.1
初始能散 (%) | 0.05 | 0.05
初始束长 (mm) | 7 | 7
高频频率 (MHz) | 2856 | 2856
高频腔压 (MV) | 14.5 | 19.3
加速相位 (度) | 86 | 87
R56 (m) | -4 | -3
出口能量 (GeV) | 1.101 | 1.101
出口能散 (%) | 0.17 | 0.23
出口束长 (mm) | 2 (6.7ps) | 1.5 (5ps)
Compression ratio：3.5~4.7
Compression ratio is flexible.

## Slide 44: BC energy spread and VRF vs. bunch length
At the end of bunch compressor, shorter bunch length gives larger energy spread and need higher RF voltage.