## Slide 1: CEPC APDR Study
Zhenchao LIU
2016-11-4

## Slide 2: Problems in PDR
The peak power of bunch train is very high(several MW), however, there is no such large power input coupler.
Power compensation will cause low RF efficiency.
No power compensation will cause RF voltage drop and phase shift.
Power coupler limit.
Initial Eacc(MV/m)
Final Eacc/Initial Eacc
RF cycles
Final Eacc/Initial Eacc
Field decrease in one cavity at the bunch train passing period
Field decrease vs. various initial field gradient of the cavity
e.g. Accelerator gradient decrease in one RF cavity (H-high lumi.)(The peak beam power is 4.9MW@15MV/m; Assume 300kW input power & 15MV/m of the 5cell cavity）
The design is very challenging for the RF!

## Slide 3: Limitations on the power coupler
The average power of input coupler is ~300kW
The peak power of input coupler is ~1MW .
The maximum power is limited by the ceramic window
S. Belomestnykh，OVERVIEW OF INPUT POWER COUPLER DEVELOPMENTS PULSED AND CW，WE305, SRF2007

## Slide 4: New idea：APDR

## Slide 5: Nonconstant Voltage and Phase (NVP) Acceleration method
New acceleration method for CEPC to solve RF efficiency
The bunches in a bunch train will be accelerated at different Vci
The bunches in a bunch train will be accelerated at different synchrotron phase to keep constant energy gain.
Vai=Vci*cosϕsi=C

## Slide 6: parameter for CEPC partial double ring （wangdou20160325）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 54 | 54 | 54 | 54
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.59 | 0.062
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.6 | 5 | 7.6
Ne/bunch (1011) | 3.79 | 2.85 | 2.67 | 0.74 | 0.46
Bunch number | 50 | 67 | 44 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 10.5 | 26.2 | 45.4
SR power /beam (MW) | 51.7 | 50 | 31.2 | 15.6 | 2.8
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.1 | 6.1
Momentum compaction (10-5) | 3.4 | 2.5 | 2.2 | 2.4 | 3.5
IP x/y (m) | 0.8/0.0012 | 0.25/0.00136 | 0.268 /0.00124 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.45/0.0074 | 2.06 /0.0062 | 1.02/0.003 | 0.62/0.0028
Transverse IP (um) | 69.97/0.15 | 24.8/0.1 | 23.5/0.088 | 10.1/0.056 | 7.9/0.053
x/IP | 0.118 | 0.03 | 0.032 | 0.008 | 0.006
y/IP | 0.083 | 0.11 | 0.11 | 0.074 | 0.073
VRF (GV) | 6.87 | 3.62 | 3.53 | 0.81 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 3.1 | 3.0 | 3.25 | 3.9
Total z (mm) | 2.65 | 4.1 | 4.0 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 2.2 | 1.3 | 0.99 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.09 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.1 | 1.7 | 1.1
n | 0.23 | 0.47 | 0.47 | 0.3 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 36 | 32 |  | 
F (hour glass) | 0.68 | 0.82 | 0.81 | 0.92 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 2.96 | 2.01 | 3.09 | 3.09

## Slide 7: New SRF layout-6 ring
RF station
Double Ring
(1km/3km)
C≈60km
IP1
IP3
RF&DR center 30°equispaced

## Slide 8
6 double ring | APDR(HL VRF=3.62) | APDR (H-low power) | APDR (Z)
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 45.5
Circumference (km) | 54 | 54 | 54
SR loss/turn (GeV) | 2.96 | 2.96 | 0.062
Half crossing angle (mrad) | 15 | 15 | 15
Piwinski angle | 2.5 | 2.6 | 8.5
Ne/bunch (1011) | 2.85 | 2.67 | 0.46
Bunch number | 22x3 | 15x3 | 367x3
Beam current (mA) | 17 | 10.5 | 45.4
SR power /beam (MW) | 50 | 31.2 | 2.8
Bending radius (km) | 6.2 | 6.2 | 6.1
VRF (GV) | 3.62 | 3.53 | 0.357/0/12
f RF (MHz) | 650 | 650 | 650
Cavity No. | 384 | 384 | 48/24
Cavity gradient | 20.6 | 20 | 16.2/21.7
Accelerating phase | 35.2-32.3 | 33-30.9 | 80.2-79.8/58.9-56.9
CW power/cavity （kW） | 260 | 163 | 117/233
Peak power/train (kW) | 2345 | 1148 | 1237
Total Power （MW) | 100.4 | 62.7 | 5.6
Cell/cavity | 2 | 2 | 2/1
Cavity/module | 8 | 8 | 4/4
Module/station | 8 | 8 | 2/1
Total module | 48 | 48 | 12/6
R/Q (Ω) | 206 | 206 | 206/103
G | 268 | 268 | 268
HOM loss factor/cavity (V/pC) | 0.54 | 0.54 | 0.54
HOM power/cavity (kW) | 0.838 | 0.485 | 0.361/0.18
Working Temperature（K） | 2 | 2 | 2
Q0 | 2E10 | 2E10 | 2E10
τ（ms） | 0.811 | 1.242 | 2.243/0.507
QL | 1.656e6 | 2.536e6 | 4.58e6/1.03e6
Bandwidth(kHz) | 0.196 | 0.128 | 0.071/0.314
Detuning F (kHz) | -0.138 | -0.083 | -0.234/-0.520
Stored energy/cavity(J) | 107.4 | 100 | 65.3/59.1
Frev(kHz) | 5.484 | 5.484 | 5.484
Gap length (us) | 26.7 | 26.7 | 26.7
η(RF to beam efficiency)(%) | ~100 | ~100 | ~100
Vc decrease(%) | 3.3 | 2.2 | 2.5/5.3
TB/τ | 0.0158 | 0.021 | 0.012/0.053

## Slide 9: Accelerator gradient decrease in one RF cavity (Z)
Initial Eacc(MV/m)
Final Eacc/Initial Eacc
RF cycles
Final Eacc/Initial Eacc
Field decrease vs. various initial field gradient of the cavity
Bunch train passing
Bunch train space
Assume matching
Field evolution in cavity

## Slide 10: New SRF layout-8 ring
RF station
Double Ring
(1km/3km)
C≈62km
IP1
IP3
RF&DR center 22.5°equispaced

## Slide 11
8 double ring | APDR(HL VRF=3.62) | APDR (H-low power VRF=3.53) | APDR (Z)
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 45.5
Circumference (km) | 54 | 54 | 54
SR loss/turn (GeV) | 2.96 | 2.96 | 0.062
Half crossing angle (mrad) | 15 | 15 | 15
Piwinski angle | 2.5 | 2.6 | 8.5
Ne/bunch (1011) | 2.85 | 2.67 | 0.46
Bunch number | 17x4 | 11x4 | 275x4
Beam current (mA) | 17 | 10.5 | 45.4
SR power /beam (MW) | 50 | 31.2 | 2.8
Bending radius (km) | 6.2 | 6.2 | 6.1
VRF (GV) | 3.62 | 3.53 | 0.357/0.12/0.12
f RF (MHz) | 650 | 650 | 650
Cavity No. | 384 | 384/768/192 | 48/16/16
Cavity gradient | 20.6 | 20/20/20 | 16.2/16.3/32.6
Accelerating phase | 35.2-33 | 33-31.6/33-31.6/33-31.6 | 80.1-79.9/58.9-56.9/58.9-58
CW power/cavity （kW） | 260 | 163.3/81.6/326.6 | 117/350/350
Peak power/train (kW) | 1389 | 843 | 884
Total Power （MW） | 100.4 | 62.7 | 5.6
Cell/cavity | 2 | 2/1/4 | 2/2/1
Cavity/module | 6 | 6/12/3 | 6/2/2
Module/station | 8 | 8/8/8 | 1/1/1
Total module | 64 | 64/64/64 | 8/8/8
R/Q (Ω) | 206 | 206/103/412 | 206/206/103
G | 268 | 268 | 268
HOM loss factor/cavity (V/pC) | 0.54 | 0.54/0.27/1.08 | 0.54/0.54/0.27
HOM power/cavity (kW) | 0.838 | 0.485/0.24/0.97 | 0.36/0.36/0.18
Working Temperature（K） | 2 | 2 | 2
Q0 | 2E10 | 2E10 | 2E10
τ（ms） | 0.811 | 1.242 | 2.243/0.76/0.76
QL | 1.656e6 | 2.53e6 | 4.58e6/1.55e6/1.55e6
Bandwidth(kHz) | 0.196 | 0.128 | 0.071/0.209/0.209
Detuning F (kHz) | -0.138 | -0.083 | -0.234/-0.347/-0.347
Stored energy/cavity(J) | 107.4 | 100 | 65.3/65.3/133
Frev(kHz) | 5.484 | 5.484 | 5.484
Gap length TB (us) | 20 | 20 | 20
η(RF to beam efficiency)(%) | ~100 | ~100 | ~100
Vc decrease(%) | 2.5 | 1.6 | 1.7/5.3/2.5
TB/τ | 0.025 | 0.0098 | 0.0089/0.0263/0.0263

## Slide 12: Phase shift
Pcw<<Ppulse case:
Larger synchrotron phase will make smaller phase shift for the bunches in a bunch train for the same voltage drop
Large voltage drop should choose larger synchrotron phase
Large synchrotron phase means more cavities (more cost)
Synchrotron phase of first bunch (degree)
Phase shift (degree)
2% Vc decrease
4% Vc decrease
10% Vc decrease
20% Vc decrease
← PDR case
←APDR case

## Slide 13
Bunch No. | Pre CDR (CW, Pg=Pavg) |  | PDR (CW, Pg=Ppulse, very low RF efficiency) |  | APDR 8 ring (HL, CW, Pg=Pavg) |  | APDR 8 ring (H-low power, CW, Pg=Pavg) |  | APDR 8 ring (Z, Pg=Pavg) | 
 | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift
1 | 1 | 0 | 1 | 0 | 1 | 2.00 | 1 | 1.40 | 1 | 2.0000
2 | 1 | 0 | 1 | 0 | 0.9984 | 1.88 | 0.9984 | 1.26 | 0.9998 | 1.9927
3 | 1 | 0 | 1 | 0 | 0.9969 | 1.75 | 0.9968 | 1.12 | 0.9996 | 1.9855
4 | 1 | 0 | 1 | 0 | 0.9953 | 1.63 | 0.9952 | 0.98 | 0.9994 | 1.9782
5 | 1 | 0 | 1 | 0 | 0.9938 | 1.50 | 0.9936 | 0.84 | 0.9992 | 1.9709
6 | 1 | 0 | 1 | 0 | 0.9922 | 1.38 | 0.992 | 0.70 | 0.9990 | 1.9636
7 | 1 | 0 | 1 | 0 | 0.9906 | 1.25 | 0.9904 | 0.56 | 0.9988 | 1.9564
8 | 1 | 0 | 1 | 0 | 0.9891 | 1.13 | 0.9888 | 0.42 | 0.9987 | 1.9491
9 | 1 | 0 | 1 | 0 | 0.9875 | 1.00 | 0.9872 | 0.28 | 0.9985 | 1.9418
10 | 1 | 0 | 1 | 0 | 0.9859 | 0.88 | 0.9856 | 0.14 | 0.9983 | 1.9345
11 | 1 | 0 | 1 | 0 | 0.9844 | 0.75 | 0.984 | 0 | 0.9981 | 1.9273
15 | 1 | 0 | 1 | 0 | 0.9781 | 0.25 |  |  | 0.9973 | 1.8982
17 | 1 | 0 | 1 | 0 | 0.9750 | 0 |  |  | 0.9969 | 1.8836
50 | 1 | 0 | 1 | 0 |  |  |  |  | 0.9906 | 1.6436
67 |  |  | 1 | 0 |  |  |  |  | 0.9873 | 1.5200
275 |  |  |  |  |  |  |  |  | 0.0947 | 0
Assume Vrf is constant at the first bunch of bunch trains and the change of Vb is negligible.

## Slide 14
Bunch No. | Pre CDR (CW, Pg=Pavg) |  | PDR (CW, Pg=Ppulse, very low RF efficiency) |  | APDR 6 ring (H-low power, CW, Pg=Pavg) |  | APDR 6 ring (HL, CW, Pg=Pavg) |  | APDR 6 ring (Z, Pg=Pavg) | 
 | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift | Vc | Phase shift
1 | 1 | 0 | 1 | 0 | 1 | 2.20 | 1 | 2.60 | 1 | 2.6000
2 | 1 | 0 | 1 | 0 | 0.9984 | 2.04 | 0.9984 | 2.48 | 0.9998 | 2.5929
3 | 1 | 0 | 1 | 0 | 0.9968 | 1.89 | 0.9969 | 2.35 | 0.9996 | 2.5858
4 | 1 | 0 | 1 | 0 | 0.9952 | 1.73 | 0.9953 | 2.23 | 0.9994 | 2.5787
5 | 1 | 0 | 1 | 0 | 0.9936 | 1.57 | 0.9937 | 2.10 | 0.9992 | 2.5716
6 | 1 | 0 | 1 | 0 | 0.992 | 1.41 | 0.9921 | 1.98 | 0.9989 | 2.5645
7 | 1 | 0 | 1 | 0 | 0.9904 | 1.26 | 0.9906 | 1.86 | 0.9987 | 2.5574
8 | 1 | 0 | 1 | 0 | 0.9888 | 1.10 | 0.9890 | 1.73 | 0.9985 | 2.5503
9 | 1 | 0 | 1 | 0 | 0.9872 | 0.94 | 0.9874 | 1.61 | 0.9983 | 2.5432
10 | 1 | 0 | 1 | 0 | 0.9856 | 0.79 | 0.9859 | 1.49 | 0.9981 | 2.5361
11 | 1 | 0 | 1 | 0 | 0.984 | 0.63 | 0.9843 | 1.36 | 0.9979 | 2.5290
15 | 1 | 0 | 1 | 0 | 0.9776 | 0 | 0.9780 | 0.87 | 0.9971 | 2.5005
22 | 1 | 0 | 1 | 0 |  |  | 0.9670 | 0 | 0.9956 | 2.4508
50 | 1 | 0 | 1 | 0 |  |  |  |  | 0.9897 | 2.2519
67 |  |  | 1 | 0 |  |  |  |  | 0.9861 | 2.1311
367 |  |  |  |  |  |  |  |  | 0.0923 | 0
Assume Vrf is constant at the first bunch of bunch trains and the change of Vb is negligible.

## Slide 15: Compare with LEP
Assume:
  φe= 1deg., φs=116deg., φalign=3deg., Ib=0.45mA, h=31324, Q=40000, Rs=774MΩ（14 cavities）
  V0 (initial peak voltage)from 20MV-100MV
  2.3MV/cavity(acc. voltage)
V0(V)
Vleft/V0
1 bunch ~1%
4 bunches ~4%
Voltage decrease:
APDR:
8 DR: 2.5%(HL)5.3/2.5%(Z)
6 DR: 3.3%(HL)
Voltage drop is acceptable!

## Slide 16: Bunch position
The e+ and e- bunch trains should be symmetry to the two IPs.
The phase shift of the synchrotron phase between each bunch in a bunch train is 0.14 degree for the H low power mode. The total phase shift is 1.4 degree.
After enough synchrotron damping, the bunches will be at its synchrotron phase separately.
If the transport matrix from cavity to IP is the same for e+ and e- bunch trains, there will be no shift for the position of colliding.
RADIATION DAMPING, R.P. Walker

## Slide 17: Cavity requirements
Aim: To minimize the RF voltage drop of the cavity
Solutions:
  Voltage drop formula:
  R/Q=Vc^2/ωU, assume Ppulse>>Pcw
  d, cavity effective length, q bunch charge, Nb bunches per train, Ncav cavity number.
  Proper RF cavity number
  Proper RF cavity gradient
  Proper RF cavity R/Q for the large voltage drop cavities
(by Z.C. Liu)

## Slide 18: Conclusion
The 8-double ring and 6-double ring are available when using the same parameter as PDR(VRF=3.62GV) for HL. The 8-double ring has a lower phase variation than the 6-double ring .
The phase region is from 35.2-33 degree for bunches in a bunch train for the 8-double ring HL mode. The phase region is from 35.2-32.3 degree for the 6-double ring HL mode.
The bunch energy gain in each cavity is constant.
The RF to beam efficiency is ~100%.
Vb reaches constant value after about 65 circles (Ib=C, ~0.012s).
Beam can be stored by increasing bunch charges stably (with reflection in low current).
Vc should keep constant phase and value for each bunch separately.

## Slide 19: RF compensation
Aim : To compensate the voltage drop.
Solutions:
  DF cavity?
  Keep voltage constant
  RF induce no higher order perturbation
n, total cavity number; q, bunch charge; Vi, cavity voltage when the ith bunch passed; φi, RF phase of the ith bunch in cavity; m, total DF cavity number; Vdi, DF cavity voltage when the ith bunch passed; φdi, RF phase of the ith bunch in DF cavity.
Assume each bunch has a constant phase φi in the cavity and φdi in the DF cavity.

## Slide 20: Simple case
Assume there are two bunches
First order of energy gain:
Energy gain:

## Slide 21: Problems
DF cavity should be proper located to fix the bunch position at equal space at IP or RF cavity.
Asymmetry is needed in the two rings.
Lattice simulation with two types of cavity is needed.

## Slide 22: Thanks!