## Slide 1
Hongjuan Zheng
2016-11-04
HOM coupler design and collective instability study

## Slide 2: Outline
HOM coupler design
  Research target
  Research content
  Research achievement
Collective instability study
  Bunch lengthening analysis
Conclusion
References

## Slide 3: HOM coupler design
Research target
Cut off TE11：1126MHz
Cut off TM01：1471MHz
Beam stability:
HOM Qe~104
HOM power:
If beam spectrum coincide with HOM, the requirement for Qe should less than 103. (For TM011, if resonance happen, Pt=300W (Qe=103))
Maximum power: 1 kW
Dangerous monopole: aroud1200MHz
Dangerous dipole: 800MHz~900MHz, 1200MHz
HOM coupler bandwidth: 800~1400MHz
HOM damper: ＞1400MHz

## Slide 4: HOM coupler design
HOM coupler layout and size
FM
HOM
HOM
HOM coupler
Bandwidth: 800~1400MHz
HOM damper
Bandwidth: ＞1400MHz
cryogenic
RT
80mm
100mm
156mm

## Slide 5: HOM coupler design
HOM coupler design scheme
LEPII: 850 W /coupler (CW test)
LHC narrow band and broadband coupler: design value—1 kW, test—600 W (4.5K)
Coupler structure: coaxial LC filter
Design content
RF design
detuning approach:
equivalent circuit (transmission line model)
optimize each part according to S21 curve
change to 3D model
electromagnetic optimization
thermal analysis
surface heating analysis, static heat loss and dynamic heat loss
broadband filter

## Slide 6: HOM coupler design
Transmission line equivalent circuit results
l1
l2
l3
l4
Values for the transmission line equivalent circuit：
l1=4.83cm, l2=10.027cm, l3=2.0cm, l4=1.0cm, Ln=13.52nH, Cn=4.43pF, M23=8.29nH, C3=1.57pF, Zt=96.6 Ω, Z=50 Ω
Outer diameter of the coupling tube is 80 mm. Inner diameter of the coupling tube is 16 mm.

## Slide 7: HOM coupler design
3D model construction
Design requirement: M23=6.79 nH
a=30 mm, b=12 mm M23=6.78 nH
Design requirement: M12=8.29 nH
r=4.7 mm M12=11.925 nH
mutual inductance
notch filter inductance
TM01-TEM
after tune fundamental mode f
S21 curve

## Slide 8: HOM coupler design
Monopole mode damping results
TM011
TM020
use average current to calculate the threshold
not include the frequency spread
For Z, 32 cavity used
Continue to optimize the broadband damping results
Increase the probe head area
Increase the insert depth

## Slide 9: HOM coupler design
Dipole mode damping results
TE111
TM110
Hybrid
TM111/TE121
use average current to calculate the threshold
not include the frequency spread
For Z, 32 cavity used
Continue to optimize the broadband damping results
Increase the probe head area
Increase the insert depth

## Slide 10: Parameters for CEPC partial double ring （wangdou20160918/23）
 | Pre-CDR | H-high lumi. | H-low power | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 5.2 | 6.4
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 1.16 | 0.78
Bunch number | 50 | 107 | 70 | 400 | 1100
Beam current (mA) | 16.6 | 16.9 | 11.0 | 36.5 | 67.6
SR power /beam (MW) | 51.7 | 50 | 32.5 | 21.3 | 4.1
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.44 | 2.9
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.1/0.001 | 0.1/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.0078 | 0.88/0.008
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 9.7/0.088 | 9.4/0.089
x/IP | 0.118 | 0.041 | 0.042 | 0.013 | 0.01
y/IP | 0.083 | 0.11 | 0.11 | 0.073 | 0.072
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.74 | 0.11
f RF (MHz) | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 2.95 | 3.78
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.88 | 0.99
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.7 | 1.2
n | 0.23 | 0.35 | 0.34 | 0.49 | 0.34
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.92 | 0.93
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 4.3 | 4.48

## Slide 11: Bunch lengthening analysis
Impedance budget (from Na Wang)
Coupling impedance dominated by
  Resistive wall impedance
  Vacuum elements with large numbers (RF cavities, flanges, BPMs, bellows, …)
  Vacuum elementts with large impedances (IP duct, collimators, kickers, …)
Components | Number | R, kΩ | L, nH | Z¦¦/n, mΩ | kloss, V/pC
Resistive wall | - | 6.7 | 487.7 | 17.0 | 138.4
RF cavities | 384 | 14.9 | -132.7 | - | 307.5
Flanges | ~10000 | 0.7 | 165.5 | 5.8 | 15.1
BPMs | 2300 | 0.6 | 21.4 | 0.7 | 11.6
Bellows | ~10000 | 5.9 | 331.5 | 11.6 | 122.3
Pumping ports | ~10000 | 0.007 | 3.1 | 0.1 | 0.1
Total(σ=4.1mm) |  | 28.8 | 876.5 | 35.2 | 595.0

## Slide 12: Bunch lengthening analysis
Theory used
The analytical expression that describes the wake potential of a storage ring is:
The bunch lengthening equation is as follows:
Energy spread is:
[1] J. Gao, On the single bunch longitudinal collective effects in electron storage rings, Nuclear Instruments and Methods in Physics Research A 491(2002) 1-8.

## Slide 13: Bunch lengthening analysis
Bunch lengthening for Higgs high luminosity design
With σ=2.95 mm, bunch current = 0.158 mA
bunch lengthening is 44.9%
energy spread is 23.7%

## Slide 14: Bunch lengthening analysis
Bunch lengthening for Higgs low power design
With σ=2.9 mm, bunch current = 0.157 mA
bunch lengthening is 45.3%
energy spread is 24.2%

## Slide 15: Bunch lengthening analysis
Bunch lengthening for W design
With σ=3.35 mm, bunch current = 0.091 mA
bunch lengthening is 78%
energy spread is 52.2%

## Slide 16: Bunch lengthening analysis
Bunch lengthening for Z design
With σ=4 mm, bunch current = 0.061 mA
bunch lengthening is 184.2%
energy spread is 169.1%

## Slide 17: Bunch lengthening analysis
Conclusion for bunch lengthening analysis
The estimated results show that the bunch lengthening is a problem in CEPC, especially for Z design.
The cavities in the ring contribute more than half total loss factors.
The resistive wall contributes more than half total inductance.
It is better to remove most of the cavities for the Z design no matter for the bunch lengthening problem or the RF considerations.

## Slide 18: Conclusion
The preliminary design of HOM coupler is given. In order to meet the requirement, more work need to do.
Improve the damping for TE111 mode.
Improve the notch filter design for the fundamental mode.
Thermal analysis.
The bunch lengthening analysis results show that the bunch lengthening is a problem for CEPC, especially for Z design.

## Slide 19: References
K. Papke, U. Van Rienen,F. Gerigk. HOM Couplers for CERN SPL Cavities[J]. 2013.
David M. Pozar. Microwave Engineering, Publishing House of Electronics Industry, Beijing. P160
Byrd, J. and J. Corlett. Study of Coupled-bunch Collective Effects in the ALS. in Particle Accelerator Conference, Proceedings of the 1993. IEEE
Frank Gerigk, CERN, Studienarbeit
J. Gao, On the single bunch longitudinal collective effects in electron storage rings, Nuclear Instruments and Methods in Physics Research A 491(2002) p. 1-8.
J. Gao, An empirical equation for bunch lengthening in electron storage ring, Nuclear Instruments and Methods in Physics Research A 432 (1999) p. 539-543.
J. Gao, Review of some important beam physics issues in electron positron collider designs, Modern Physics Letters A, Vol. 30, No. 11 (2015), 1530006 (20 pages).
P. Wilson, et al., Bunch lengthening and related effects in SPEARII, IEEE Trans. Nucl. Sci. NS-24 (1977) p.1211.