## Slide 1: Sawtooth effect in CEPC PDR
Sha Bai, Yiwei Wang, Huiping Geng,
Chenghui Yu, Feng Su, Tianjian Bian, Jie Gao
CEPC-AP-meeting
2016-12-09

## Slide 2: Scale magnets
Scaling B,Q,S magnets in all arc section
Scaling B,Q manets in public beamline
Lattice version: CEPC-ARC4-PDR3-IR1
Energy loss of each B magnet=U0/Bnumber

## Slide 3: Without sawtooth

## Slide 4: With sawtooth (8 arc section scaling)

## Slide 5: Twiss parameters comparison (8 arc section scaling)
 | NO Sawtooth | Sawtooth |  | 
μx | 0.0800001 | 0.0791565 |  | 
μy | 0.2200000 | 0.2162617 |  | 
βx* | 0.219915 | 0.220747 |  | 
βy* | 0.001000 | 0.001013 |  | 
εx | 2.15121nm | 2.25805nm |  | 
εz | 3.38423E-6 m | 3.89783E-6 m |  | 
Bunch length | 2.53716622 mm | 2.92415163 mm |  | 

## Slide 6: Dynamic aperture comparison (8 arc section scaling)
No sawtooth
With sawtooth
Off-momentum DA reduced obviously.

## Slide 7: With sawtooth (8 arc section and public magnets scaling)

## Slide 8: Twiss parameters comparison (8 arc section and public magnets scaling)
 | NO Sawtooth | Sawtooth (only 8 arc magnets) | Sawtooth (add public magnets) | 
μx | 0.0800001 | 0.0791565 | 0.0792002 | 
μy | 0.2200000 | 0.2162617 | 0.2164171 | 
βx* | 0.219915 | 0.220747 | 0.220100 | 
βy* | 0.001000 | 0.001013 | 0.001008 | 
εx | 2.15121 nm | 2.25805 nm | 29.8862 nm | 
εz | 3.38423E-6 m | 3.89783E-6 m | 3.29575E-6 m | 
Bunch length | 2.53716622 mm | 2.92415163 mm | 2.65484053 mm | 

## Slide 9: Dynamic aperture comparison (8 arc section and public magnets scaling)
No sawtooth
With sawtooth
Both On-momentum and Off-momentum DA reduced obviously.

## Slide 10: Harmonic function comparison
No sawtooth
With sawtooth

## Slide 11: Reduce Synchrotron Radiation to 1/n
Horizontal orbit change
With sawtooth
1/10
1/2
1/5
1/20
1/15

## Slide 12: Twiss parameters comparison
 | NO Sawtooth | Sawtooth | 1/2 | 1/5 | 1/10 | 1/20
μx | 0.0800001 | 0.0792002 | 0.0791472 | 0.0794170 | 0.0795570 | 0.0796365
μy | 0.2200000 | 0.2164171 | 0.2184707 | 0.2193135 | 0.2195299 | 0.219626
βx* | 0.219915 | 0.220100 | 0.219942 | 0.219865 | 0.219842 | 0.219832
βy* | 0.001000 | 0.001008 | 0.001002 | 0.00100 | 0.001000 | 0.001000
εx | 2.15121 nm | 29.8862 nm | 5.72227nm | 3.1867nm | 2.86467nm | 2.77596nm
εz | 3.38423E-6 m | 3.29575E-6 m | 3.56944e-6m | 3.80118e-6m | 3.84369e-6m | 3.85693e-6m
Bunch length | 2.53716622 mm | 2.65484053 mm | 2.79529913mm | 2.88737412mm | 2.90361538mm | 2.90857672mm

## Slide 13: Dynamic aperture
No sawtooth
1/2
1/5
1/10
1/20
With sawtooth

## Slide 14: Conclusions
With sawtooth effect, tune change at 3 digits after the decimal point.
Both On-momentum and Off-momentum DA reduced a lot with sawtooth effect. Off-momentum DA beyond 0.5% reduced to zero.
Resonance coefficients at interaction point with sawtooth change a lot compared with no sawtooth.
Reduce Synchrotron radiation to 1/20, DA still can not recovered.