## Slide 1: Lattice design for double ring scheme of CEPC main ring
Yiwei Wang, Feng Su, Chenghui Yu, Dou Wang, Jie Gao
CEPC AP meeting, 16 Dec 2016

## Slide 2: Outline
CEPC parameters for C=100km
Lattice design and survey for the Arc region
Lattice design and survey for the RF region
Lattice design and survey for the IR region (TBD)

## Slide 3: CEPC parameters for C=100km
 | Pre-CDR | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.9 | 2.9 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 0.97 | 0.97 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 644 | 425 | 1000 | 10520 | 65716
Beam current (mA) | 16.6 | 29.97 | 19.8 | 50.6 | 232.1 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 33 | 16.7 | 8.0 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.144 /0.002 | 0.144 /0.002 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 1.56/0.0047 | 1.56/0.0047 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 15/0.097 | 15/0.097 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.0126/0.083 | 0.0126/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 131.2 | 131.2 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 2.22 | 2.22 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 (217800) | 650 (217800) | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.64 (2cell) | 0.42 (2cell) | 1.0 (2cell) | 1.0 (1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.2 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.95 | 0.95 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.05 | 4.08 | 11.36 | 70.97
wangdou20161202-100km

## Slide 4: Lattice design and survey for the Arc region
FODO cell
Dispersion Suppressor
ex=1.54e-09 m*rad, rhoB_o=12090 m, rhoB_i=12089.4 m

## Slide 5: Lattice design and survey for the RF region
An electrostatic separator, combined with a dipole magnet to avoid bending of incoming beam (ref: Oide, ICHEP16)
x=0.6 m, =0, Dx=0, Dx’=0