## Slide 1: MDC Data Check
Wu Linghui
2016-12-21

## Slide 2: Noise occupancy after T/Q match
Run 43646 ~ 45000, round09
Run 39355 ~ 42934, round08
Run 47467 ~ 47613, round10
2016.12.11 ~ 2016.12.19
2014.12.31 ~ 2015.6.8
2016.1.6 ~ 2016.3.19

## Slide 3: Noise occupancy of T channel
Run 43646 ~ 45000, round09
Run 39355 ~ 42934, round08
Run 47467 ~ 47613, round10
2016.12.11 ~ 2016.12.19
2014.12.31 ~ 2015.6.8
2016.1.6 ~ 2016.3.19
Noise level of the inner chamber from T channel is much higher

## Slide 4: Resolutions of run47543
Run47543 (Low noise occupancy)
Resolutions are normal
  Spatial resolution: 120mm
  sP=15.7MeV/c @2.1GeV/c
Alignment: No big displacement

## Slide 5: Layer by layer comparison (1)
Calibration not finished
Calibration samples are contaminated

## Slide 6: Layer by layer comparison (2)

## Slide 7: Time distribution
Run 47501, layer3
25ns
T (ns)
T (ns)
T/Q match
T channel
Run 47501, layer3
Run 47543, layer3
T channel
Low noise level

## Slide 8: Run by run monitor

## Slide 9: Summary
Noise level of the inner chamber from T channel is higher compared with old data.
High noise occupancy causes bad resolutions and low hit efficiency.
No big displacement is found.
Shift of vertex in z is a little bigger.