## Slide 1
30th March, 2017
LIU Xing
Joint PhD student
Accelerator Lab, Tsinghua University, Beijing, China
LAL, Universite Paris-Sud, Orsay, France
Optical Cavity for high flux X-ray Compton
Machines at Orsay and Tsinghua

## Slide 2
X-ray sources
Facilities | Properties
Synchrotron Radiation | High brightness, high energy electron storage ring GeV, large device, high cost
Free Electron Laser | Far exceed brightness, intensity , but high energy electron Linac, large device, high cost,
Thomson scattering machine | Compact, relative low cost, acceptable brightness
Adjustable for energy of X-ray
Quasi-Monochromatic spectrum
Radiation in a small angle（～1/g)
High Peak Brightness
Polarization
compact and affordable
…
Ne: electron number
Nl: laser photon number
sT: Thomson scattering cross-section
Frep: colliding repetition rate
sr: electron beam size r.m.s and laser beam size r.m.s

## Slide 3
Tsinghua Thomson Scattering X-ray Source (TTX)
Compact Light Source in China: TTX
Existing linac Thomson scattering source
45MeV Linac
X-ray pulse:
Photon energy: 24 keV (90deg)
Number photons: 8.4X106 (90deg)

## Slide 4
Electron beam |  | Laser beam | 
Energy | 45MeV | Wavelength | 800nm
Bunch length | 1~4ps | Pulse duration | ~30fs
Charge | ~0.7nC | Pulse energy | ~500mJ
Beam size | 30(H)x 25(V)um | Beam size | ~30um
Main features:
High peak power
Low average power
Short pulse duration
Huge pulse energy
Linac
Tsinghua Thomson Scattering X-ray Source (TTX)
Low repetition frequency
10Hz

## Slide 5
Thom-X project
1011 – 1013 ph/s
Linac S-band (3GHz)
Electron Ring
Laser Cavity
Transfer Line
10 m
• Location : Orsay - Size : 10mx7m
• Funding: 12M€
• Optical cavity : Gain 10k, <P>=500kW
High repetition frequency

## Slide 6
Injected laser pulses
Intra-cavity pulses
accumulation
FSR=
Frep
Mirror 1
Mirror 2
Lcav
c
2 Lcav
• Small Compton cross-section → important to recycle laser and electrons → Use of a Fabry-Perot cavity to accumulate and recycle the laser power
• Allows significant enhancement factors on the laser power (103104)
• This is difficult to achieve → Laser and cavity frequency combs need to match perfectly
Laser pulses stacking
Dn/nLaser = 10-11
STRONG & ROBUST laser/cavity
feedback needed

## Slide 7
Thom-X project
Optical Cavity
33.3 MHz

## Slide 8
Thom-X project
Laser choice: low phase noise
If laser oscillator « too noisy »
 no error signal = no laser/cavity locking
ThomX 150W fibre amplifier
Laser oscillator
Amplifier
Optical cavity
IP
<P> ~ 10 mW
<P> ~ 150 W
<P> ~ 500 kW
e- ring
Stretcher
Compressor
Amp. #3
Amp. #2
Amp. #1
5 mW
150 W
Gain ~ 30000
Amplifier divided in 3

## Slide 9
Thom-X project
ULE (Ultra Low Expension) Mirrors
Power transmission coefficients
M1: 180 ppm
M2, M3, M4: 2 ppm
wLMA Coating (Lyon, France)
Theoretical finesse ~ 28000
Theoretical gain ~ 15000
ith design values
Cavity mirrors
Finesse is measured by using four methods.
Finesse ~ 26000
Any dust on the mirrors has a strong
effect on finesse.
S-Box @ LAL

## Slide 10
TTX2
• New setup at TSU (TTX2)
resonant cavity, 79.3MHz,10ps  >1010 ph/s
3.6 m ring
Main features:
High average power
High repetition rate
High X-rays flux

## Slide 11
Collaboration between LAL & TSU
• LAL and Tsinghua University are working on a similar project to build a compact Compton X-ray source: ThomX / TTX2
• There are several areas on which we already cooperate:
- Optical cavity design
- Feedback system
- Mechanical design
We will continue to cooperate deeply.
• For my PhD project, I designed and will install TTX2-prototype setup, based on S-Box setup at LAL. Then, this prototype will be upgraded to achieve final specifications.

## Slide 12
Preliminary tests on Air Pressure, in accelerator
TTX2-prototype
Optical elements
Feedback system
Vacuum system
Cavity mirrors
3
2
4
----Shopping list LAL by Xing LIU
1
2017.04
2017.12
2018.12
2019
2021
Accelerator Integration
Final tests - UHV
TTX2
Cavity : 4M, HV compatible
Feedback : from LAL
Locking : laser to cavity
Cavity to ext. clock (e-)
Laser : One-five laser
T-Box & TTX
Schedule for TTX2

## Slide 13
Thanks