## Slide 1: CEPC SRF System
Jiyuan Zhai
2017-1-3

## Slide 2: Outline
2017 plan and milestones
New 100 km parameters
RF transient simulation with KEK code and transfer function
Superconducting (RF) Physics

## Slide 3: CEPC SRF System Design and R&D Plan (2017)
1月 CDR Status Report IAS会议（香港） | 2月 基金申请 TTC会议（MSU） | 3月
4月 CEPC会议（华师） | 5月 FCC会议（柏林） | 6月 ERL会议（CERN)
7月 SRF会议（兰州） | 8月 | 9月
10月 CDR统稿 | 11月 CDR定稿，中文翻译 | 12月

## Slide 4: CEPC 100 km & FCC-ee (w/o tt) Machine Top Parameters
CEPC-WD161123; FCC-V3 | C-H-HV | C-H-LP | C-H-HL | C-W | C-Z-LL | C-Z-HL | F-H | F-W | F-Z-HL | F-Z-LL
Luminosity / IP [1034 cm-2s-1] | 2 |  | 3 | 4.5 | 1.2 | 70 | 5 | 19 | 207 | 90
Beam energy [GeV] | 120 |  |  | 80 | 45.5 |  | 120 | 80 | 45.6 | 
SR power / beam [MW] | 33 |  | 50 | 18.3 | 0.84 | 50 | 50 |  |  | 
Beam current / beam [mA] | 20 |  | 30 | 56 | 24 | 1450 | 30 | 152 | 1450 | 
Bunches / beam | 1006 | 425 | 644 | 1100 | 1100 | 65716 | 780 | 5260 | 30180 | 91500
Bunch spacing [ns] APDR / DR | 20 / 166 | 47 / 391 | 31 / 257 | 17 / 151 | 17 / 151 | NA / 1.5 | 400 | 50 | 7.5 | 2.5
Bunch population [1011] | 0.41 | 0.97 |  | 1.05 | 0.46 |  | 0.8 | 0.6 | 1 | 0.33
Horizontal emittance εx [nm] Vertical emittance εy [pm] | 0.88 2.7 | 1.56 4.7 |  | 2.68 8 | 0.93 4.9 |  | 0.61 1.2 | 0.26 1 | 0.2 1 | 0.09 1
Momentum compaction [10-5] | 0.87 | 1.3 |  | 3.1 | 3.3 |  | 0.7 |  |  | 
Betatron function at IP βx* [m] βy* [mm] | 0.08 2 | 0.14 2 |  | 0.1 1 | 0.12 1 |  | 1 2 | 1 2 | 0.5 1 | 1 2
Horizontal beam size σx* [μm] σy* [nm] | 8.46 73 | 15 97 |  | 16.4 90 | 10.5 70 |  | 25 49 | 16 45 | 10 32 | 9.5 45
Energy spread [%] SR Total | 0.1 1.95 | 0.1 1.5 |  | 0.07 ? | 0.04 ? |  | 0.10 0.12 | 0.07 0.10 | 0.04 0.22 | 0.04 0.09
Bunch length [mm] SR Total | 1.53 1.63 | 2.72 2.9 |  | 3.8 3.9 | 3.93 4.0 |  | 2.0 2.4 | 2.0 3.1 | 1.2 6.7 | 1.6 3.8
Energy loss / turn [GeV] | 1.67 |  |  | 0.33 | 0.03 |  | 1.67 | 0.33 | 0.03 | 0.03
Total RF voltage [GV] | 3.56 | 2.22 |  | 0.63 | 0.11 |  | 3 | 0.8 | 0.4 | 0.2
RF frequency [MHz] | 650 |  |  |  |  |  | 400 |  |  | 
Energy acceptance / RF [%] | 1.95 / 6 | 1.5 / 2.2 |  | 1 / 1.5 | 1 / 1.1 | 1 / 1.1 | 2 / 7 | 2 / 5.5 | 1 / 7.2 | 1 / 4.7
Hourglass factor | 0.98 | 0.95 |  | 0.84 | 0.91 | 0.91 | 0.92 | 0.95 | 0.92 | 0.98
Beam-beam parameter ξx ξy | 0.009 0.083 | 0.013 0.083 |  | 0.008 0.055 | 0.008 0.054 |  | 0.08 0.14 | 0.07 0.16 | 0.025 0.16 | 0.05 0.13
Lifetime [min] BS or BB | 52 | 25? |  | 144 | 238 | 238 | 67 | 90 | 94 | 185
circumference 100 km, bending radius 11 km, crossing angle 30 mrad, two IPs

## Slide 5: Constraints for SRF Parameter Choice
Common cavity for DR, RF sections NRF-DR-CC = 2 , half ring bucket filled; common cavity for (A)PDR, RF sections NRF-PDR-CC = 8, 2 half sections each
Total bunch train length per beam Tt /T0 < 6 % of the circumference ((A)PDR)
Cavity operation gradient Eacc < 20 MV/m ( < 16 MV/m if use beat cavity)
HOM power / cavity PHOM < 1 kW (HOM coupler limit including pulsed HOM power of (A)PDR; not for HL-Z)
Input power / cavity PCPL< 300 kW (only consider one coupler per cavity, variable input coupler, otherwise large extra power of mismatching; not for HL-Z)
Cavity operation Q0 < 2E10 at 2 K (magnetic shielding and field emission limit, long-term cavity performance degradation)
Cryogenic heat load of total cavity wall loss at 4.5 K eq. WCAV < 30 kW
Detuning frequency Δf < 3 kHz (revolution frequency). For HL-Z, use direct loop and comb filter loop feedback to cure the fundamental mode instability (PEP-II, LHC), bunch by bunch may not work
Max phase shift of bunch train Δφmax < 5 deg (lifetime, luminosity, instability)
Cryomodule length LCM < 12 m

## Slide 6: Considerations for SRF Parameter Choice
Higgs and W share the same cavities, coupler mismatching if fixed coupling
HL-Z should use independent SRF cavity system (e.g. KEKB/BEPCII type)
Higgs cavities on-line detuned or off-line during W run
Higgs (and W) cavities off-line during Z run
Less cell number for easy HOM damping, cavity handling and processing
Klystron output power (< 1.2 MW) and distribution (even cavity number per klystron), could have two types of klystron with different power level
Input coupler must be assembled with cavity in Class 10 cleanroom, and should have small static and dynamic heat load
Two or even more input couplers per cavity should be considered especially for HL-Z
Instability feedback for large detuning of HL-Z
Phase shift correction with beat cavity for (A) PDR

## Slide 7
WD161123, Zhai161130 | H-HV | H-LP | H-HL | W | Z-LL | Z-HL
Luminosity [1034 cm-2s-1] | 2 |  | 3 | 4.5 | 1.2 | 70
SR power / beam [MW] | 33 |  | 50 | 18.3 | 0.84 | 50
Beam current / beam [mA] | 20 |  | 30 | 56 | 24 | 1450
Bunches / beam | 1006 | 425 | 644 | 1100 | 1100 | 65716
Bunch spacing [ns] APDR / DR | 20 / 166 | 47 / 391 | 31 / 257 | 17 / 151 | 17 / 151 | NA / 1.5
Bunch charge / length [nC / mm] | 6.6 / 1.6 | 15.5 / 2.9 | 15.5 / 2.9 | 16.8 / 3.9 | 7.4 / 4.0 | 7.4 / 4.0
RF voltage [GV] (w/ para. loss) | 3.57 | 2.24 |  | 0.65 | 0.12 | 
Synchrotron phase [deg] (from low zero) | 152.1 | 131.3 |  | 148.5 | 161.7 | 
Number of cells in a cavity | 2 |  |  |  |  | 1
Number of 650 MHz cavities | 384 | 240 | 384 | 128 | 16 | 64
Number of cryomodules / cavity per module | 64 / 6 | 48 / 5 | 64 / 6 | 32 / 4 | 16 / 1 | 64 / 1
Cavity operating gradient [MV/m] (< 20) | 20 | 20 | 12.6 | 11.0 | 16.7 | 8.4
Q0 at operating gradient @ 2 K (< 2E10) | 2.0E+10 | 1.2E+10 | 8.0E+09 | 8.0E+09 | 8.0E+09 | 8.0E+09
Input power / cavity (match) [kW] (< 300) | 173 | 277 | 263 | 295 | 117 | 1757
HOM power / cavity [kW] (< 1) | 0.25 | 0.42 | 0.63 | 1.04 | 0.20 | 5.84
Cavity wall loss @ 4.5 K eq. [kW] (< 30) | 28.7 | 30.0 | 28.2 | 7.1 | 2.1 | 1.0
QL (match) | 2.4E+06 | 1.5E+06 | 6.3E+05 | 4.3E+05 | 2.5E+06 | 2.1E+04
Cavity bandwidth / fill time [kHz / μs] | 0.3 / 1196 | 0.4 / 747 | 1.0 / 308 | 1.5 / 209 | 0.3 / 1207 | 31.4 / 10
Detuning frequency [kHz] (< 3) | -0.25 | -0.19 | -0.45 | -1.24 | -0.40 | -47.62
Cavity stored energy [J] | 103.2 | 103.4 | 40.5 | 30.8 | 70.8 | 8.9
Max voltage drop (4 trains / beam) [%] | 7 | 7 | 16 | 34 | 10 | decelerate
Max phase shift (4 trains / beam) [deg] | 4.3 | 5.8 | 14.1 | 23.0 | 6.0 | decelerate
CEPC 100 km SRF Parameters (DR and 4+4 APDR)

## Slide 8: Parameters for CEPC double ring （wangdou20161202-100km_2mmy）
 | Pre-CDR | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.9 | 2.9 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 0.97 | 0.97 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 644 | 425 | 1000 | 10520 | 65716
Beam current (mA) | 16.6 | 29.97 | 19.8 | 50.6 | 232.1 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 33 | 16.7 | 8.0 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.144 /0.002 | 0.144 /0.002 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 1.56/0.0047 | 1.56/0.0047 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 15/0.097 | 15/0.097 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.0126/0.083 | 0.0126/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 131.2 | 131.2 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 2.22 | 2.22 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 (217800) | 650 (217800) | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.64 (2cell) | 0.42 (2cell) | 1.0 (2cell) | 1.0 (1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.2 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.95 | 0.95 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.05 | 4.08 | 11.36 | 70.97

## Slide 9: parameter for CEPC double ring （wangdou20161110-100km_1mmy）
 | Pre-CDR | H-high lumi. | H-low power I | H-low power II
Number of IPs | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 54 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 1.67
Half crossing angle (mrad) | 0 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.5 | 2.5
Ne/bunch (1011) | 3.79 | 1.12 | 1.12 | 1.12
Bunch number | 50 | 555 | 333 | 211
Beam current (mA) | 16.6 | 29.97 | 17.98 | 11.4
SR power /beam (MW) | 51.7 | 50 | 30 | 19
Bending radius (km) | 6.1 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 0.96 | 0.96 | 0.96
IP x/y (m) | 0.8/0.0012 | 0.3/0.001 | 0.3/0.001 | 0.3 /0.001
Emittance x/y (nm) | 6.12/0.018 | 1.01/0.0031 | 1.01/0.0031 | 1.01/0.0031
Transverse IP (um) | 69.97/0.15 | 17.4/0.055 | 17.4/0.055 | 17.4/0.055
x/IP | 0.118 | 0.029 | 0.029 | 0.029
y/IP | 0.083 | 0.083 | 0.083 | 0.083
VRF (GV) | 6.87 | 2.0 | 2.0 | 2.0
f RF (MHz) | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.72 | 2.72 | 2.72
Total z (mm) | 2.65 | 2.9 | 2.9 | 2.9
HOM power/cavity (kw) | 3.6(5cell) | 0.75(2cell) | 0.45(2cell) | 0.28(2cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.098
Energy acceptance (%) | 2 | 1.5 | 1.5 | 1.5
Energy acceptance by RF (%) | 6 | 1.8 | 1.8 | 1.8
n | 0.23 | 0.26 | 0.26 | 0.26
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 | 52
F (hour glass) | 0.68 | 0.83 | 0.83 | 0.83
Lmax/IP (1034cm-2s-1) | 2.04 | 5.42 | 3.25 | 2.06

## Slide 10: Parameters for CEPC double ring （wangdou20161219-100km_2mmy）
 | Pre-CDR | tt | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 175 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 7.55 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.6 | 2.9 | 2.9 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 1.41 | 0.97 | 0.97 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 98 | 644 | 425 | 1000 | 10520 | 65716
Beam current (mA) | 16.6 | 6.64 | 29.97 | 19.8 | 50.6 | 232.1 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 50 | 33 | 16.7 | 8.0 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3 | 1.3 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.2/0.002 | 0.144 /0.002 | 0.144 /0.002 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 3.19/0.0097 | 1.56/0.0047 | 1.56/0.0047 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 25.3/0.14 | 15/0.097 | 15/0.097 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.016/0.055 | 0.0126/0.083 | 0.0126/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 122.2 | 131.2 | 131.2 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 8.92 | 2.22 | 2.22 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 | 650 (217800) | 650 (217800) | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.62 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.7 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.53(5cell) | 0.64 (2cell) | 0.42 (2cell) | 1.0 (2cell) | 1.0 (1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.14 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 2 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.6 | 2.2 | 2.2 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 50 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.89 | 0.95 | 0.95 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 0.62 | 3.1 | 2.05 | 4.08 | 11.36 | 70.97

## Slide 11: CEPC Main Ring SRF Parameters
Machine Parameter： wangdou20160918/23 (61 km) | H | H Low Power | H High Lumi | W | Z
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5
Main Ring Type | Single Ring | PDR or APDR |  |  | 
Luminosity / IP (1034 cm-2s-1) | 2.0 | 2.0 | 3.1 | 4.3 | 4.5
SR Power (MW) | 100 | 66 | 100 | 43 | 9
Beam Current / beam (mA) | 16.6 | 11.0 | 16.9 | 36.5 | 67.6
VRF (GeV) | 7 | 3.51 | 3.48 | 0.75 | 0.12
650 MHz Cavity | 5-cell | 2-cell | 2-cell | 2-cell | 2-cell
Number of Cavity | 384 | 480 | 480 | 192 | 32
Number of Cryomodule | 96 | 80 | 80 | 32 | 16
Eacc (MV/m) | 16.2 | 16.0 | 15.8 | 8.5 | 8
Q0 @ 2 K | 4E10 | 2E10 | 2E10 | 2E10 | 2E10
Input Power / cavity (kW) | 267 | 137 | 209 | 226 | 277
HOM Power / cavity (kW) | 3.7 | 0.5 | 0.7 | 0.8 | 0.9
Wall Loss @ 4.5 K eq. (kW) | 23 | 22.5 | 22.1 | 2.5 | 0.4

## Slide 12: Phase Shift and Beat Cavity
Machine Parameter： wangdou20160918/23（Circumference 61 km） | H Low Power | H High Lumi | W | Z | Z 1-cell
Bunch charge (nC) | 32 | 32 | 18.6 | 12.5 | 12.5
Bunch number (one beam) | 70 | 107 | 400 | 1100 | 1100
Bunch spacing (ns) [bunch train length < 3.2 km] | 152.3 | 98.5 | 26.2 | 9.2 | 9.2
Cavity voltage (MV) | 7.4 | 7.3 | 3.9 | 3.7 | 3.7
Synchrotron phase (deg) | 123 | 122 | 128 | 146 | 146
PDR 1+1 max voltage drop | 11 % | 18 % | 72 % | 140 % | 70 %
PDR 1+1 max phase shift (deg) | 12 | 19 | 67 | / | 49
PDR 3rd order beat cavity# (29 kHz) | 33 | 51 | 83 | 28 | 14
APDR 4+4 max voltage drop | 3 % | 4 % | 18 % | 35 % | 18 %
APDR 4+4 max phase shift (deg) | 3 | 4.8 | 16.7 | 24.2 | 12.1
APDR 2nd order beat cavity# (79 kHz) | 10 | 16 | 27 | 9 | 4

## Slide 13
Higgs LP (61 km)

## Slide 14: Higgs LP (61 km)

## Slide 15: Z pole LL (61 km)

## Slide 16: Z pole LL (61 km)

## Slide 17: RF transient simulation with transfer function
Pedersen Model

## Slide 18: RF transient simulation with transfer function
黄雪芳、王群要
F. Pedersen, RF Cavity Feedback, CERN/PS 92-59 (RF)

## Slide 19: Superconducting (RF) Physics
Three fundamental questions:
Why 120 C bake can cure Q-slope after EP of FG Nb?
Why Nitrogen doping can raise Q0?
Why Nb3Sn cannot reach high gradient?
Two-layer theory (SS)
Multilayer coating (SIS)
Bean-Livingston Barrier
Density of States

## Slide 21: 铁基超导材料

## Slide 22: Material Test
Hiroki Oikawa LINAC2016