## Slide 1: PDR multipole error effect on DA
Sha Bai, Yiwei Wang, Yingshun Zhu, Dou Wang, Feng Su, Dengjie Xiao, Tianjian Bian, Yuan Zhang, Huiping Geng, Jie Gao
2017-01-13

## Slide 2: Multipole error source
Multipole error from two parts:
      Systematic: intrinsic of magnet geometric charactor
      Random: from manufacture, due to material character difference and pole tip difference etc on. Also the differences between individual magnet
Systematic error associated to magnet type, could be controlled well.

## Slide 3
 | BEPCII |  |  | LEP |  | 
 | Bend | Quad | Sext | Bend | Quad | Sext
Dx(mm) | 0.2 | 0.15 | 0.15 | 0.3 | 0.1 | 0.15
Dy(mm) | 0.2 | 0.15 | 0.15 | 0.2 | 0.1 | 0.15
Tilt(mrad) | 0.1 | 0.2 | 0.5 | 0.1 | 0.1 | 0.5
B*L | 3e-4 | 3e-4 | 2e-3 | 5e-4 | 5e-4 | 4e-3
quadrupole(s) | 3e-4 |  |  | 8e-4 |  | 
sextupole(s) | 6e-4 | 5e-5 |  | 2e-4 | 6e-4 | 
Octupole(s) |  | 7e-5 | 6e-4 | 7e-5 | 5e-4 | 1.7e-3
Decapole(s) | 5e-4 | 9e-5 | 2e-4 | 1.3e-4 | 6.9e-4 | 3.4e-3
Dodecapole(s) |  | 6e-4 | 5e-4 | 1.4e-4 | 1e-3 | 6.5e-3
Quadrupole(r) | 1e-4 | 3e-4 |  | 2e-4 |  | 
Sextupole(r) | 1e-4 | 1e-4 | 3e-3 | 2.9e-4 | 1.2e-3 | 
Multipole(r) | 1e-4 | 1e-4 | 3e-4 | 2e-4 | 1e-3 | 2e-2
BEPCII and LEP errors

## Slide 4: DA with no error
Without damping
With damping
Lattice version: CEPC-ARC4-PDR3-IR1

## Slide 5
No error/with multipole error | 0 | -0.5% | +0.5% | -1% | +1% | -1.5% | +1.5% | -2% | +2%
X(sigma) | 40 | 10 | 20 | 5 | 5 | 1 | 1 | 0 | 0
Y(sigma) | 100 | 40 | 50 | 30 | 30 | 1 | 1 | 0 | 0
X(sigma) | 30 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Y(sigma) | 180 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0
X(sigma) | 35 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Y(sigma) | 180 | 5 | 5 | 0 | 0 | 0 | 0 | 0 | 0
DA due to multipole error
No error
With multipole error
B,Q,S set to be multipole
BEPCII multipole error are used
Lattice version: CEPC-ARC4-PDR3-IR1
Without damping
With multipole error
add two multipoles besides of B,Q,S
consistent

## Slide 6: DA due to multipole error ~ add two multipoles besides of each B,Q,S
No error
1e-4
3e-5
1e-5
BEPCII multipole error are used
Lattice version: CEPC-ARC4-PDR3-IR1
With damping
Only normal components
multipoles in middle of two same quads delete
Multipole errors devided by two
Tracking for 240 turns, coupling factor 0.3%

## Slide 7: Multipole error level ~ under construction
Systematic error beyond 18 pole is quite small, can be ignored.
Systematic error | Bending magnet | quadrupole | sextupole | Random error
quadrupole(s) | 0/1e-4 | 0/0 | 0/0 | quadrupole(r)
sextupole(s) | 1e-4/1e-4 | 0/3e-4 | 0/0 | sextupole(r)
Octupole(s) | 0/1e-4 | 0/3e-4 | 0/3e-3 | Octupole(r)
Decapole(s) | 1e-4/1e-4 | 0/1e-4 | 0/1e-4 | Decapole(r)
12 pole(s) | 0/1e-4 | 1e-4/1e-4 | 0/1e-4 | 12 pole(r)
14 pole(s) | 1e-4/1e-4 | 0/1e-4 | 0/1e-4 | 14 pole(r)
16 pole(s) | 0/0 | 0/1e-4 | 0/1e-4 | 16 pole(r)
18 pole(s) | 0/0 | 0/1e-4 | 1e-3/1e-4 | 18 pole(r)
20 pole(s) | 0/0 | 1e-4/1e-4 | 0/1e-4 | 20 pole(r)
22 pole(s) | 0/0 | 0/1e-4 | 0/1e-4 | 22 pole(r)
24 pole(s) | 0/0 | 0/1e-4 | 0/1e-4 | 24 pole(r)
26 pole(s) | 0/0 | 0/1e-4 | 0/1e-4 | 26 pole(r)
28 pole(s) | 0/0 | 1e-4/1e-4 | 0/1e-4 | 28 pole(r)
30 pole(s) | 0/0 | 0/1e-4 | 1e-3/1e-4 | pole(r)
32 pole(s) | 0/0 | 0/1e-4 | 0/0 | 32 pole(r)
34 pole(s) | 0/0 | 0/1e-4 | 0/0 | 34 pole(r)
36 pole(s) | 0/0 | 0/1e-4 | 0/0 | 36 pole(r)

## Slide 8: DA due to multipole error ~ add two multipoles besides of each B,Q,S
1e-4
BEPCII random multipole error are used, systematic multipole errors set to be the best level
Lattice version: CEPC-ARC4-PDR3-IR1
Vertical tune recovered but horizontal a little bit smaller: (.0795, .220)
With damping
Only normal components
Tracking for 240 turns, coupling factor 0.3%
No error

## Slide 9: DA due to multipole error ~ add two multipoles besides of each B,Q,S
1e-4
BEPCII random multipole error are used, systematic multipole errors set to be the best level
Lattice version: CEPC-ARC4-PDR3-IR1
Vertical tune recovered but horizontal a little bit smaller: (.0795, .220)
Without damping
Only normal components
Tracking for 240 turns, coupling factor 0.3%
No error

## Slide 10: DA due to multipole error ~ add two multipoles besides of each B,Q,S
BEPCII random multipole error
Sextupole/octupole component
set to be 1e-4
BEPCII random multipole error are used beyond octupole component error, sextupole and octupole component increased, systematic multipole errors set to be the best level
Lattice version: CEPC-ARC4-PDR3-IR1
Vertical tune recovered but horizontal a little bit smaller: (.0795, .220)
Without damping
Only normal components
Tracking for 240 turns, coupling factor 0.3%
No error
Sextupole and octupole component
Increased

## Slide 11: DA due to multipole error ~ add two multipoles besides of each B,Q,S
BEPCII random multipole error
Sextupole/octupole component
set to be 1e-4
BEPCII random multipole error are used beyond octupole component error, sextupole and octupole component increased, systematic multipole errors set to be the best level
Lattice version: CEPC-ARC4-PDR3-IR1
Vertical tune recovered but horizontal a little bit smaller: (.0795, .220)
With damping
Only normal components
Tracking for 240 turns, coupling factor 0.3%
No error
Sextupole and octupole component
Increased

## Slide 12: Analysis of horizontal tune change
!----------------------- multiple errors ( random )----------------------------------------
! Q S O DEC DOC 14 16 18 20 22 24 26 28 30 32 34 36 38 40 42 44
! k1 k2 k3 k4 k5 k6 k7 k8 k9 k10 k11 k12 k13 k14 k15 k16 k17 k18 k19 k20 k21
!!!!!!!!!!!!CEPC
ber =0.0001*{1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0}! bending magnets
qer =0.0001*{0, 3, 3, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0}! quadrupoles
ser =0.0001*{0, 0, 30, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0}! sextupoles
Change quadrupole component in bending magnets from 1e-4 to zero.
Tune change from
(.0795, .220) to (.08, .22)
(.0795, .220)
Tune change back to (.08, .22)
With damping
(.0795, .220)
Tune change back to (.08, .22)
Without damping

## Slide 13: Conclusions
Systematic multipole errors have large effect on the off-momentum DA, while random multipole errors of sextupole and octupole component have large effect on the vertical on-momentum DA.
The horizontal tune change mainly comes from the quadrupole component of bending magnets.
With multipole errors of the magnet manufacture best level, without damping, the vertical on-momentum DA reduced to 1/3 and horizontal seems no obvious change, while the horizontal off-momentum DA reduced a little but vertical seems no obvious change; but with damping, the dynamic aperture can be recovered to almost the same with the one with no error.