## Slide 1: Transverse Tune Shift Caused by Space-charge Effects in HEPS Storage Ring and Booster
Chongchong Du
IHEP

## Slide 2: Outline
Introduction
Why do and how do
Tune shift in storage ring
Tune shift in booster
Summary

## Slide 3: Space-charge effects
Direct Space-charge effects (direct Coulomb force)
Indirect Space-charge effects (image charges and currents)
0
b
2b
-b
-2b
Beam
Vacuum
chamber

## Slide 4: Tune shift
The self-fields created by the particles act back on the beam and influence its motion and change the betatron frequencies.
Incoherent tune shift
The beam as a whole does not oscillate, the space-charge forces are stationary and affect only the focusing of the individual particles.
Coherent tune shift
A beam execute a center-of-mass motion, the source of the space-charge fields changes ,beam result in a coherent tune shift.
discussed

## Slide 5: Comparisons between longitudinal and horizontal tune Shift caused by direct space-charge effects in storage ring
Longitudinal tune shift *
Horizontal tune shift*
Longitudinal Tune Shift is not discussed
HEPS Storage Ring
h: beam sizem
Z: bunch lengthm
：s
： horizontal tune 116.16
*Chao Alex, Physics of Collective Beam Instabilities in High Energy Accelerators.

## Slide 6: Influence factors of Transverse Tune Shift
Booster
Energy : 300 MeV 6 GeV
The “swap-out” mode with 60 bunches N=9e10(14.4 nC)
Storage ring
59.4/5.94 pmrad
z=3mm
The mode with 60 bunches N=9e10(14.4 nC)
N: Bunch population
Z : Bunch length
: Emittance

## Slide 7: Transverse Tune Shift*
the linear particle density
classical particle radius
the beam size
bunch occupation along the ring circumference
b vertical half axis of elliptical vacuum chamber,
a horizontal half axis
, the Laslett form factors,
a/b | 1 | 6/5 | 5/4 | 4/3 | 3/2 | 2/1 | 
 | 0 | 0.065 | 0.09 | 0.107 | 0.134 | 0.172 | 
a/b | 1 | 6/5 | 5/4 | 4/3 | 3/2 | 2/1 | 
 | 0 | 0.065 | 0.09 | 0.107 | 0.134 | 0.172 | 
* Helmut Wiedemann, Particle Accelerator Physics, third edition.

## Slide 8: Elegant simulation*
Particles are tracked through a zero length multipole to simulate space charge effects in elegant
*M. Borland, "elegant: A Flexible SDDS-Compliant Code for Accelerator Simulation," Advanced Photon Source LS-287, September 2000.
，L integrating length, the beam size

## Slide 9: Tune shift in storage ring(calculation)
The radius of circular vacuum chamber is 11mm， ，
Parameter | Symbol, unit | HEPS
Beam energy | E, GeV | 6
Beam current | , mA | 200
Bunch number |  | 648/60
Bunch current | , mA | 0.3/3.3
Bunch Population | N | 8.33e9/9e10
Bunch length | , mm | 3
Emittance | /, nm | 5.94e-2/5.94e-3
Betatron tune | / | 116.16/41.12
Parameter | Symbol, unit | HEPS
Beam energy | E, GeV | 6
Beam current |  | 200
Bunch number |  | 648/60
Bunch current |  | 0.3/3.3
Bunch Population | N | 8.33e9/9e10
Bunch length |  | 3
Emittance |  | 5.94e-2/5.94e-3
Betatron tune |  | 116.16/41.12
 | Tune shift | Bunch number | 
HEPS |  | 648 | 60
6Gev |  | -3.2e-3 | -0.035
 |  | -1.82e-2 | -0.196
 | Tune shift | Bunch number | 
HEPS |  | 648 | 60
6Gev |  | -3.2e-3 | -0.035
 |  | -1.82e-2 | -0.196

## Slide 10: The range of tune shift
648bunches
60bunches

## Slide 11: simulation for the mode of 60 bunches
 | Tune shift | Bunch number
HEPS |  | 60
6Gev |  | -0.035
 |  | -0.196
 | Tune shift | Bunch number
HEPS |  | 60
6Gev |  | -0.035
 |  | -0.196
= –0.0343
weight mean = –0.164
No particles are lost, the simulation results are consistent with the calculated results.

## Slide 12: Tune shift in booster(calculation)
The vertical and horizontal half axis of elliptical vacuum chamber are 12.5mm and 15mm in HEPS booster， ，
Parameter | Symbol, unit | Low energy | High energy
Beam energy | E, Gev | 0.3 | 6
Beam current | , mA | 15 | 15
Bunch number |  | 30 | 30
Bunch current | , mA | 0.5 | 0.5
Bunch Population | N | 4.5e9 | 4.5e9
Bunch length | , mm | 30 | 10
Emittance | /, nmrad | 70/70 | 4.1/0.4(k=0.1)
Betatron tune | / | 26.3/8.13 | 26.3/8.13
Parameter | Symbol, unit | Low energy | High energy
Beam energy | E, Gev | 0.3 | 6
Beam current |  | 15 | 15
Bunch number |  | 30 | 30
Bunch current |  | 0.5 | 0.5
Bunch Population | N | 4.5e9 | 4.5e9
Bunch length |  | 30 | 10
Emittance |  | 70/70 | 4.1/0.4(k=0.1)
Betatron tune |  | 26.3/8.13 | 26.3/8.13

## Slide 13: Tune shift in booster(calculation)
 | Tune shift | N=4.5e9
300Mev |  | -5.1e-4
 |  | -7.1e-4
6Gev |  | -1.49e-5
 |  | -2.91e-5
 | Tune shift | N=4.5e9
300Mev |  | -5.1e-4
 |  | -7.1e-4
6Gev |  | -1.49e-5
 |  | -2.91e-5
Space-charge effects is often overlooked in the discussion of high-energy accelerators. In cases of low beam energy and high particle densities, space-charge effects become necessary discussions on transverse beam dynamics. It may cause a big enough tune shift in a circular accelerator moving the beam onto a resonance.
In “swap-out” mode, a single beam injection replaces a portion of stored beam.

## Slide 14: Tune shift for “swap-out” mode
 | Tune shift | N=8.33e9（1.3 nC） | N=9e10（14.4 nC）
300MeV |  | -9.44e-4 | -1.02e-2
 |  | -1.3e-3 | -1.42e-2
6GeV |  | -2.76e-5 | -2.98e-4
 |  | -5.39e-5 | -5.82e-4
 | Tune shift | N=8.33e9（1.3 nC） | N=9e10（14.4 nC）
300MeV |  | -9.44e-4 | -1.02e-2
 |  | -1.3e-3 | -1.42e-2
6GeV |  | -2.76e-5 | -2.98e-4
 |  | -5.39e-5 | -5.82e-4
1.3 nC
14.4 nC
14.4 nC

## Slide 15: Simulation for “swap-out” mode (60bunches)
= –0.015
= –0.0145
 | Tune shift | N=9e10（14.4 nC）
300MeV |  | -1.02e-2
 |  | -1.42e-2
 | Tune shift | N=9e10（14.4 nC）
300MeV |  | -1.02e-2
 |  | -1.42e-2
Some particles are lost, the simulation results are consistent with the calculated results. After simulation with different bunch charge, we can obtain the threshold is 8.6 nC.

## Slide 16: Summary
Storage ring : The vertical tune shift is at the level of 0.2 in the operation mode with 14.4nC bunch charge, it move the beam onto a resonance, may result in loss of the beam or deterioration of the beam quality.
Advice: Stretch bunch length and adjust tune.
Booster : In the "swap-out" mode, 14.4nC bunch charge is the case of low beam energy and high particle densities while start ramping. Some particles are lost and the threshold is 8.6 nC.
Advice: In the "swap-out" mode, bunch charge should be less in the case of low beam energy.

## Slide 17
Thank you