## Slide 1
Xinying Zhang
Mechanical analysis of 650MHz 2cell cavity
17th January, 2017

## Slide 2
Xinying Zhang
2016.11.07 start
2016.12.31 mechanical calculation (cavity without stiffening)
  df/dp
  Tuning
  LFD

## Slide 3: model
Xinying Zhang
Parameter | Value(mm)
Riris | 78
Alpha | 3.22
A | 94.4
B | 94.4
a | 20.123
b | 22.09
L | 115.3
D | 204.95
Lequator | 1.463
Lbeam pipe | 300
different views
Cavity wall thickness: 3mm
flange thickness: 15mm

## Slide 4: material
304 Stainless Steel
Ti-45Nb
Nb
vacuum
Xinying Zhang
Parameter | Nb* | Ti-45Nb* | 304 Stainless Steel*
Young's modulus [Pa] | 1.03e11 | 6.21e10 | 1.95e11
Poisson's ratio | 0.38 | 0.34 | 0.29
Density [g/cc] | 8.56 | 5.7 | 8.0
Yield strength[MPa] at 295K | 70.26 | 475.8 | 172-241
Ultimate strength[MPa] at 293K | 184.72 | 544.7 | 448-517
Allowable limits[MPa] | <47 | <156 | <115/147
*Reference: Material properties for engineering analyses of SRF cavities.5500.000-ES-371110, Rev.--
Shell: Nb
Cavity flange: Ti-45Nb
blankoff flange: 304 Stainless Steel
Allowable limits
  Min(Ultimate strength/3.5, Yield strength x 2/3)

## Slide 5: df/dp, @ports fixed
Xinying Zhang
df/dp= -6.4Hz/mbar
the frequency drift: ±12.8 Hz if the LHe bath pressure is ±2mbar
1.5bar
  Deformation: 0.412mm
  Von mises stress: 18.5MPa
  the stress belows allowable limits
Chart: Pressure(mbar)
| 1000 | 1500 | 2000
deformation(mm) | 0.0274 | 0.0412 | 0.0549
von mises stress(MPa) | 12.4 | 18.5 | 24.7
deformation
stress
  The results vary linearly with the pressure change

## Slide 6: df/dp, @ports free
Xinying Zhang
df/dp= -255.9Hz/mbar
the frequency drift: ±511.8 Hz if the LHe bath pressure is ±2mbar
1.5bar
  Deformation: 0.767mm
  Von mises stress: 86.3MPa
  the stress exceeds allowable limits
deformation
stress
Chart: Pressure(mbar)
| 1000 | 1500 | 2000
defromation(mm) | 0.511 | 0.767 | 1.023
von mises stress(MPa) | 57.5 | 86.3 | 115
  The results vary linearly with the pressure change

## Slide 7: Tuning
Xinying Zhang
The tuning range R and the tuning force F are related to the stiffness k and the tuning sensitivity s.
Tuning sensitivity s: -279.0kHz/mm
Stiffness k: 7303N/mm
Chart: Tuning force(N)
| 2940 | 1960 | 980 | -980 | -1960 | -2940
deformation(mm) | 0.402 | 0.268 | 0.1338 | -0.1338 | -0.268 | -0.402
von mises stress(MPa) | 22.3 | 14.8 | 7.42 | 7.42 | 14.8 | 22.3
The results vary linearly with the tuning force
The max tuning force is about 650kgf (the stress will reach allowable limits), the frequency shift by tuning is about 243kHz.

## Slide 8: Tuning
Xinying Zhang
300kgf
  Deformation: 0.402mm (the sum of two side)
  Stress: 22.3MPa
Pull cavity and push cavity
  The deformation: equal and opposite
  The stress is same @ same force
Deformation @ pull cavity
Deformation @ push cavity
stresss @ push cavity
  300kgf
  300kgf
  300kgf

## Slide 9: LFD, @ports fixed
Xinying Zhang
LFD coefficient
  -0.88 Hz/(MV/m)2
deformation
stress
  5MV/m
Chart: Eacc2((MV/m)2)
| 0 | 1 | 9 | 25
ports fixed | 0 | -1 | -8 | -22
  5MV/m

## Slide 10: LFD, @ports free
Xinying Zhang
LFD coefficient
  -8.2 Hz/(MV/m)2
deformation
stress
  5MV/m
Chart: Eacc2((MV/m)2)
| 0 | 1 | 9 | 25
ports free | 0 | -8 | -74 | -205
  5MV/m

## Slide 11: summary
Xinying Zhang
df/dp
  The frequency drift will vary in the range of ±12.8 Hz to ±511.8 Hz
  The results vary linearly with the pressure change
  The stress under 1.5 bar (86.3 MPa @ ports free) exceeds allowable limits
Tuning
  Tuning sensitivity s: -279.0kHz/mm
  Stiffness k: 7303N/mm
  The max tuning force is about 650kgf (the stress will reach 47MPa), the frequency shift by tuning is about 243kHz
LFD
  LFD coefficient= -0.88 Hz/(MV/m)2, ports fixed
  LFD coefficient= -8.20 Hz/(MV/m)2, ports free
Conclusion: the stiffening is needed.

## Slide 12: Work plan for the next step
Xinying Zhang
2017.1~2017.6 The stiffening design
2017.1~2017.6 Multipacting simulation

## Slide 13: Backup slides

## Slide 14: Data1
Xinying Zhang
df/dp;beam ports fixed |  |  |  |  |  |  |  | 
pressure/mbar | deformation/mm | peak stress/Mpa | f/Hz | △f/Hz | △p/mbar | df/dp/(Hz/mbar) |  | 
1000 | 0.0274 | 12.4 | 650090957 |  |  |  |  | 
1500 | 0.0412 | 18.5 | 650087746 | -3211 | 500 | -6.422 |  | 
2000 | 0.0549 | 24.7 | 650084527 | -6430 | 1000 | -6.43 |  | 
df/dp;beam ports free |  |  |  |  |  |  |  | 
1000 | 0.511 | 57.5 | 649804355 |  |  |  |  | 
1500 | 0.767 | 86.3 | 649656606 | -147749 | 500 | -295.498 |  | 
2000 | 1.023 | 115 | 649508454 | -295901 | 1000 | -295.901 |  | 
Tuning, beam ports fixed |  |  |  |  |  |  |  | 
force/N | deformation/mm | peak stress/Mpa | f/Hz | △f/Hz | △F/N | △l/mm | △f/△l(Hz/mm) | △F/△l(N/mm)
980 | 0.1338 | 7.42 | 650059958 |  |  |  |  | 
1960 | 0.268 | 14.8 | 650022520 | -37438 | 980 | 0.1342 | -278971.6841 | 7302.533532
2940 | 0.402 | 22.3 | 649985039 | -74919 | 1960 | 0.2682 | -279340.0447 | 7307.97912
-980 | 0.1338 | 7.42 | 650134707 |  |  |  |  | 
-1960 | 0.268 | 14.8 | 650172017 | 37310 | -980 | 0.1342 | 278017.8838 | 
-2940 | 0.402 | 22.3 | 650209285 | 74578 | -1960 | 0.2682 | 278068.6055 | 

## Slide 15: Data2
Xinying Zhang
LFD ports fixed |  |  |  |  |  | 
Eacc | deformation/mm | peak stress/Mpa | f/Hz | △f/Hz | Eacc2/(MV/m)2 | 
0 | 0 | 0 | 650097353 | 0 | 0 | 
1 | 1.05E-09 | 394.273 | 650097352 | -1 | 1 | -1
3 | 9.49E-09 | 3548.45 | 650097345 | -8 | 9 | -0.888888889
5 | 2.64E-08 | 9856.82 | 650097331 | -22 | 25 | -0.88
LFD ports free |  |  |  |  |  | 
0 | 0.00E+00 | 0 | 650097353 | 0 | 0 | 
1 | 1.31E-08 | 1466.56 | 650097345 | -8 | 1 | -8
3 | 1.18E-07 | 13199 | 650097279 | -74 | 9 | -8.222222222
5 | 3.28E-07 | 36663.9 | 650097148 | -205 | 25 | -8.2