## Slide 1
Reactor Neutrino Experiment
Jun Cao
Institute of High Energy Physics
CCEPP Summer School, Daya Bay, July 1-9, 2017

## Slide 2: 提 纲
反应堆中微子实验
反应堆产生中微子（为什么要近点实验厅）
天然放射性（为什么要泡在水里，要3层探测器）
宇宙线（为什么要到地下，要有反符合）
液体闪烁体（为什么能探测到中微子）
探测器响应与刻度（看到的数字信号与物理量）
事例的构成与挑选（从物理量到中微子事例）
本底（真的是中微子吗？）
效率与误差（不能多挑也不能少挑）
2分析（从中微子事例数到振荡）

## Slide 3: 1 – Reactor Neutrino Experiments

## Slide 4: Hanford experiment
Hanford reactor
0.3m3 liquid scintillator
90 2” PMTs
Paraffin to shield neutrons
Lead to shield gammas
Expected events: 0.1~0.3 /min
Observed: 5/min（bkg >>signals）
Cowan: The lesson of the work was clear: It is easy to shield out the noise men make, but impossible to shut out the cosmos.
Savannah River experiment：12 m rock overburden + veto  Discovery of Neutrino

## Slide 5: Savannah River experiment
The first observation of neutrinos in 1956 by Reines & Cowan.
  Inverse beta decay in CdCl3 water solution  coincidence of prompt and delayed signal
  Liquid scintillator + PMTs
  Underground
Modern experiments are still quite similar, except
  Loading Gd into liquid scintillator
  Larger, better detector
  Deeper underground, better shielding
Notes: cadmium

## Slide 6: Neutrino Signal (IBD)
Capture on H or Gd, Delayed signal, 2.2, 8 MeV
Prompt signal
Peak at 4 MeV
Capture on H
Capture on Gd
Neutron capture after thermalization
Time constant ~30 us（0.1% Gd）
Inverse beta decay reaction, proposed by Pontecorvo, called Cowan-Reines reaction
Coincidence of
  Prompt: positron, energy correlated to neutrino energy
  Delayed: neutron capture
10,000 times bkg reduction

## Slide 7: CHOOZ
Baseline 1.05 km
1997-1998, France
8.5 GWth
300 mwe
5 ton 0.1% Gd-LS
Bad Gd-LS
Parameter | Relative error
Reaction cross section | 1.9 %
Number of protons | 0.8 %
Detection efficiency | 1.5 %
Reactor power | 0.7 %
Energy released per fission | 0.6 %
Combined | 2.7 %
R=1.012.8%(stat) 2.7%(syst), sin2213<0.17
Eur. Phys. J. C27, 331 (2003)

## Slide 8: Palo Verde
1998-1999, US
11.6 GWth
Segmented detector
12 ton 0.1% Gd-LS
Shallow overburden
32 mwe
Baseline 890m & 750m
R=1.012.4%(stat) 5.3%(syst)
Palo Verde Gd-LS
Chooz Gd-LS
1st year 12%, 2nd year 3%
60%/year
Phys.Rev.D64, 112001(2001)

## Slide 9: KamLAND
2002-, Japan
53 reactors, 80 GWth
1000 ton LS
2700 mwe
Radioactivity  fiducial cut, Energy threshold
Baseline 180 km

## Slide 10: KamLAND
The first observation of reactor anti-neutrino disappearance
Confirmed antineutrino disappearance at 99.998% CL
Excluded neutrino decay at 99.7% CL
Excluded decoherence at 94% CL
R=0.6580.044(stat) 0.047(syst)

## Slide 11: Neutrino Mixing @ 2003
23 ~ 45
Atmospheric Accelerator
12 ~ 34
Solar
Reactor
0
13 = ?
Reactor
Accelerator
In a 3- framework

## Slide 12: Reactor Neutrion Oscillation
KamLAND: Phys.Rev.Lett.90, 021802 (2003)
2km
60 km

## Slide 13
How large is 13?
PRD 62, 072002
Allowed region
Fogli et al., J.Phys.Conf.Ser.203:012103 (2010)
Gonzalez-Garcia et al., JHEP1004:056, 2010
Fogli et al., hep-ph/0506307
sin2213<0.16
sin2213~0.04
sin2213~0.04
sin2213~0.08, non-zero 2

## Slide 14: How to measure 13
Reactor (disappearance)
Clean in physics, only related to 13
Precision measurement
Accelerator (appearance)
Related with CPV and matter effect
T2K
4MeV ͞e

## Slide 15: Precision Measurement at Reactors
Parameter | Error | Near-far
Reaction cross section | 1.9 % | 0
Energy released per fission | 0.6 % | 0
Reactor power | 0.7 % | ~0.1%
Number of protons | 0.8 % | < 0.3%
Detection efficiency | 1.5 % | 0.2~0.6%
CHOOZ Combined | 2.7 % | < 0.6%
Major sources of uncertainties:
Reactor related ~2%
Detector related ~2%
Background 1~3%
Lessons from past experience:
CHOOZ: Good Gd-LS
Palo Verde: Better shielding
KamLAND: No fiducial cut
Near-far relative measurement
Mikaelyan and Sinev, hep-ex/9908047

## Slide 16: Proposed Reactor Experiments
Angra, Brazil
Diablo Canyon, USA
Braidwood, USA
Double Chooz, France
Krasnoyarsk, Russia
KASKA, Japan
Daya Bay, China
RENO, Korea
8 proposals, most in 2003 (3 on-going)
Fundmental parameter
Gateway to -CPV and Mass Hierachy measurements
Less expensive

## Slide 17: The Daya Bay Experiment
6 reactor cores, 17.4 GWth
Relative measurement
  2 near sites, 1 far site
Multiple detector modules
Good cosmic shielding
  250 m.w.e @ near sites
  860 m.w.e @ far site
  Redundancy
3km tunnel

## Slide 18: Double Chooz
Daya Bay
Double Chooz

## Slide 19: RENO
6 cores
16.5 GW
16t, 450 MWE
16t, 120 MWE
Daya Bay
RENO
Double Chooz

## Slide 20: Three on-going experiments
Experiment | Power (GW) | Detector(t) Near/Far | Overburden (m.w.e.) Near/Far | Sensitivity (3y,90%CL)
Daya Bay | 17.4 | 40 / 80 | 250 / 860 | ~ 0.008
Double Chooz | 8.5 | 8 / 8 | 120 / 300 | ~ 0.03
RENO | 16.5 | 16 / 16 | 120 / 450 | ~ 0.02
Huber et al. JHEP 0911:044, 2009

## Slide 21: Theta13 and Dmee
NH
3.9%
3.4%
DYB: running to 2020, 3% precision (1.5x stat. in 2018 summer)
RENO: running to 2020
Double Chooz: Dec. 2017

## Slide 22: Mass Hierarchy
NPP | Daya Bay | Huizhou | Lufeng | Yangjiang | Taishan
Status | Operational | Planned | Planned | Under construction | Under construction
Power | 17.4 GW | 17.4 GW | 17.4 GW | 17.4 GW | 18.4 GW
Yangjiang NPP
Taishan NPP
Daya Bay NPP
Huizhou NPP
Lufeng NPP
53 km
53 km
Hong Kong
Macau
Guang Zhou
Shen Zhen
Zhu Hai
2.5 h drive
Kaiping,
Jiang Men city,
Guangdong Province
Previous site candidate
Overburden ~ 700 m
by 2020: 26.6 GW
Daya Bay
~60 km JUNO

## Slide 23: The JUNO Experiment
20 kton LS detector
3% energy resolution
700 m underground
Rich physics possibilities
  Reactor neutrino for Mass hierarchy and precision measurement of oscillation parameters
  Supernovae neutrino
  Geoneutrino
  Solar neutrino
  Atmospheric neutrino
  Proton decay
  Exotic searches
L. Zhan, Y.F. Wang, J. Cao, L.J. Wen, PRD78:111103, 2008; PRD79:073007,2009
Jiangmen Underground Neutrino Observatory, a multiple-purpose neutrino experiment, approved in Feb. 2013. ~ 300 M$.

## Slide 24: Determine MH with Reactors
Precision energy spectrum measurement
interference between P31 and P32
: Relative measurement
Further improvement with Δm2μμ measurement from accelerator exp.
: Absolute measurement
4 MeV e

## Slide 25: Very Short Baseline Exps.
Different technologies: (Gd, Li, B) (seg.)(movable)(2 det.)
Most have sensitivity 0.02~0.03 @m~1eV2 @90%CL
Talk by Nathaniel Bowden @NEUTRINO2016

## Slide 26: Reactor Neutrino Experiments
1953, Hanford, 0.3 ton
1956, Savannah River, 4.2 ton
Discovery of ν
Early searches for oscillation
1980 Savannah, YES
1980 ILL, NO
1984 Bugey, YES
1986 Gosgen, NO
1995 Bugey-3, NO
1997, CHOOZ, 8 ton
2000, Palo Verde, 12 ton
Reactor ν spectra ~2%
Reactor ν oscillation (θ12)
2002, KamLAND, 1000 ton
sin22θ13<0.15
2012,
Daya Bay, 160 ton
Double Chooz, 16 ton
RENO, 32 ton
Non-zero θ13
2020, JUNO, 20 000 ton
Mass Hierarchy,
Precision meas.
Very short baseline exp. for sterile ν

## Slide 27: 2 - Neutrino from Reactor

## Slide 28: 大亚湾核电站
绝大部分商用反应堆为压水堆或沸水堆，两者原理相同
电功率约为热功率的1/3。大亚湾：2.9 GWth，900 MWe1080 MWe

## Slide 29: Structure of a Reactor Core
压力容器、活性区、组件、燃料棒、元件
157个组件（assembly），3.7m高，3m直径
每组件1717根棒（其中264根燃料棒，25根导管）
每燃料棒271个燃料元件。燃料元件二氧化铀烧结成1厘米大小的陶瓷状圆柱体，U-235 4.45%（1.8-4.45%)
锆合金管
红色：可燃毒物棒 8% Gd
72吨核燃料
每天消耗3kg U235

## Slide 30: Fuel Evolution
Initial 4.45% U235, Others:U238 and O
U238  n capture  Pu239 2x n capture  Pu241
Four major fission isotopes
  U235, Pu239, Pu241
  U238 fission w/ fast n
燃耗(Burnup)：MWday/ton U

## Slide 31: 每裂变释放能量
Isotopes | Energy (MeV)
U-235 | 201.7±0.6
U-238 | 205.0±0.9
Pu-239 | 210.0±0.9
Pu-241 | 212.4±1.0
M.F. James, J. Nucl. Energy 23, 517 (1969)
Kopeikin et al, Physics of Atomic Nuclei, Vol. 67, No. 10, 1892 (2004)
每裂变释放能量是指核燃料裂变时放出的能量中，在反应堆内被吸收转化为热能的部分。
核燃料释放的能量
  一部分作为裂变产物的动能转化为热能；
  一部分被中微子带走；
  一部分来自子核的衰变能，长寿命子核能量释放延后（时间变化）
  还有一部分来自富余中子的俘获（时间变化）
采用整个寿期内的平均值做为近似，误差 (0.30-0.47)%.

## Slide 32: 反应堆会不会发生核爆炸？
第一个反应堆：费米，芝加哥大学的体育场
链式反应，反应性
燃料的温度效应（多普勒效应）：温度上升  U238吸收共振峰覆盖的能谱加宽  吸收更多的中子  负反应性
  瞬发过程，对功率的变化响应很快：自稳机制
只有高浓度铀才能发生核爆炸（核弹）
高温下锆水反应生 成氢气，化学爆炸 抛撒放射性物质
铀同位素的微观截面
)/

## Slide 33: 反应堆产生中微子
Neutrinos from subsequent -decays of fission fragments.
两裂变为主。钱三强、何泽慧发现存在三裂变
裂变产物是富中子核，平均每裂变释放6个中微子
累加各核素得到的能谱误差较大：
1000多种核素，6000道，10%误差

## Slide 34: Spectra of Isotopes
Ab initio: Nuclear database, Σ fragments, Σ chains, Σ branches  10% uncertainty (e.g. Vogel et al., PRC24, 1543 (1981)).
Conversion: ILL measured the β-spectra  convert to neutrino spectra
  ILL spectra: Use spectra of 30 virtual (allowed) decays, fit amplitude and endpoints (ILL-Vogel spectra)
  Mueller: 90% ab initio + 10% fit  rate anomaly
  Huber: fit w/ improved nuclear effects (Huber-Mueller spectra)
  1.34% at 3 MeV to 9.2% at 8 MeV.
K. Schreckenbach et al. PLB118, 162 (1985)
A.A. Hahn et al. PLB160, 325 (1985)
Shape verified by Bugey-3 data
Normalization by Bugey-4, 1.6%

## Slide 35: ILL实验（劳厄-朗之万研究所）

## Slide 36: 反应堆非增殖监测
Bowden, LLNL, 2008
U235释放更多的中微子

## Slide 37: Flux Calculation
Thermal Power
Wth
Core Simulation fi/F
U, Pu Spectra
Si(E)
E : Neutrino energy
fi : Fission rate of isotope i
Si(E) : Neutrino energy spectra/f
Neutrino Flux
(fi /F): Fission fraction
Wth : Reactor thermal power
ei : Energy release per fission
Heat balance test
Online calibration
Core configuration
Thermal power
Operations
Temperature pressure
… …
Measurements
Calculations
Spent fuel
Non-equilibrium
Energy release/fission
Flux
NNP
Sim.

## Slide 38: Event Rate
Peak at 4 MeV
Back-on-the-envelope: 2.9GWth, 200 MeV/fission, 6 /fission
  5.41020 ͞e/s (only 1/3 higher than 1.8 MeV threshold
IBD event rate at 1 km from reactor ~ 1 IBD/(daytonGW)  20 ton  2.9GW2/(0.360.36km)

## Slide 39: Small Corrections
90Sr
90Y
Fission
Fission
89Sr neutron capture
89Y neutron capture
neutron capture
neutron capture
28.78y
0.546MeV
64.1h
2.284MeV
Ratio to all neutrinos
Ratio to neutrinos in 2-4 MeV
Weighted by inverse- decay Xsec.
1) Non-equilibrium isotope (~0.3%)
2）Spent fuel (~0.3%)

## Slide 40: 四个要素
Isotope neutrino spectra (ILL+Vogel, Huber+Mueller, Vogel, Fallot, etc.)
Thermal Power Wth (Provided by NPP)
Fission Fraction (fi/F) (Provided by NPP or independent core simulation)
Energy release per fission ei (database）
Correlation among uncertainties.

## Slide 42: Reactor Anomaly (Rate)
ILL spectra agree w/ data
2011, Huber-Mueller spectra higher than data by 6%
Sterile neutrino?
G. Mention et al.
Phys.Rev. D83 (2011) 073006
fit with sterile

## Slide 43: 热功率
KME, thermal power, Secondary Heat Balance Method.
  The most accurate measurement.
  Offline measurement, weekly or monthly
  Generally cited with (0.6-0.7)% uncertainties in literature.
KIT/KDO, thermal power. Good for analysis.
  Primary Heat Balance
  Online
  Weekly calibrated to KME power.
RPN, nuclear power
  Ex-core neutron flux monitoring
  Online
  Safety and reactor operation control
  Daily calibrated to KIT/KDO power

## Slide 44: 热功率误差
Chooz 0.6%, Palo Verde 0.7%.
Motivation of power uprates by the power plants  Study the power uncertainties and improve the instrumentation.
Uncertainties of secondary heat balance is dominated by the flow rate.
  Venturi flow meter. Most US reactors. Uncertainty is often 1.4%. It can be as low as 0.7% if properly calibrated and maintained, but suffering from fouling effects, which could grow as high as 3% in a few years.
  Orifice plate. France EDF reactors. Typically 0.72%. No fouling effects. Could be improved to 0.4% with lab tests.
  Note: Above flow meter uncertainties are at 95% C.L. as defined in ISO 5167. Unless specified, the thermal power uncertainty given by the power plant is also at 95% C.L.
  Ultrasonic. Start to use in some US and Japan reactors. Type I TT 0.45%, Type II TT 0.2% (Djurcic et al.)

## Slide 45: An example
EPRI document prepared by EDF, Improving Pressurized Water Reactor Performance Through Instrumentation:…… (2006)
For N4 reactor (Chooz type) with 4 steam generators:
If not assuming the discharge coefficients of the 4 orifice plates are independent, the power uncertainty at 68.3% C.L. will be 0.37%.
Empirical formula and uncertainty specified in ISO 5167-1-2003.
Correlated or Uncorrelated for the 4 flow meters?
Orifice Plate

## Slide 46: Another Example
Daya Bay and Ling Ao reactors (EDF, 2.9GWth) are all calibrated with SAPEC system, an EDF portable high precision secondary heat balance test system with its own sensors, databases, and data processing, of uncertainty 0.45%. Ling Ao KME is predicted to have an uncertainty of 0.48% (95% C.L.)
4 tests on Ling Ao KME show differences from 0.031% to 0.065%. Why?
  Used the same orifice plates but different pressure transmitters.
  It proves that the uncertainty is dominated by discharge coefficient.
  Ling Ao KME is in very good agreement with SAPEC.
Thermal power
Uncertainty Analysis
(MW)
(MW)
Difference (MW)
Difference
Test 1
Test 2
Test 3
Test 4

## Slide 47: Uncertainties of fission fraction
Depends on the simulation code. Only slightly on the inputs (has not been checked on other simulation code.)
Compare measured and calculated concentration of fuel isotopes, sampled at different burn-up. Part of the qualification of the code.
Apollo/Science模拟：裂变份额误差5%
Lester Miller thesis, ROCS
One analysis of Apollo 2.5

## Slide 48: Correlation of fission fractions
由于总功率的限制，5%的裂变份额误差对应0.5%的中微子数误差
考虑到各同位素之间的关联，0.5% 0.6%
Djurcic et al. J. Phys. G: Nucl. Part. Phys. 36 (2009) 045002
  Dragon模拟

## Slide 49: Uncertainties from Past Experiments
Parameter | Relative error
Reaction cross section | 1.9 %
Number of protons | 0.8 %
Detection efficiency | 1.5 %
Reactor power | 0.7 %
Energy released per fission | 0.6 %
Combined | 2.7 %
R=1.012.8%(stat) 2.7%(syst)
CHOOZ, Eur. Phys. J. C27, 331 (2003)
Neutrino spectra (1.9%  1.6% with Bugey data)
Inverse -decay cross section (0.2%)
Fission fraction fk (~5%)
Non-equilibrium fragments (0%)
KamLAND,PRL94:081801, 2005.
Palo Verde, PRD62, 072002
Parameter | Relative error
Neutrinos/fission | 1.4 %
Power, target, distance | 1.5%
Combined | 2.1 %
Power contributes ~0.7%

## Slide 50: 大亚湾反应堆中微子流强误差

## Slide 51: Daya Bay Absolute Rate Measurement
  Data/(Huber+Mueller)：0.946±0.020
  Past global average: 0.942±0.009
  Data/(ILL+Vogel)： 0.992±0.021
Chin. Phys. C41, 013002 (2017)
Special calibration in Jan. 2017
Stay tuned

## Slide 52: Daya Bay Fuel Evolution
Combined fit for major fission isotopes 235U and 239Pu
σ235 is 7.8% lower than Huber-Mueller model (2.7% meas. uncertainty)
σ239 is consistent with the prediction (6% meas. uncertainty)
2.8σ disfavor equal deficit (H-M model & sterile hypothesis)
PRL118, 251801 (2017)

## Slide 53: Reactor Anomaly (Spectrum)
5 MeV Bump
Not due to energy non-linearity
Not due to sterile ν
Possibly due to forbidden decays (PRL112: 2021501; PRL114:012502)
DC, JHEP 1410 (2014) 086
RENO:arXiv:1610.04326
Chin. Phys. C41, 013002 (2017)

## Slide 54: Measuring the spectrum
Unfolding the reactor neutrino spectrum
  Between 1.5 and 7MeV: 1.0% at 3.5 MeV, 6.7% at 7 MeV
  Above 7 MeV it is larger than 10%.
New prediction besides ab initio method and conversion method
W/ the direct measurement, spectra uncertainty comes mainly from energy non-linearity uncertainty (do not double counting): 1% energy scale  10% uncertainty in spectrum.
Aim at 1% for JUNO

## Slide 55: Precision Spectrum with Gas TPC
How to reach 1% spectrum uncertainty?
Improving Daya Bay
  Electronics non-linearity
    192 channels Flash ADC for AD1. Data taking completed.
  Liquid scintillator non-linearity
    Replaced LS in AD1 for JUNO R&D
     Consequence: Daya Bay from 8 AD to 7 AD since Dec. 2016
    Testing detector responses with 13 different LS configurations (PPO from 0.5g/L to 4g/L, bis-MSB from 0.1-15 mg/L)
     Building precision Monte Carlo
  Relative meas. to cancel non-linearity btwn Daya Bay and JUNO
Other experiments, like PROSPECT (4.5% energy resolution)
  Gas TPC detector at ~20 m from a reactor (Prototyping at IHEP)
  ν-e scattering
  High energy resolution (1%/sqrt(E), Daya Bay 8%, JUNO 3%)
  Other motivations: w, abnormal magnetic moment (to 10-12)

## Slide 56: Reactor Neutrino Experiments
Elastic scattering with electron
  Abnormal magnetic moment (TEXONO, GEMMA, NUMU)
  Weak mixing angle θw
Inverse Beta Decay
  Most experiments (LS detector)
1.8-10 MeV means
  Natural radioactivity
  Long-lived isotopes produced by cosmic muons
Peak at 4 MeV

## Slide 57: 3 – Natural Radioactivity

## Slide 58: 天然放射性
天然放射性无处不在，例如：
  238U (222Rn，210Pb来历)
  232Th
  有灰尘的地方就会有以上两种放射性
  40K （玻璃、人体 ~ 5000Bq）
宇生放射性 14C测定年代
人工放射性，例如：
  60Co （不锈钢、育种、刻度源）
  137Cs （水、刻度源）
岩石、土壤、空气

## Slide 59
粒子：穿不过一层纸
射线：厘米
射线：衰减长度20 cm水

## Slide 60: U、Th衰变链
平衡态
非平衡态
  纯化光除U、Th不够，还需要除掉Ra
  Pb-210（老铅）
级联衰变 (Cascade)
模拟的产生子
45亿年
140亿年

## Slide 61: 大亚湾花岗石伽马谱
贝克（Bq）：每秒一次衰变
居里（Ci）：3.71010 Bq， 微居=安全，毫居=小心，居里=致命
ppm, ppb：
  1 ppb 40K = 258.4 mBq/kg
  1 ppb 238U = 12.4 mBq/kg
  1 ppb 232Th = 4.0 mBq/kg
花岗石（火成岩）是放射性比较高的岩石；大亚湾花岗石是世界平均值的3倍：
10 ppm U
30 ppm Th
5 ppm K40

## Slide 62: Where the radioactivities come from?
大亚湾花岗石放射性较高
  8.8ppm U, 28.7ppm Th, 4.5ppm K
  ~ 20 Hz 单事例率（2米水，0.45米油）
氡气（铀的衰变产物，从石缝逸出）
  液闪存储、探测器运行时需要流氮
PMT玻璃，不能与液闪接触，找低本底玻璃
钢罐材料，需选低本底钢材
不能用铝（摄像头）、玻璃（全反射镜）等
所有探测器材料，特别是与液闪接触的，必须进行低本底测量。
探测器安装在清洁间中进行（万级）防灰尘

## Slide 63
Why Daya Bay dope Gadolinium into LS?
Why JUNO will not dope Gadolinium into LS?
2.62 MeV

## Slide 64
Reactor Neutrino Experiment
Jun Cao
Institute of High Energy Physics
CCEPP Summer School, Daya Bay, July 1-9, 2017

## Slide 65: 4 – Cosmic Muon

## Slide 66: Cosmic Muon
Minimum ionization muon: ~200MeV/m.w.e.
 Flux on surface ~ 200Hz/m2

## Slide 67: Muon Flux
Muon on surface: Gaisser formula
Modified Gaisser formula
More precise flux need simulation (Earth Magnetic field), See Honda’s lecture

## Slide 68: Muon Energy Loss
Continuous process —— Ionization energy loss
Discrete process ——Bremsstrahlung, pair production, hadron process, important for high energy muon
Minimum muon energy to pass xmin thick rock
=500GeV, the energy at which the continuous process has equal contribution to discrete process

## Slide 69: Propagate Muon to Underground Lab
Mount map of Daya Bay area
  12 km high precision (1m)
  34 km 1:5000 map (5m)
  1010 km SRTM map
Muon propagation software:
MUSIC, FLUKA
Muons at Daya Bay Lab
Rock density：~2.6 g/cm3

## Slide 70: Muon Simulation
Daya Bay
LingAo
LingAo II
Mid
Far
 | DYB | LA | Mid | Far
Elevation (m) | 93 | 100 | 208 | 324
Flux (Hz/m2) | 0.88 | 0.69 | 0.17 | 0.039
Mean Energy (GeV) | 57 | 58 | 97 | 142
Muon rate at surface ~200Hz/m2

## Slide 71: Spallation Neutron
Cosmogenic neutron is one of the most important bkg
Neutron yield
（当物质密度为1 g/cm3时）每个muon经过1cm产生的中子数（中子的海洋）
Neutron density at Daya Bay near (far) site 0.03（0.001） neutron/m3/sec
muon Spallation
Gamma-N
中子可打出次级中子
muon在核上俘获产生中子（低能）
Y.F. Wang et al

## Slide 72: Muon capture on nuclei
Stopping muon: e+, Michel e, lifetime 2.19703 s
Form a － molecule, then decay －e－+, or capture on nuclei.

## Slide 73: Cosmogenic Longlived Isotopes
Hard to remove by muon veto
The most important bkg in DYB: He8/Li9 with a delayed neutron

## Slide 74: RPC + Water Cherenkov Detector
高10米
宽10米（近点）或16米（远点）
长16米
~2000 ton pure water


## Slide 75: 5 - Liquid Scintillator

## Slide 76: Daya Bay Liquid Scintillator
LS: ~ 10 k photons/MeV (NaI 40 k photons/MeV), isotropic
Recipe: LAB + 3g/L PPO + 15mg/L bis-MSB (+0.1% Gd)
Daya Bay photoelectron yield: 163 p.e./MeV
10 k photon/MeV (?)
Attenuated: 70%
PMT photocathode coverage: 12%
PMT quantum efficiency: ~ 20%
1.68%  168 p.e./ MeV

## Slide 77: Make a Liquid Scintillator
Solvent
  含苯环的芳香族化合物
  三甲苯、二甲苯(PX)、甲苯、苯、PXE、DIN、LAB
  Solvent itself has very low light yield
Fluor (1-5 g/L)
  PPO、PBD、TP、PMP
(Optional) Wavelength Shifter (~10 mg/L）
  bis-MSB、POPOP、BBQ
  Match PMT response, shifting photon wavelength to transparent reagion

## Slide 78: 分子的能级结构
π 电子的能级结构。S0 为基态，S1, S2, S3 为激发单重态，T1 为激发三重态。
正是有了斯托克斯位移（1852年发现），闪烁体产生的荧光才可以在自身材料中传播

## Slide 79: Energy Transfer in LS
Resonance
Absorption and reemisson of UV light
二元液闪（不带波长位移）
三元液闪

## Slide 80: Light Yield vs PPO (Bis-MSB) Concentration
LAB为溶剂时PPO的浓度与发光效率的关系
bis-MSB的浓度与发光效率的关系
???
Concentration Quenching

## Slide 81: Attenuation, absorption, scattering
Attenuation: also noted as extinction length.
Absorption: the molecular are heated by incident light.
Rayleigh scattering: scatter off the bound electrons of molecular.
Mie, Raman, absorb&re-emit…

## Slide 82: Attenuation
1-m tube
  L=2~3 m (Tap water)，50% light absorbed in DYB detector
  L=10m ：20% light absorbed in DYB
5米
Result of water sample
39.6 m
分光光度计 UV-vis

## Slide 83: Quenching
Thermal Quenching
Oxygen uenching
11%
Energy quenching
Pulse shape

## Slide 84: Non-linearity due to energy quenching

## Slide 85: 大亚湾液体闪烁体的主要性能
光产额：~1万光子/MeV
发射光谱：380-500 nm
衰减长度：15米（未扣除散射）@430nm
吸收谱
吸收重发射几率?
衰减时间：3ns+10ns+150ns
氧气淬灭：通氮可提高~10%的光产额
温度效应：从20度到-75度，光产额提高70%
波形分辨：有些液闪对不同粒子的时间谱相差较大

## Slide 86: Liquid Scintillator Hall
LS mixing equipment
185 ton 0.1% Gd-LS
Liquid Scintillator
Mineral Oil
Filling Equipment
ISO tank equiped with load cell. Target mass errorr ~0.1%

## Slide 87: 6 – Detector Response and Calibration

## Slide 88
Detectors
3 layers separated by Acrylic Vessels

Neutron
RPC
Water Cherenkov
Water shields radioactivity and neutron
Two layer water Cherenkov detector
RPC
Combined eff. 99.5%+-0.25%

## Slide 89: 探测反应堆中微子
PMT
中微子
可见光子
中子
正电子
白油
液闪
掺钆液闪
中微子与氢核反应，生成正电子与中子
正电子直接电离激发液闪发光；然后与电子湮灭生成一对伽马；伽马与电子发生康普顿散射，将能量传递给电子，电子再电离激发液闪发光。
中子在液闪中慢化（平均~30微秒），在钆和氢上俘获，释放总能量为8MeV或2.2MeV的伽马光子，同上，激发液闪发光。
液闪发的光由PMT探测。

## Slide 90: Photoelectrons
LS ~ 10k photons/MeV, isotropic, point-like
Photocathode coverage (with reflector): 12%
Light attenucation ~exp(-3/20)=0.86
PMT quantum eff. ~20%, PMT collection eff. 0.8
10k*0.12*0.86*0.8 ~ 165 p.e./MeV

## Slide 91: 触发
去掉噪声和低能本底事例
NHIT（100ns内PMT击中数）
ESUM（总光电子数）
PMT暗噪声，常温下 kHz – 10 kHz

## Slide 92: Energy Calibration
R=0
R=1.7725 m
R=1.35m
LED (PMT gain，timing)
Ge68 (positron threshold 1.022 MeV)
Co60 (2.506 MeV) + Am-C (neutron)
Co60: 100 Hz
1.173 + 1.332 MeV
Ge68: 15 Hz
0.511x2 MeV
Am-C：
0.5 Hz

## Slide 93: Energy Scale Uncertainty
能标误差 0.2%
通过Monte Carlo方法传递能标误差到效率误差不同AD有 0.12% 的相对效率差别

## Slide 94: 7- Event in Detector and Event Selection

## Slide 95: 数据的构成
Neutron event rate（0.01 Hz@near site)
Trigger ~ 0.4 MeV
AD event rate 280 Hz
  PMT dark noise
  PMT flasher
  Radioactivity (low E）
  Muon(high E)
  Cosmogenic n, isotope
  Neutron source bkg
  Neutrino
Muons in Inner Water Pool (IWS), outer (OWS)
RPC、FADC readout

## Slide 96: 水池宇宙线事例
Nhit > 12
IWS
OWS

## Slide 97: First look at the delayed (n) signal
Delayed signal
Delayed signal after muon veto
Delayed signal within muon window
(spallation n)

## Slide 98: PMT Flasher
顶点分布，说明存在未知本底，本底有固定hit pattern
AD1/2的能谱应该相同
正常事例
Flasher本底

## Slide 99: PMT Flasher
光电倍增管底座打火。
打火PMT电荷最大
对面一些PMT也被照亮
IBD
Flasher

## Slide 100: Reject PMT Flasher
5%的PMT会打火，形成的本底事例占总事例5%
中微子
Flasher
会带来0.01%的相对误差 

## Slide 101: Cross Check
Time correlation
distance
energy
Time correlation
distance
energy
Flasher

## Slide 102: Data Reduction
首先去掉非物理事例——Flasher
再去掉宇宙线、以及宇宙线引起的本底
  大信号后PMT过冲形成的电子学噪声
  米歇尔电子
  spallation中子
  其它长寿命同位素

## Slide 103: 全能谱
去掉Flasher，排除宇宙muon及其后200微秒的事例后，得到的能谱
210Po 

## Slide 104: Neutrino Selections
0.7-12 MeV
6-12 MeV
Prompt candidate
Delayed candidate
Correlated Events in 1-200 s
Reactor Neutrinos
(Prompt)
Neutrons (Delayed )

## Slide 105: Neutrino Event Selection
Pre-selection
  Reject Flashers
  Reject Triggers within (-2 μs, 200 μs) to a tagged water pool muon
Neutrino event selection
  Multiplicity cut
    Prompt-delayed pairs within a time interval of 200 μs
    No triggers(E > 0.7MeV) before the prompt signal and after the delayed signal by 200 μs
  Muon veto
    1s after an AD shower muon
    1ms after an AD muon
    0.6ms after an WP muon
  0.7MeV < Eprompt < 12.0MeV
  6.0MeV < Edelayed < 12.0MeV
  1μs < Δte+-n < 200μs

## Slide 106: Selected Signal Events
Time between prompt-delayed
Distance between prompt-delayed
Prompt energy

## Slide 107: Efficiency and Uncertainty
Total 78.8% 1.9% 0.2%
每做一次挑选（cut条件）就会带来一个误差！
不同探测器之间的差别当成误差（非关联）

## Slide 108: Functional Identical Detectors
Why systematics is so small? c.f. An et al. NIM. A 685 (2012) 78
  Idea of "identical detectors" throughout the procedures of design / fabrication / assembly / filling.
  For example: Inner Acrylic Vessel, designed D=31205 mm
    Variation of D by geometry survey=1.7mm, Var. of volume: 0.17%
    Target mass var. by load cell measurement during filling: 0.19%
Diameter | IAV1 | IAV2 | IAV3 | IAV4 | IAV5 | IAV6
Surveyed(mm) | 3123.12 | 3121.71 | 3121.77 | 3119.65 | 3125.11 | 3121.56
Variation (mm) | 1.3 | 2.0 | 2.3 | 1.8 | 1.5 | 2.3
  "Same batch" of liquid scintillator
5x40 t Gd-LS, circulated
200 t LS, circulated
4-m AV in pairs
Assembly in pairs
20 t filling tank

## Slide 109: Side-by-side Comparison
Expected ratio of neutrino events: R(AD1/AD2) = 0.982
Measured ratio: 0.987  0.004(stat)  0.003(syst)
This check shows that systematic errors are under control, and will verify the final systematic error
Data set: Dec 24 to May 11

## Slide 110: 8 - Background

## Slide 111: 本底（设计值）
9Li/8He （关联本底）（估计B/S 0.3%）
  宇宙线产生的长寿命同位素，-n级联衰变，与中微子信号类似。
“快中子” 本底 （关联本底）（估计B/S 0.1-0.2%)
  宇宙线产生的高能中子，中子与质子碰撞形成快信号，慢化中子形成慢信号。
  中子在碳、氧核中俘获，发射高能中子。
偶然符合本底（估计B/S ~1%，减除误差 ~0.1%）
  类正电子信号 (单事例率 <100 Hz)
    天然放射性 (PMT, 岩石, 钢罐, 液闪, … <50 Hz)
    宇宙线、宇宙线产生的同位素，等等
  类中子信号 (<200/day)
    单中子：宇宙线产生的、未留下质子反冲信号的中子。
    宇宙线产生的长寿命同位素 (例如 12B/12N)
    其它在 6-10 MeV 范围内的事例 (例如 Michel’s electron, 宇宙线等)
来源：宇宙线，天然放射性，从以前实验的经验：

## Slide 112: 1 – 8He/9Li
Cosmic m produced 9Li/8He in LS
  b-decay + neutron emitter
  t(8He/9Li ) = 171.7ms/257.2ms
  8He/9Li, Br(n) = 12%/48%, 9Li dominant
  Production rate follow Em0.74 power law
Measurement:
  Time-since-last-muon fit
  Improve the precision by reducing the muon rate:
    Select only muons with an energy deposit >1.8MeV within a [10us, 200us] window
    Issue: possible inefficiency of 9Li
  Results w/ and w/o the reduction is studied
NIM A564 (2006)471
9Li yield
Error follows

## Slide 113: 2 - Fast Neutron
方法2： 按来源累加
方法1 ：外推
宇宙线muon产生高能中子
质子反冲（快信号）
慢化中子俘获（慢信号）

## Slide 114: 3 - Accidental
方法1：Evaluated by coincidence probability
方法2：off-windows coincidence
方法3： vertex distance distribution
0.7-12 MeV
6-12 MeV
Prompt candidate
Delayed candidate

## Slide 115: 4,5 – neutron souce and 13C(α,n)16O
B/S @ EH1/2 ~ 0.01%, B/S @ EH3 ~ 0.05%， DB/B ~ 50%
Time correlations of the cascade decays
(1ms, 3ms)
(10ms, 160ms)
(1ms, 2ms)
Total
232Th
238U
227Ac
227Ac
Delayed energy (MeV)
Prompt energy (MeV)
  中子源本底：大亚湾独有
  Alpha-n本底，KamLAND实验

## Slide 116: 排它性分析
为什么中子能区有这么多事例？(6.0~12.0MeV)?
Possible sources
排它性分析（Exclusive）：假如我们找到了全部事例的来源，就不存在未知本底

## Slide 117: 中子能区事例
12B

## Slide 118: 中子能区事例能谱的比较
各分量求和得到的能谱与总能谱比较
理解了探测器事例，没有大的未知本底（排它性）

## Slide 119: 信号与本底
 | AD1 | AD2 | AD3 | AD4 | AD5 | AD6
Antineutrino candidates | 69121 | 69714 | 66473 | 9788 | 9669 | 9452
DAQ live time (day) | 127.5470 |  | 127.3763 | 126.2646 |  | 
Efficiency em*em | 0.8015 | 0.7986 | 0.8364 | 0.9555 | 0.9552 | 0.9547
Accidentals (/day) | 9.73±0.10 | 9.61±0.10 | 7.55±0.08 | 3.05±0.04 | 3.04±0.04 | 2.93±0.03
Fast neutron (/day) | 0.77±0.24 | 0.77±0.24 | 0.58±0.33 | 0.05±0.02 | 0.05±0.02 | 0.05±0.02
8He/9Li (/day) | 2.9±1.5 |  | 2.0±1.1 | 0.22±0.12 |  | 
Am-C corr. (/day) | 0.2±0.2 |  |  |  |  | 
13C(α, n)16O (/day) | 0.08±0.04 | 0.07±0.04 | 0.05±0.03 | 0.04±0.02 | 0.04±0.02 | 0.04±0.02
Antineutrino rate (/day) | 662.47 ±3.00 | 670.87 ±3.01 | 613.53 ±2.69 | 77.57 ±0.85 | 76.62 ±0.85 | 74.97 ±0.84

## Slide 120: 10 - 2 Analysis

## Slide 121: Observed Neutrino Rate
6个数据点（探测器），三大误差来源：反应堆、探测器、本底

## Slide 122: 远近比值
归一化条件：无振荡时R＝1
假如无振荡，则远点中微子丢失5.6%。总误差为0.0076。由统计涨落造成缺失的概率为7.4 sigma
误差最小化条件

## Slide 123
2 function
How to take in account systematic errors correctly?
Simplest one:
Suppose divide the data into two sub-sets:
?

## Slide 124
2 function
How to take in account systematic errors correctly?
Simplest one:
Suppose divide the data into two sub-sets:
?
Let each sub-set to be one half, T1=T2=T/2.
Same data, different binning, results should be the same.

## Slide 125
Correlation
Two sub-sets share the same systematic error. They are correlated.
Now
Another form:
It is straight forward to get for two sub-sets.
We know there is only one σsys. Correlations are included automatically.

## Slide 126
General Form
J. Pumplin et. al. PRD65,014011(2001)
We have N measurements mi
ti is the true value, σi is uncorrelated errors,
βji is the j-th kind correlated error to measurement i. (K parameters)
ri and r'j are supposed to have standard gaussian distribution.
The probability distribution of the measurements is
(1)
(2)

## Slide 127
2 method 1
Integrate over ri
Can be minimized with respect to r'j with, e.g., MINUIT (K parameters)
We may need many bins in spectrum analysis.
Fitting on a quadratic polynomial is easy and stable.
(4)
(3)

## Slide 128
Equation (3) can be integrated over r'j analytically.
Evaluation of 2 function need inverse a K×K matrix.
(5)
2 method 2

## Slide 129
Evaluation χ2 function need inverse a N×N matrix.
Inverse V analytically, we can find that method 3 is equivalent to method 2.
=======================================================
Now we have 3 equivalent χ2 function.
  Method 1: K parameter fitting. K is number of correlated errors.
  Method 2: K×K matrix inversion.
  Method 3: N×N matrix inversion. N is number of data points.
Covariance Matrix Estimator
(6)
2 method 3

## Slide 130: 2 与2
假设检验与参数拟合
假设检验：理论与数据符合得好不好，2/ndf（拟合的优度）
参数拟合：假定理论是对的，确定参数。
2, 2 min , 与2

## Slide 131: Rate-only analysis
sin22θ13=0.089±0.010(stat)±0.005(syst)
：整体归一化系数，对应反应关联误差与探测器关联误差3.6%。分析时未加约束，即完全相对测量
dr：第r个反应堆对第d个探测器的中微子贡献比例
r：反应非关联误差，对应r＝0.8%
d：探测器非关联误差，对应d＝0.2%
d：本底误差，对应d=0.2-0.37%（对应的信号与本底表）
Md：第d个AD的测量中微子数
Td：第d个AD的预测中微子数
Bd：第d个AD的本底数
大亚湾分析中ndf应该等于几？

## Slide 132: Precision Measurement at Daya Bay
1230 days
Sin22θ13 = [8.41 ± 0.33] × 10-2
NH: Δm232 = [2.45 ± 0.08] × 10-3 eV2
IH: Δm232 = [-2.55 ± 0.08] × 10-3 eV2
1230 days
PRD 95, 072006 (2017)

## Slide 133: 11 – JUNO: Measure Mass Hierarchy with reactors

## Slide 134: Neutrino Rates
700米
Cosmic muons
~ 250k/day
Atmospheric 
~ 4/day
Geo-neutrinos
1-2/day
打石山
Solar 
tens/day
reactor , ~ 60/day
700 m
Supernovae 
~ 5k in 10s for 10kpc
20k ton LS
36 GW, 53 km
0.003 Hz/m2
210 GeV

## Slide 135: JUNO Location/Collaboration
Taishan NPP
Guang Zhou
Daya Bay
Hong Kong
JUNO
53 km
53 km
Yangjiang NPP
71 Institutions, 533 collaborators
China (32), Thailand (3), Pakistan, Armenia
Italy (8), Germany (7), France (6), Russia (3), Belgium, Czech, Finland, Slovakia
Brazil (2), Chile (2), USA (2)

## Slide 136: JUNO Detector
Central detector
Water Cherenkov
Top Tracker
(OPERA TT)
Calibration
Pool Depth: 44m
Pool ID:43.5m
Acrylic Sphere: ID35.4m
Steel Latticed Shell: ID40.1m
Filling +
Overflow
Acrylic sphere
(contracted)
18000 20” PMT
(contracted:
Hamamatsu 5K
NNVT 15 K)
25000 3’’ PMT
(contracted: HZCT)
~2000 20’’ PMT
SS latticed shell
Electronics
Acrylic Sphere:
ID: 35.4m
Thickness:120mm
SSLS:
ID: 40.1m
OD: 41.1m
Water pool
ID: 43.5m
Height: 44m
Water Depth: 43.5m

## Slide 137: Sensitivity on MH
PRD 88, 013008 (2013) | Relative Meas. | Use absolute Dm2
Statistics only | 4s | 5s
Realistic case | 3s | 4s
JUNO MH sensitivity with 6 years' data:

## Slide 138: Complementary MH Determination
and Interference ()
and difference
Matter Effect
atmospheric
Reactor
Accelerator
Reactors
  JUNO: approved, data in 2020, 3-4 in 6 years.
  RENO-50: R&D
Atmospheric
  INO: approved, data in 2019-2020, 3 in 10 years
  PINGU： planned, data in 2021，3 in 4 years
  ORCA： planned, data in 2020，3 in 4 years
  Hyper-K：planned, data in 2025.
Accelerator
  NOvA: operation
  DUNE：10 kton from 2024, 40 kton from 2030, >5 for all CPs

## Slide 139: Precision Measurements
 | Statistics | +BG+1% b2b+1% Scale +1% EnonL
sin2 θ12 | 0.54% | 0.67%
Δm221 | 0.24% | 0.59%
Δm2ee | 0.27% | 0.44%
Probing the unitarity of UPMNS to ~1%
more precise than CKM matrix elements !
Smeared by 3%/sqrt(E)

## Slide 140: Supernova Neutrinos
Less than 20 events observed so far
Assumptions:
  Distance: 10 kpc (our Galaxy center)
  Energy: 31053 erg
  Ln the same for all types
Possible candidate

## Slide 141: Supernova Neutrinos
LS detector vs. Water Cerenkov detectors: much better detection to these correlated events
 Measure energy spectra & fluxes of almost all types of neutrinos
Estimated numbers of neutrino events in JUNO
 mass: < 0.830.24 eV at 95% CL (arXiv:1412.7418)
Locating the SN: ~9
Pre-SN  (> 1 day)
SN Nucleosynthesis via vx spectra
Collective  oscillation
MH

## Slide 142: Diffuse Supernova Neutrino
DSNB: Past core-collapse events
  Cosmic star-formation rate
  Core-collapse neutrino spectrum
  Rate of failed SNe
10 Years’ sensitivity

## Slide 143: Mass Hierarchy from Atmospheric
Due to matter effect, oscillation probability of atmospheric muon neutrino when passing the Earth depends on mass hierarchy
JUNO will have 1-2  sensitivity.
  Measure both lepton and hadron energy
  Good tracking and energy resolution
IH
NH

## Slide 144: Geo-neutrinos
Geo-neutrinos
  Current results
  KamLAND: 30±7 TNU (PRD 88 (2013) 033001)
  Borexino: 38.8±12.2 TNU (PLB 722 (2013) 295)
  Statistics dominant
  Desire to reach an error of 3 TNU
  JUNO: ×20 statistics
    Huge reactor neutrino backgrounds
    Need accurate reactor spectra
 | Best fit | 1 y | 3 y | 5 y | 10 y
U+Th fix ratio | 0.96 | 17% | 10% | 8% | 6%
U (free) | 1.03 | 32% | 19% | 15% | 11%
Th (free) | 0.80 | 66% | 37% | 30% | 21%
Combined shape fit of geo- and reactor-

## Slide 145: Solar and other Physics
Solar neutrino
  Metallicity? Vacuum oscillation to MSW?
  7Be and 8B at JUNO
  Threshold
  Backgrounds
Sterile , Indirect dark matter, Nucleon decay, etc.
Reject events at the center  0.1 MeV threshold
5  rejection of dark noise
Liquid Scintillator | U238 | Th232 | K40 | Pb210 (Rn222) | Ref.
No Distillation | 10-15 | 10-15 | 10-16 | 1.4·10-22 | Borexino CTF, KamLAND
After Distillation | 10-17 | 10-17 | 10-18 | 10-24 | 

## Slide 146: JUNO Progress and Schedule
Ground breaking in Jan. 2015
  slope tunnel done (1265 m)
  vertical shaft done (575 m)
  Delayed by unexpected water
  Schedule:
  Detector assembly & installation: 2018-2019
  Filling & data taking: 2020
  Delayed by ~1 year
Slope tunnel
40% slope
vertical shaft