## Slide 1: 100km CEPC parameter and lattice design
Dou Wang, Jie Gao, Yuan Zhang, Chenghui Yu, Yiwei Wang, Feng Su, Huiping Geng, Cai Meng, Bai Sha, Tianjian Bian, Na Wang
CEPC AP meeting, 2017.1.13

## Slide 2
LEP2

## Slide 3: FCC-ee

## Slide 4: Oide’s comments

## Slide 5: Machine constraints / given parameters
Energy E0
Circumference C0
NIP
Beam power P0
y*
Emittance coupling factor 
Bending radius 
Piwinski angle 
y enhancement by crab waist Fl ~1.5 (2.6)
Energy acceptance (DA)
Phase advance per cell (FODO)

## Slide 6: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 7: parameter for CEPC partial double ring （wangdou20161109-61km）
 | Pre-CDR | H-high lumi. | H-low power | W | Z | Z-5cell
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 61 | 61 | 61 | 61 | 61
SR loss/turn (GeV) | 3.1 | 2.96 | 2.96 | 0.58 | 0.061 | 0.061
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.88 | 1.84 | 4.11 | 5.86 | 5.87
Ne/bunch (1011) | 3.79 | 2.0 | 1.98 | 0.85 | 0.6 | 0.6
Bunch number | 50 | 107 | 70 | 400 | 1100 | 700
Beam current (mA) | 16.6 | 16.9 | 11.0 | 26.8 | 52.0 | 33.1
SR power /beam (MW) | 51.7 | 50 | 32.5 | 15.7 | 3.2 | 2.0
Bending radius (km) | 6.1 | 6.2 | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-5) | 3.4 | 1.48 | 1.48 | 1.48 | 3.1 | 3.1
IP x/y (m) | 0.8/0.0012 | 0.272/0.0013 | 0.275 /0.0013 | 0.16/0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 2.05/0.0062 | 2.05 /0.0062 | 0.93/0.003 | 0.87/0.0046 | 0.87/0.0046
Transverse IP (um) | 69.97/0.15 | 23.7/0.09 | 23.7/0.09 | 12.2/0.056 | 10.2/0.068 | 10.2/0.068
x/IP | 0.118 | 0.041 | 0.042 | 0.0145 | 0.0098 | 0.0098
y/IP | 0.083 | 0.11 | 0.11 | 0.084 | 0.073 | 0.073
VRF (GV) | 6.87 | 3.48 | 3.51 | 0.7 | 0.12 | 0.12
f RF (MHz) | 650 | 650 | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.7 | 2.7 | 3.23 | 3.9 | 3.9
Total z (mm) | 2.65 | 2.95 | 2.9 | 3.35 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 | 0.74 | 0.48 | 0.47 | 0.59 | 0.93
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.087 | 0.05 | 0.05
Energy acceptance (%) | 2 | 2 | 2 |  |  | 
Energy acceptance by RF (%) | 6 | 2.3 | 2.4 | 1.3 | 1.1 | 1.1
n | 0.23 | 0.35 | 0.34 | 0.28 | 0.24 | 0.24
Life time due to beamstrahlung_cal (minute) | 47 | 37 | 37 |  |  | 
F (hour glass) | 0.68 | 0.82 | 0.82 | 0.89 | 0.92 | 0.92
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.01 | 3.5 | 3.44 | 2.2

## Slide 8: parameters for CEPC double ring （wangdou20161202-100km_2mmy）
 | Pre-CDR | H-high lumi. | H-low power | W | Z |  | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 80 | 45.5 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.9 | 2.9 | 3.57 | 5.69 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 0.97 | 0.97 | 1.05 | 0.46 | 0.46 | 0.46
Bunch number | 50 | 644 | 425 | 1000 | 10520 | 16666 | 65716
Beam current (mA) | 16.6 | 29.97 | 19.8 | 50.6 | 232.1 | 367.7 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 33 | 16.7 | 8.0 | 12.7 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3 | 3.1 | 3.3 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.144 /0.002 | 0.144 /0.002 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 1.56/0.0047 | 1.56/0.0047 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 15/0.097 | 15/0.097 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.0126/0.083 | 0.0126/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 131.2 | 131.2 | 149 | 160.8 | 160.8 | 160.8
VRF (GV) | 6.87 | 2.22 | 2.22 | 0.63 | 0.11 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 (217800) | 650 (217800) | 650 (217800) | 650 (217800) |  | 
Nature z (mm) | 2.14 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.64 (2cell) | 0.42 (2cell) | 1.0 (2cell) | 1.0 (1cell) | 1.6(1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037 | 0.037
Energy acceptance (%) | 2 | 1.5 | 1.5 |  |  |  | 
Energy acceptance by RF (%) | 6 | 2.2 | 2.2 | 1.5 | 1.1 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 |  |  |  | 
F (hour glass) | 0.68 | 0.95 | 0.95 | 0.84 | 0.91 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.05 | 4.08 | 11.36 | 18.0 | 70.97

## Slide 9: parameters for CEPC double ring （wangdou20161219-100km_2mmy）
 | Pre-CDR | tt | H-high lumi. | H-low power | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 175 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 7.55 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.6 | 2.9 | 2.9 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 1.41 | 0.97 | 0.97 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 98 | 644 | 425 | 1000 | 10520 | 65716
Beam current (mA) | 16.6 | 6.64 | 29.97 | 19.8 | 50.6 | 232.1 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 50 | 33 | 16.7 | 8.0 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3 | 1.3 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.2/0.002 | 0.144 /0.002 | 0.144 /0.002 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 3.19/0.0097 | 1.56/0.0047 | 1.56/0.0047 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 25.3/0.14 | 15/0.097 | 15/0.097 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.016/0.055 | 0.0126/0.083 | 0.0126/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 122.2 | 131.2 | 131.2 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 8.92 | 2.22 | 2.22 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 | 650 (217800) | 650 (217800) | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.62 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.7 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.53(5cell) | 0.64 (2cell) | 0.42 (2cell) | 1.0 (2cell) | 1.0 (1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.14 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 2 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.6 | 2.2 | 2.2 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 50 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.89 | 0.95 | 0.95 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 0.62 | 3.1 | 2.05 | 4.08 | 11.36 | 70.97

## Slide 10: parameter for CEPC double ring （wangdou20161110-100km_1mmy）
 | Pre-CDR | H-high lumi. | H-low power I | H-low power II
Number of IPs | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 54 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 1.67
Half crossing angle (mrad) | 0 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.5 | 2.5
Ne/bunch (1011) | 3.79 | 1.12 | 1.12 | 1.12
Bunch number | 50 | 555 | 333 | 211
Beam current (mA) | 16.6 | 29.97 | 17.98 | 11.4
SR power /beam (MW) | 51.7 | 50 | 30 | 19
Bending radius (km) | 6.1 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 0.96 | 0.96 | 0.96
IP x/y (m) | 0.8/0.0012 | 0.3/0.001 | 0.3/0.001 | 0.3 /0.001
Emittance x/y (nm) | 6.12/0.018 | 1.01/0.0031 | 1.01/0.0031 | 1.01/0.0031
Transverse IP (um) | 69.97/0.15 | 17.4/0.055 | 17.4/0.055 | 17.4/0.055
x/IP | 0.118 | 0.029 | 0.029 | 0.029
y/IP | 0.083 | 0.083 | 0.083 | 0.083
VRF (GV) | 6.87 | 2.0 | 2.0 | 2.0
f RF (MHz) | 650 | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.72 | 2.72 | 2.72
Total z (mm) | 2.65 | 2.9 | 2.9 | 2.9
HOM power/cavity (kw) | 3.6(5cell) | 0.75(2cell) | 0.45(2cell) | 0.28(2cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.098
Energy acceptance (%) | 2 | 1.5 | 1.5 | 1.5
Energy acceptance by RF (%) | 6 | 1.8 | 1.8 | 1.8
n | 0.23 | 0.26 | 0.26 | 0.26
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 | 52
F (hour glass) | 0.68 | 0.83 | 0.83 | 0.83
Lmax/IP (1034cm-2s-1) | 2.04 | 5.42 | 3.25 | 2.06

## Slide 11: 100km CEPC luminosity potential (50MW/beam)
tt
H
z

## Slide 13: Parameter for single ring-100km （wangdou20161122）
 | Pre-CDR | New-100km | 
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120
Circumference (km) | 54 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67
Ne/bunch (1011) | 3.79 | 1.79 | 1.79
Bunch number | 50 | 350 | 100
Beam current (mA) | 16.6 | 30.0 | 8.6
SR power /beam (MW) | 51.7 | 50 | 14.3
Bending radius (km) | 6.1 | 11 | 11
Momentum compaction (10-5) | 3.4 | 3.15 | 3.15
IP x/y (m) | 0.8/0.0012 | 0.4/0.0012 | 0.4/0.0012
Emittance x/y (nm) | 6.12/0.018 | 6.18/0.019 | 6.18/0.019
Transverse IP (um) | 69.97/0.15 | 49.5/0.15 | 49.5/0.15
x/IP | 0.118 | 0.055 | 0.055
y/IP | 0.083 | 0.055 | 0.055
VRF (GV) | 6.87 | 4.88 | 4.88
f RF (MHz) | 650 | 650 | 650
Nature z (mm) | 2.14 | 2.41 | 2.41
Total z (mm) | 2.65 | 2.47 | 2.47
HOM power/cavity (kw) | 3.6 | 3.2 | 0.92
Energy spread (%) | 0.13 | 0.098 | 0.098
Energy acceptance (%) | 2 | 0.94 | 0.94
Energy acceptance by RF (%) | 6 | 4.5 | 4.5
n | 0.23 | 0.15 | 0.15
Life time due to beamstrahlung_cal (minute) | 47 | 54 | 54
F (hour glass) | 0.68 | 0.7 | 0.7
Lmax/IP (1034cm-2s-1) | 2.04 | 2.5 | 0.72

## Slide 14: Primary consideration of lattice design
Arc cell : 90 FODO cell
Cell length: 76m
Bending radius of dipole: 11km
Bending angle per cell: 0.00616761rad
Emittance : 1.56 nm
Number of FODO cell: 1018
Total length of arc: 77 km
Total length of PDR(inc. IR): 10km
Total length of straight (inc. APDR): 13 km
alphap = 1.3×10-5

## Slide 16: Final doublet + triplet
x=0.75, y=0.5
Betax=0.22m
Betay=0.002m

## Slide 17: FFS optics
x=1.5, y=1.25
x=1.0, y=0.75

## Slide 18: W function
98
98
28
-37
184
98
98
98
98
98

## Slide 20: Pure Arc

## Slide 21: DA of arc

## Slide 22: Tuning working point in straint

## Slide 23: Tuning working point in arc

## Slide 24: Arc DA (2 fam)
No damping
Tracking 240 turns

## Slide 25: Arc + FFS

## Slide 26
CCX is necessary for CEPC?

## Slide 27: Arc + FFS

## Slide 28: Arc + FFS (2 fam)
No damping
Tracking 200 turns
Energy acceptance： 0.5%

## Slide 29: Arc + FFS (104 fam)
Without damping
Tracking 200 turns
Energy acceptance： 1.0%

## Slide 30: Arc + FFS (104 fam)
With damping
Tracking 200 turns
Energy acceptance： 1.5%

## Slide 31: FFS optics
x=1.5, y=1.25
x=1.0, y=0.75
Betax=0.144m
Betay=0.002m

## Slide 32: Chromaticity of FFS

## Slide 33: Arc + FFS (2 fam)

## Slide 34: W function of whole ring
Betax=0.144m
Betay=0.002m
Betax=0.22m
Betay=0.002m

## Slide 35: Tuning phase of FFS
Betax=0.144m
Betay=0.002m

## Slide 36: Arc + FFS (2 fam)
No damping
Tracking 200 turns
Energy acceptance： 0.5%

## Slide 37: Arc + FFS (104 fam)
With damping
Tracking 200 turns
Energy acceptance： 1.0%

## Slide 38: Arc + FFS (104 fam)
Betax=0.22m
Betay=0.002m
Betax=0.144m
Betay=0.002m
Energy acceptance： 1.5%
Energy acceptance： 1.0%