## Slide 1: Performance of MDC during New Data Taking
WU Linghui, WANG Meng
2007-03-15

## Slide 2: Outline
Overview of new data
Noise issue

## Slide 3: MDC data performance from tracking calibration
Run 47467 – 49830 (2016/12/11 ~ 2017/03/07)
Boss release: 7.0.2.p01
Finish 1st round of calibration
  Calibration of X-T, electronic T0 and Q-T using Bhabha
Use old alignment parameters
Final calibration will be performed after data taking
  Low pT tracks are selected to calibrate X-T relations with large entrance angle

## Slide 4: Hitmap & dead channels
T/Q match
T channel
Wire ID
Layer | Cell
13 | 88
16 | 14
16 | 81-88
17 | 13
19 | 28
19 | 43
20 | 111
29 | 56
33 | 145
33 | 148
38 | 246
39 | 89
42 | 38
43 | 168
Run 48000

## Slide 5: Resolutions vs run
Spatial resolution vs run
sP vs run

## Slide 6: Hit efficiency vs run

## Slide 7: Resolutions
Run47543 (Low noise occupancy)
Resolutions are normal
  Spatial resolution: 116mm
  sP=14.4MeV/c @2.1GeV/c
Alignment: No big displacement

## Slide 8: Layer by layer comparison

## Slide 9: dE/dx performance is normal
All fluctuations are within reasonable ranges.
The resolution is fine.
From Jinfa Qiu and Kai Zhu

## Slide 10: Noise issue
Beam related background
  Reflected from leakage current and has impact on both T and Q channels (BG)
Two types of electronics noises
  Electron beam related noise in T channels of the inner chamber (N I)
  Beam-independent noise in T & Q channels of all layers (N II)

## Slide 11: Electron beam related noise (N I)
Features:
  Only has a relationship with the current of the e- beam, and become more serious with the increase of the current of the single e- bunch.
  Just impact on the time measurement of the inner chamber cells
  The noise in the odd layer (layer 1,3,5…, read out from the east end of the MDC) is more serious than the even layer (layer 0,2,4…, read out from the west end )
Noise source: DCCT (DC current transfer) in the e- storage ring
Solution: Replace the new DCCT shielding box with the old one, and the noise disappears (The new shielding box is bigger than the old one, which benefit the cooling, but the new shielding box have no magnetic layers ) (Feb 14, 2017)
Provided by Mingyi Dong

## Slide 12
TDC (ns)
TDC distribution
layer3

## Slide 13: Beam-independent noise (N II)
Features:
  This noise has no relationship with the beam
  Has an relationship with the current of AS (reverse solenoid) at the west end
  Has an effect on both the time and the charge measurement of all cells from the inner chamber to the outer chamber
Noise source: the ground from the west end
Solution: reconnect the ground of the accelerator together with the ground of the west door of BESIII and west end cap of EMC, and the noise disappears (Feb 23, 2017)
Provided by Mingyi Dong

## Slide 14
T channel
TDC distribution
Layer 16
T/Q match
TDC (ns)

## Slide 15
T channel
TDC distribution (Layer 16)
T/Q match
TDC (ns)
Run 49375
TDC (ns)
Run 47543
Low noise level
T channel
T/Q match
noise

## Slide 16: Noise occupancy and leakage current
Layer 1
N I
BG

## Slide 17: Noise occupancy and trigger rate
N_inner_track ≥2
N_long_track ≥2
N II
N I
Mixture of BG and different kinds of noises in data

## Slide 18: Impact on MDC performance
Low noise levelgood resolution & hit efficiency
NI causes low hit efficiency by contaminating the drift time

## Slide 19: Impact on MDC performance
The impact of NII is not too bad due to the noise can be distinguished with drift time

## Slide 20: Impact on MDC performance
Why the resolution is so worse?
Gain? ×
Calibration? ×
Tracking algorithm? ×
Other reasons?

## Slide 21: Impact on MDC performance
48503
48605

## Slide 23
TDC (ns)
TDC distribution of layer 5
Run 48605
Run 48503

## Slide 24
TDC (ns)
TDC distribution of layer 5
Run 48605
Run 48503
25ns
25ns

## Slide 25: Summary
Resolutions and hit efficiency are good at low noise level
No big displacement
dE/dx performance is normal
Noise
  Mixture of beam background and different kinds of electronics noises
  Need more study
Thanks for your attention!

## Slide 26: backup