## Slide 1: Parameters and DA of 100km CEPC
Dou Wang, Chenghui Yu, Yuan Zhang, Yiwei Wang, Sha Bai, Feng Su, Cai Meng, Chuang Zhang, Na Wang, Tianjian Bian, Huiping Geng, Jie Gao
CEPC AP meeting, 2017.04.07

## Slide 2: Parameter difference between CEPC and FCCee
 | CEPC | FCCee
Ne/bunch (1011) | 0.97 | 0.8
Momentum compaction (10-5) | 1.3 | 0.7
IP x/y (m) | 0.144 /0.002 | 1/0.002
Emittance x/y (nm) | 1.56/0.0047 | 0.61/0.0012
Coupling factor (%) | 0.3 | 0.2
x/y/IP | 0.0126/0.083 | 0.08/0.14
VRF (GV) | 2.22 | 3
f RF (MHz) | 650 | 400
Nature z (mm) | 2.72 | 2
Total z (mm) | 2.9 | 2.4
Energy acceptance by RF (%) | 2.2 | 7.0
Energy acceptance requirement (%) | 1.5 | 2.0
Lmax/IP (1034cm-2s-1) | 3.1 | 5.1

## Slide 3: Constraints for parameter choice
Limit of Beam-beam tune shift
Beam lifetime due to beamstrahlung
Beamstrahlung energy spread
HOM power per cavity (coaxial coupler)
Fl: y enhancement by crab waist
*J. Gao, emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings, Nucl. Instr. and methods A533（2004）p. 270-274.
BS life time: 30 min
A=0/BS (A3)
V.I. Telnov

## Slide 4: parameters for CEPC double ring （wangdou20161219-100km_1mmy）
 | Pre-CDR | H-high lumi. | H-low power |  | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 2.5 | 2.5 | 2.5 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 1.12 | 1.12 | 1.12 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 555 | 333 | 211 | 1000 | 16666 | 65716
Beam current (mA) | 16.6 | 29.97 | 17.98 | 11.4 | 50.6 | 367.7 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 30 | 19 | 16.7 | 12.7 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 0.96 | 0.96 | 0.96 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.3/0.001 | 0.3/0.001 | 0.3 /0.001 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 1.01/0.0031 | 1.01/0.0031 | 1.01/0.0031 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 17.4/0.055 | 17.4/0.055 | 17.4/0.055 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.029/0.083 | 0.029/0.083 | 0.029/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 123.3 | 123.3 | 123.3 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 2.0 | 2.0 | 2.0 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 | 650 | 650 | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.72 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.9 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.75(2cell) | 0.45(2cell) | 0.28(2cell) | 1.0 (2cell) | 1.6(1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.098 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 1.5 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 1.8 | 1.8 | 1.8 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.26 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.83 | 0.83 | 0.83 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 5.42 | 3.25 | 2.06 | 4.08 | 18.0 | 70.97

## Slide 5: parameters for CEPC double ring （wangdou20161202-100km_2mmy）
 | Pre-CDR | H-high lumi. | H-low power
Number of IPs | 2 | 2 | 2
Energy (GeV) | 120 | 120 | 120
Circumference (km) | 54 | 100 | 100
SR loss/turn (GeV) | 3.1 | 1.67 | 1.67
Half crossing angle (mrad) | 0 | 15 | 15
Piwinski angle | 0 | 2.9 | 2.9
Ne/bunch (1011) | 3.79 | 0.97 | 0.97
Bunch number | 50 | 644 | 425
Beam current (mA) | 16.6 | 29.97 | 19.8
SR power /beam (MW) | 51.7 | 50 | 33
Bending radius (km) | 6.1 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.3
IP x/y (m) | 0.8/0.0012 | 0.144 /0.002 | 0.144 /0.002
Emittance x/y (nm) | 6.12/0.018 | 1.56/0.0047 | 1.56/0.0047
Transverse IP (um) | 69.97/0.15 | 15/0.097 | 15/0.097
x/y/IP | 0.118/0.083 | 0.0126/0.083 | 0.0126/0.083
RF Phase (degree) | 153.0 | 131.2 | 131.2
VRF (GV) | 6.87 | 2.22 | 2.22
f RF (MHz) (harmonic) | 650 | 650 (217800) | 650 (217800)
Nature z (mm) | 2.14 | 2.72 | 2.72
Total z (mm) | 2.65 | 2.9 | 2.9
HOM power/cavity (kw) | 3.6 (5cell) | 0.64 (2cell) | 0.42 (2cell)
Energy spread (%) | 0.13 | 0.098 | 0.098
Energy acceptance (%) | 2 | 1.5 | 1.5
Energy acceptance by RF (%) | 6 | 2.2 | 2.2
n | 0.23 | 0.26 | 0.26
Life time due to beamstrahlung_cal (minute) | 47 | 52 | 52
F (hour glass) | 0.68 | 0.95 | 0.95
Lmax/IP (1034cm-2s-1) | 2.04 | 3.1 | 2.05

## Slide 6: Luminosity vs. crossing angle
Keep beamstrahlung life time constant (52min)

## Slide 7: Luminosity vs. crossing angle
Keep emittance constant (1.56nm)

## Slide 8: Luminosity vs. y*
Keep beamstrahlung life time constant (52min)

## Slide 9: Luminosity vs. y*
Keep emittance constant (1.56nm)

## Slide 10: Luminosity vs. SR power
goal

## Slide 11: parameters for CEPC double ring （wangdou20170306-100km_2mmy）
 | Pre-CDR | tt | Higgs | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 175 | 120 | 80 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 7.55 | 1.67 | 0.33 | 0.034
Half crossing angle (mrad) | 0 | 16.5 | 16.5 | 16.5 | 16.5
Piwinski angle | 0 | 1.6 | 3.19 | 5.69 | 4.29
Ne/bunch (1011) | 3.79 | 1.41 | 0.968 | 0.365 | 0.455
Bunch number | 50 | 98 | 412 | 5534 | 21300
Beam current (mA) | 16.6 | 6.64 | 19.2 | 97.1 | 465.8
SR power /beam (MW) | 51.7 | 50 | 32 | 32 | 16.1
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.14 | 1.14 | 4.49
IP x/y (m) | 0.8/0.0012 | 0.2/0.002 | 0.171/0.002 | 0.171 /0.002 | 0.16/0.002
Emittance x/y (nm) | 6.12/0.018 | 3.19/0.0097 | 1.31/0.004 | 0.57/0.0017 | 1.48/0.0078
Transverse IP (um) | 69.97/0.15 | 25.3/0.14 | 15.0/0.089 | 9.9/0.059 | 15.4/0.125
x/y/IP | 0.118/0.083 | 0.016/0.055 | 0.013/0.083 | 0.0055/0.062 | 0.008/0.054
RF Phase (degree) | 153.0 | 122.2 | 128 | 126.9 | 165.3
VRF (GV) | 6.87 | 8.92 | 2.1 | 0.41 | 0.14
f RF (MHz) (harmonic) | 650 | 650 | 650 | 650 (217800) | 650 (217800)
Nature z (mm) | 2.14 | 2.62 | 2.72 | 3.37 | 3.97
Total z (mm) | 2.65 | 2.7 | 2.9 | 3.4 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.53(5cell) | 0.41(2cell) | 0.36(2cell) | 1.99(2cell)
Energy spread (%) | 0.13 | 0.14 | 0.098 | 0.065 | 0.037
Energy acceptance (%) | 2 | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 2.6 | 2.1 | 1.1 | 1.1
n | 0.23 | 0.23 | 0.26 | 0.15 | 0.12
Life time due to beamstrahlung_cal (minute) | 47 | 50 | 52 |  | 
F (hour glass) | 0.68 | 0.89 | 0.96 | 0.98 | 0.96
Lmax/IP (1034cm-2s-1) | 2.04 | 0.62 | 2.0 | 5.15 | 11.9

## Slide 12
For Z pole, if we use the same RF system as Higgs and feedback system, the luminosity is 1.21035cm-2s-1.
Considering the constraint of 10 ns bunch separation from detector, the maximum bunch number is 30870 and the according beam power is 23MW.

## Slide 14
x=1.5, y=1.25
x=1.0, y=0.75

## Slide 15: arc

## Slide 18: DA without crab

## Slide 19: FFS optics （L*=2.2m,Betax=0.171m,Betay=0.002m）
Tune: 348.338/348.22

## Slide 20
L*=2.2m
Betax=0.171m
Betay=0.002m

## Slide 21: DA optimization （112fam）
Damping open
Damping close

## Slide 22: FFS optics （L*=2.2m,Betax=1.0m,Betay=0.002m）
Tune: 348.338/348.22

## Slide 23
L*=2.2m
Betax=1.0m
Betay=0.002m

## Slide 24: DA optimization （112fam）
Damping open
Damping close

## Slide 25: Z parameters with different coupling
 | Z-0.303% | Z-0.527% | Z-0.714% | Z-1% | Z-1%
Number of IPs | 2 |  |  |  | 
Energy (GeV) | 45.5 |  |  |  | 
Circumference (km) | 100 |  |  |  | 
SR loss/turn (GeV) | 0.034 |  |  |  | 
Half crossing angle (mrad) | 16.5 |  |  |  | 
Piwinski angle | 4.29 |  |  |  | 
Ne/bunch (1011) | 0.346 | 0.455 | 0.532 | 0.63 | 0.455
Bunch number | 30870 | 21300 | 15580 | 11120 | 21300
Beam current (mA) | 513.3 | 465.8 | 398.3 | 336.7 | 465.8
SR power /beam (MW) | 17.7 | 16.1 | 13.7 | 11.6 | 16.1
Bending radius (km) | 11 |  |  |  | 
Momentum compaction (10-5) | 4.49 |  |  |  | 
IP x/y (m) | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002
Emittance x/y (nm) | 1.48/0.0045 | 1.48/0.0078 | 1.48/0.0106 | 1.48/0.015 | 1.48/0.015
Transverse IP (um) | 15.4/0.095 | 15.4/0.125 | 15.4/0.145 | 15.4/0.172 | 15.4/0.17
x/y/IP | 0.006/0.054 | 0.008/0.054 | 0.009/0.054 | 0.011/0.054 | 0.008/0.039
RF Phase (degree) | 165.2 | 165.3 | 165.4 | 165.6 | 165.3
VRF (GV) | 0.13 | 0.14 | 0.14 | 0.14 | 0.14
f RF (MHz) (harmonic) | 650 (217800) |  |  |  | 
Nature z (mm) | 3.99 | 3.97 | 3.96 | 3.93 | 3.96
Total z (mm) | 4.0 |  |  |  | 
HOM power/cavity (kw) | 1.67(2cell) | 1.99(2cell) | 1.99(2cell) | 1.99 | 1.99
Energy spread (%) | 0.037 |  |  |  | 
Energy acceptance by RF (%) | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
n | 0.09 | 0.12 | 0.14 | 0.17 | 0.12
F (hour glass) | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
Lmax/IP (1034cm-2s-1) | 13.1 | 11.9 | 10.2 | 8.62 | 8.61

## Slide 26: Z parameters with different coupling-2cell
 | Z-0.303% | Z-0.527% | Z-0.714% | Z-1% | Z-1.5% | Z-2%
Number of IPs | 2 |  |  |  |  | 
Energy (GeV) | 45.5 |  |  |  |  | 
Circumference (km) | 100 |  |  |  |  | 
SR loss/turn (GeV) | 0.034 |  |  |  |  | 
Half crossing angle (mrad) | 16.5 |  |  |  |  | 
Piwinski angle | 4.29 |  |  |  |  | 
Ne/bunch (1011) | 0.346 | 0.455 | 0.532 | 0.63 | 0.77 | 0.89
Bunch number | 27018 | 21300 | 15580 | 11120 | 7410 | 5550
Beam current (mA) | 449.3 | 465.8 | 398.3 | 336.7 | 274.9 | 237.9
SR power /beam (MW) | 15.5 | 16.1 | 13.7 | 11.6 | 9.5 | 8.2
Bending radius (km) | 11 |  |  |  |  | 
Momentum compaction (10-5) | 4.49 |  |  |  |  | 
IP x/y (m) | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002
Emittance x/y (nm) | 1.48/0.0045 | 1.48/0.0078 | 1.48/0.0106 | 1.48/0.015 | 1.48/0.022 | 1.48/0.029
Transverse IP (um) | 15.4/0.095 | 15.4/0.125 | 15.4/0.145 | 15.4/0.172 | 15.4/0.21 | 15.4/0.243
x/y/IP | 0.006/0.054 | 0.008/0.054 | 0.009/0.054 | 0.011/0.054 | 0.014/0.054 | 0.016/0.54
RF Phase (degree) | 165.2 | 165.3 | 165.4 | 165.6 | 166.0 | 166.4
VRF (GV) | 0.13 | 0.14 | 0.14 | 0.14 | 0.14 | 0.15
f RF (MHz) (harmonic) | 650 (217800) |  |  |  |  | 
Nature z (mm) | 3.99 | 3.97 | 3.96 | 3.93 | 3.88 | 3.81
Total z (mm) | 4.0 |  |  |  |  | 
HOM power/cavity (kw) | 1.46(2cell) | 1.99(2cell) | 1.99(2cell) | 1.99(2cell) | 1.99(2cell) | 1.99(2cell)
Energy spread (%) | 0.037 |  |  |  |  | 
Energy acceptance by RF (%) | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
n | 0.09 | 0.12 | 0.14 | 0.17 | 0.2 | 0.23
F (hour glass) | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
Lmax/IP (1034cm-2s-1) | 11.5 | 11.9 | 10.2 | 8.62 | 7.04 | 6.1

## Slide 27: Z parameters with different coupling-1cell
 | Z-0.303% | Z-0.527% | Z-1% | Z-1.5% | Z-2%
Number of IPs | 2 |  |  |  | 
Energy (GeV) | 45.5 |  |  |  | 
Circumference (km) | 100 |  |  |  | 
SR loss/turn (GeV) | 0.034 |  |  |  | 
Half crossing angle (mrad) | 16.5 |  |  |  | 
Piwinski angle | 4.29 |  |  |  | 
Ne/bunch (1011) | 0.346 | 0.455 | 0.63 | 0.77 | 0.89
Bunch number | 27018 | 27018 | 22250 | 14810 | 11090
Beam current (mA) | 449.3 | 590.8 | 673.7 | 549.5 | 475.4
SR power /beam (MW) | 15.5 | 20.4 | 23.2 | 18.95 | 16.4
Bending radius (km) | 11 |  |  |  | 
Momentum compaction (10-5) | 4.49 |  |  |  | 
IP x/y (m) | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002
Emittance x/y (nm) | 1.48/0.0045 | 1.48/0.0078 | 1.48/0.015 | 1.48/0.022 | 1.48/0.029
Transverse IP (um) | 15.4/0.095 | 15.4/0.125 | 15.4/0.172 | 15.4/0.21 | 15.4/0.243
x/y/IP | 0.006/0.054 | 0.008/0.054 | 0.011/0.054 | 0.014/0.054 | 0.016/0.54
RF Phase (degree) | 165.2 | 165.3 | 165.6 | 166.0 | 166.4
VRF (GV) | 0.13 | 0.14 | 0.14 | 0.14 | 0.15
f RF (MHz) (harmonic) | 650 (217800) |  |  |  | 
Nature z (mm) | 3.99 | 3.97 | 3.93 | 3.88 | 3.81
Total z (mm) | 4.0 |  |  |  | 
HOM power/cavity (kw) | 0.73(1cell) | 1.26(1cell) | 1.99(1cell) | 1.99(1cell) | 1.99(1cell)
Energy spread (%) | 0.037 |  |  |  | 
Energy acceptance by RF (%) | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
n | 0.09 | 0.12 | 0.17 | 0.2 | 0.23
F (hour glass) | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
Lmax/IP (1034cm-2s-1) | 11.5 | 15.1 | 17.25 | 14.1 | 12.2

## Slide 28: Z parameters with different coupling-1cell （without 10ns constraint of detector）
 | Z-0.303% | Z-0.527% | Z-1% | Z-1.5% | Z-2%
Number of IPs | 2 |  |  |  | 
Energy (GeV) | 45.5 |  |  |  | 
Circumference (km) | 100 |  |  |  | 
SR loss/turn (GeV) | 0.034 |  |  |  | 
Half crossing angle (mrad) | 16.5 |  |  |  | 
Piwinski angle | 4.29 |  |  |  | 
Ne/bunch (1011) | 0.346 | 0.455 | 0.63 | 0.77 | 0.89
Bunch number | 73770 | 42700 | 22250 | 14810 | 11090
Beam current (mA) | 1226.7 | 933.7 | 673.7 | 549.5 | 475.4
SR power /beam (MW) | 42.3 | 32.2 | 23.2 | 18.95 | 16.4
Bending radius (km) | 11 |  |  |  | 
Momentum compaction (10-5) | 4.49 |  |  |  | 
IP x/y (m) | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002 | 0.16/0.002
Emittance x/y (nm) | 1.48/0.0045 | 1.48/0.0078 | 1.48/0.015 | 1.48/0.022 | 1.48/0.029
Transverse IP (um) | 15.4/0.095 | 15.4/0.125 | 15.4/0.172 | 15.4/0.21 | 15.4/0.243
x/y/IP | 0.006/0.054 | 0.008/0.054 | 0.011/0.054 | 0.014/0.054 | 0.016/0.54
RF Phase (degree) | 165.2 | 165.3 | 165.6 | 166.0 | 166.4
VRF (GV) | 0.13 | 0.14 | 0.14 | 0.14 | 0.15
f RF (MHz) (harmonic) | 650 (217800) |  |  |  | 
Nature z (mm) | 3.99 | 3.97 | 3.93 | 3.88 | 3.81
Total z (mm) | 4.0 |  |  |  | 
HOM power/cavity (kw) | 1.99(1cell) | 1.99(1cell) | 1.99(1cell) | 1.99(1cell) | 1.99(1cell)
Energy spread (%) | 0.037 |  |  |  | 
Energy acceptance by RF (%) | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
n | 0.09 | 0.12 | 0.17 | 0.2 | 0.23
F (hour glass) | 0.96 | 0.96 | 0.96 | 0.96 | 0.96
Lmax/IP (1034cm-2s-1) | 31.4 | 23.8 | 17.25 | 14.1 | 12.2

## Slide 29: Z luminosity vs. coupling

## Slide 30: Z luminosity vs. coupling
3ns
12ns
21ns
30ns
6ns