## Slide 1: parameters for CEPC double ring （wangdou20170426-100km_2mmy）
 | Pre-CDR | Higgs | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 
Energy (GeV) | 120 | 120 | 80 | 45.5 | 
Circumference (km) | 54 | 100 | 100 | 100 | 
SR loss/turn (GeV) | 3.1 | 1.67 | 0.33 | 0.034 | 
Half crossing angle (mrad) | 0 | 16.5 | 16.5 | 16.5 | 
Piwinski angle | 0 | 3.19 | 5.69 | 4.29 | 11.77
Ne/bunch (1011) | 3.79 | 0.968 | 0.365 | 0.455 | 0.307
Bunch number | 50 | 412 | 5534 | 21300 | 2770
Beam current (mA) | 16.6 | 19.2 | 97.1 | 465.8 | 408.7
SR power /beam (MW) | 51.7 | 32 | 32 | 16.1 | 1.4
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.14 | 1.14 | 4.49 | 1.14
IP x/y (m) | 0.8/0.0012 | 0.171/0.002 | 0.171 /0.002 | 0.16/0.002 | 0.171 /0.002
Emittance x/y (nm) | 6.12/0.018 | 1.31/0.004 | 0.57/0.0017 | 1.48/0.0078 | 0.18/0.0037
Transverse IP (um) | 69.97/0.15 | 15.0/0.089 | 9.9/0.059 | 15.4/0.125 | 5.6/0.086
x/y/IP | 0.118/0.083 | 0.013/0.083 | 0.0055/0.062 | 0.008/0.054 | 0.006/0.054
RF Phase (degree) | 153.0 | 128 | 126.9 | 165.3 | 136.2
VRF (GV) | 6.87 | 2.1 | 0.41 | 0.14 | 0.05
f RF (MHz) (harmonic) | 650 | 650 | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.72 | 3.37 | 3.97 | 3.83
Total z (mm) | 2.65 | 2.9 | 3.4 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.41(2cell) | 0.36(2cell) | 1.99(2cell) | 0.12(2cell)
Energy spread (%) | 0.13 | 0.098 | 0.065 | 0.037 | 
Energy acceptance (%) | 2 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.1 | 1.1 | 1.1 | 0.68
n | 0.23 | 0.26 | 0.15 | 0.12 | 0.22
Life time due to beamstrahlung_cal (minute) | 47 | 52 |  |  | 
F (hour glass) | 0.68 | 0.96 | 0.98 | 0.96 | 0.99
Lmax/IP (1034cm-2s-1) | 2.04 | 2.0 | 5.15 | 11.9 | 1.1

## Slide 2
We chose 2mm y* and 32MW SR power for CDR.
Higgs mode and W mode will use the same lattice.
Give a new column for Z which use same lattice as Higgs. (L=1.11034, coupling=2%, PSR=1.4MW)

## Slide 3: parameters for CEPC upgrade （wangdou20161219-100km_1mmy）
 | Pre-CDR | tt | H-high lumi. | H-low pow. | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 175 | 120 | 120 | 80 | 45.5 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 7.55 | 1.67 | 1.67 | 0.33 | 0.034 | 0.034
Half crossing angle (mrad) | 0 | 15 | 15 | 15 | 15 | 15 | 15
Piwinski angle | 0 | 1.6 | 2.5 | 2.5 | 3.57 | 5.69 | 5.69
Ne/bunch (1011) | 3.79 | 1.41 | 1.12 | 1.12 | 1.05 | 0.46 | 0.46
Bunch number | 50 | 98 | 555 | 211 | 1000 | 16666 | 65716
Beam current (mA) | 16.6 | 6.64 | 29.97 | 11.4 | 50.6 | 367.7 | 1449.7
SR power /beam (MW) | 51.7 | 50 | 50 | 19 | 16.7 | 12.7 | 50
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 0.96 | 0.96 | 3.1 | 3.3 | 3.3
IP x/y (m) | 0.8/0.0012 | 0.2/0.002 | 0.3/0.001 | 0.3 /0.001 | 0.1 /0.001 | 0.12/0.001 | 0.12/0.001
Emittance x/y (nm) | 6.12/0.018 | 3.19/0.0097 | 1.01/0.0031 | 1.01/0.0031 | 2.68/0.008 | 0.93/0.0049 | 0.93/0.0049
Transverse IP (um) | 69.97/0.15 | 25.3/0.14 | 17.4/0.055 | 17.4/0.055 | 16.4/0.09 | 10.5/0.07 | 10.5/0.07
x/y/IP | 0.118/0.083 | 0.016/0.055 | 0.029/0.083 | 0.029/0.083 | 0.0082/0.055 | 0.0075/0.054 | 0.0075/0.054
RF Phase (degree) | 153.0 | 122.2 | 123.3 | 123.3 | 149 | 160.8 | 160.8
VRF (GV) | 6.87 | 8.92 | 2.0 | 2.0 | 0.63 | 0.11 | 0.11
f RF (MHz) (harmonic) | 650 | 650 | 650 | 650 | 650 (217800) | 650 (217800) | 
Nature z (mm) | 2.14 | 2.62 | 2.72 | 2.72 | 3.8 | 3.93 | 3.93
Total z (mm) | 2.65 | 2.7 | 2.9 | 2.9 | 3.9 | 4.0 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.53(5cell) | 0.75(2cell) | 0.28(2cell) | 1.0 (2cell) | 1.6(1cell) | 6.25(1cell)
Energy spread (%) | 0.13 | 0.14 | 0.098 | 0.098 | 0.065 | 0.037 | 0.037
Energy acceptance (%) | 2 | 2 | 1.5 | 1.5 |  |  | 
Energy acceptance by RF (%) | 6 | 2.6 | 1.8 | 1.8 | 1.5 | 1.1 | 1.1
n | 0.23 | 0.23 | 0.26 | 0.26 | 0.26 | 0.18 | 0.18
Life time due to beamstrahlung_cal (minute) | 47 | 50 | 52 | 52 |  |  | 
F (hour glass) | 0.68 | 0.89 | 0.83 | 0.83 | 0.84 | 0.91 | 0.91
Lmax/IP (1034cm-2s-1) | 2.04 | 0.62 | 5.42 | 2.06 | 4.08 | 18.0 | 70.97