## Slide 1: Update of lattice design for CEPC main ring
Yiwei Wang, Feng Su, Sha Bai, Yuan Zhang, Dou Wang,
Huiping Geng, Chenghui Yu, Jie Gao
IHEP, CAS
CEPC AP meeting, 19 May 2017

## Slide 2
Introduction
The geometry of CEPC is compatible for the SPPC.
With new parameter list (20170306-100km_2mmy)
With new IR parameters L*=2.2m, c=33mrad, GQD0=150T/m
  to lower the requirements of anti-solenoid and QD0 field
  Bsol=6.6T, BQD0=3.3T which are realizable
Compatible lattices for H, W and Z modes
  geometry, *, emittance
  common cavities for H, W and Z modes, bunches filled in full ring for
  W&Z modes

## Slide 3: Parameters for CEPC double ring
 | Pre-CDR | tt | Higgs | W | Z
Number of IPs | 2 | 2 | 2 | 2 | 2
Energy (GeV) | 120 | 175 | 120 | 80 | 45.5
Circumference (km) | 54 | 100 | 100 | 100 | 100
SR loss/turn (GeV) | 3.1 | 7.55 | 1.67 | 0.33 | 0.034
Half crossing angle (mrad) | 0 | 16.5 | 16.5 | 16.5 | 16.5
Piwinski angle | 0 | 1.6 | 3.19 | 5.69 | 4.29
Ne/bunch (1011) | 3.79 | 1.41 | 0.968 | 0.365 | 0.455
Bunch number | 50 | 98 | 644 (412) | 5534 | 21300
Beam current (mA) | 16.6 | 6.64 | 29.97 (19.2) | 97.1 | 465.8
SR power /beam (MW) | 51.7 | 50 | 50 (32) | 32 | 16.1
Bending radius (km) | 6.1 | 11 | 11 | 11 | 11
Momentum compaction (10-5) | 3.4 | 1.3 | 1.14 | 1.14 | 4.49
IP x/y (m) | 0.8/0.0012 | 0.2/0.002 | 0.171/0.002 | 0.171 /0.002 | 0.16/0.002
Emittance x/y (nm) | 6.12/0.018 | 3.19/0.0097 | 1.31/0.004 | 0.57/0.0017 | 1.48/0.0078
Transverse IP (um) | 69.97/0.15 | 25.3/0.14 | 15.0/0.089 | 9.9/0.059 | 15.4/0.125
x/y/IP | 0.118/0.083 | 0.016/0.055 | 0.013/0.083 | 0.0055/0.062 | 0.008/0.054
RF Phase (degree) | 153.0 | 122.2 | 128 | 126.9 | 165.3
VRF (GV) | 6.87 | 8.92 | 2.1 | 0.41 | 0.14
f RF (MHz) (harmonic) | 650 | 650 | 650 | 650 (217800) | 650 (217800)
Nature z (mm) | 2.14 | 2.62 | 2.72 | 3.37 | 3.97
Total z (mm) | 2.65 | 2.7 | 2.9 | 3.4 | 4.0
HOM power/cavity (kw) | 3.6 (5cell) | 0.53(5cell) | 0.64(2cell) (0.41) | 0.36(2cell) | 1.99(2cell)
Energy spread (%) | 0.13 | 0.14 | 0.098 | 0.065 | 0.037
Energy acceptance (%) | 2 | 2 | 1.5 |  | 
Energy acceptance by RF (%) | 6 | 2.6 | 2.1 | 1.1 | 1.1
n | 0.23 | 0.23 | 0.26 | 0.15 | 0.12
Life time due to beamstrahlung_cal (minute) | 47 | 50 | 52 |  | 
F (hour glass) | 0.68 | 0.89 | 0.96 | 0.98 | 0.96
Lmax/IP (1034cm-2s-1) | 2.04 | 0.62 | 3.13 (2.0) | 5.15 | 11.9
(20170306-100km_2mmy, D. Wang)

## Slide 4
Lattice design for interaction region
Provide local chromaticity correction
L*=2.2m, c=33mrad, GQD0=150T/m
Reverse bending direction of last bends to avoid synchrotron radiation hitting IP
IR of IP upstream: Ec < 100 keV within 400m, last bend Ec < 60 keV
IR of IP downstream: Ec < 300 keV within 250m, last bend Ec < 120 keV
L*= 2.2m
x*= 0.171mm
y*= 2mm
GQD0-150T/m
GQF1100T/m
LQD0=1.73m
LQF1=1.48m
Notes: New IR bends

## Slide 5: Lattice design for ARC region
FODO cell, 90/90, non-interleaved sextupole scheme
  period N=5cells
  all 3rd and 4th resonance driving terms (RDT) due to sextupoles cancelled, except small 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy
  tune shift dQ(Jx, Jy) is very small
    DA on momentum: large
  Chromaticity dQ() need to be corrected with many families
    DA off momentum: with many families to correct dQ() and –I break down
-I
-I
Bin=12320 m
Bout=12321 m
Notes: Should be 5 cells

## Slide 6: FODO cell for cryo-module
336 / 6 / 2RF stations / 2 sections / 2= 7 cells in each section
get a smallest average beta function to reduce the multi-bunch instability caused by RF cavities
  90/90 degree phase advance
  as short as possible distance between quadrupoles, but should be larger than a module length (12m)
90/90 deg
Half cell: 14m+2m
max: 53.8 m
min: 9.5 m
cryo-module
quadrupole

## Slide 7: Lattice design of RF region
Common RF cavities for e- and e+ ring (Higgs)
An electrostatic separator combined with a dipole magnet to avoid bending of incoming beam (ref: Oide, ICHEP16)
RF region divided into two sections for bypassing half numbers of cavities in Z mode
Deviation of outgoing beam is x=1.0 m for bypassing the cryo-modules
common RF cavities
combined magnet
Esep=1.8 MV/m
Lsep=50m
Ldrift=75m
x=10cm at entrance of quad

## Slide 8
Lattice design for whole ring
  A lattice fulfilling requirements of the parameters list, geometry, photon background and key hardware

## Slide 9: Magnets
ARC
  Sextupole: 56*4*4=896, 0.4 m
  Quadrupole: 56*4*5*2+2*8*2=2272, 2 m
  Dipole: 56*4*5*2+2*8*2=2272, 34 m in half of cell
IR
  Sextupole : (6 to 12) *4=24 to 48, 0.3 m

## Slide 10: Re-design of the ARC region
Fit the circumference of ring C=100 km
  Lringr
  = (Ncell+6+2)*Lcell*8 + Nstr1*Lcell*4 + Lstr2*4+Pi*1m
  = 99996.8 + 3.14 m
Fix the problem of residual dispersion due to half bend scheme of dispersion suppressor

## Slide 11: Dispersion suppressor
Half bend scheme
  Simple but destroy the geometry (2, 2 )
Full bend scheme
  Keep geometry
  2 cells w/ bend, 3 cells w/ bend+1 cell, 4 cells w/ bend, 3 cells w/ bend
    3 cells w/ bend for  matching in Z mode

## Slide 12: RINGQI

## Slide 13: Parameters of ARC region (rough)