## Slide 1: AGS Dynamic Aperture Issue with Partial Siberian Snake Inserted
Nov. 2, 2017
ICFA-DA2017, Beijing
H. Huang, F. Meot, N. Tsoupas

## Slide 2: AGS as Polarized Proton Injector for RHIC
Partial Siberian Snake helical dipole magnets are needed for intermediate energy synchrotrons to preserve polarization of polarized proton beams. Such strong magnets are not easily rampable for fast synchrotron. So the strong field at injection causes inevitably shrinking of dynamic aperture. The quadrupoles are inserted to compensate the optical distortion due to the strong helical dipole fields.
The AGS used to be a high intensity synchrotron: 1.2E13 ppb. The energy range is 1.5GeV to 25GeV.
AGS dipole magnets are combined function and the natural tune is about 8.7 in both plane. The beam pipe size is 3inch(V) by 7inch(H).
In the high intensity operation period, beam pipe is filled at injection due to space charge. For polarized proton beam operation, the AGS serves as the injector to RHIC, and the required intensity is 2E11 at RHIC top energy.
For polarization preservation, a pair of partial snake magnets(helical dipole magnets) are inserted in the AGS: 2.1T and 1.5T. For the injection, this caused huge optical distortion and the dynamic aperture is greatly reduced.
Without any compensation, the intensity was down to 0.6E11ppb.

## Slide 3: AGS as Polarized Proton Injector for RHIC (2)
AGS has been running as RHIC polarized proton injector with dual partial snakes and two horizontal tune jump quads. It has delivered ~70% polarization with ~2*1011/bunch intensity with 80% as input polarization.
[1] H. Huang, et al., Phys. Rev. Lett .99, 154801(2007).
[2] F. Lin, et al., Phys. Rev. ST AB 10, 044001 (2007).
[3] H. Huang, et al., Phys. Rev. ST AB 17, 081001 (2014).
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
AGS Polarimeter
Cold Helical Partial Snake
Warm Helical Partial Snake
To RHIC Injection
Gg= 4.5 … 45.5
Gg= 2.2... 4.5
Jump quads in adjacent super-periods I &J
For proton, G=1.7982
Notes: Show layout & point of polarimeters and experimental locations
  Emphasize bunch polarizations prepared at source going through AGS etc. to RHIC
  Time spacing between them ~100 ns
  Transverse polarization in ring, longitudinal at experiments (optional) using spin rotators
  Emphasize none of these techniques existed just 4-5 years ago, all developed here at RHIC with international collaborations led by US and Japanese teams.

## Slide 4: Tune Measurement on Ramp
(Jeff Wood)
36+y
37+y
35+y
48-y
24+y
36-y
12+y
0+y
1+y
-1+y
8.98
For polarization preservation, the vertical tune needs to stay about 8.98, or as high as 8.99.

## Slide 5: AGS Partial Snakes
The two-snake solution provides better spin match at injection and extraction.
A20
E20

## Slide 6: 2-3T AGS Super-Conducting Helical Snake
2.6 m
15 cm warm bore Helix with changing pitch

## Slide 7: AGS Parameters

## Slide 8: Intensity with Limited Compensation: 6E10
To compensate the large optical distortion from helical magnets, a pair of thin quads were added next to the cold snake. But this is not enough: still huge beam loss near injection.
Main magnet
Intensity

## Slide 9
Compensation Quads Setting vs. Beam Energy
Notes: K = quad strength (B’/B

## Slide 21: AGS Injection Lattice (2 Quads)

## Slide 22: AGS Injection Lattice(4 Quads)

## Slide 23: AGS Injection Lattice (CSNK only, 4 Quads)

## Slide 24: AGS Dynamic Aperture w/o Snakes
Ray-tracing code ZGOUBI is used to calculate the dynamic aperture. The dynamic aperture of the ring for δp/p = 0, ± 1, ±2, ±3%. These (x, y) limits are obtained by scanning the x-axis, step size 3 cm, and looking, at each x-step, for the maximum vertical stable amplitude upon 1000-turn tracking, with 2 mm precision on that y-limit.

## Slide 25: AGS Dynamic Aperture with Snakes
[1]Spin dynamics simulations at the AGS, H. Huang, W. W. MacKay, F. Meot, T. Roser, Proc. IPAC 2010, Kyoto.
[2] Modeling of the AGS using Zgoubi - status, F. Meot et al., Proc. IPAC 2011, San Sebastian.
[3] Development of a stepwise ray-tracing based, on-line model of the AGS, F. Meot et al., Proc. PAC 2011, New York.
[4] Modeling of the AGS using Zgoubi - status, F. Meot et al., Procs PAC 2012, New Orleans.

## Slide 26: Summary
AGS polarized proton operation requires two helical dipole magnets (partial Siberian Snakes). These two magnets caused significant optical distortion near injection.
Two compensation quads at the stronger dipole magnet is not enough to restore the lattice.
Four thin quads were added to both helical dipole magnets. The beta beat was greatly reduced in this case, and the vertical aperture is improved enough to get required intensity (more than doubled in the first test: 0.6E11-> 2.2E11).
Over years, various improvement has increased the bunch intensity to 3E11, which is critical for RHIC high intensity operation (2.5E11) in the e-lens operation mode.

## Slide 27: Backup Slides

## Slide 28: Spin Dynamics
Spin tune is given by
coss=cos (/2) cos G
 =0.05 in AGS, s can not be an integer, avoided all imperfection resonances;
 = in RHIC, s =1/2, avoided all imperfection and intrinsic resonances.
Polarization after passing an isolated resonance with strength  and passing speed  =Gd/d is given by Froissart-Stora Formula
Pf/Pi=2exp[-||2/(2)]-1
||2/(2)<<1, Pf/Pi1;
||2/(2)>>1, Pf/Pi-1.