## Slide 1: Effects of detector solenoid & magnet imperfections on dynamic aperture of JLEIC ion collider ring
Vasiliy Morozov, Fanglei Lin, Guohui Wei, Yuhong Zhang (Jefferson Lab)
Yunhai Cai, Yuri Nosochkov (SLAC)
ICFA Mini-Workshop on Dynamic Apertures of Circular Accelerators
Institute of High Energy Physics, Beijing, China
November 1, 2017
Notes: F. Lin
1

## Slide 2: Outline
JLEIC overview
Chromaticity compensation
Dynamic aperture
Alignment and field errors
Multipoles
Detector solenoid

## Slide 3: JLEIC Layout
3-12 GeV
8-100(400) GeV
8 GeV
2015
arXiv:1504.07961
Electron complex
  CEBAF
  Electron collider ring
Ion complex
  Ion source
  SRF linac (285 MeV/u for protons)
  Booster
  Ion collider ring
Optimum detector location for minimizing background
May 17 update:
https://eic.jlab.org/wiki/index.php/Main_Page
SRF Linac &

## Slide 4: Key Design Concepts
High luminosity: high collision rate of short modest-charge low-emittance bunches
  Small beam size
    Small β*  Short bunch length  Low bunch charge, high repetition rate
    Small emittance  Cooling
  Similar to lepton colliders such as KEK-B with L > 21034 cm-2s-1
High polarization: figure-8 ring design
  Net spin precession zero
  Spin easily controlled by small magnetic fields for any particle species
Full acceptance primary detector including far-forward acceptance
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Crab crossing
Damping
Synchrotron radiation
Electron cooling

## Slide 5: JLEIC Energy Reach and Luminosity
CM Energy (in each scenario) | Main luminosity limitation
low | space charge
medium | beam-beam
high | synchrotron radiation

## Slide 6: JLEIC Parameters (3T option)
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80% | 80% | 80% | 80% | 80% | 75%
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emittance, hor / ver | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1.0 | 10.5/2.1 | 4/0.8
Ver. beam-beam parameter |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 | 

## Slide 7: Ion Collider Ring Layout
Protons: 100 GeV/u (63 GeV/u in COM with 10 GeV e) Lead: 40 GeV/u (40 GeV/u in COM with 10 GeV e)
Super-ferric magnets (cos under consideration as risk mitigation)
R = 155.5 m
Arc, 261.7
IP
disp. supp./
geom. match #3
disp. supp./
geom. match #1
disp. supp./
geom. match #2
disp. supp./
geom. match #3
det. elem.
disp. supp.
norm.+
SRF
tune
tromb.+
match
beam exp./
match
elec. cool.
ions
81.7
future 2nd IP
Polarimeter

## Slide 8: Chromaticity Compensation Schemes
Large bh at CCB sextupoles for reasonable sextupole strength
Large bx/by (or by/bx) ratio at X (Y) sextupoles for orthogonal X & Y correction
Compensation of sextupole non-linear geometric effects
Linear chromaticity correction  Conventional two family interleaved sextupoles in periodic arc cells. Number of cells with sextupoles is chosen to make the total phase advance of 2p*integer for compensation of the sextupoles non-linear effects.
Linear-x sext
FF sext
Arc cells
CCB with two non-interleaved –I pairs of sextupoles with high b at the sextupoles.
Good chromatic correction, cancellation of sextupole geometric effects.
Preferred scheme
Distributed interleaved –I sextupole pairs with small to moderate b.
Less efficient correction, residual amplitude-dependent tune shift due to pairs overlap.

## Slide 9: Chromaticity Compensation
CCB is based on regular 90 degree FODO arc cells with increased b at –I sextupole pairs
p/2+np phase advance between CCB sextupoles and IP
12 x 90 degree cells in each arc for linear chromaticity sextupoles
W-function at IP is cancelled for minimum variation of b*(d)
Adequate chromatic compensation over 10sp range
IP

## Slide 10: DA & Momentum Acceptance
DA without errors (shown at IP)
Elegant tracking
Tune = 24.22, 23.16 selected based on optimal chromatic correction
On-energy DA ≈90s
Large energy range of at least ±0.5%
6
Qx,y = 24.22 / 23.16
Qx,y = 24.22 / 23.16
Q(d)
b*(d)
±10s

## Slide 11: Tune Scan
DA without errors is scanned vs tune
Elegant tracking
Good on-energy DA at tune of 24.10, 23.14
However, energy range is reduced
13
24.22, 23.16
24.10, 23.14
Horiz. DA
Vert. DA
DA at 45 deg

## Slide 12: Alignment & Field Errors
Thread the beam through, find closed orbit and minimize distortion using BPMs and correctors
 | Dipole | Quadrupole | Sextupole | BPM (noise) | Corrector
X (mm) | 0.3 | 0.3, FFQ 0.03 | 0.3 | 0.05 | -
Y (mm) | 0.3 | 0.3, FFQ 0.03 | 0.3 | 0.05 | -
Roll (mrad) | 0.3 | 0.3, FFQ 0.05 | 0.3 | - | 0.3
Z (mm) | 0.3 | 0.3, FFQ 0.03 | 0.3 | - | -
Field (%) | 0.1 | 0.2, FFQ 0.03 | 0.2 | - | 0.01
< 410-4
< 110-4
510-6
510-6

## Slide 13: DA with Errors
Corrections: orbit, tune, chromaticity, coupling, beta beat
10 seeds of random errors using Elegant
No errors
With errors and corr.

## Slide 14: Dipole Multipoles
Systematic multipoles of super-ferric arc dipoles
When applied to all dipoles in the ring
Multipole errors of super-ferric dipole at radius 20 mm (unit: 10^-4) |  |  |  |  |  |  |  |  |  | 
multipole type |  |  |  |  |  |  |  |  |  | 
systematic | -0.151 | -0.537 | 0.126 | 0.850 | 0.714 | 0.366 | -0.464 | -0.410 | 0.009 | 0.027
Random |  |  |  |  |  |  |  |  |  | 
Without multipoles
With multipoles
Δp/p = 0
Δp/p = 0.3%
Δp/p = 0.3%

## Slide 15: Dipole Multipoles
Different categories of magnets
Different specifications for different categories
 | D | Q | S
ALL | 133 | 205 | 75
IR area, β > 1 km | 2 | 6 | 0
β > 200 m | 21 | 19 | 8
only  < 1 km
> (20) in x & y
only  < 200 m
~ (50) in x & y

## Slide 16: FFQ Multipoles
Using LHC FFQ multipole data

## Slide 17: FFQ Multipoles
Dynamic aperture is scanned versus systematic bn and an non-linear field terms in FF quads (one term at a time)
bn, an “tolerances” are determined based on DA of 20s (corresponding to one term at a time)
DA with “tolerance” settings of all bn, an terms is 10s
Performed for different emittance settings
Tolerances are comparable to or looser than LHC MQXB magnet data
DA = 10s
DA with FFQ non-linear field “tolerances”

## Slide 18: Detector Solenoid Effects
Effects | e ring | ion ring
Coherent orbit distortion | N | Y
Coupling | Y | Y
Rotates crabbed beam planes at IP | Y | Y
Generates vertical dispersion | N | Y
Linear and non-linear optics perturbation | Y | Y
Violation of figure-8 spin symmetry | Y | Y
JLEIC Detector solenoid | 
Length | 4 m (1.6 m-IP-2.4 m)
Strength | < 3 T
Crossing Angle | 50 mrad
Ion
e

## Slide 19
Solenoid Integration Scheme
: Skew Quadrupole
Two dipole correctors on each side of IP for closed orbit correction
Anti-solenoid & 4 small skew quads on each side of IP for decoupling
Notes: 19

## Slide 20: Closed Orbit Correction
Two x/y dipole correctors on each side of IP correct not only x/y beam offsets at IP but orbit x/y slopes as well

## Slide 21: Coupling Compensation
Before compensation
Skew quads produce effect equivalent to FFQ rotation needed to compensate the detector solenoid by an anti-solenoid
Coupling is not only compensated locally in IR but locally at IP as well
After compensation

## Slide 22: Optics Rematch
Additional solenoid focusing is compensated locally leaving the rest of the optics unchanged
Vertical dispersion is not yet compensated by it is small, <0.2 m
x = 12.5
y = 7.5
x = 8.5
y = 5.5

## Slide 23: Dynamic Aperture
After solenoid compensation, DA shrinks to ~50 but is still acceptable
Red: no solenoid
Black: with solenoid

## Slide 24: Summary
Non-linear dynamics optimization of JLEIC ion collider ring is complete
Misalignment and strength error effects studied, error tolerances specified, correction scheme implemented
FFQ multipole tolerances studied and specified
Detector solenoid integrated into the lattice and its effects compensated