## Slide 1: DA Studies in HEPS
Jiao, Yi
Institute of High Energy Physics, CAS, Beijing, China
2017-11-03

## Slide 2: Outline
1
Brief Introduction of the HEPS
2
Recent HEPS DA Optimization
3
A Few DA Optimization Experiences
4
Conclusion

## Slide 3
Brief Introduction of the HEPS
HEPS: High Energy Photon Source
The aim is to realize ultralow emittance (e.g., approaching 10 pm) and high-brightness ring light source
Almost 10 years’ evolution of the HEPS design
Layout: Linac + Booster + Ring

## Slide 4: Trend of ring light source
Lower emittances (  0.1 nmrad)
Higher brilliances (↗2~3 orders)
More advanced beam lines and end-stations (Better resolutions, higher speeds, etc.)
SR-based research centers
Sirius,Brazil, 518 m, 3 GeV, 0.27 nm
MAX-IV, Sweden, 528 m, 3 GeV, 0.2-0.4 nm
ESRF-EBS, France, 844 m, 6 GeV, 0.13 nm

## Slide 5
Low emittance
Reasonable budget
Strong focusing
Small circumference
Compact MBA
Compact magnets
Small aperture magnets
Small aperture vacuum chamber
NEG-coating
Distributed bumping
Large natural chromaticity
Strong sextupoles
Low dispersion
stronger collective effects
Expected Ring performance
Limited beam current
Strong nonlinearities
Bad beam dynamics (e.g., DA, MA, etc.)
higher dispersion
Hybrid MBA design
Even strong focusing
Not a full list …
Short lifetime or low inj. efficiency
To reach high brightness (ultralow emittance) and to simultaneously obtain large ring acceptance are both important & challenging …
[1] see, e.g., R. Hettel, J. Synchrotron Radiat. 21, 843-855 (2014).
[2] ESRF-EBS: Farvacque L, et al., In: Proc. of IPAC2013. Shanghai: 2013. 79-81

## Slide 6: HEPS: The Next Ring Light Source in China
HEPS
BSRF
HLS
SSRF
A new photon science research center at the north of China
Preliminary studies started on 2008
The HEPS-test facility (TF) project (2016-2018)
R&D on the accelerator and beam line techniques for a DLSR.
HEPS Project (from 2018?)
  Selected in the 13th 5-year plan (2016-2021) of the National Development and Reform Commission of China
Finish conceptual design report and the feasibility study report
About 80 km from the IHEP
IHEP
HEPS
Notes: In the research area, today’s most used and successful photon source is the storage ring based synchrotron radiation light source.
Till now, there are more than 50 facilities, and the light sources has evolved with three generations.
In china mainland, there are three ring based light sources, there are in Beijing, Hefei, and Shanghai.

## Slide 7: HEPS Design Evolution (2008-)
Lattice Structure | Time | Brief Description
DBA | 2008-2012 | 48*DBA, 1200 m, 1.5 nm.rad w/o DW, 0.5 nm.rad w/DW [1]
Nominal 7BA | 2012-2013 | 36*7BA, 1370 m, 51 pm.rad, 10 pm w/DW & local round beam production [2]
TBA | 2014 | 60*TBA, 1280 m, 0.46 nm.rad, 0.15 nm.rad w/ID & DW [3]
Nominal 7BA w/ H.G. quadrupole | 2014-2015 | 44*7BA, 1294 m, 90 pm.rad @ 6 GeV (62 pm.rad @ 5 GeV) [4]
Hybrid 7BA | 2015- | 40*7BA, 1295 m, 60 pm.rad @ 6 GeV (42 pm.rad @ 5 GeV) [5,6,7]
7BA with novel layout | 2016- | 1360.4 m, as low as possible emittance, & as large as possible DA, underway [8]
  [1] X.M. Jiang et al., internal report, 2012 (in Chinese).
  [2] G. Xu, Y. Jiao, Chin. Phys. C, 37(5), 057003 (2013).
  [3] G. Xu, Y. Peng, Chin. Phys. C, 2015, 39(3): 037005.
  [4] Y. Jiao, G. Xu, Chin. Phys. C, 39(6), 067004 (2015).
  [5] G. Xu, Y. Jiao, Y. Peng, Chin. Phys. C, 40(2): 027001 (2016).
  [6] Y. Jiao, Chin. Phys. C, 40(7): 077002 (2016).
  [7] Y. Jiao, G. Xu, Chin. Phys. C, 41(2): 027001 (2017).
  [8] Work to be submitted.
Pioneer or on-phase studies: MAX-IV, Sirius, PEP-X, ESRF-EBS, SPring8-II, APS-U, ALS-U, etc.

## Slide 8: Schematic view of HEPS
Booster:
300 MeV to 6 GeV
Rep. rate: 1 Hz
FODO structure
Emittance: ~40 nm
max. bunch charge: ~2 nC
Storage Ring:
6 GeV, 48*7BAs
Circumference: 1360.4 m
Natural emittance: 30-60 pm
Beam current: 200 mA
Mainly consider Swap-out injection, and if possible, compatible with longitudinal and/or off-axis injection
For high-charge operation mode, the beam extracted from the ring is merged with the bunch from the Linac and re-injected to the ring

## Slide 9
Recent HEPS Designs with Optimized DA
HEPS-TF (HEPS-test facility) baseline, hybrid-7BA design. Small DA, just enough for on-axis swap-out injection
With the same layout, brightness can be 30% higher, or DA area can be three times larger (w/ the similar brightness or emittance)
With improved 7BA design, brightness can be 30% even higher, and DA can be kept the same (if not larger)

## Slide 10: Baseline for the HEPS-TF
This type of lattice is able to create dispersion bumps which facilitate compensation for very large natural chromaticities, it also adopts aggressively strong focusing which results in a compact layout as well as an ultralow emittance. These features allow practical and cost effective storage ring designs, even when the natural emittance is reduced down to approaching the diffraction limit of hard X-rays.
First used in ESRF-EBS, and now adopted in the design of APS-U, HEPS, ALS-II, etc.
6 GeV, ~1.3 km, 60 pm

## Slide 11: Very Difficult DA Optimization
y (mm)
x (mm)
ux
uy
x (mm)
d
Still hard to get large DA even with:
Local cancellation
 Approximately -I transportation between each sextupole pair (interleaved)
Global cancellation
 Quasi-4th order geometric achromat (the whole ring, tune close to [113, 41])
Optimization of tunes, sextupole/octupole strengths (grid scan)
 ‘Effective’ on-momentum DA (x/y): ~2.5/3.5 mm, ~100/250 sx/y; effective MA: ~3%.
‘Effective’ DA/MA: DA bounded by nearest integer and half-integer resonances.
(Y. Jiao, et al., IPAC17-WEPAB055)
Injection with high efficiency:
On-axis swap-out injection
On-axis longitudinal accumulation
Off-axis injection & accumulation

## Slide 12: Global Optimization of Hybrid-7BA
All tenable parameters scanned & linear and nonlinear dynamics simultaneously optimized
G. Xu, et al., IPAC2017, WEPAB052
If keeping 60 pm emittance, the DA can be increased to be close to (if not larger than) 8 mm in x plane.
If considering only on-axis swap-out injection scheme, the emittance can be further pushed down to ~45 pm.rad
Color bar: Effect. DA area×MA/3% (mm2)

## Slide 13: Even Possible for off-axis injection at 60 pm
w/o high-b section, effective DA (x/y): 8/3.3 mm, ~350/200 sx/y, effective MA size > 3.5%
Very good, but can be even better!
Courtesy of M. Borland
30-35 pm w/ Antibend & Superbend
Recent work, unpublished.

## Slide 14: Higher Brightness & Large DA w/ new 7BA Design
Objective(2): - weighted DA area = DA(x)*DA(y)*MA/3%*weight functions
Solutions for Hybrid-7BA
Emittance: 40~60 pm
DA(x/y): up to ~300 sx/y
Solutions for new 7BA designs
Emittance: 30~40 pm
DA(x/y): up to ~250/400 sx/y
Optimization study is underway

## Slide 15
A Few DA Optimization Experiences
Dependence relations between DA and the related parameters are very complex
Global optimization is essentially required with stochastic optimization algorithms
Ways of avoiding local optima …

## Slide 16: Smaller Driving Terms  Good Nonlinear performance?
Not definitely true.
X. Huang, J. Safranek, Online optimization of storage ring nonlinear beam dynamics, PRAB, 18, 084001 (2015)
L. Yang, Y. Li, W. Guo, S. Krinsky, Multiobjective optimization of dynamic aperture, PRST-AB 14, 054001 (2011)
Similar experience in HEPS
Objectives: Analytically derived detuning, chromatic, and resonance driving terms
  G. Xu, Y. Jiao, Chin. Phys. C, 37(5), 057003 (2013).
  Y. Jiao, G. Xu, Chin. Phys. C, 39(6), 067004 (2015).

## Slide 17: Global Cancellation  Good Nonlinear performance?
It appears not definitely.
HEPS Hybrid-7BA baseline
Closed to the 4th order geometric achromat condition (Tunes: 113.20/41.28)
Effective DA (x/y): 2.5/2 mm
Effective MA: 2.4%
Optimization tuning quadrupole & multipole strengths
Away from the 4th order geometric achromat condition (Tunes: 116.16, 41.12)
Effective DA (x/y): 2.5/3.5 mm
Effective MA: 3.0%
Additionally, the MA size is highly dependent on choice of the fractional tune.
  G. Xu, Y. Jiao, Y. Peng, Chin. Phys. C, 40(2): 027001 (2016).
  Y. Jiao, Chin. Phys. C, 40(7): 077002 (2016).

## Slide 18: Weaker focusing & sextupoles  Good Nonlinear performance?
It appears not definitely.
HEPS Hybrid-7BA baseline,
Except quadrupoles, sextupoles, and octupoles, drft lengths also changed.
Solutions with weakest possible sextupoles
Max. DA area: ~2.5 mm2 at ~60 pm
Solutions with largest possible acceptance
Max. DA area: ~4.5 mm2
  Y. Jiao, G. Xu, Chin. Phys. C, 41(2): 027001 (2017).

## Slide 19: Local Cancellation  Good Nonlinear performance?
It appears not definitely.
HEPS Hybrid-7BA,
Global scan of all tunable parameters
Keeping condition of –I transportation between sextupole pairs first
But then release this condition in the last iterations of optimization
Color bar: Effect. DA area×MA/3% (mm2)
The horizontal phase advance is not exactly on the –I transportation condition.
The vertical phase advance is away from the –I transportation condition.
Recent work, unpublished.

## Slide 20: Global Optimization w/ Stochastic Algorithms
Test MOGA (NSGA-II) and PSO performance in an optimization problem with a known answer.
Fix the lattice structure and circumference, shortening the long straight section results in lower emittance and better dynamics?
Yes. (more room for variation of magnetic parameters).
PSO solutions with variable Lss
MOGA solutions with variable Lss
MOGA solutions with fixed Lss
PSO solutions with variable Lss
MOGA solutions with variable Lss
MOGA solutions with fixed Lss
Evolve with PSO for 800 generations as well
Further Evolve with PSO and MOGA for 500 more generations
A rational combination of the PSO and MOGA is more effective than either of them alone, in approaching the true global optima of an explorative multi-objective problem with many optimizing variables and local optima.
  Y. Jiao, G. Xu, Chin. Phys. C, 41(2): 027001 (2017).
PSO breeds more diversity. And once with enough diversity, MOGA reach better convergence.
Such a way helps a lot in HEPS optimization.

## Slide 21: In Closing …
To design a ring light source with high brightness and robust nonlinear dynamics is a challenging but also an exciting work
After 10 years’ evolution, for HEPS, we can achieve emittance of 30~60 pm, and at the same time, ensure large enough ring acceptance
The DA optimization work is and will always be underway, even after the beginning of the HEPS project construction.

## Slide 22
Thanks:
A. Chao, Y. Cai, X. Huang (SLAC), M. Borland (APS), S.Y. Lee (Indiana U.), L. Yu, Y. Li (BNL), S. Liuzzo, N. Boaz (ESRF), S. Tian, B. Jiang (SSRF), Z. Bai (HLS), etc. for their enthusiastic help, discussions and guidance for the HEPS design.
Thanks for your attention!