## Slide 1: IHEP PAPS SRF facility layout design
Feisi He
On behalf of colleagues in IHEP SRF group
Institute of High Energy Physics (IHEP)

## Slide 2: Outline
Background
  Brief introduction to the PAPS project
  Future project that may need PAPS
The SRF facility
  Layout and workflow
  Labs for R&D purpose
  Cryogenic system
  Public service facilities

## Slide 3: PAPS project overview
“Platform of Advanced Photon Source Technology R&D”, to provide infrastructure for construction of future project.
Budget: 500M CNY funded by Beijing Gov.
Construction: 2017.5-2020.6
Consist of 7 systems:
  RF system
  Cryogenic system
  Magnet technology
  Beam test
  X-ray optics
  X-ray detection
  X-ray application

## Slide 4: PAPS-RF system
The PAPS-RF system has two targets :
  Build a SRF facility
  Conduct R&D on cavities and ancillaries
The SRF facility is biased on mass production for SRF projects
  Post-processing, clean assembly, VT/HT/conditioning of cavities, couplers, and cryomodules.
  Compatible of 166MHz, 325MHz, 500MHz, 650MHz, and 1.3GHz
  200-400 cavities (couplers) per year
  ~20 cryomodules per year
  Support R&D on new material
  and new technology
  Total area of 4500 m2
Cryogenic system:
300W @ 2K
PAPS-RF
Testing
Clean assembly
Cavity VT
Labs
Cavity HT
CM conditioning
Coupler conditioning
Post processing
Microwave & LLRF
SC materials
Cavity R&D

## Slide 5: Outline
Background
  Brief introduction to the PAPS project
  Future project that may need PAPS
The SRF facility
  Layout and workflow
  Labs for R&D purpose
  Cryogenic system
  Public service facilities

## Slide 6: Future project: HEPS
High Energy Photon Source will be built in Beijing by IHEP from 2018 to 2024
Budget: 4.8B CNY

## Slide 7: Future project: HEPS (2)
Solid-state amplifier: 166MHz, 200kW
500MHz, 75kW
Klystron: 500MHz, 250kW

## Slide 8: Future project: CIADS
Approved by Chinese government in Dec. 2015
Budget: >1.8B CNY
Proton CW linac > 250MeV
In collaboration of IMP, IHEP, and many other institutes

## Slide 9: Future project: CIADS (2)
Current optics design:
  HWR009
  HWR019
  56 of Double spoke β0=0.42

## Slide 10: Future project: Shanghai-XFEL
Approved with 10B CNY, to be built in 7 years
Dominated by Shanghai-Tech University and Sinap at Shanghai
8GeV CW Linac, with ~700 of 1.3GHz TESLA cavities
8 cavities in one cryomodule

## Slide 11: Future project: CEPC
Proposed by IHEP, pre-research in progress
Circular electron-positron collider at 2 x 120GeV
e+e- Higgs (Z) factory for precision measurement of the Higgs boson (and the Z boson)
  Ecm~240GeV, luminosity ~2×1034 cm-2s-1, two detectors, 1M ZH events in 10yrs

## Slide 12: Future project: CEPC (2)
~600 of SRF 2-cell elliptical cavities at 650MHz needed. 2 or 6 cavities in one cryomodule.
5-cell cavities at 650MHz are possible according to optics design
Operation specification: Q0>2e10@Eacc=16MV/m
VT specification: Q0>4e10@Eacc=22MV/m

## Slide 13: Outline
Background
  Brief introduction to the PAPS project
  Future project that may need PAPS
The SRF facility
  Layout and workflow
  Labs for R&D purpose
  Cryogenic system
  Public service facilities

## Slide 14: Layout of the SRF facility
3 VT dewars
2 HT caves
500m2 CR
FPC aging in CR ISO7
Optic inspec.
Pre-tuning
Furnace
Nb3Sn oven
Nb-Cu sputtering
T-mapping
Second sound
……
Blue lines: Cavity VT workflow
Black lines: FPC conditioning workflow
Red lines: CM assembly and test workflow

## Slide 15: Workflow for vertical test
Compatible with 166/325/500/650/1300 MHz
Four 1.3GHz or two 650MHz cavities in one single test
1 VT/wk with HPR, or 2 VTs/wk with cavities ready to test
VT workflow:
  ② D1, validation
  ④ D2-5, HPR+dry
  +assembly
  ⑤ D5-8, baking
  +mounting
  ⑥ D8-12, Cool+VT
  +Warm
  ⑤ D13, dismount

## Slide 16
  VT workflow
  ② Validation(1d)
  ④ HPR+dry+assembly (4d)
  ⑤ baking+mounting (3d)
  ⑥ Cool+VT+warm (4d)
  ⑤ Dismount (1d)
1
2
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 17
  VT workflow
  ② Validation (1d)
  ④ HPR+dry+assembly (4d)
  ⑤ baking+mounting (3d)
  ⑥ Cool+VT+warm (4d)
  ⑤ Dismount (1d)
1
2
3
4
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 18
  VT workflow
  ② Validation (1d)
  ④ HPR+dry+assembly (4d)
  ⑤ baking+mounting (3d)
  ⑥ Cool+VT+warm (4d)
  ⑤ Dismount (1d)
1
2
3
4
5
6
7
8
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 19
  VT workflow
  ② Validation (1d)
  ④ HPR+dry+assembly (4d)
  ⑤ baking+mounting (3d)
  ⑥ Cool+VT+warm (4d)
  ⑤ Dismount (1d)
1
2
3
4
5
6
7
8
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 20
  VT workflow
  ② Validation (1d)
  ④ HPR+dry+assembly (4d)
  ⑤ baking+mounting (3d)
  ⑥ Cool+VT+warm (4d)
  ⑤ Dismount (1d)
5
6
7
8
1
2
3
4
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 21: Workflow for FPC conditioning
Compatible with 166/325/500/650/1300 MHz single test stand
Upgradable for multiple test stand run at the same time
FPC workflow:
  ② D1-2, leak check
  ③ D3-10, cleaning
  +assembly+bake
  +conditioning
  +disassembly
  +Storage
  Or④String assembly

## Slide 22
  FPC workflow
  ② Reception+Leak check+S11 (2d)
  ③ Cleaning+assembly+Conditioning +disassembly+Storage
  Or ④ String assembly
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 23
  FPC workflow
  ② Reception+Leak check+S11
  ③ Cleaning+assembly+Conditioning +disassembly+Storage (8d)
  Or ④ String assembly
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 24
  FPC workflow
  ② Reception+Leak check+S11
  ③ Cleaning+assembly+Conditioning +disassembly+Storage
  Or ④ String assembly
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 25: Workflow for CM assembly and test
Two shielding buckers with one cryostat for HT of single cavities at 166/500/650MHz
Upgradable for full test capacity of two CMs/week at a specific frequency
CM workflow:
①③ D0, storage
⑦ D1-15, Cold mass
  assembly
④ D16-24, Cryomodule
assembly
⑤⑥ D25-44, HT
⑤① D45, shipment

## Slide 26
  CM workflow
  ①③ Storage (1d)
  ⑦ Cold mass assembly (15d)
  ④ CM assembly (9d)
  ⑤⑥ HT preparation, cool (10d)
  ⑥ HT, warm (10d)
  ①or③ Shipment or storage (1d)
5
6
7
8
1
2
3
4
1
2
3
4
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 27
  CM workflow
  ①③ Storage (1d)
  ⑦ Cold mass assembly (15d)
  ④ CM assembly (9d)
  ⑤⑥ HT preparation, cool (10d)
  ⑥ HT, warm (10d)
  ①or③ Shipment or storage (1d)
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 28
  CM workflow
  ①③ Storage (1d)
  ⑦ Cold mass assembly (15d)
  ④ CM assembly (9d)
  ⑤⑥ HT preparation, cool (10d)
  ⑥ HT, warm (10d)
  ①or③ Shipment or storage (1d)
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 29: 垂直测试动线
  CM workflow
  ①③ Storage (1d)
  ⑦ Cold mass assembly (15d)
  ④ CM assembly (9d)
  ⑤⑥ HT preparation, cool (10d)
  ⑥ HT, warm (10d)
  ①or③ Shipment or storage (1d)
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 30: 垂直测试动线
  CM workflow
  ①③ Storage (1d)
  ⑦ Cold mass assembly (15d)
  ④ CM assembly (9d)
  ⑤⑥ HT preparation, cool (10d)
  ⑥ HT, warm (10d)
  ①or③ Shipment or storage (1d)
Notes:   ② 频率/漏率检查
  ④ (HPR+洁净组装)
  ⑤ 上吊架
  ⑥ 吊入竖井垂测
  ⑤ 出杜瓦
  ④ (HPR+)腔串组装
  或⑧ 实验/存放

## Slide 31: Outline
Background
  Brief introduction to the PAPS project
  Future project that may need PAPS
The SRF facility
  Layout and workflow
  Labs for R&D purpose
  Cryogenic system
  Public service facilities

## Slide 32: Labs for R&D purpose
Inspection and measurement
  Optical inspection and grinding
  Pre-tuning machine
New material and technology
  Oven for high baking and N-infusion
  Oven for Nb3Sn treatment
  Nb-Su sputtering
High precision measurement
  T-mapping
  Second sound
  Vibration analysis
  ……

## Slide 33: The cryogenic system
Cryogenic system
  2.5KW@4.5K and 300W@2K LHe system
  210m3/h gas recycle and 100m3/h gas purify capability

## Slide 34: Function of the cryogenic system
VT dewars and HT CMs could be cooled, warmed, or tested separately. Cooling capacity is 100W for each.
Every two of the three VT dewars could be cooled or warmed at the same time; single test at the same time.
Each of the two HT CMs could be cooled or warmed at the same time; single test at the same time.

## Slide 35: Compressed air and N2 gas
5 bar compressed air for valve, gauges, pneumatic tool, blow.
5 bar N2 from LN, 0.5um pp filter to remove particles, 0.1um fiberglass filter to remove moisture.
是
Compressed air supply
Clean N2 supply
Compressed air tank
Notes: N2: 0.05um，H20 <0.1ppm

## Slide 36: RF and vacuum equipment for general purpose
RF equipments | Quantity | Note
Signal generator | 2 | 9K--3GHz
Power meter | 2 | Dual channels
Power meter | 1 | Handheld
Oscilloscope | 1 | 1.5GHz
Oscilloscope | 2 | 100M,4 channels
Vector network analyzer | 1 | 2Hz--20GHz
Vector network analyzer | 1 | Handheld
Arbitrary wave generator | 3 | 30MHz
Frequency counter | 1 | 1.5GHz
Spectrum analyzer | 1 | 2Hz--6GHz
Vacuum equipments | Quantity | Note
Molecular pump unit | 1 | Oil-free, with garge
Leak detector | 2 | One for oil-free
Scroll pump | 1 | Oil-free
SPSV unit | 1 | MFC, 0.03um filter
PID Baking Controller | 2 | Up to 200C
RGA set | 1 | 1e-5 Pa to 1bar
Notes: N2: 0.05um，H20 <0.1ppm

## Slide 37: Public service facilities (2)
30 tons cranes to cover the whole hall, including the passageway of the second floor.
Gantry crane and manual folklift for light-weight pieces.
Total electric power about 800kW, with plugs and power and distribution ready; separate gound for control and high power
Notes: N2: 0.05um，H20 <0.1ppm

## Slide 38
Thanks for your attention!