## Slide 1: Cryogenic System at Peking University
Jiankui Hao
On behalf of SRF Laboratory
Institute of Heavy Ion Physics
Peking University
The 8th International Workshop on Cryogenics Operations (Cryo-Ops 2018)
Beijing, June 4-7, 2018
Cryo-Ops 2018, Beijing, June 4-7

## Slide 2
Outline
Cryogenic System for Superconducting Injector and Accelerator
PKU Vertical Test System
Summary

## Slide 3
PKU SRF Accelerator for THz
3.5-cell DC-SRF Injector
2×9-cell Cryomodule
Undulator
SRF-based THz platform at PKU
1.3 GHz SRF cavities must run at 2 K

## Slide 4
Layout of PKU SRF Laboratory
Accelerator
2K
Undulator
RF Power Laser
Cryogenic System
Clean Room
Cooling Water
Injector
VTS
Control Room

## Slide 5
2K Cryogenic System
Design Parameters
Total Cooling Power （2K） | 57.5 W
Liquifaction rate （with LN precooling) | 120 L/h
Liquifaction rate （without LN precooling) | 70 L/h
2K pumping system | 3.2 g/s
Storage dewar | 2000 L
Pressure instability | within 0.1 mbar
Liquid Helium level | within 1 L
Helium buffer tank | 150 m3
Liquid Nitrogen tank | 30 m3
Cooling water | 180 kW
Cooling air | 15000 m3/h

## Slide 6
2K Cryogenic System at PKU
Coldbox
2K Pumps
Dewar
SCA
DC-SRF Injector
2K CBX
2K
2K
Compressor
TL

## Slide 7
Compressor | KAESER DSD238, 40.7 g/s
Oil removal system | L140 standard
Liquefier/Coldbox | Linde L140
Control system | SIEMENS SIMATIC S7-300
LHe Dewar | 2000 L
2K Coldbox | 2 sleeves, recuperator heat exchanger
Gas heater | ~6 kW
2K pumps (2x) | RUTA WS2001FU/SV630BF/A, 3.2 g/s
Transfer Lines | TIPC
He gas buffer tank | 2  75 m3
Cooling water | 180 kW
Components of 2K Cryogenic system

## Slide 8
Layout of 2K Cryogenic System
Cryogenic Hall
Accelerator Hall
Buffer Tanks
Cooling Water

## Slide 9: History
2005-2007, conception and design
2007, contract with Linde
2008-2009, installation
2010.03-06, commissioning of liquefier and 2K CBX
2010.07-10, commissioning with 2K transfer lines
2010.11-2011.06, commissioning with DC-SRF Injector
2011.06-2012.06, beam loading test with Injector
2013.08-2015.06, THz radiation with Injector
2015.07- now, THz radiation with DC-SRF Injector and 29 Accelerator

## Slide 10: Commissioning
Liquefaction rate
  > 80 l/h w/o LN pre-cooling
  > 140 l/h with LN pre-cooling
2 K commissioning
  Cooling power at 2K:
  ~ 58-59 W

## Slide 11: Commissioning
2 K commissioning
  Pressure instability:
  <  0.1 mbar
  Helium level: <  5%
Injector Eacc: 12MV/m
36W
44W
50W
Recovery from heat load change:
  ~10 min

## Slide 12
10~20 MeV, Ave. current ~1mA (long macropulse)
Applications: UED, THz radiation
Cryomodule with 29-cell cavities (since 2015)
DC-SRF injector with 3.5-cell cavity (since 2014)
Stable electron beam loading at 2 K

## Slide 13
Outline
Cryogenic System for Superconducting Injector and Accelerator
PKU Vertical Test System
Summary

## Slide 14
Shanghai Soft XFEL Project
Tasks of PKU
Series researches of 9-cell superconducting cavities
  25～30 MV/m
Construction of SRF Facilities
  Vertical Test System (VTS)
  Surface treatment devices
SRF researches for XFEL

## Slide 15
Layout of PKU SRF Laboratory
Accelerator
2K
Undulator
RF Power Laser
Cryogenic System
Clean Room
Cooling Water
Injector
VTS
Control Room

## Slide 16: Design of VTS
Components
  Cryostat
  Insert for cavities
  Magnetic shield
  Radiation Shield
  2K valve box
  Transfer lines
  2K pumping system
Capacity
  2 K temperature
  Static heat loss: < 18 W
  Heium mass flow (@25 mbar):
  10 g/s
  Cooling power:
  > 200 W @ 2 K

## Slide 17: Process Flow Diagram

## Slide 18: Design of PKU-VTS

## Slide 19
Outer Magnetic Shield
Vacuum Vessel
LN Shield
LHe Vessel
Inner Magnetic Shield
Ribs on LHe Vessel
LN Pipe
Top Flange of LN Shield
Insert Thermal Shields
Hanger Rods
Vacuum Vessel Flange
LHe Vessel Flange
Insert Flange
Outer Magnetic Shield
Inner Radiation Shield
Cavity
Sealing Gas
Cryostat and Insert

## Slide 20
Cryostat and Insert

## Slide 21: Magnetic shield
1J79 Alloy
Simulation (CST EM): < 1mGs
Measure: <2mGs

## Slide 22
2K pumping & VTS
（2+4）RUTA WS2001FU/SV630BF/A
3.2 g/s for old pumps
6.8 g/s for new pumps
2K Pumping System
VTS

## Slide 23
Commissioning（Jan. - March, 2017)
Heaters instead of cavity in cryostat
2K pumping system
VTS dewar & 2K box
Control system
Pressure：
300.1 mbar
Level:
42 0.6 %
Capacity:
210W @ 2K

## Slide 24
Vertical test of different cavities (since April 2017)
1.3 GHz single cell
650 MHz 2-cell
1.3 GHz 9-cell
162.5 MHz HWR

## Slide 25
Vertical test (4.2K, 2.0K, 1.8K, 1.6K)

## Slide 26
Stable operation of the first 2K cryogenic system in China is successful.
Electron beam loading experiments have been carried out based on the stable operation of cryogenic system.
Peking University Vertical Test System (PKU-VTS) is constructed, commissioned and operated successfully.
Various of cavities (9-cell 1.3 GHz, 1-cell 1.3 GHz, HWR, 2-cell 650 MHz) have been tested on PKU-VTS.
Summary

## Slide 27
Thank you for your attention!
Cryo-Ops 2018, Beijing, June 4-7