## Slide 1: Simulation of Signal Propagation in RPC for Atlas Phase II Upgrade
Xiangyu Xie
on behalf of
ATLAS RPC Software Simulation Group(USTC, Roma II and INFN)
At Third CLHCP, Nanjing University

## Slide 2: Outline
1. Motivation
2. Simulation method
3. Results
4. More functions
5. Conclusion

## Slide 3: 1. Background ——Too large cluster size
Prototype RPC with new readout panel and electronics has been made
Beam test shows it has larger cluster size than expect
→Too many strips have response to an event
Disadvantages:
Reduce online spatial resolution
Influence signal identification
Decay counting capability
Prototype CS is around 6,
While 3 is more acceptable

## Slide 4
1. Background ——Readout Diagram
From readout diagram:
Besides the highest signal, three more strips have significant response.
Considering the 25mm-width-strip, this is not reasonable
These three strips’ signal could be called as ‘Crosstalk’ (CT).
Readout from prototype RPC

## Slide 5
1. Background ——Targets
Find out how crosstalk comes by simulation
Give suggestions from simulation results
One more step forward…
Help design RPC with new structure

## Slide 6: 2. Simulation Method ——Simulation Tools
1/2:PCB Studio of CST SUITE
For physical modelling
The layer by layer structure of RPC ≈ PCB
Terminals (white points) connecting to Design Studio
Modeling half RPC for saving computing source
Top view of model (strip layer)
Model(Green block) with circuits
2/2:Design Studio of CST SUITE:
Accomplishing circuits
  e.g. matching resistor, AMP
Set simulation task
Define signal

## Slide 7: 2. Simulation Method ——Simulation model
① strips:
5 strips
25mm in width
2mm gap between strips
Terminated at both ends(white points)
②
①
② signal position:
Y axis: in the middle of strips3
X axis: variable
Z axis: under bakelite
Via a copper pad (D=2mm)
③
③
③ propagation distance:
Distance between signal position and terminal
Depending on signal’s
X-coordinate
Top view of model (strip layer):
‘main strip’

## Slide 8: 2. Simulation Method ——Simulation signal
Stimulate source: A current signal
Signal waveform:
I[t]=(gap-v*t)*e^(a*v*t)
Time of rise ≈ 4ns
Time of fall ≈ 1ns
(A simple assumption)
PS. The strength of signal doesn’t matter.

## Slide 9: 2. Simulation Method ——Method Reviews
Peripheral circuits
Transfer to simulation
RPC
Current signal
Model

## Slide 10
1st causation: Strip-Strip Coupling
EM coupling
→ CT has bipolar waveform
→ like derivative of main signal
Relative to propagation distance
→ proportional relationship
（dispersion appears @90cm）
Five strips voltage readout (by matching resistors)
Model @propagation distance =10cm(left circle), 90cm(right circle)
3. Simulation Results ——Two main causations of CT
Graphite@
100kΩ/SQ
Def. Cross talk = Vmax(neighbor)/Vmax(main) (%)
This kind of CT has bipolar waveform

## Slide 11
1st causation: Strip-Strip Coupling
Chart: CTs VS Propagation Distance @ different surface resistivity
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
100k | 5.2054 | 6.1412 | 6.9623 | 7.9504 | 8.9803 | 10.0381 | 11.381 | 12.3174 | 13.5255 | 14.4099
50k | 5.3712 | 6.3733 | 7.2445 | 8.2976 | 9.3833 | 10.5078 | 11.9196 | 12.9144 | 14.1919 | 15.1272
10k | 6.5986 | 8.0689 | 9.3853 | 10.8981 | 12.456 | 14.0476 | 15.9798 | 17.4302 | 19.2288 | 20.6227
5k | 7.9381 | 9.9309 | 11.7399 | 13.7833 | 15.8578 | 17.989 | 20.4871 | 22.4581 | 24.8221 | 26.7193
1k | 14.8466 | 19.4484 | 23.7721 | 28.4412 | 33.1325 | 37.9091 | 43.1338 | 47.4539 | 52.4417 | 56.3164 | 61.078
20k | 5.848 | 7.031 | 8.0753 | 9.3083 | 10.5727 | 11.8742 | 13.4903 | 14.6529 | 16.1262 | 17.2455
2k | 11.0734 | 14.3024 | 17.2865 | 20.5646 | 23.8737 | 27.2722 | 31.0987 | 34.2365 | 37.921 | 40.9089
CT grow linearly with longer propagation distance
Lower graphite surface resistivity → Higher slope
PS. The value of slope is dependent on how fine the model is divided, but tendency not
3. Simulation Results ——Two main causations of CT

## Slide 12
2nd causation: surface resistivity of graphite
Direct voltage readout (of matching R) over time(ns)
Graphite @ 100kΩ/SQ, Propagation distance=50cm
High surface resistivity
→ no such enhancement
Low surface resistivity
→ CT’s positive part enhanced
→ larger CT
Direct voltage readout (of matching R) over time(ns)
Graphite @ 1kΩ/SQ, Propagation distance=50cm
Graphite@
1kΩ/SQ
Graphite@
100kΩ/SQ
3. Simulation Results ——Two main causations of CT
This kind of CT has similar waveform

## Slide 13
2nd causation: surface resistivity of graphite
Chart: Crosstalk VS graphite surface resistivity (@propagation distance =50cm)
| 100 | 50 | 20 | 10 | 5 | 2 | 1
 | 8.9803 | 9.3833 | 10.5727 | 12.456 | 15.8578 | 23.8737 | 33.1325
Graphite is ‘transparent’
3. Simulation Results ——Two main causations of CT

## Slide 14: 3. Simulations Results ——Comparing with prototype
PS. Two diagrams have different time scale and amplifiers
Beam test: @120kΩ/SQ
Integral readout in simulation: @1kΩ/SQ
Prototype RPC graphite surface resistivity isn’t high enough
Beam test results
Simulation integral results
Second neighbors have ‘steps’

## Slide 15: 3. Simulations Results ——Comparing with second edition
Beam test: @620kΩ/SQ
Integral readout in simulation: @100kΩ/SQ
At ‘high’ surface resistivity, quite small CT with advanced peak time
Main discrepancy is the bias of surface resistivity
Beam test results
Simulation integral results

## Slide 16: 4. More functions ——1. grounded wires
Under low graphite surface resistivity:
CT is dominated by graphite
Under high graphite surface resistivity:
Wires reduce about 1/3 CT
Chart: CT between wired or not wired model @propagation distance=50cm
| 1k | 2k | 5k | 10k | 20k | 50k | 100k
With grounded wires crosstalk percentage | 33.5968 | 24.7165 | 17.2993 | 14.252 | 12.5584 | 11.5247 | 11.1037
No wires crosstalk percentage | 35.5063 | 27.1729 | 20.3879 | 17.6782 | 16.2656 | 15.328 | 15.321
Wires between strips
Wires won’t be effective in reducing CT caused by low graphite resistivity

## Slide 17: 4. More functions ——2. segmented graphite
Two 0.1mm-wide-segments under gaps between ‘main strip’ and neighbor strips
Graphite @1kΩ/SQ with segments better than graphite @100kΩ/SQ
Could help improve RPC counting capability
Graphite layer
Chart: CT VS propagation distance
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
100k | 5.2054 | 6.1412 | 6.9623 | 7.9504 | 8.9803 | 10.0381 | 11.381 | 12.3174 | 13.5255 | 14.4099
1k | 14.8466 | 19.4484 | 23.7721 | 28.4412 | 33.1325 | 37.9091 | 43.1338 | 47.4539 | 52.4417 | 56.3164
1k with segements | 3.9759 | 4.301 | 4.7654 | 5.2246 | 5.6996 | 6.1881 | 6.5534 | 7.1248 | 7.6155 | 8.1981

## Slide 18: 5. Conclusion
1. Problem comes:
Prototype RPC has large cluster size
2. Results:
  Set up a new method to simulate RPC
  Two main causations of CT have been found and fit beam teats readouts
  New design could be simulated by this method
3. Future plan:
  Improve model
  Test existing applied material
  Try new design RPC in USTC RPC lab.

## Slide 19: Back up
Stack up of model:

## Slide 20: Bach up ——3. Ideal probes
Terminals on graphite(blue layer)
Y position(mm)
Voltage (V)
Graphite voltage distribution
Terminals along strips
Connect to a tremendous resistor(10e20Ω) to monitor voltage
Procession of signal transmission along strip
An easy and clear way to observe signal propagation