## Slide 1: Neutrino Detector -- Principle and Design
Jun Cao
Institute of High Energy Physics, Beijing
Nov.15, 2017, Nanning

## Slide 2
反应堆中微子探测原理
大亚湾探测器设计
其它中微子探测器原理简介

## Slide 3: Detecting a Neutrino
Neutrino
  no charge
  Almost no reaction with matter
  We can only observe a neutrino after it reacts with matter and produces (finally) a charged particle
"I have done a terrible thing. I have postulated
a particle that cannot be detected." -- Puali
Wolfgang Pauli
 | Strength | Range
Strong force | 100 | 10-15
Electromagnetic force | 1 | 
Weak force | 10-11 | 10-18
Gravitity | 10-36 | 
 | Strength | Range
Strong force | 100 | 10-15
Electromagnetic force | 1 | 
Weak force | 10-11 | 10-18
Gravitity | 10-36 | 
The lesson of the work was clear: It is easy to shield out the noise men make, but impossible to shut out the cosmos. -- Cowan

## Slide 4: Typical Reactions (1)
Accelerator neutrino, Atmospheric neutrino
Why anti-nu has less events than nu in accelerator exp.?
νμ CC Event
νe CC Event
NC Event
Total nm CC cross section

## Slide 5: Typical Reactions (2)
Reactor neutrino
Solar neutrino
Neutrino coherent scattering (SNS, reactor?)
Solar, reactor, etc

## Slide 6: Detecting with Liquid Scintillator
PMT
neutrino
UV-vis photon
n
positron
Mineral Oil
LS
Gd-LS
Detecting reactor neutrinos with a liquid scintillator
As an example of a complete experiment

## Slide 7: Liquid Scintillator

## Slide 8: Scintillation light
Expose my room with a UV flashlight:
Some plastic
Bleached paper
Washed clothes

## Slide 9: Make a Liquid Scintillator
Easier than making a cocktail
Solvent
  Aromatic compounds, e.g. Pseudocumene , Mesitylene, Xylene(PX), Toluene, PXE, DIN, LAB
  Solvent itself has very low light yield
Fluor (1-5 g/L)
  PPO、PBD、TP、PMP
(Optional) Wavelength Shifter (0~15 mg/L）
  bis-MSB、POPOP、BBQ
  Match PMT response, shifting photon wavelength to transparent region
Very difficult to make good LS

## Slide 10: Molecule Energy Level
Energy level of pi bond, S0 is ground state, S1, S2 are excited single states, T1 is excited triplet state
Due to Stokes shift (found in 1852) scintillation light can transmit in itself.

## Slide 11: Energy Transfer in LS
Resonance
Absorption and re-emisson of UV light
Binary LS (w/o wl shifter)
Ternary LS
What happens when exciting with UV light?
Excitation by Ionization

## Slide 12: Light Yield vs PPO (Bis-MSB) Concentration
Light yield versus PPO concentration
Light yield versus bis-MSB concentration
LAB solvent, measured w/ small cell. Light yield may be impacted by cell size, due to absorption reemission process
Concentration Quenching

## Slide 13: Attenuation, absorption, scattering
Attenuation: also noted as extinction length.
Absorption: the molecular are heated by incident light.
Rayleigh scattering: scatter off the bound electrons of molecular.
Mie, Raman, absorb&re-emit…
L=2~3 m (Tap water)，50% light absorbed in DYB detector
L=10m ：20% light absorbed in DYB

## Slide 14: Quenching
Thermal Quenching
Oxygen quenching
11%
Energy quenching
Pulse shape

## Slide 15: Non-linearity due to energy quenching

## Slide 16: Daya Bay Liquid Scintillator
LS: ~ 10 k photons/MeV (NaI 40 k photons/MeV), isotropic
Recipe: LAB + 3g/L PPO + 15mg/L bis-MSB (+0.1% Gd)
Daya Bay photoelectron yield: 163 p.e./MeV
10 k photon/MeV (?)
Attenuated: 70%
PMT photocathode coverage: 12%
PMT quantum efficiency: ~ 20%
1.68%  168 p.e./ MeV

## Slide 17: Summary of DYB LS
Light Yield: ~ 10, 000 photon/MeV
Emission Spectrum (bis-MSB): 380-500 nm
Attenuation Length 15m@430nm (incl. Rayleigh)
Absorption spectrum
Absorption re-emission
Decay time: 3 ns + 10 ns + 150 ns
Oxygen Quenching: light yield increase ~11% after N2 bubbling
Temperature eff.: Light yield increase 70% from 20 ℃ to -75 ℃
PID with pulse shape

## Slide 18: Doping with Gadolinium
Increase n-capture E from 2.2 to 8 MeV
Gd has the largest n-capture xsec.
Challenging of dissolving metal into organic liquid
phosphors, β-diketones, or carboxylates
GdCl3 + carboxylic acid (TMHA)
  0.1% Gd by mass
Doping with Li (alpha)
Doping with Te (0vbb)
…

## Slide 19: Liquid Scintillator Hall
LS mixing equipment
185 ton 0.1% Gd-LS
Liquid Scintillator
Mineral Oil
Filling Equipment
ISO tank equiped with load cell. Target mass errorr ~0.1%

## Slide 20: Photomultiplier Tube (PMT)
APOD

## Slide 21: Dynode PMT
Glass bulb
Photocathode
Al reflective coating
Dynode
Anode
voltage divider
The first PMT in the world in 1933
“Kubetsky’s tube”
DE= QE * CE ~ 12-30%
Photoelectrons (p.e.)
Signal
Quantum Eff. (QE) : ~20%
Collection Eff. (CE): 60-90%

## Slide 22: Micro Channel Plate (MCP)
MCP-PMT

## Slide 23: QE of the Photocathode
Photocathode Sensitivity
Overlay w/ LS emission spectrum

## Slide 24: Performance of the 20-inch PMTs
JUNO Specification

## Slide 25: Electronics Readout

## Slide 26: Charge Measurement (Q)
Using CR-(RC)4 shaping + Peak finding
Analog  Digital signal (ADC)
FPAG: Field Programmable Gate Array, online algorithm to process signals
blue - input to FEE
green - shaper out
yellow - shaper out

## Slide 27: Timing Measurement (T)
Determine the timing with the rising edge
FPGA-Based clock, precision (RMS) 0.78ns
Can measure multiple hits
Multi-phase clock method

## Slide 28: Trigger
To ignore noise (PMT dark noise and electronics noise) and low energy events. PMT dark noise: 1–10 kHz at room temperature for 8-in PMT
  NHIT (# PMT fired in 100 ns)
  ESUM (total p.e.)
FEE send info to trigger board， logic decision online, read out data from FEE buffer to DAQ, or override in the buffer

## Slide 29: Natural Radioactivity

## Slide 30: Natural Radiation
Natural radiation is everywhere, born w/ the Earth
  238U  222Rn
  232Th
  40K
1 Bq = 1 decay per second
  Human body has ~ 5000 Bq K-40
  1 kg rock (granite) ~ 150 Bq
  1 kg Uranium ~ 12,000,000 Bq
  1 kg Co-60 = ? Bq
Cosmogenic radiation: 14C, neutron, and many
Artificial radiation, e.g.
  60Co (In stainless steel, for industry and research)
  137Cs (N bomb test, for research)
In rock, mud, air, sea water

## Slide 31
Three kinds of radiation:
 particle: can not penetrate a paper
 particle (electron): cm
 ray: attenuation length = 20 cm water, or one order per 50 cm water

## Slide 32: Gamma spectrum of DYB granite
ppb to Bq conversion
  1 ppb 40K = 258.4 mBq/kg
  1 ppb 238U = 12.4 mBq/kg
  1 ppb 232Th = 4.0 mBq/kg
Granite has high radiation in all kinds of rock. Radiation of Daya Bay granite is 3 times higher than world average
10 ppm U
30 ppm Th
5 ppm K40
γ Energy < 2.6 MeV (Tl-208)

## Slide 33: Where the radioactivities come from?
Rock
  8.8ppm U, 28.7ppm Th, 4.5ppm K
  Almost 0 after 2.5m water shielding
Liquid scintillator
  Radon (product of U238 decay, emitted from rock)
  Contamination, additives
  Liquid scintillator need cover with N2
PMT glass, can not contact with LS directly (oil shielding); use low background glass
Stainless steel tank: need low bkg steel.
Avoid aluminum, glass components in detector
All detector material need radio-assay
Assembly of detector in clean room (10,000 class)

## Slide 34: Use water to shield gamma from rock
w/o water, DYB detector will see 1,000,000 Hz from rock
w/ 2.5m water, rate lowers to 200 Hz (almost 0 from rock)

## Slide 35: Estimate the Shielding Power
MeV γ deposit energy in matter via Compton scattering on electron. Therefore, attenuation is proportional to electron density, thus matter density (almost independent of material)
“mass attenuation coefficient”
attenuation length ~ 20 cm water. Reduce 1 order/50 cm.
What’s the shielding power of DYB water pool?
 | γs (>1 MeV) | E (MeV) | mass attenuation coefficient in oil(cm2/g) | mass attenuation coefficient in steel(cm2/g)
1 Bq U | 0.82 | 1.5 | 0.0575 | 0.0486
1 Bq Th | 0.88 | 2 | 0.0493 | 0.0425
1 Bq K | 0.105 | 1.5 | 0.0575 | 0.0486
1 Bq Co | 2 | 1.17+1.33 | 0.0493 | 0.0425

## Slide 36: Final natural radiation bkg in DYB
W/o enough shielding, we can’t see any neutrino:
Imaging how to find 0.002 neutrinos in 1,000,000 backgrounds
Why DYB use Gd-LS? Why JUNO won’t dope Gd in LS?

## Slide 37: Cosmic Muon
The lesson of the work was clear: It is easy to shield out the noise men make, but impossible to shut out the cosmos. -- Cowan

## Slide 38: Cosmic Muon
Minimum ionization muon: ~200 MeV/m.w.e.
(meter-water-equivalent)
 Flux on surface ~ 200Hz/m2

## Slide 39: Muon Tomography

## Slide 40: Muon Flux
Muon on surface: Gaisser formula
Modified Gaisser formula
More precise flux need simulation (Earth Magnetic field)

## Slide 41: Muon Energy Loss
Continuous process —— Ionization energy loss
Discrete process ——Bremsstrahlung, pair production, hadron process, important for high energy muon
Minimum muon energy to pass xmin thick rock
=500GeV, the energy at which the continuous process has equal contribution to discrete process
Minimum ionization muon: ~200MeV/m.w.e.

## Slide 42: Propagate Muon to Underground Lab
Mount map of Daya Bay area
  12 km high precision (1m)
  34 km 1:5000 map (5m)
  1010 km SRTM map
Muon propagation software:
MUSIC, FLUKA
Muons at Daya Bay Lab
Rock density：~2.6 g/cm3

## Slide 43: Muon Simulation
Daya Bay
LingAo
LingAo II
Mid
Far
 | DYB | LA | Mid | Far
Elevation (m) | 93 | 100 | 208 | 324
Flux (Hz/m2) | 0.88 | 0.69 | 0.17 | 0.039
Mean Energy (GeV) | 57 | 58 | 97 | 142
Muon rate at surface ~200Hz/m2

## Slide 44: Spallation Neutron
Cosmogenic neutron is one of the most important bkg
Neutron yield
(when matter density is 1 g/cm3, number of neutron produced for each muon passing 1 cm path  neutron’s sea)
Neutron density at Daya Bay near (far) site 0.03 (0.001) neutron/m3/sec
muon Spallation
Gamma-N
Muon capture on nuclei can produce neutron
Y.F. Wang et al

## Slide 45: Muon capture on nuclei
Stopping muon:   e+, Michel’s e, lifetime 2.19703 s
Form a － molecule, then decay －e－+, or capture on nuclei.

## Slide 46: Cosmogenic Longlived Isotopes
Hard to remove by muon veto
The most important bkg in DYB: He8/Li9 with a delayed neutron

## Slide 47
Daya Bay Detectors
3 layers separated by Acrylic Vessels

Neutron
RPC
Water Cherenkov

## Slide 48: 靶质量
根据物理目标确定靶质量（探测器大小）：80吨
  中微子事例率低，统计量很关键
物理目标：三年测量sin22θ13到好于0.01 （90%置信度)
假定系统误差和本底

## Slide 49: 多模块、远近相对测量
多模块：
  0.2%的系统误差需要验证(side-by-side)
  多模块统计性地减少系统误差
  80吨/4=20吨
参数 | 相对误差 | 远近相对测量
反应截面 | 1.9% | 0
总质子数 | 0.8% | 0.02%
探测效率 | 1.5% | 0.2%
反应堆功率 | 0.7% | ~ 0.1%
每裂变能量 | 0.6% | 0
CHOOZ合计 | 2.75% | ~0.2%

## Slide 50: 三层探测器
法国CHOOZ：Gd-LS + LS，外层LS用来收集n-Gd伽马能量  PMT泡在LS中，本底高
日本KamLAND：LS + Oil，液袋有放射性  需要Fiducial volume cut，误差大
新一代反应堆中微子实验：三层 Gd-LS + LS + Oil
20吨
?
?

## Slide 51: Gamma Catcher
外层LS用来减少n-Gd 8MeV峰的伽马能量逃逸
20 ton Gd-LS
20 ton LS
两层:
Eff. ~ 73%
Error ~ 0.4%
三层:
Eff. ~ 92%
Error ~ 0.2%
The most important error!

## Slide 52: Gamma Catcher
Neutron Energy (MeV)
Recon.
GEANT energy
6 MeV
Neutron energy cut eff. 92%
Error ~0.2% (Suppose 1% energy scale error）
45cm gamma catcher
Energy Resolution | 10%/sqrt(E) | 7%/sqrt(E) | Geant E
6MeV | 92.03% | 92.05% | 92.08%
5.94MeV | 92.23% | 92.23% | 92.25%
6.06MeV | 91.79% | 91.85% | 91.89%
δEff. | -0.24% | -0.20% | -0.19%
 | +0.20% | +0.18% | +0.17%
能量精度

## Slide 53: Positron Eff.
Chooz
Daya Bay
Chooz 1.3MeV, error 0.8%（bad LS)
KamLAND 2.6MeV, error 0.26%
Positron Eff. 99.6%
Error ~ 0.05% (suppose 2% energy scale error）
必须做低本底探测器
白油屏蔽层

## Slide 54: 屏蔽层
矿物油（白油）~50cm
  使光源远离PMT
  屏蔽PMT玻璃、钢罐的放射性
III
低本底玻璃PMT：~10Hz
钢罐（低本底钢、低本底焊条）：~30Hz
实际起作用的是PMT距光源20cm + PMT自身高度 = 50 cm

## Slide 55: # of PMTs
Tech. Spec.: ~ 5% energy resolution @ 8 MeV
200 PMTs/module  10% effective coverage w/ reflection  ~ 100 p.e./MeV 7000 * 0.6 * 0.22 * 0.8 * 10% = 74 + scattered photon
We chose a “cheap” design
 | Wall Area (m2) | #PMT 10% coverage
No Ref. | 102 | 360
Reflection | 58 + 3210% | 215
Vertex ~ 14 cm

## Slide 56: 中心探测器尺寸优化
 | PMT | Coverage | pe yield | pe yield/Coverage
Daya Bay | 192 8" | ~6% | 163 pe/MeV | 1.77
RENO | 354 10" | ~15% | 230 pe/MeV | 1
Double Chooz | 390 10" | ~16% | 200 pe/MeV | 0.81
 | Gd-LS | LS | Oil | Eff.
Daya Bay | 310x310 cm 23.25 m3 20 ton | 400x400 cm 26.7 m3 23 ton Thick 45 cm | 500x500 cm M3 37 ton Thick 50 cm | 
RENO | 280x320 cm 18.7 m3 16.1 ton | 400x440 cm 33.2 m3 28.5 ton Thick 60 cm | 540x580 cm 76.5 m3 64.2 ton Thick 70 cm | 
Double Chooz | 230x240 cm 10.3 m3 8 ton | 340x357 cm 22.6 m3 17.5 ton Thick 55 cm | 552x567 cm 114 m3 88 ton Thick 105 cm | 
 | Gd-LS | LS | Oil | Eff.
Daya Bay | 310x310 cm 23.25 m3 20 ton | 400x400 cm 26.7 m3 23 ton Thick 45 cm | 500x500 cm M3 37 ton Thick 50 cm | 
RENO | 280x320 cm 18.7 m3 16.1 ton | 400x440 cm 33.2 m3 28.5 ton Thick 60 cm | 540x580 cm 76.5 m3 64.2 ton Thick 70 cm | 
Double Chooz | 230x240 cm 10.3 m3 8 ton | 340x357 cm 22.6 m3 17.5 ton Thick 55 cm | 552x567 cm 114 m3 88 ton Thick 105 cm | 

## Slide 57: Assembly of Antineutrino Detector

## Slide 58: 水屏蔽层大小
Fast Neutron
Vetoed muon
Not Vetoed muon
n
n
阻挡岩石天然放射性
阻挡岩石中子
探测宇宙线

## Slide 59
2004年的设计
探测器模块: 高~4米，直径~4.5米
内部充满液体闪烁体和矿物油
全重约50吨，运输时可将液体抽空，容器约重5吨。
近端实验室：2模块
远端实验室：4~8模块
用2米厚的纯水做屏蔽层，搭建成“水房子”，然后在水房子内放置探测器模块。

## Slide 60: 实际设计

## Slide 61: Filled Water Pool

## Slide 62
氮气密封罩（10米 X 16米）
40/52米长密封拉链

## Slide 63: Energy Calibration
R=0
R=1.7725 m
R=1.35m
LED (PMT gain，timing)
Ge68 (positron threshold 1.022 MeV)
Co60 (2.506 MeV) + Am-C (neutron)
Co60: 100 Hz
1.173 + 1.332 MeV
Ge68: 15 Hz
0.511x2 MeV
Am-C：
0.5 Hz

## Slide 64: Neutrino Selections
0.7-12 MeV
6-12 MeV
Prompt candidate
Delayed candidate
Correlated Events in 1-200 s
Reactor Neutrinos
(Prompt)
Neutrons (Delayed )

## Slide 65: Various Neutrino Sources
Reactor
Accelerator
Supernova
Atmosphere
Sun
Earth
Big Bang

## Slide 66: Neutrino Sources
arXiv:1111.0507

## Slide 67: Neutrino Detectors
… … …

## Slide 68: Atm. and Solar Neutrino

## Slide 69: Super-Kamiokande: Water Cherenkov
50 kt water Cherenkov
22.5 kt fiducial volume
11146 20” PMT
1885 8” PMT
1000 m underground

## Slide 70: History of Super-Kamiokande
11146 ID PMTs
(40% coverage)
5182 ID PMTs
(19% coverage)
11129 ID PMTs
(40% coverage)
Energy
Threshold
(Total energy)
(Kinetic energy)
1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
SK-I
SK-II
SK-III
SK-IV
Acrylic (front)
+ FRP (back)
Electronics
Upgrade
SK-I
SK-II
SK-III
SK-IV
5.0 MeV
~4.5 MeV
7.0 MeV
~6.5 MeV
5.0 MeV
~4.5 MeV
< 4.0 MeV
<~3.5 MeV

## Slide 71: Cherenkov Light

## Slide 73: Cherenkov Ring in SK detector

## Slide 74: Neutrino detection
Stopping muons
FC
Through-going muons
PC
Charged interactions:
nm+ N  m + N’ + x
ne+ N  e + N’ + x
Neutral interactions:
nm+ N  nm + N’ + x
ne+ N  ne + N’ + x
Elastic scattering:
nx + e  nx + e
Charged particles:
Cerenkov rings

## Slide 75: Particle Identification (PID)

## Slide 76: Future Atmospheric Exp.
INO
Hyper-K
KM3NET-ORCA
PINGU
260 kton each

## Slide 77: Homestake experiment
1949 L. Albarez: neutrino detection by e + 37Cl  37Ar + e-
Proposed by J.Bahcall & R. Davis
Experiment by R. Davis since 1964
Overburden: 1500 m
Eth>817 keV, sensitive to 8B and 7Be
615t tetrachloroethylene
Extract and count Ar every 3 months
Detected 2000 neutrino in 30 years
Solar Neutrino Problem

## Slide 78: GALLEX & SAGE
Proposed by V.A. Kuzmin and G.T. Zatsepin in 1966
SAGE in Baksan (1990~):
  60t Metallic Ga
GALLEX in Gran SASSO(1991~)
  60t GaCl3
Chemical extraction of 71Ge

## Slide 79: The SNO Detector

## Slide 80: Neutrino Detection in SNO
nx + d nx + n + p
Neutral-Current (NC)
nx + e- nx + e-
Forward Peaking
Elastic Scattering (ES)
ne + d e- + p + p
Ee~En, ~isotropic
Charged-Current (CC)
n  d  t  g , Eg = 6.25 MeV
ne
nx= ne+(nm+ nt)/6
nx= ne+nm+ nt

## Slide 81: Borexino Detector
278t target liq. Scint.
890t buffer liq.
2214 PMT
2100t water shielding

## Slide 82: Accelerator Neutrino

## Slide 83: Neutrinos at the Main Injector(NUMI)
120 GeV proton beam from the main Injector on graphite target, power ~ 310 kW
Produced hadrons, mainly pi and K, will decay to neutrinos

## Slide 84: Detection
νμ CC Event
νe CC Event
NC Event
Total nm CC cross section

## Slide 85: US Accelerator Neutrinos
MINOS
NOvA
DUNE

## Slide 86: MiniBooNE
1000 ton mineral oil, Cherenkov light in oil, 1000 8-in PMTs

## Slide 87: MINOS Detectors
Imperial College/RAL
Dave Wark

## Slide 90: PID
νμ CC Event
νe CC Event
NC Event
νμ CC Event
UZ
VZ
long μ track & hadronic activity at vertex
3.5m
NC Event
short event, often diffuse
1.8m
νe CC Event
short, with typical EM shower profile
2.3m

## Slide 92: CNGS and OPERA
nm
nt ?
Pb
Emulsion layers
n
t
1 mm
Plastic base
Signature of
t appearance
Direct approval of nm  nt oscillation

## Slide 95: Future Accelerator Exp.
DUNE
T2HK
DUNE/LBNF

## Slide 96: Liquid Argon Detector

## Slide 97: Neutrinoless Double Beta Decay
Exploring nature of v’s mass
Are neutrinos Dirac or Majorana particles?

## Slide 98: NLDBD Experiments
136Xe
76Ge
130Te
82Se
(130Te, 116Cd, 48Ca, 96Zr, 150Nd, 100Mo)
130Te
LUCIFER, ……

## Slide 99: Time Projection Chamber (TPC)
Avalanche Photo Diodes
-8 kV
Energy meas.  Combine Light and Ionization
EXO
Liquid TPC:
Single Phase
Dual Phases

## Slide 100
> 25 cm
25 mm ea
High purity
Heat transfer fluid HFE7000 > 50 cm
1.37 mm
VETO PANELS
The EXO-200 Detector
G.Gratta 2013

## Slide 101
G.Gratta 2013

## Slide 102
A two-site Compton
scattering event.
All scintillation light arrives at
the same time, indicating that
the two energy depositions
are simultaneous.
The scintillation light is
Brighter and more localized
on Side 1 where the
scattering occurs
V
U
V
U
Side 1 Side 2
G.Gratta 2013

## Slide 103: IceCube

## Slide 104: Ice drilling with hot water
Hot water heaters
-25 C
-2450 m
-50 m
-55 C

## Slide 105: Distinguish Neutrinos from Different Sources
Super-K: solar ν, atm. ν, acc. ν from J-Parc
JUNO: reactor ν, geo-ν, solar ν, atmospheric ν, supernova ν, DSNB
Energy range
ν and anti- ν
Acc. ν beam timing
Supernova in 10 s
Sun has a direction
Inevitably, some bkgs
Fit Spectrum
geo-ν
reactor-ν

## Slide 107: Dark Blue Water

## Slide 108
SuperK,SNO
Homestake
Gallex/SAGE
Borexino