## Slide 1
Tianchi Zhao
IHEP, Beijing
Comments on Dual Readout Calorimeter
Sept. 20, 2017
tianchi@u.washington.edi

## Slide 2
RD52 approaches with finer sampling granularity and therefore better performance
But module and projective tower construction more difficult
Richard Wigmans
Finer sampling
Finer sampling
2017-04-20

## Slide 3
Assumed parameters in this talk
1.5 m
1.8 m
~5 m
Tracker
TPC, Silicon, DC
Projection in  and 
2 m
2.5 m

## Slide 4
Main Issues to be Addressed for CDR
Projective towers ?
Depth of calorimeter?
Prototypes are 2 – 2.5 m long
Pre-shower detector?
Readout method?
SiPMs (or other method)
Segmentation size
Total number of readout channels

## Slide 5
A Projective Tower of Dual Readout Calorimeter
1.5 m
Short fibers
Full length fibers
Total area to be covered by PMT determined by OD and barrel length of calorimeter
OD = 7 m, L = 6 m
Total area = 190 m2
Barrel = 130 m2
End caps = 2 x 30 m2
2（ 6 x 6 ）PMTs
5 cm
Total PMTs = 2 x 400 x 190 = 152000

## Slide 6
Ternary Readout
Scintillating light
Cherenkov light
Shower time profile
plastic scintillator plate/light guide
Fast PMTs
(C-fibers)
Fast PMTs
(UV-fiber)
Cu/Fiber module (6-10 )
Correct light attenuation
Correct sampling ratio change
Correct e/h change
PFA friendly?
plastic scintillator plate/light guide
An Alternative Readout Scheme
All full length fiber
Sampling ratio changes

## Slide 7
0 30 60 90 120 150
15
10
5
0
Depth in calorimeter tower (cm)
Scintillation light arrival time (ns)
Forward particle speed ~ 30 cm/ns
Backward scintillation light speed ~ 17 cm/ns
Light to PMT (ns)
Scintillation light start time (ns)
13.8 ns
5 Gs/s waveform digitization
200 ps ~ 2.2 cm
Effective light speed ~ 11 cm/ns
The meaning and usefulness of timing information needs to be understood

## Slide 8
1 mm
1.5 mm
2.0 mm
1.5 mm
1 mm
2.0 mm
A possible Cu unit
(average ~ 20 cm)
Front
Rear
RD52 coper module (2012)
1 mm
1.5 mm
X0 ~ 2.4 cm
lint ~ 25 cm
Cu~60%
Fiber~ 35%
Air~5%
1.5 mm

## Slide 9
Another RD 52 Dual Readout Calorimeter Cell
1.0 mm
1.0 mm
2.0 mm
Front
1.5 mm
1.0 mm
3.0 mm
Back

## Slide 10
Inner surface area of the calorimeter barrel and two end caps
Readout segmentation
Area to be Covered Determine by
Crude estimation：2 x (65 m2 + 2 x 12.5 m2) = 180 m2
Take
Rin = 2 m
Barrel Length = 5 m
Barrel area
End cap area
2.5 cm x 2.5 cm  288,000 PMTs
5 cm x 5 cm  72,000 PMTs

## Slide 11
25 mm
25 mm
SiPM modules used in TOF-PET
PMT size: 25 mm x 25 mm
Pixel size: 3 mm x 3 mm
or 4 mm x 4 mm
A PET ring typically ~0.2 m2
One CEPC calorimeter 
1000 to 2000 medical PET scanners
SiPMs
For TDR, we do not have time to do prototypes. We need a scheme that is likely to work

## Slide 12
Example of SiPM Modules used in TOF-PET

## Slide 13
MCP-PMT
We believe we can develop and make MCP-PMTs at an affordable cost in China
MCP-PMTs that work in 2 T magnetic field and in all directions may not be possible

## Slide 14
B  2 T
Using MCP-PMT in barrel region is difficult
End caps probably OK

## Slide 15
Go back to KLOE EMCal configuration
Fibers along the barrel
MCP-PMTs at two ends
Will it work in high energy collider?