## Slide 1: 宇宙线热中子探测技术及PRISMA-LHAASO实验介绍
崔树旺 1，陈天禄2，马欣华3，刘茂元3，周荣4，Yuri Stenkin5
1. 河北师范大学，2. 西藏大学，3. 中科院高能物理研究所，
4. 四川大学，5. Institute for nuclear Research, RAS
第十届高能物理分会全国会员代表大会 上海
2018.06.22

## Slide 2: 内容摘要
背景知识
宇宙线热中子探测器工作原理
从PRISMA-YBJ到PRISMA-LHAASO
实验进展与未来计划
丰富的研究内容
总结

## Slide 3: 宇宙线全粒子能谱：膝区

## Slide 4
现有探测结果的典型差异30%，以质子为例：
KASCADE: 拐折在2-3PeV(模型依赖)，尖锐的，模型依赖
ASgamma：拐折在~400TeV，缓慢的

## Slide 5
LHAASO：
KM2A : e,μ
WCDA: e,μ
WFCTA: Č/F
WCDA++: γ family at core →π0
⊕ PRISMA: thermal neutrons →π+π-
→ Full particle measurement of cosmic showers!
→ significant capability of component separation!
Budget of neutron detector array is only 2% of LHAASO.
PRISMA
PRISMA-----PRImary Spectrum Measurement Array

## Slide 6
强子是宇宙线簇射的“骨架”，对成份十分敏感。
簇射中少量的强子与周围环境中的物质（土壤、建筑物、探测器材料、空气等）发生核反应产生大量MeV量级的蒸汽中子，蒸汽中子经过周围环境中的物质的慢化而产生热中子
EAS热中子探测器可以确定EAS芯区强子，比昂贵的强子量能器有更强的规模优势，有更高的性能-价格比。

## Slide 7: EAS热中子探测技术的优势
河北师大、高能所、俄罗斯合作发表的文章 Thermal neutron flux produced by EAS at various altitudes, Yu.V. Stenkin, V.V. Alekseenko, D.M. Gromushkin, LIU Ye ,MA Xin-Hua, ZHAO Jing, Chinese Physics C Vol. 37, No. 1 (2013) 015001
EAS中少量的强子成分能够产生大量的热中子，其数量比强子多2-3个数量级。高海拔要比海平面高1-2个数量级

## Slide 8
Good component separation
Single detector rate ~ 7Hz.

## Slide 10
闪烁体
反射层
reflector
PMT
tank
scintillator 0.4m2
ZnS(Ag)+6LiF
ZnS(Ag)+10B
北京滨松CR165
en-探测器设计

## Slide 11
Neutron capture efficiency with thickness of scintillator by using neutron source Cf252.
→ 50mg/cm2, 22.5%
50mg/cm2
实验室装配探测器单元

## Slide 12: 宇宙线簇射事例：得到电磁成分和中子，包含时序
电磁成分
中子

## Slide 13
探测器电子学系统

## Slide 14
Running time: 2013.11——2017.05
PRISMA-YBJ+ARGO-YBJ：高海拔联合观测
闪烁体采用：ZnS(Ag)+6LiF
“Detection of thermal neutrons with the PRISMA-YBJ array in extensive air showers selected by the ARGO-YBJ experiment”
Astroparticle Physics 81 (2016) 49–60

## Slide 15: PRISMA-LHAASO-16
Detectors are housed against raining.
EAS thermal neutron detection with the PRISMA-LHAASO-16 experiment, 2017 JINST 12 P12028

## Slide 16
FADC: 四川大学
DAQ-50-32
SB
AB
DB
PB
NB
Digital Board
Net Board
Power Board
16
Channels
ADC
ADC
FPGA
FPGA
RJ45
Analog Board
Switch Board
16
Channels
Amplifier
Computer
BNC to SMB
序号 | 名称 | 单位 | 数量 | 规格
1 | 模拟电路 | 块 | 2 | 16路信号输入输入输出
2 | ADC电路 | 块 | 1 | 32路、50MHz、14位ADC
3 | 数据采集电路 | 块 | 1 | 最大数据传输率60Mbits/s
4 | 低压直流电源 | 块 | 1 | 220V AC输入
5 | 仪器机箱 | 个 | 1 | 1U标准机箱
6 | 随机软件 | 套 | 1 | Windows平台

## Slide 17: Specification of detector
Threshold of PMT is 3mV.
50-100 photoelectrons per neutron capture
The efficiency for thermal neutron detection is ~20%.
Pulse shapes of electrons in dynode 8 and dynode 5 are recorded in 500μs after trigger (the 8th bin is trigger time). Time bin width of the first 64 bins are 20ns, and others are 1 μs.
Pulse shapes of neutrons are recorded in 20ms time gate after trigger

## Slide 18: Sp: charged spectrum
PRISMA-LHAASO-16: 2018/05/10-180609
All detectors in all days are stable (D16 is stopped)
Detector 2
180510
180609
阵列运行良好

## Slide 19: Sp
Mean value
RMS
Detector 1
Detector 1
Detector 15
Detector 15
days
days

## Slide 20: Nm
Mean value
RMS
Detector 1
Detector 1
Detector 15
Detector 15
days
days
Raining cover of D2 was blew off

## Slide 21
2017/12/20
event 9623
Core (14.8m,6.4m)
Zen. 43.0°
Azi.-77.5°
d8信号幅度(mV)
d5信号幅度(mV)
到达时间(ns)
中子数
Too few neutrons on the roof

## Slide 22
计划进行中
 | PRISMA-LHAASO-16 | PRISMA-LHAASO-64 | PRISMA-LHAASO-400
detectors | 4×4=16 | 8×8=64 | 20×20=400
clusters | 1 | 4 | 25
Array Area(m2) | 15×15=225 | 35×35=1225 | 95×95=9025
Trigger rate (2-fold) (Hz) | 0.14 | 0.56 | 3.5
Data (GB/day) (trigger + scaler) | 0.036+0.0002=0.0362 | 0.144+0.0008=0.1448 | 0.9+0.005=0.905

## Slide 23
16 en-detectors in cluster,
25 clusters,
400 en-detectors
100m
5m
探测器单元
4” PMT CR165 (Beijing Hamamtsu)
100m
Boron scintillator
ZnS(Ag)+B2O3
16个探测器1个CLUSER(2016)
64个探测器4个CLUSER(2017-2018)——目标
未来目标PRISMA-LHAASO
建设400个探测器构成的10000平米阵列(20？？)

## Slide 24
64个探测器装配调试正在进行中。。。
河北师范大学 热中子探测器实验室

## Slide 25
大气物理：暴风雨，rain – yes, lightning - no
Summary: no any neutron excess during thunderstorms but instead sometimes we see
decrease of neutron flux
可开展的相关物理研究

## Slide 26: 地球物理：lunar tidal effect
在独立运行的1年半中测到了热中子周期性变化←日月地系统引力引起地壳变形的潮汐效应。发表SCI文章 Pure Appl. Geophys. 174 (2017) 2763–2771。
如此微弱的效应都能测到，说明这种探测器可用来监测地壳突发变化。
周周期
月周期
full moon
New moon

## Slide 27: 地球物理：地震活动
Abnormal behavior of neutron flux on 2, May 2004
Local North Caucasus seismic activity and full Moon
BAKSAN
V.V.Alekseenko et al. Tidal effect in the radon-due neutron flux from the Earth’s crust. J. of Physics: Conference Series. 203, 012045 (2010)

## Slide 28: 太阳物理
the solar maximum was ~ 4 years ago. in these 2.5 years, solar activity becomes weaker to cause cosmic ray flux and then neutron flux increasing.
Long-Term Variations in the Natural Thermal Neutron Flux at 4300 m above Sea Level， Bulletin of the Russian Academy of Sciences: Physics, 2017, Vol. 81, No. 2, pp. 160–161.

## Slide 29
太阳物理：Forbush 下降
One Forbush decrease on March 8, 2012 detected by (from top to bottom) (1) Moscow neutron monitor, (2) Gran Sasso (Italy), (3) MEPhI (Moscow Engineering Physics Institute) and (4) Obninsk (Moscow).
V. Alekseenko, et al. Registration of Forbush decrease 2012/03/08 with a global net of the thermal neutron scintillation en-detectors. Journal of Physics:Conference Series 409 (2013) 012190

## Slide 30: 总结： 1.EAS热中子探测技术方案作为LHAASO实验新技术研发和拓展正在不断完善和成熟 2.希望在科学家和各基金部门的认可、帮助和大力支持下推进项目规模化发展。
谢谢！