## Slide 1: The STAR Event Plane Detector Upgrade
Ming SHAO
USTC
Physics Motivation
EPD Design
Construction/Commission/Performance
Summary

## Slide 2
RHIC Beam Energy Scan
Key measurements and goals:
Location of critical point and first order phase transition
Notes: Explain QCD phase diagram first, then fly in the RHIC beam energy scan project (STAR), and shrink the QCD phase diagram into the bottom-right corner.

## Slide 3: Collision Geometry and Physics
Some examples:
polarization
fluctuation analyses
flow measures & correlations
high sensitivity to collision geometry selection
  physics?
  volume fluctuations?
  auto-correlations?
  want a separate reference, an unit of rapidity away!
STAR PRL 2014
  STAR Nature 2017
STAR PRL 2014
Reaction
plane
x
z
y

## Slide 4: EPD Location
EPD
EPD
The EPD will allow us to measure the centrality and event plane with high precision!

## Slide 5: EPD vs BBC
EPD – 372 tiles
16 eta segments
24 phi segments (12 at highest eta)
BBC – 36 tiles but only 18 inner tiles used
has served STAR extremely well so far
BBC inner:
18 tiles
1 BBC tile ~ 5-7 EPD tiles
快度覆盖增加1倍
通道数增加10倍
本底抑制提升10倍
触发能力提高100倍

## Slide 6: Timeline
2013 – R&D proposal submitted
2014 – R&D (LBNL)
2015
  Pre-prototype (EEMC tiles + FPS electronics) run in STAR
  Prototype construction
2016
  Prototype run in STAR (behind BBC)
  Construction proposal of 1/8 EPD approved
  Analysis of 2016 data
  Install 1/8 EPD in STAR behind BBC
2017
  Commissioning run in STAR of 1/8 EPD behind BBC
  Full EPD construction proposal approved
  Analysis of 2017 data
  completion of EPD & installation at STAR
2018
  Commissioning run in STAR of full EPD
  Analysis of 2018 data
beyond 2018
– EPD as trigger and physics detector

## Slide 7: Design 2017 (final)
2 Wheels of 12 supersectors with 31 optically-isolated tiles
  1.2-cm-thick scintillator
  3 turns of Wavelength shifting (WLS) fiber
Total of 12x31x2=744 channels
  Optical signal transported 5.5 m on clear fiber
  Coupled to SiPM
Read out by STAR electronics
Custom-built connector components
  3D-printed

## Slide 8: Machining
CNC milling high volume water/oil for cooling, debris
50”x20” mill platform @OSU

## Slide 9: Rear isolation grooves
Mill “half-way” and fill groves with TiO2 + epoxy mixture
Mill another “half-way” and fill groves again
Optical isolation!

## Slide 10: Front WLS grooves
WSL fibers glued in with optical glue
Front isolation grooves glued with reflexive epoxy
Notes: SolidWorks ramp design

## Slide 11: Front isolation grooves

## Slide 12: Wrapping
One layer of Tyvek (for reflectivity) & 2 layers of thick black paper (for light tightness)

## Slide 13: Fiber connectors
Connected to 5 meters of clear fiber with 3D-printed custom connectors – WLS attenuation is too high
Fibers must be polished for optimal coupling

## Slide 14: 5.5-m-long Clear fiber bundles
All connector components custom-designed and 3D printed
Fiber-to-SiPM

## Slide 15: Fiber-SiPM coupling
Fiber-to-SiPMconnector (FSC)

## Slide 16: Clear fiber bundle meets readout electronics
EPD SiPM card
EPD FSC spacer block (3D printed)
Edge connector plugs
into EPD FEE card
SiPM assembly monitored by micrometer

## Slide 17: Coupling to FEE
Far end of optical bundles
contact (air gap) connection to SiPMs
16-channel FEE
~ 2 inches

## Slide 18
Rx and QT boards cabled and mapped
FEE  RX  QT  STAR DAQ
Digital signals
EPD FEEs designed by G. Visser (IU)
Dedicated for SiPM
Excellent resolution and linearity
Test stand set up at OSU and BNL
Key performance verified by cosmic-ray test

## Slide 19: Mechanical: Super-Sector mount
BBC
pEPD
2016
2017
2018

## Slide 20: Hit/No-hit
All 93 channels show good signals
Very nice uniformity
p+p 500 GeV (2017)
We have been blind here, until now
η
Φ

## Slide 21: Correlation with Other detectors
TOF (|η|<1)
EPD (<2η<5)

## Slide 22
EPD - ADC Spectra
Extremely uniform performance across all 744 channels
1MIP
2MIP
3MIP
4MIP
200 GeV RuRu + ZrZr

## Slide 23
EPD – Timing performance
Difference between offline z_Vertex reconstructed by TPC and EPD.
The spatial resolution of EPD is 11.8cm, corresponding to ~0.4ns time resolution.
ADC vs TDC for 1 tile
Average TDC east vs west
200 GeV RuRu + ZrZr

## Slide 24
Forward Event Plane Determination
Basic analysis methods tested on isobar data
The EPD is a significant improvement on the BBC

## Slide 25
Centrality Determination
The spectators and produced particles have opposite correlations, they have
characteristically different rapidity ranges
By weighting the multiplicitl of the 16 rings of EPD tiles differently
No models describe forward rapidity well, instead use neural network (NN)
The improvement must be done on an energy-by-energy basis
only 1/8 EPD (η>0, 3π/2 < φ < 2π)

## Slide 26: Summary
Granular coverage at 2<|η|<5 crucial to BES-II physics mission
  opens up phasespace & reduces centrality-related systematics for fluctuation analyses
  improved EP resolution allows statistical reach of EP-dependent studies (flow, polarization, CME, ...)
  new flow-correlation analyses over wide eta range
EPD upgrade
  highly segmented detector of straightforward design, with some new aspects
  two prototype runs (2015, 2016) & 1/8 “engineering” run in 2017
  Full EPD “commissioning” run in 2018
Performance
  744/744 tiles: response understood, very uniform response
  operates well under conditions exceeding design requirements
  physics results anticipated from “commissioning” run
  radiation damage acceptable
EPD analysis underway
  Ready for 2018+ (BES-II) trigger and physics

## Slide 27: People
LBNL: SS design, R&D, early production
SSL: Trigger/RDO electronics & algorithms
Ohio State: SS construction, design, FEE mechanics, testing, coordination
Lehigh U: Fiber bundles, online QA
Indiana U: Front-end electronics design
BNL: Electronics, mechanical, DAQ
USTC: Electronics production and testing; SS construction & testing
Kent State: Simulations
Tsukuba: Simulations, and....
Fudan U: SS construction, online QA
NCKU: SS construction & testing
Thank you !

## Slide 28: Backup slides

## Slide 29: SiPM radiation damage in high-luminosity pp
beam on (“light current”)
beam off (“dark current”)
Vbias changes
present Id~ 1 μA
we are okay if Id < ~15 μA
SiPMs good for equivalent of
12 more pp runs ✓
(H.I. running much less radiation)