## Slide 1: Status of CEPC HCAL CDR
Tao Hu, Jianbei Liu, Haijun Yang, Boxiang Yu
For the CEPC-Calo Group
CEPC CDR Mini-Review
November 11, 2017

## Slide 2: Requirements for CEPC Detector Design
Critical Physics Benchmarks for CEPC Detectors design.
Goal: Jet Energy Resolution 3 – 4 % or 30% / √E @ 100GeV
based on Particle Flow Algorithm (PFA)

## Slide 3: Calorimeter Options
ECAL with Silicon and Tungsten (LLR, France)
ECAL with Scintillator+SiPM and Tungsten (IHEP + USTC)
SDHCAL with RPC and Stainless Steel (SJTU + IPNL, France)
HCAL with ThGEM/GEM and Stainless Steel (IHEP + UCAS + USTC)
AHCAL with Scintillator+SiPM and Stainless Steel (IHEP+U.Mainz+BNU)
Dual readout calorimeters (INFN, Italy)
https://twiki.cern.ch/twiki/bin/view/CALICE/CalicePapers

## Slide 4: Outline of CEPC Calorimeters CDR

## Slide 5
DHCAL with RPC
The SDHCAL-GRPC is one of the two HCAL options based on PFA and proposed for ILD. Modules are made of 48 RPC chambers (6λI), equipped with semi-digital, Hardroc2 readout and placed in self-supporting mechanical structure (stainless steel) to serve as absorber.
Cell size: 1x1 cm2
 Substantial improvement for beam energy >  40 GeV

## Slide 6
6
Assembling procedure
6mm(active area) + 5mm(steel) =
11 mm thickness
PCB support (polycarbonate)
PCB (1.2mm)+ASICs(1.7 mm)
Mylar layer (50μ)
Readout ASIC
(Hardroc2, 1.6mm)
PCB interconnect
Readout pads
(1cm x 1cm)
Mylar (175μ)
Glass fiber frame (≈1.2mm)
Cathode glass (1.1mm)
+ resistive coating
Anode glass (0.7mm)
+ resistive coating
Ceramic ball spacer (1.2mm)
Gas gap
Large area gRPC:
Negligible dead zone
(tiny ceramic spacers)
Large size: 1  1 m2
Cost effective
Efficient gas distribution system
Homogenous resistive coating
Schematic of RPC
Notes: 6

## Slide 7
Assembling procedure
6mm(active area) + 5mm(steel) =
11 mm thickness
4.7 mm
4.3mm
ASICs : HARDROC2
64 channels
Trigger less mode
Memory depth : 127 events
3 thresholds
(115fC, 5pC, 15pC)
Range: 10 fC-15 pC
Gain correction  uniformity
Readout Electronics for RPC
Printed Circuit Boards (PCB) were designed to reduce the cross-talk with 8-layer structure and buried vias.
Tiny connectors were used to connect the PCB two by two so the 24X2 ASICs are daisy-chained. 11m2 has 6 PCBs and 9216 pads.
DAQ board (DIF) was developed to transmit fast commands and data to/from ASICs.
Notes: 7

## Slide 8
Energy Resolution vs No. of Layers
SDHCAL has 48 layers which
aims for ILC Detector
6mm gRPC + 20mm absorber
Optimization no. of layers for CEPC at 240GeV
40-layer SDHCAL yields decent
energy resolution.

## Slide 10
DHCAL based on THGEM

## Slide 11
Analog Hadronic Calorimeter
- 32 super modules
- 40 layers per module
Active layer 4-5mm
Absorber 20mm
Total thickness 100cm

## Slide 12
Analog Hadronic Calorimeter

## Slide 13
Analog Hadronic Calorimeter

## Slide 14: Join the CALICE Collaboration
THU and SJTU joined the CALICE Collaboration
Collaborating with Imad Laktineh (IPNL) on SDHCAL R&D.
We have a joint Ph.D student via CSC program (2years). CAN-059 about using BDT to improve pi/e/mu separation is under review process.
SJTU will host the CALICE collaboration meeting on Sept. 19-21, 2018. https://agenda.linearcollider.org/event/7799/
IHEP and USTC plan to join the CALICE to work on ScW ECAL and AHCAL.
IHEP/USTC/SJTU received MOST grant (2017-2021) for CEPC Calo R&D, we are currently applying for MOST funding (2018-2022) to build HCAL prototype based on Scintillator + SiPM.

## Slide 15: Some open issues
Performance from SiW-ECAL and SDHCAL combined TB (2017.9)
Optimization of cell size/layers for CEPC to reduce channels/power
Cooling system, water vs CO2 cooling? Design of low power ASIC, FEE.
For SDHCAL-RPC, plan to build larger RPC (1x3m2), new gas circulation system, new electronics (HARDROC3), additional timing info? (MRPC).
For AHCAL based on Scintillator+SiPM, we plan to build a prototype in next 5 years. How to collaborate within CALICE collaboration.
Temperature distribution in an active layer of the SDHCAL operated with no power-pulsing.
The cooling system is made of a circulating water inside copper tubes in contact with the
ASICs. DT ~ 2.6 degrees

## Slide 16
Dual-readout Calorimeter
The independent sampling of hadronic showers, through scintillator and Cerenkov light
Emission, allows to fully reconstruct energy and fem on event-by-event basis.

## Slide 20: Backup Slides

## Slide 21: SiPM light output
Photon detection efficiency of 10um SiPM is about
23% photon detection efficiency from the 25um SiPM
Light output of 45mm strip coupled with 10um SiPM
Pulse height spectrum
SiPM type No.: S12571-010C

## Slide 22: PFA and Imaging Calorimeter
Simulation of W, Z reconstructed masses in hadronic mode.
60%/E
30%/E