## Slide 1: New Ideas about Calorimetry
Chris Tully
(Princeton University)
November 12-14, 2018
Institute of High Energy Physics, Beijing, China
Low Mass Gas Tracking
High Resolution Calorimetry
Full Silicon Tracker
High Granularity Calorimeter
Notes: It’s an honor for me to be here today and to be able to share some ideas I have with my old colleagues. I became fascinated five years ago with the suggestion – I believe
from Yifang – of building a collider that encircled a city. And I hope that vision becomes a reality.

## Slide 2: Balancing Jets and EM particle resolutions
For HZ production, all Z recoils matter
  ~70% of Z decay are hadronic
Particle Flow Principle
  Optimal use of measurement information applied to each reconstructed particle
    Charged hadrons (~65%)
      Replaced by track (~0.1%)
    Neutral hadron (~10%)
      HCAL (~45%/√E)
    Photons/EM (~25%)
      ECAL (~15%/√E)
Z Jets ~ 3.5 - 5.5% (Limited by HCAL & EM)
~4.5%/√E
~3.8%/√E

## Slide 3: Electron should be done well at e+e- Collider
Muons
Electrons
Not yet there w/ CDR reference design
(needs Brem. recovery w/ EM res.)
~2-4%*15%/√E  ~0.3-0.6%
From track

## Slide 4: Three Regimes of EM Resolution
For EM showers in a sampling calorimeter, the energy resolution is dominated by the sampling fluctuations:
(sE /E)EM *√E [%]
(Courtesy of R. Wigmans)
* Si-W (300mm - HGC)
* Si-W (100mm - HGC)
Homogeneous crystals
Silicon
Plastic/Quartz
Fiber
Segmented
Crystal?
X0(Si)/X0(W)=27

## Slide 5: Imaging Capabilities of High Granularity
CO2 (-35 C)
Fluctuations driven by counting statistics
(one event can look like many)

## Slide 6: Small Crystal Geometries for Timing Detectors
Tiles and Bars (few mm thick w/ area of ~1cm2)
  Single layer ~500,000 channels
  Stereo readout for bars (L/R) ~25ps timing resolution
Fully segmented crystal EM calorimeter:
Low occupancy timing layer timing for ~1 X0
Transverse orientation w/ stereo readout
Ultra-high EM resolution (~5%/√E)
Pointing geometry (fine transverse granularity)
5-10cm bars of ~1cm2 area for ~20 X0
Yuexin Wang (poster)
Still w/ PFA capabilities? Or with S/C crystal fibers?
3x3x50mm3
3x10x10mm3

## Slide 7: CMS MTD Tray Assembly (Concept)

## Slide 8: Silicon Photomultiplier (SiPM) Cells
Typical dynamic range customization for SiPM
  More (small) SPADS to count more photons (5015μm)
  Bright crystal (LYSO, GAGG) and high photodetection efficiency (PDE) and light collection efficiency (LCE)
Currently:
Large device ~6x6mm2
CMS MTD ~4.5 m2 of SiPMs
(of 3x3mm2)
Segmented Crystal ECAL:
~200 m2 of crystal surface
(3-4 layers)
Which SiPM device?
Notes: One of the technical challenges of precision timing with crystals is to maximize the photon flux. One doesn’t wait for the exponential decay of the light from a signal, we
care only about the step function of light flux relative to the dark count rate – and apply thresholds within the first 20 pe recorded by our photodetectors. That imposes
a minimum flux rate for the timing precision and beyond having bright crystals we have to be clever and efficient about how we collect light.
These are views of the micro-structure of SiPMs for different features sizes and one of the features of these detectors is that each individual SPAD needs it’s own bias
line and quench resistor and that blocks photosensitivity.

## Slide 9: Large Area Light Collection Techniques
Winston Cone is a light collector in the shape of an off-axis parabola of revolution with a reflective inner surface.
SiPM: Each SPAD (15μm x 15μm)
Optical image: 100X

## Slide 10: Winston Cone on each SPAD
SiPM PDE micro-scanner
(15 micron)
TIFR Group
S. Dugad
Increase Photo Detection Efficiency by adding a metalized mini Winston Cones on top of SiPM array.

## Slide 11: Fabrication Process
1.Heidelberg greyscale Photolithography Writing
  By BMP and DXF flies
2. Transfer Winston cones pattern to PDMS
  Spin coat PDMS first time (20um)
  Dissolve photoresist
  Transfer on glass carrier slides
  Cr metal coating as a sacrificial layer
  Spin coat PDMS second time
  Transfer on a Si or glass substrate
3. Deposit the Al reflective metal layer on Winston cones structures by Sputter
4. Laser dicing tool to drill holes in the bottom center of Winston cone to create opening windows for SiPM
5. Transfer on target substrates
6. Fill the Winston cones by Parylene (reflective index 1.65-1.7)
12um<L(Top)<15um
Si
Photoresist
Spin coat PDMS
Cr metal deposition
spin coat PDMS
PDMS
Glass
Glass
Dissolve photoresist
Al deposition
Laser drill windows
Transfer on targets
Fill Parylene
Target
Target
Glass
Step 1
Step 2
Step 3
Step 4
Step 5

## Slide 12
Greyscale Writing
BMP image
DXF greyalue file
Greyscale writing:
SEM of grayscale writing

## Slide 13: SEM images of Greyscale Writing
Greyscale writing tests by different laser parameters: Intensity, Filter and Focus
SEM 1
SEM 2
Top View
View of the stage tilted 60o
Cross-section View

## Slide 14: SEM images with n-over20 writing
Tilt 45o
Tilt 45o

## Slide 15: Dynamic Range and Packing Density
Large pixel count w/ large gain leads to current output limitations for large area devices
  Multiple analog outputs per device
    Regional lumped analog sums - split output currents per region and sum (1/128, 1/32,1/8,1/2)
    Multi-gain SPADs (5, 15, 50μm) for different cell sizes and fill factors – dynamic range built into SPAD layout
  On-chip ADC with regional serializers
  Commercial market for LIDAR advances is growing rapidly – many new developments expected
Notes: Technological development – when involving timing impacts
LIDAR
and TOFPET medical imaging

## Slide 16: New Advances in SiPMs (included in CDR)
EQR-SiPM from Novel Device Laboratory (NDL, China)
  Possibilities to further develop new structures for CEPC
Backside Illumination (LFoundry subs. SMIC)
  Higher PDE
  Integrated CMOS on back of each SPAD
  Adjustable fill-factor

## Slide 17: Front-end Engineering
~6 M channels w/ CO2 cooling and highly granular total absorption technology w/ precision timing (sampling fraction O(1))
  Example layout
High
Resolution
w/
4D Granular
DATA
Front
Timing Layer

## Slide 18: EM Resolution and Photon Counting
EM Resolution also improves angular measurements and resolves N𝛄 counting
Recoil photons (~8% of full √s collision rate)
    New Physics Searches and Neutrino Counting
Improved Syst.
(A. Blondel)
E. Bartos et al., “2γ and 3γ annihilation as calibration processes for high energy e+e− colliders,”
https://arxiv.org/abs/0801.1592

## Slide 19: Future
Future is in our hands
  Assess the physics performance goals
    Z Jet resolution not limited by EM resolution
    Ze+e- recoil resolution w/ Brem. recovery methods
    Counting statistics for PFA shower separation
    Photon counting with high fidelity/angular resolution
  SiPM development with vendors is an active area
    Large area photodetection methods
    High dynamic range for calorimeters
    Dedicated front timing layers
  Applications across particle physics and beyond