## Slide 1: Progress and plans, Mechanics system of CEPC
Haijing Wang
On behalf of mechanics group
November 12-14, 2018, IHEP
The 2018 International Workshop on High Energy circular Electron Positron Collider

## Slide 2: outline
Progress and Plans
  Regular supports
  Transport vehicles
  Equipment layout
  Support system of MDI
  Movable collimators
Summary

## Slide 3: Regular supports
CEPC is composed by the double ring Collider, the Booster, the Linac and Transport lines.
Over 80% of the length is covered by magnets of about 138 types, each magnet needs to be supported.
Accelerating tubes, vacuum tubes, instruments…, all need supports.
Aims
  Simple & flexible structure: plates or standard elements
  Small deformation & good stability: multi-point support, optimization
  Low cost: concrete or steel frames, adjusted manually

## Slide 4: Regular supports
Booster
Collider
Adjusting methods
  Bolts & push-pull bolts
  simple and low cost
  Adjusting ranges
Support method
  Magnets in Collider, Linac, Damping Ring: supported to the ground by concrete.
  Magnets in Booster: hanged on the wall of the tunnel by steel frame
  Magnets in Transport Line: due to the location of the magnet
Range of adjustment |  |  | 
X | ≥±20 mm | Δθx | ≥±10 mrad
Y | ≥±30 mm | Δθy | ≥±10 mrad
Z | ≥±20 mm | Δθz | ≥±10 mrad

## Slide 5: Magnet supports
Mounting plate
Adjusting mechanism
Pedestal
or steel frame
Main support
Auxiliary support
Supports for dipoles
  Four supporting points: Response Surface design & Theoretical calculation using MATLAB for the distribution.
  Main support: 6 DOFs; Auxiliary support: 1 DOFs.

## Slide 6: Magnet supports
Supports in Booster
  Magnets in Booster: 2.4 meters above the Collider
  Topology optimization is used
    Aim: minimum degree of flexibility (best static stability)
    Steel frame is designed vertical due to the results

## Slide 7: Magnet supports
图需换
Dipole in Collider and its support：
4 support points，5670mm
Quadrupole in Collider and its support：
2 support points，2000mm
Sextupole in Collider and its support：
2 support points，1400mm

## Slide 8: Magnet supports
Dipole in Booster and its support：
4 support points，5445mm
Quadrupole in Booster and its support：
2 support points，940 mm
Accelerating tube in Linac and its support:
2 support points，3000 mm

## Slide 9: Transport vehicles
Two types of vehicles
  One for “long” magnets and the other for “short” magnets.
  Transport, adjustment (horizontal and vertical)
  Uneven ground is considered.

## Slide 10: Equipment layout
Arc section layout: 2D and 3D model

## Slide 11: Equipment layout
Primary design of tunnel mockup (Arc section)
  Interface checking of the equipment placement, installation, alignment and transportation.
Booster dipole magnet and their supports
Collider dipole magnet and their supports
Equipment for SPPC
Air duct

## Slide 12: Equipment layout
Linac: 3D Model assembly of different accelerating tubes, wave guides, bunchers…

## Slide 13: Equipment layout
Draft layout design at MDI
Scheme 1: small yoke
Scheme 2: big yoke
Yoke
Solenoid in detector
IP
SC magnets in Accelerator
Support system

## Slide 14: Support system of MDI
Adjustment mechanism: push-pull bolts for horizontal, wedge jacks for vertical.
Movement mechanism: tracks & screw rod for baseline, tracks & pinions also under consideration.
SC magnets
Support for SC magnets
Adjustment mechanism
Movement mechanism
Pedestal
Tracks & pinions from HepcoMotion

## Slide 15: Support system of MDI
TDR plan
  Design the structure for SC magnets support and adjustment scheme.
  Design the long distance movement mechanism with high precision.
  Do the FEA and structure optimization, especially for the natural frequency and displacement, to meet the physical requirement.
  Design the assembly process of relative devices at MDI.
  Fabrication and test.

## Slide 16: Movable collimators
Collimator of PEPII
Collimator of SKEKB
Collimator of LEP
Sketch of movable collimator of CEPC
Two types of collimators.
  Movable and fixed. TDR stage mainly focus on movable collimators.

## Slide 17: Movable collimators
TDR plans:
  Design the collimators with simple and flexible structure.
  Design the inner section of the collimator according to the physical requirements. Optimize the profile to obtain low impedance.
  Calculate the thermal and mechanical stress and optimize the structure and materials to improve performance.
  Fabrication and test.

## Slide 18: Summary
Primary design of supports for typical magnets and accelerating tubes have been done, and is on-going for other devices and refining. The primary 3D model layout has been done for some typical equipment, and will be updated according to the design progress.
The in-depth study for support system of MDI and movable collimators will be done in the future.

## Slide 19: Thanks for your attention!