## Slide 1: Division of Nuclear Technology and Applications
WEI Long
Institute of High Energy Physics
Jun. 14 , 2018
International assessment of 2018

## Slide 2: Contents
1
2
Overview of DNTA
Research of DNTA
3
Future plan
4
Summary

## Slide 3: Contents
1
Overview of DNTA
  Mission
  Manpower
  Project & budget
  Laboratory

## Slide 4: About DNTA
Mission of DNTA (Division of Nuclear Technology & Applications )
The former "High-tech Research and Development Center" was established in 2002
Restructured to form " Division of Nuclear Technology and Applications " (DNTA) in 2012
DNTA is an application-oriented, non-profit R&D affiliation of IHEP, aiming at instrumentation, product development and technology transfer.
Research areas include (currently)
  Medical imaging technology
  X-ray inspection technology
  Nuclear safety monitoring technology
  (former industrial accelerator)
Historic note:

## Slide 5: Mission of DNTA
Reviewers’ Recommendation (2013):
“The Committee supports this concept and direction, and recommends that IHEP consider strengthen the institute-level Office for Technology Transfer and Management to provide legal and business expertise to assist the scientific staff to pursue technology transfer and commercialization.”
Response to Reviewers’ Recommendation:
To achieve the objective, DNTA must work in close cooperation with other research divisions, the Office for Technology Transfer and Management and the downstream company.

## Slide 6: Manpower
Staff: 58
Postdoctoral : 2
Postgraduate: 25
Postgraduate from Universities: 16
Others: 4
Total: 105
Chart: Age Structure
| ＞50 | 40-50 | 30-40 | ＜30
 | 4 | 8 | 41 | 5
Chart: Turnover of Personnel
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
STAFF | 60 | 64 | 66 | 65 | 64 | 58
FLOAT IN | 5 | 7 | 7 | 3 | 2 | 1
FLOAT OUT | 3 | 1 | 5 | 3 | 5 | 4
Notes: 人员比较稳定，满足项目需求

## Slide 7: Manpower
Chart: Educational background
| DOCTOR | MASTER | COLLEGE&BELOW
 | 37 | 16 | 5
Chart: Title distribution
| Professors | Associate Professors | Assistant Professors | Administrative Staff
人数 | 6 | 33 | 18 | 1
比例 | 0.10345 | 0.56897 | 0.31034 | 0.017241
Chart: 
| Linac | Instrumentation | Eletronics | Software engineering | Detector | Molecular imaging | Molecular probe | Irradiation application
 | 5 | 13 | 11 | 7 | 13 | 3 | 3 | 2
Major structure
We have a solid team for our work (85% working on instrumentation).
We are taking age advantage now and in next 5-10 years (over 95% under 50 years old).

## Slide 8: Manpower
Long Wei
(Nuclear imaging)
Rongjian Shi
(Accelerator)
Cunfeng Wei
(X-ray imaging)
Yu Liu
(nuclear chemistry)
Baoci Shan
(Molecular Imaging)
Zhiming Zhang
(Nuclear detecting )
Academic leaders
Notes: 1、人数
2、项目及经费 大多在仪器研制

## Slide 9: Project & budget
NSFC grants > 20
State key R&D program, MoST ×2
Key deployment project, CAS
Main project for scientific instruments, CAS ×9
International cooperation project, CAS
Funds from company or organization, 12 M RMB(¥)
Chart: FUNDS (MILLION ¥)
| 2013 | 2014 | 2015 | 2016 | 2017
 | 24 | 32.8 | 38.1 | 23.5 | 21.1
Chart: FUNDS/MANPOWER (MILLION ¥)
| 2013 | 2014 | 2015 | 2016 | 2017
 | 0.375 | 0.49697 | 0.58615 | 0.36719 | 0.36379
2013-2017 Total funds > 142 M RMB (¥)

## Slide 10: Budget structure
Chart: 
| competitive funds | noncompetitive funds
 | 0.9 | 0.1
Noncompetitive Funds 13%
Competitive Funds 87%
8.4% from company
91.6% from government
About 90% funds from government & 88% of all budget are competitive.
DNTA has the capability to compete for projects nation widely.

## Slide 11: Laboratory
Qualification and the infrastructure meet the needs for nuclear technology.
Having usage permissions of isotopes, X-ray tubes, neutron source and other radiation devices.

## Slide 12: Publications & patents
Over 60 papers were published within 5 years as primary organization.
Many papers were published in IEEE serials and in RSI recently.
Encourage researchers to participate in IP training, and to promote and protect
intellectual property.
For many years, DNTA ranked the No.1 contributors of new applied patents and granted invention patents (~about 32% of the total granted to IHEP).
Plan: 50-60 new patents in next 5 years
Category | Applied/ pending | Granted
Invention patent | 54 | 57
Petty patent | 5 | 4
Registration of Computer Software Copyright | 17 | 17
Registration License | 1 | 1
Total | 77 | 79
Chart: Issued patents in 2015
| DNTA | MDRD | EPD | PAD | AD
系列 1 | 16 | 13 | 7 | 5 | 3
列2
列1
Summary of IP (2013-2017)

## Slide 13: Contents
2
Research of DNTA
Medical imaging technology
X-ray inspection technology
Nuclear safety monitoring technology

## Slide 14: Medical imaging Systems
2005
PEM prototype
2011
2012
2018
2017
2015
Before 2013
2013~2018
2008
Micro-PET
Micro-PET/CT
Breast CT
MBI system
Primates animal
PET
Clinical trials
of PEM
2012
2015
CFDA registration
of PEM
Breast spectral CT

## Slide 15: PET for Breast Cancer Diagnosis (Positron emission mammography - PEM)
  Close-proximity breast imaging to:
  Improve spatial resolution
  Improve photon detection efficiency (sensitivity)
  Lower the examination dose
  Early detection of tumor & tumor characterization
Characteristics of PEMi System:
Ring detector design and uncompressed breast imaging suited to oriental female
The prone position makes stable imaging quality
Real 3D imaging
Notes: The most important part is the design of ring detector with long axis gives real tree-dimensional imaging.

## Slide 16: Performance of PEM systems
IHEP PEMi
David F.C. Hsu, David L. Freese, and Craig S. Levin,
THE JOURNAL OF NUCLEAR MEDICINE
Vol. 57 • No. 2 • February 2016
18 institutions to develop PEM system worldwide.

## Slide 17: Performance of PEM systems
David F.C. Hsu, David L. Freese, and Craig S. Levin, THE JOURNAL OF NUCLEAR MEDICINE • Vol. 57 • No. 2 • February 2016
Note: usually the iterative reconstruction gives better value comparing with FBP.
Notes: PEMi achieved quite good performance, compared with other systems.

## Slide 18: Performance of PEM system
 | PEMi by IHEP | Product A | Product B | Product C
Performance | Resolution 1.38mm sensitivity 6.88% | Resolution 1.4mm sensitivity 2.5% | Resolution 1.6mm Sensitivity 6.9% | Resolution 2mm sensitivity ~0.5%
Scanning method | Prone, free-hand | Prone, free-hand | Prone, free-hand | breast compression
Scanning beds | One bed | Multi-bed or image-merging | One bed | Multi-bed or image-merging
Speed | Fast (~5min.) | fair | fast | fair
Table：Summary of commercialized PEM systems
Notes: 李琳：Now only four commercialized PEM systems.

## Slide 19: Technology transfer of PEMi
“Gao Neng Medical Co., Ltd.”
Long Wei, PhD., Prof.
“New Century National Hundred, Thousand and Ten Thousand Talent Project” in 2009
“Science Beijing One Hundred Leading Talents Cultivation Project” in 2013
Zhiming Zhang, PhD., Prof.
He has led the development of animal PET, animal PET/CT. Working on scintillation detectors.
Long Wei and Zhiming Zhang led the “863 Hi-tech project” of MoST to develop the proto-type of PEM scanner.
The technology of PEM transferred to the company “Gao Neng Medical Co., Ltd.”
is a spin-off company of IHEP. It has place in Z-park (Beijing) for incubation and factory in Hangzhou for manufacture.

## Slide 20: Clinical Applications of PEMi
Clinical applications in physical examination center
began to build 3 image centers for physical examination in Beijing, Jiangsu and Hebei.
They provided total solution for all the image centers, based on specific requirement.
More installations are expected this year.

## Slide 21: Ongoing project: Design of new MBI system
Technology developed：
  SiPM based planar detector for 511 keV (18F agent) and 140 keV gamma rays (99mTc agent)
  64chs high speed DAQ system with precise TDC embedded in FPGA
  Reconstruction algorithm based on single gamma response (SGR) can reduce the DOI effect & data missing artefacts effectively.
Molecular breast imaging (MBI) system:
  Multi-modality: PET & Gamma Camera imaging
  Multi location: breast、axilla、thyroid、legs
  Large FOV： 150mm × 200mm
  High spatial resolution: better than 2mm
  High sensitivity: better than 10%
Xianchao Huang
PhD, Assoc. Prof.
SiPM based detector

## Slide 22: System Performance of MBI

## Slide 23
Spectral imaging technology for high contrast and low dose
the image is true 3D & isotropic.
K-edge imaging technology enhances tumor detectability
Prone position, comfortable and safe
  A State-key R&D project to develop multi-energy CT imaging techniques based on energy-resolved photon counting detector and provide an effective tool for early diagnosis, qualitative analysis, and quantitative evaluation of breast cancer.
Mammography
Ongoing project: Breast Dedicated Spectral CT
Zhe Wang
PhD
Assoc. Prof.
CT technology
Notes: Spectral CT has many merits:
the Spectral imaging technology gives high resolution and high contrast with low dose
…

## Slide 24: Contents
2
Research of DNTA
Medical imaging technology
X-ray inspection technology
Nuclear safety monitoring technology

## Slide 25: Developed X-ray imaging Systems
2006
130 keV Micro-CT
2010
2012
2014
2016
2017
2018
2015
Before 2013
2013~2018
2008
450 keV & 6 MeV CT
Dedicated fossil-CT
Mobile micro-CT
Spiral CT
Micro-CL
9 MeV CT
CL for IC testing
Rock mechanics CT

## Slide 26: CT for Rock Mechanics Testing
Formation & evolution of fracture of rock
Gas-liquid motion pattern of rock
Variation of rock properties
Observing the cracks of rock under pressure and high temperature (~5km deep)
A State-Key Scientific Instrument and Equipment R&D Project of NFSC
Rongjian Shi
Prof., Co-PI of the project.
Developed 6MeV, 9MeV standing wave linacs for high-energy X-ray sources.
Notes: 26
This system integrated a high energy CT system and a presses, which can heat the rock and provide confining and axial pressure.

## Slide 27: CT for Rock Mechanics Testing
6 MeV high-energy X-ray CT based on accelerator & 450 keV GP X-ray CT
for end-user: The Institute of Geology and Geophysics, CAS
Notes: The preliminary results of experiment. The 3D CT images show the crack propagation process of a rock under confining and axial pressure.

## Slide 28: Micro-CL (Computed Laminography)
Micro-CL has became a NOVEL tool for paleontology research.
With the help of the micro-CL, IVPP team has published more than 20 papers in top journals
(Inc. Nature 3, Science 3, PNAS 1)
The first X-ray Laminography system for plate-like fossil research.
CL for Institute of Vertebrate Paleontology and Paleoanthropology (IVPP), CAS

## Slide 29: Micro-CL (other applications)
IGBT solder void testing
BGA packaging testing
PCB testing
We also developed the micro-CL system to an IGBT company for QC.
Many companies scanned their products using micro-CL system in IHEP to test their products.
Notes: 为什么：Many electronic products are also plate-like.

## Slide 30: Invention patents on Micro-CL
10 patents for our developed micro-CL system have been applied.

## Slide 31: Technology transfer of CL
Cunfeng Wei led the “state-key R&D project” of MoST to develop the proto-type of CL and he is leading the ongoing project of 3D X-ray metrology system for WLP.
The technology of CL transferred to the company “Beijing HENT Co., Ltd.”
is a spin-off company of IHEP located in Z-park (Beijing) for incubation and manufacture.
Cunfeng Wei, PhD., Prof.
led the Micro-CL project and the ongoing project of 3D X-ray metrology system for Wafer Level Packaging (WLP).
“Beijing HENT Co., Ltd”

## Slide 32: Ongoing project: 3D X-ray metrology system for WLP
2018-2021
Nano-scale
Micro-CT
Thermal imaging
Ultrasonic microscope
Common NDT
3D X-ray for IC packaging
(e.g. TSV)
Precise
Fast
AI
3D X-ray metrology system for WLP
Notes: TSV，Through -Silicon-Via

## Slide 33: Contents
2
Research of DNTA
Medical imaging technology
X-ray inspection technology
Nuclear safety monitoring technology

## Slide 34: Imager & other monitors developed
(key methods of coding)
(prototypes of coding imager)
(vehicular
unit）
(UAV onboard )
(coding imaging for neutron)
(portable unit)
(dynamic imaging)
(Compton imaging)
(position indicator in 4π)
（RAMO dosimeter）
(RAMO C
dosimeter)
(environmental radiation monitor)
(distribution system for personal dose devices)
2006
2010
2013
2014
2016
2017
2017
2018
2015
Coded-aperture imager
Other radiation monitors
Notes: 干了什么：We have developed a serials of radiation monitor and radiation imager for environmental use.
典型是什么：One typical device is the coded-aperture camera for gamma-ray and X-ray imaging.

## Slide 35: Historic notes on radiation imaging
Research on coded-aperture imaging started form 2006 support by IHEP
China’s 1st coded-aperture Gamma-ray Imager
Financial supports from CAS, NSFC and MoST
1st Stand-alone system and portable type on the world market
Series products for different applications
Lei Shuai, PhD., Assoc. Prof.
Working on CA imaging since as a postgraduate.
Inventor of a novel large square-hole aperture for CA imaging.
Leading the follow up imager projects.
Long Wei,
PhD., Prof.
Notes: Modified Uniformly Redundant Array

## Slide 36: Series imager products
vehicle-mounted imager | Portable radiation imager | Solid-state imager | Radiation monitor for customs | Gamma ray imager for high background radiation | Tunnel inspection robot
HENT3-011A | HENT-013A | HENT3-014A | HENT3-015A | HENT-016A | HENT-017A
Tunnel inspection robot for radiation environment in CSNS
HD visible camera, infrared thermometer, gamma-ray imager, laser rangefinder and dosimeter integrated

## Slide 37
System Performance
Highlights:
Far-field distance and activity measurement of hot spots
  activity estimation error ≤20% in 10 meters range
Chasing of moving “hot” object
  adaptive algorithm for strong & weak sources
Invention of large square-hole aperture for CA Imaging
  with ¼ transparent mask area for CA imaging
  The aperture is a MURA, which can be extended

## Slide 38: Applications
Applied to most nuclear power plants in China, providing the state-of-the-art technology for the safe operation and maintenance of NPP.
Radiation field Imaging of reactor end faces
(CAN DU reactor)
Hotpot imaging with high background
Radiation deposition imaging of pipeline
(LWR)

## Slide 39: Applications
Hangzhou
G20 Summit
Applied to many major activities or events to ensure the public security.
Nanjing
2014 Youth Olympics
Radiation emergency exercise

## Slide 40: Applications
Inspection in customs tunnel/port
  entry-exit inspection (Shenzhen / Hong Kong)
  Vehicle inspection in highway toll-gate (Beijing)

## Slide 41: Applications
Captured people who carried contraband or injected with nuclear medicine
@ Hong Kong→Shenzhen port.
May, 2018

## Slide 42: Technology transfer
The technology of imagers and dosimeters transferred to the company “Beijing HENT Co., Ltd.”
is a spin-off company of IHEP located in Z-park (Beijing) for incubation and manufacture.
“Beijing HENT Co., Ltd”
Notes: 40Million transfer funding (MOST + INVESTMENT)

## Slide 43: Ongoing Project
Mainland China has near 40 nuclear power reactors in operation, about 20 under construction, and more about to start construction. Rapid growth in nuclear power has given rise to the importance of nuclear safety.
Miniaturization
  Develop more compact, multifunctional and highly integrated devices.
Applications in multi-platform
  Develop small UAV onboard/portable units for routine environmental monitoring and nuclear emergency response.
Information network
  Information integration and sharing by IoT technology with multi-platform detector terminals

## Slide 44: Contents
2
Research of DNTA
Medical imaging technology
X-ray inspection technology
Nuclear safety monitoring technology
Industrial & Medical Accelerators
Notes: 1、电子加速器完成了转化 工厂可以完成加速管等加工生产
2、散列的质子加速器

## Slide 45: BNCT (Boron Neutron Capture Therapy)
BNCT accelerator was developed and applied through the cooperation with companies. The agreement has been signed and the budget is available.
The demonstration facility will be constructed in the CSNS site, and will be the first accelerator-based BNCT facility in China.
The beam energy of a typical BNCT facility is always more than 8MeV. The 3.5 MeV beam can ease the construction of accelerator, but the low energy beam energy will be a challenge to develop the neutron target.
The layout of BNCT beam line
Signing ceremony of a cooperation agreement

## Slide 46: Comments from 2013 Assessment & Responses
Comments | Implementation & achievement
Too many projects | Ended some small and isolated projects.
Need further cooperation with companies | “Gao Neng Medical Co., Ltd.” is responsible for the industrialization of PEM, and next MBI system. “Beijing HENT Co., Ltd” is responsible for the industrialization of CL, radiation imagers and dosimeters.
Offer free use in exchange for usage data | All instruments have been opening to public to provide services. (mPET, CT’s, CL and data analysis)

## Slide 47: Contents
3
Future plan of DNTA

## Slide 48: Future plan
Technology research
  High-performance electronics,
  3D-Compton & hybrid imaging technology,
  Time-coded imaging technology,
  Rapid quantitative mapping of regional radiation distribution
Components and instrumentation
  Photon counting detector (CZT detector),
  Multi-energy breast CT,
  CT for Paleontology fossils and human remains,
Technology transfer
  MBI for breast,
  3D X-ray system for IC packaging,
  Nuclear safety inspection devices

## Slide 49: Contents
4
Summary

## Slide 50: Summary remarks for DNTA
  DNTA’s work is based on the technologies developed with large facilities in IHEP, which are our legacy;
  We hope, the successful demonstration (accelerator, PEM and radiation imager) should be modeled by following projects;
  DNTA should perform further R&D according to demands of application, market, and establish some R&D platforms with industry to carry out the technology transfer and industrialization;
  Innovation and entrepreneurship in DNTA to meet the needs along with the rapid development of economy in China - are our vision. .

## Slide 51
Thank you for your attention!