## Slide 1: Belle实验  2008诺贝尔奖[小林-益川]
~ 1 km in diameter
Mt. Tsukuba
KEKB
Belle
e+ source
Ares RF
cavity
Belle detector
亮度世界纪录:
L = 2.1 x 1034/cm2/sec
SCC RF(HER)
1999-2010
1014/fb
The KEKB Collider
ARES(LER)
8 x 3.5 GeV
22 mrad crossing
Notes: Here is a nice picture of the KEK Laboratory, with the sacred Mt. Tsukuba in the background.

## Slide 2
e- 7 GeV 2.6A
e+ 4 GeV 3.6A
Target: L = 8x1035/cm2/s
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of HER & LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting / permanent final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)
2010年起加速器升级为SuperKEKB
Grey is recycled, colored is new
Notes: 2

## Slide 3: Belle II 探测器升级 [高计数率、高本底、高辐照]
CsI(Tl) EM calorimeter:
waveform sampling
electronics
4 layers DSSD →
2 layers PXD
(DEPFET) +
4 layers DSSD
Central Drift Chamber:
smaller cell size,
long lever arm, fast electronics
7.4 m
7.1 m
Time-of-Flight, Aerogel
Cherenkov Counter →
Time-of-Propagation counter (barrel),
proximity focusing Aerogel RICH (forward)
RPC m & KL counter:
scintillator + Si-PM
for end-caps
1.5 m
3.3 m
Beryllium beam pipe
2cm diameter,
QCSR and QCSL

## Slide 4: Belle II Milestones
April 11th, 2017, Belle II at IP!
March, 2018, Phase II commissioning
first collision very soon!
Notes: we reached on april 11， 2017， the very important milestone of rolling-in of belle2 in the collision point on the beam line

## Slide 5: SuperKEKB 亮度预期
Expected data sample @ full luminosity
Assumptions:
  same commission time to reach design lum. as KEKB
  9 months/year running
  20 days/month
逐步增加的数据量将逐步提高物理研究的灵敏度！
目标数据量为 Belle 实验的 50-100 倍!
2018年4月对撞，
2019年初物理运行！
Notes: The plot on the right shows the luminosity profile of SuperKEKB, assuming the same commissioning time to reach nominal luminosity as in KEKB, 9 months/year of running time and 20 days/month of physics operations.
With this assumption the goal of 50 ab-1 will be reached in the year 2025.

## Slide 6
Belle II实验关注度较高的热点问题
★CKM矩阵元的精确测量，新物理？
★是否存在新的CP破坏的相角？b→s过程新的时间依赖的CP破坏的测量：B→,.
★新物理是否对right-handed currents过程中有贡献？ 关键性的过程包括，VV; Vl (V=)
★超出标准模型的夸克味改变的中性流过程？ b→s：
★超出标准模型的LFV过程？
★测量前后端的不对成性寻找新物理的迹象： b→sl+l-
★B介子的纯轻半轻衰变：带电轻Higgs的作用 ？
★CPV的测量在混合？
★ 暗物理暗能量的寻找：e+e- →l+l-
之前中国组在B的衰变中参与的不多。将来在B物理中对新物理的寻找会投入
更多的资源。竞争程度增加，难度加大，希望得到理论学家的指导！

## Slide 7: Past at Belle (only physics!)
DD mixing (PKU, USTC)
XYZ & quarkonium (IHEP)
  ISR, continuum production
  Two-photon processes
  Y(nS) decays
Light hadron spectroscopy (PKU, IHEP)
  Two-photon processes
  J/psi recoil, double-vector production
  B decays

## Slide 8: Now at Belle
DD mixing (USTC, IHEP)
Heavy flavor (Fudan, BUAA)
  Bs decay
  B semileptonic decays
XYZ & quarkonium (IHEP, BUAA, Fudan)
  ISR, continuum production
  Two-photon processes
  Y(nS) radiative decays, transitions b, b, …
hadron spectroscopy (BUAA, PKU, IHEP)
  Two-photon processes (’)
  Charmed baryons (c), Tcs, Tcc, …
  Glueballs, light tetraquarks, …

## Slide 9
感兴趣的一些问题
★XYZ: 更多的衰变和产生模式 ？Y(1S,2S,3S,5S,6S)衰变 ？衰变率？
★4.6 GeV上以上XYZ的态 ？双重子态？重子+介子？粲重子+介子 ？产生的过程？
★Missing的激发态的重子？ Y(1S,2S,3S,5S,6S)衰变 ？衰变率？
★Missing的窄共振的底夸克偶素/粲夸克偶素 ？,
★B介子标记方法的改进 ？（欢迎实验物理学家的更多的讨论）
★具有更加明显特征的多夸克态：Tcc, Tcs, …
★五夸克态，六夸克态的寻找： , …
★具有奇异量子数的胶球？ 更多的衰变产生过程？
★衰变的CPV的测量 ？
★暗物理暗能量在Y(1S,2S,3S）的衰变 ？
欢迎理论学家和实验物理学家的参与和指导！