## Slide 1: Offline Data Processing of MRPC End cap TOF@BESIII
SUN Shengsen
EPD Seminar
Dec. 27th, 2017

## Slide 2: Outline
Particle Identification (PID)
Time-of-Flight Detector (TOF)
Multi-gap Resistive Plate Chamber (MRPC)
BESIII Endcap TOF system
  Detector and Electronics
  Multi-peak of Time-Over-Threshold (TOT)
  Alignment of detector
  Reconstruction and Calibration
Summary

## Slide 3: A “traditional” particle physics experiment
Conceptual design of a “traditional” particle physics experiment
  Tracking system
  EM calorimeter
  Hadron calorimeter
  Muon system
Particle identification is a crucial aspect.

## Slide 4: WHY PID is crucial?
Invariant mass
Improvement in the signal-to-background ratio
without PID
with PID

## Slide 5: Particle Identification (PID)
Measurement of the energy deposit by ionization
Time-of-flight measurements
Detection of Cherenkov radiation
Detection of transition radiation

## Slide 6: Particle identification capability
Separation power

## Slide 7: Time-of-Flight detector
飞行时间探测器是通过测量带电粒子的飞行时间，结合径迹探测器测量的粒子的动量和飞行径迹长度，得到粒子的质量，实现粒子鉴别。
，，

## Slide 8: TOF PID
Comparison between measured and expected time:
，，
 Normal distribution
Particle separation power of TOF depends on:
  The flight time difference between different species particles with same momentum.
  Time resolution

## Slide 9: Scintillation TOF
Scintillator bar coupled with PMT
  Good time resolution
  PMT under strong magnetic field
  Increase of granularity

## Slide 10: Multi-gap Resistive Plate Chamber
MRPC-TOF
Charged particle  Primary ionization  Avalanche  Induced signal
Readout of scintillator is expensive, RPC is much cheaper.
The RPC design was improved by Multi-gap RPC:
  Reducing gap sizes
  restrict fluctuation of drift time
  improve time resolution
  Increasing the electric field
  sum of the induced signals
  good detection efficiency

## Slide 11: Scintillator End cap TOF @ BESIII
Intrinsic time resolution: 80 ps
Uncertainty of bunch time: 20 ps
Uncertainty of bunch length: 8-15mm
20—35ps
Extrapolation of track: 10mm
50ps
Electronics: 25 ps
Expected time: 30 ps
Time slewing: 10ps
Overall time resolution: 110—120 ps
The designed target is 110—120ps
The time res for pions is 138ps.
Multiple scattering has worsen the performance

## Slide 12: MRPC End cap TOF
Intrinsic time resolution < 55 ps
12
OLD NEW
Detector Scintillator MRPC
Modules 96 72
Electronics 96 72122=1728
Time Res 138ps < 80~100ps

## Slide 13: Structure of the MRPC
3mm
9.1cm
14.1cm
2.4cm
Readout strip:
  Width: 2.4 cm
  Length: 9.1-14.1 cm
Gas gap: 2 x 6
Gap size: 0.22 mm
Resistive plate: floating glass
Total thickness: ~20 mm

## Slide 14: Electronics
Time precision contributed by electronics (RMS) < 25ps

## Slide 15: Trigger / Slow Control / Gas
Trigger conditions:
NETOF>=1, NETOF>=2,
Back to Back

## Slide 16: MRPC Installation
Oct. 2015, new MRPC End cap TOF take place of scintillator endcap TOF
The total last about 60 days.

## Slide 17: Procedure of MRPC Installation
leakage
Ratio check
location
guarantee
electronics check
installation
test with HV
gas pipes & HV wires

## Slide 18: MRPC Endcap TOF Reconstruction
Event Start Time
MDC Reconstruction  Extrapolated track
  Momentum, path length  expected time
  Hit position
TOF Raw Data
  Leading time
  Time-over-threshold (TOT)

## Slide 19: Event Start Time

## Slide 20: Signal of MRPC TOF

## Slide 21: Transmission time on the strip
Dependence of measured time on the hit position
4-order polynomial function

## Slide 22: Multi-peak TOT Distribution Reflection of the signal in strip
22

## Slide 23: Multi-peak TOT Distribution Reflection of the signal in strip
Length of strip: 13 cm
Length of foot: 2.8 cm
Velocity of signal: 55ps/cm
Transmission time for total strip
(13+2.8)*55=869ps
869ps*2=1.738ns
Time interval
(19.65ns-11.2ns)/5=1.69ns
Time interval
(18.0ns-12.8ns)/3=1.73ns；

## Slide 24: Time Walk (Time Slewing)
Measured raw time depend on hit position
Multi-peak TOT partly depend on hit position
Hit position correction

## Slide 25: MRPC TOF Calibration
Bhabha events are used for calibration sample
Empirical calibration function for single end of strip
Empirical calibration function for strip

## Slide 26: MRPC TOF Reconstruction
Extrapolated strip as center, search signals in the range of 3+5+3 strips
Multi-signals:
  Match hit position
  Compare TOT

## Slide 27: Alignment of MRPC TOF Detector
True Geometry
Ideal Geometry
Assumption no misalignment along the beam direction

## Slide 28: Alignment of MRPC TOF Detector
7mm
0.45 degree
East Endcap
West Endcap

## Slide 29: Time Resolution and Efficiency of Bhabha
left end: 69ps
right end: 69ps
combine: 57ps
29
Strip number
Module number
Hit Position
Time Resolution
Efficiency

## Slide 30: Time Resolution for
65ps
pion
Accelator | Detector | Time Resolution()
RHIC | STAR | 80ps
LHC | ALICE | 86ps (Without t0)
BEPCII | BESIII | 65ps
Accelator | Detector | 
RHIC | STAR | 80ps
LHC | ALICE | 86ps (Without t0)
BEPCII | BESIII | 65ps
Scintillator ETOF: 138 ps
Designed Target of MRPC ETOF: 80~100 ps
BESIII: 65ps

## Slide 31: Calculation in PID Algorithm
Time difference is not observed to depend on species of particle (?)
Time difference depends on the momentum and polar angle.
31

## Slide 32: STAR Experiment --- Spline Fit
96ps

## Slide 33: ALICE Experiment

## Slide 34: Summary and Discussion
Particle identification is crucial
MRPC TOF: good time resolution, high efficiency and low cost
Offline data processing of MRPC ETOF @ BESIII
  Analysis of multi-peak TOT
  Alignment of detector
  Empirical calibration function.
The time resolution of 0.8 GeV/c pion achieved 65 ps.
Thank you & Happy New Year!