## Slide 1: Effect of Construction Steel Rebars on Residue of the Magnetic Field

## Slide 2: Rebars?

## Slide 3: Effect on magnetic field

## Slide 4
Spherical coil consists of 32 circular coils laying 32.017 (inclination) in the same manner as the EMF.
All of the circular coils have the same value of space with the coil next to them (1.35 m).
Optimize for the currents at the surface of diameter 39.5 m
coil | Radius (m) | Location (m) | Current (A)
1 | 21.64 | 0.68 | 72.43
2 | 21.55 | 2.03 | 72.42
3 | 21.38 | 3.38 | 72.43
4 | 21.13 | 4.74 | 72.42
5 | 20.78 | 6.09 | 72.43
6 | 20.33 | 7.44 | 72.42
7 | 19.78 | 8.80 | 72.44
8 | 19.12 | 10.15 | 72.40
9 | 18.43 | 11.50 | 72.47
10 | 17.42 | 12.85 | 72.35
11 | 16.34 | 14.21 | 72.59
12 | 15.05 | 15.56 | 72.12
13 | 13.51 | 16.91 | 73.06
14 | 11.62 | 18.27 | 71.11
15 | 9.15 | 19.62 | 76.13
16 | 5.37 | 20.97 | 57.87
Layout 5 | 32 Coils | Equal Space

## Slide 5: Rebar arrangement
1
2
3
4
1. CD PMT
19.5m (39m)
2. Veto PMT
20.55m (41.1m)
3. Coil
21.64m (43.28m)
4. 3-Layers of Rebar
22m (44m)
22.2m (44.4m)
22.4m (44.8m)
Top down view

## Slide 6: Rebar arrangement
1
2
3
4
1. CD PMT
19.5m (39m)
2. Veto PMT
20.55m (41.1m)
3. Coil
21.64m (43.28m)
4. 3-Layers of Rebar
22m (44m) 19.19cm
22.2m (44.4m) 19.37cm
22.4m (44.8m) 19.55cm
Top down view
0.5 degrees apart

## Slide 7: Rebar arrangement
1
2
3
4
Side view
1. CD PMT
19.5m (39m)
2. Veto PMT
20.55m (41.1m)
3. Coil
21.64m (43.28m)
4. 3-Layers of Rebar
22m (44m) 19.19cm
22.2m (44.4m) 19.37cm
22.4m (44.8m) 19.55cm
44m long
2cm diameter

## Slide 8: Effect on magnetic field
15m
24.5m
-12m
12m
15m
24.5m
-12m
12m

## Slide 9: Residue of Magnetic Field
15m
24.5m
-12m
12m
Angle (Degrees) | Magnetic field residue (Gauss) |  | % of residue (% of Earth magnetic field) |  | Ratio (Without Rebar : With Rebar)
 | Without Rebar | With Rebar | Without Rebar | With Rebar | 
0 | 0.01511 | 0.05108 | 3.37 | 11.39 | 3.38
15 | 0.01506 | 0.05159 | 3.36 | 11.51 | 3.43
30 | 0.01520 | 0.04561 | 3.39 | 10.17 | 3.00