## Slide 1: CEPC parameters with larger betax*
Dou Wang, Chenghui Yu, Yuan Zhang, Yiwei Wang, Huiping Geng, Sha Bai, Jie Gao
2017.07.28

## Slide 2: Higgs parameters with larger betax* （wangdou20170713-100km_2mmy）
 | Higgs | x*=0.37m | x*=0.6m | x*=1.0m
Number of IPs | 2 |  |  | 
Energy (GeV) | 120 |  |  | 
Circumference (km) | 100 |  |  | 
SR loss/turn (GeV) | 1.67 |  |  | 
Half crossing angle (mrad) | 16.5 |  |  | 
Piwinski angle | 3.19 | 2.17 | 1.71 | 1.32
Ne/bunch (1011) | 0.968 |  |  | 
Bunch number | 412 |  |  | 
Beam current (mA) | 19.2 |  |  | 
SR power /beam (MW) | 32 |  |  | 
Bending radius (km) | 11 |  |  | 
Momentum compaction (10-5) | 1.14 |  |  | 
IP x/y (m) | 0.171/0.002 | 0.371/0.002 | 0.6/0.002 | 1.0/0.002
Emittance x/y (nm) | 1.31/0.004 |  |  | 
Transverse IP (um) | 15.0/0.089 | 22.0/0.089 | 28.0/0.089 | 36.2/0.089
x/y/IP | 0.013/0.083 | 0.025/0.079 | 0.036/0.075 | 0.051/0.069
RF Phase (degree) | 128 |  |  | 
VRF (GV) | 2.1 |  |  | 
f RF (MHz) (harmonic) | 650 |  |  | 
Nature z (mm) | 2.72 |  |  | 
Total z (mm) | 2.9 |  |  | 
HOM power/cavity (kw) | 0.41(2cell) |  |  | 
Energy spread (%) | 0.098 |  |  | 
Energy acceptance (%) | 1.5 | 1.0 | 0.77 | 0.58
Energy acceptance by RF (%) | 2.1 |  |  | 
n | 0.26 | 0.18 | 0.14 | 0.11
Life time due to beamstrahlung_cal (minute) | 52 | 60 | 60 | 60
F (hour glass) | 0.96 | 0.92 | 0.89 | 0.84
Lmax/IP (1034cm-2s-1) | 2.0 | 1.81 | 1.65 | 1.45

## Slide 3: Luminosity vs. betax*

## Slide 4:  vs. betax*

## Slide 5: Energy acceptance vs. betax*

## Slide 6: Piwinski angle vs. betax*

## Slide 7: Beam power corresponding to 21034cm-2s-1

## Slide 8: Check Higgs parameters for FCCee
 | CEPC-Higgs | FCC-Higgs | Check FCC | FCC-smaller x*
Number of IPs | 2 | 2 |  | 
Energy (GeV) | 120 | 120 |  | 
Circumference (km) | 100 | 97.75 |  | 
SR loss/turn (GeV) | 1.67 | 1.72 |  | 
Half crossing angle (mrad) | 16.5 | 15 |  | 
Piwinski angle | 3.19 |  | 1.31 | 2.94
Ne/bunch (1011) | 0.968 | 0.71 | 0.73 | 
Bunch number | 412 | 826 |  | 
Beam current (mA) | 19.2 | 29 | 28 | 
SR power /beam (MW) | 32 | 50 | 50 | 
Bending radius (km) | 11 | 10.747 |  | 
Momentum compaction (10-5) | 1.14 | 0.731 |  | 
IP x/y (m) | 0.171/0.002 | 1.0/0.002 |  | 0.2/0.002
Emittance x/y (nm) | 1.31/0.004 | 0.63/0.00126 |  | 
Transverse IP (um) | 15.0/0.089 |  | 25.1/0.05 | 11.2/0.05
x/y/IP | 0.013/0.083 | 0.081/0.14 | 0.081/0.135 | 0.023/0.16
RF Phase (degree) | 128 |  | 139 | 
VRF (GV) | 2.1 | 2.62 |  | 
f RF (MHz) (harmonic) | 650 | 400 |  | 
Nature z (mm) | 2.72 | 2.0 |  | 
Total z (mm) | 2.9 | 2.2 |  | 
HOM power/cavity (kw) | 0.41(2cell) |  |  | 
Energy spread (%) | 0.098 | 0.099 |  | 
Energy acceptance (%) | 1.5 |  | 2 (1) | 2
Energy acceptance by RF (%) | 2.1 | 2.2 | 5.3 | 
n | 0.26 |  | 0.12 | 
Life time due to beamstrahlung_cal (minute) | 52 |  | 4.45×108 (460) | 50
F (hour glass) | 0.96 |  | 0.89 | 0.97
Lmax/IP (1034cm-2s-1) | 2.0 | 4.6 | 4.54 | 5.88

## Slide 10: Higgs parameters with smaller emit.（wangdou20170719-100km_2mmy）
 | Higgs | x*=0.3m | x*=0.6m | x*=1.0m
Number of IPs | 2 |  |  | 
Energy (GeV) | 120 |  |  | 
Circumference (km) | 100 |  |  | 
SR loss/turn (GeV) | 1.67 |  |  | 
Half crossing angle (mrad) | 16.5 |  |  | 
Piwinski angle | 3.19 | 2.67 | 1.89 | 1.46
Ne/bunch (1011) | 0.968 |  |  | 
Bunch number | 412 |  |  | 
Beam current (mA) | 19.2 |  |  | 
SR power /beam (MW) | 32 |  |  | 
Bending radius (km) | 11 |  |  | 
Momentum compaction (10-5) | 1.14 | 0.95 | 0.95 | 0.95
IP x/y (m) | 0.171/0.002 | 0.3/0.002 | 0.6/0.002 | 1.0/0.002
Emittance x/y (nm) | 1.31/0.004 | 1.0/0.003 | 1.0/0.003 | 1.0/0.003
Transverse IP (um) | 15.0/0.089 | 17.3/0.078 | 24.5/0.078 | 31.6/0.078
x/y/IP | 0.013/0.083 | 0.023/0.096 | 0.04/0.091 | 0.059/0.085
RF Phase (degree) | 128 | 124 | 123 | 122
VRF (GV) | 2.1 | 2.02 | 1.99 | 1.975
f RF (MHz) (harmonic) | 650 |  |  | 
Nature z (mm) | 2.72 | 2.66 | 2.73 | 2.76
Total z (mm) | 2.9 | 2.8 | 2.8 | 2.8
HOM power/cavity (kw) | 0.41(2cell) | 0.42 | 0.42 | 0.42
Energy spread (%) | 0.098 |  |  | 
Energy acceptance (%) | 1.5 | 1.35 | 0.92 | 0.7
Energy acceptance by RF (%) | 2.1 | 1.89 | 1.77 | 1.7
n | 0.26 | 0.23 | 0.16 | 0.13
Life time due to beamstrahlung_cal (minute) | 52 | 60 | 60 | 60
F (hour glass) | 0.96 | 0.94 | 0.91 | 0.87
Lmax/IP (1034cm-2s-1) | 2.0 | 2.27 | 2.05 | 1.83

## Slide 11: Luminosity vs. betax*

## Slide 12:  vs. betax*

## Slide 13: Energy acceptance vs. betax*

## Slide 14: Piwinski angle vs. betax*

## Slide 15: FFS optics with larger betax*
betax*=0.5m, betay*=2mm

## Slide 21: DA before optimization
4 fam in FFS
2 fam in arc
Damping
200 turns

## Slide 22: DA after optimization

## Slide 23: DA after optimization-open sawtooth

## Slide 24: sawtooth+fluc
50 seeds

## Slide 25: Strength of crab sextupole
Strength of crab sextupole: ~13% of main sextupoles
Upstream of IP : negative
Downstream of IP: positive

## Slide 26: Open crab sextupoles

## Slide 27: Crab+sawtooth

## Slide 30: Crab+sawtooth+fluc
50 seeds

## Slide 32: cross-section for radiative Bhabha scattering

## Slide 33: lifetime due to radiative Bhabha
For CEPC(Pre-CDR) and FCCee,
For CEPC(CDR)
Life time of FCCee: 72 min
Life time of CEPC(Pre-CDR) : 55 min
Life time of CEPC(CDR) : 100 min