## Slide 1: MDI study of CEPC double ring βx*=0.36m
Sha Bai, Yiwei Wang, Chenghui Yu, Jie Gao
2017-09-01
CEPC AP meeting

## Slide 2: QD0/QF1物理设计参数 ~150T/m, L*=2.2m
QD0 | 水平束流清晰区 2（20x+3） | 垂直束流清晰区 2（40y+3） | 正负电子 束流中心间距
入口 | 11.31 mm | 20.24 mm | 72.61 mm
磁长度的1/2处 | 14.19 mm | 23.61 mm | 100.99 mm
出口 | 19.50 mm | 22.13 mm | 129.70 mm
所需好场区范围 | 水平方向19.50 mm；垂直方向23.61 mm |  | 
磁铁有效长度 | 1.73m |  | 
线圈起点距离IP | 2.2000m |  | 
最高磁场梯度 | 151 T/m |  | 
QF1 | 水平束流清晰区 2（20x+3） | 垂直束流清晰区 2（40y+3） | 正负电子 束流中心间距
入口 | 23.49 mm | 19.88 mm | 146.20 mm
磁长度的1/2处 | 28.06 mm | 17.46 mm | 170.63 mm
出口 | 29.57 mm | 16.65 mm | 195.05 mm
所需好场区范围 | 水平方向29.57 mm；垂直方向19.88 mm |  | 
磁铁有效长度 | 1.48m |  | 
线圈起点距离IP | 4.43m |  | 
最高磁场梯度 | 102 T/m |  | 

## Slide 3: Beam stay clear region
βx*=0.36m
βx*=0.171m
Lumical
QD0
QF1
Lumical
QD0
QF1

## Slide 4: SR from QD0 in horizontal plane
In the Gaussian distribution beam, particles in 3σ occupies 99.7% of the total amount, 1σ occupies 68.7%, and 2σ occupies 95.5%.
The total SR power generated by the QD0 magnet is 646.3W in horizontal. The critical energy of photons is about 1308.3keV. (Slice into 6 pieces)
Lumical
QD0
QF1

## Slide 5: SR from QD0 in vertical plane
In the Gaussian distribution beam, particles in 3σ occupies 99.7% of the total amount, 1σ occupies 68.7%, and 2σ occupies 95.5%.
The total SR power generated by the QD0 magnet is 168.4W in vertical. The critical energy of photons is about 423.1keV. (Slice into 6 pieces)

## Slide 6: SR from QF1 in horizontal plane
In the Gaussian distribution beam, particles in 3σ occupies 99.7% of the total amount, 1σ occupies 68.7%, and 2σ occupies 95.5%. Slice into 6 pieces.
The total SR power generated by the QF1 magnet is 1487.4W in horizontal. The critical energy of photons is about 1545.7keV.
The total SR power generated by the QF1 magnet is 32.2W in vertical. The critical energy of photons is about 188.9keV.
Lumical
QD0
QF1

## Slide 7: SR from B, FD in horizontal plane ~ last bending magnet upstream of IP and final doublet
Lumical
QD0
QF1

## Slide 8
Slices(3sigma) | QD0_SR_power_X (W) | QD0_SR_power_Y (W) | QD0_critical_energy_X(KeV) | QD0_critical_energy_Y(KeV)
3 | 685.07 | 178.49 | 1189.35 | 384.64
6 | 646.34 | 168.4 | 1308.29 | 423.10
9 | 639.19 | 166.54 | 1347.94 | 435.92
12 | 636.69 | 165.89 | 1367.76 | 442.33
18 | 634.91 | 165.42 | 1387.58 | 448.74
Slices(3sigma) | QF1_SR_power_X (W) | QF1_SR_power_Y (W) | QF1_critical_energy_X(KeV) | QF1_critical_energy_Y(KeV)
3 | 1576.49 | 34.16 | 1405.21 | 171.79
6 | 1487.36 | 32.23 | 1545.74 | 188.97
9 | 1470.93 | 31.87 | 1592.58 | 194.69
12 | 1465.18 | 31.75 | 1616.0 | 197.56
18 | 1461.08 | 31.65 | 1639.42 | 200.42
SR power and critical energy of FD in different slices
~ βx*=0.36m

## Slide 9: The synchrotron radiation in the IR ~ βx*=0.36m
Cold vacuum chamber has to be adopted within SC magnet for the sufficient coils space. The design has been accepted by cryogenic system.
The synchrotron radiation power within QD0 is 3.9W along 1.73m, on QF1 is 5.7W along 1.48m. The region between QD0 and QF1 is 90 W (0.5m) where has special cooling structure.
QD0
3.9W
90 W
QF1
5.7W