## Slide 1: CEPC Injector positron source
C. Meng, G. Pei, J. Zhang, X. Li, S. Pei, Y. Chi, J. Gao
Institute of High Energy Physics, CAS, Beijing
September 15th, 2017

## Slide 2: Sources design
Positron source and capture section
FC (Flux concentrator)
Layout
  Target
  FC (Flux concentrator)
  Capture section
    Large aperture accelerating tube
    r=15 mm

## Slide 3: Source design
 | SLC | LEP (LIL) | KEKB/SUPER KEKB | FCC-ee (conv.)* | CEPC
Incident e- beam energy | 33 GeV | 200 MeV | 3.3/3.3 GeV | 4.46 GeV | 4 GeV
e-/bunch [1010] | 3-5 | 0.5 - 30 (20 ns pulse) | 6.25/6.25 | 5.53 | 6.25
Bunch/pulse | 1 | 1 | 2/2 | 2 | 1
Rep. rate | 120 Hz | 100 Hz | 50 Hz/50 Hz | 200 Hz | 100Hz
Incident Beam power | ~20 kW | 1 kW (max) | 3.3 kW | 15 kW | 2.5 kW
Beam size @ target | 0.6 - 0.8 mm | < 2 mm | />0.7 mm | 0.5 mm | 0.5 mm
Target thickness | 6X0 | 2X0 | /4X0 | 4.5X0 | 4.5X0
Target size | 70 mm | 5 mm | 14 mm |  | 10mm
Target | Moving | Fixed | Fixed/Fixed |  | Moving/Fixed
Deposited power | 4.4 kW |  | /0.6 kW | 2.7 kW | 0.45kW
Capture system | AMD | λ/4 transformer | /AMD | AMD | AMD
Magnetic field | 6.8T->0.5T | 1 T->0.3T | /4.5T->0.4T | 7.5T->0.5T | 6T->0.5T
Aperture of 1st cavity | 18 mm | 25mm/18 mm | /30 mm | 20 mm | 25 mm
Gradient of 1st cavity | 30-40 MV/m | ~10 MV/m | /10 MV/m | 30 MV/m | 25 MV/m
length of 1st cavity | 1m | 3m | 2m | 3m | 1.5m
Linac frequency | 2855.98 MHz | 2998.55 MHz | 2855.98 MHz | 2855.98 MHz | 2856.75 MHz
e+ yield @ CS exit | ~1.6 e+/e- | ~0.003 e+/e- (linac exit) | /~0.5 e+/e- | ~0.7 e+/e- | ~0.6 e+/e-
Positron yield @ DR | ~1.1 e+/e- |  | 0.4 e+/e- |  | 
DR energy acceptance | +/- 2.5 % | +/- 1 % (EPA) | +/- 1.5 % (1 σ) | +/- 8 % | 
Energy of the DR | 1.15 GeV | 500 MeV | NO/1.1 GeV | 1.54 GeV | 
Positron source performances

## Slide 4: Accelerating tube
Same size for each cell, same Q、υg、Zs、α0
Constant impedance

## Slide 5: Accelerating tube
Constant impedance
τ0 ~ 0.5-0.8
R=30 mm
  υg=0.034
  α0=0.054
  18 MV/m
R=25 mm
  υg=0.019
  α0=0.1
  25 MV/m
Length
  1.5m~1.8m

## Slide 6: Pre-accelerating section
R=30 mm

## Slide 7: Pre-accelerating section
R=30mm

## Slide 8: Pre-accelerating section
Phase [-5,10]
Energy [100 130] MeV
Ne+/Ne-=0.66
Beam size <10 mm
Ne+/Ne-=0.57
R=30mm
3.2nc, 100%
3.2nc, 70%

## Slide 9: Pre-accelerating section
R=25 mm

## Slide 10: Pre-accelerating section
R=25mm

## Slide 11: Pre-accelerating section
Phase [-5,10]
Energy [140 170] MeV
Ne+/Ne-=0.52
Beam size <10 mm
Ne+/Ne-=0.5
R=25mm
3.2nc, 60%
3.2nc, 50%

## Slide 12: Pre-accelerating section
Larger accelerating gradient, higher positron capture efficiency
Larger aperture of accelerating tube, higher positron capture efficiency
Considering power efficiency and positron capture efficiency, maybe the accelerating tube (R=25mm, Ea=25 MV/m, L=1.5m) is better.
Need more cavity (200 MeV) simulation and further optimization.
Summary