## Slide 1: simulation
Jin Huang (黄进)
Brookhaven National Lab, NY, USA
1st sPHENIX workshop in China, School of Physics, Peking University, Beijing, China
(from three view points: simulation team, HF topical group, and DAQ)

## Slide 2: sPHENIX Software
Open source @
https://github.com/sPHENIX-Collaboration/
Core software: 200k line of code
Analysis: 59k line of code
→ G4 Simulation → Digitization
Reconstruction
Real Data
Detector performance
Physics obs. Projection
Detector Design

## Slide 3: Subsystem simulation and reconstruction

## Slide 4: Full detector simulation + reconstruction
Design to Simulation
sPHENIX Geant4 display of pT=30 GeV/c B+-hadron
Inner tracker (MVTX and INTT) _
Open source @ : https://github.com/sPHENIX-Collaboration/
_ MVTX Ladders modeled in details

## Slide 5: Event generator: event pile up
MVTX: +/- 2 µs
INTT: [-20 ns, +80 ns]
TPC: +/- 35 µs
Collisions: +/- 35 µs
High rate → Pile up → studied in our software suit
Simulated TPC data stream

## Slide 6: Tracking simulation + reconstruction
Tracking software improved significantly over the past year from a team of hardworking developers
Full simulation + reco chain
Improving details of detector description and improving tracking speed
Tracker simulation
Track fit
Detailed ladder models
Pattern recognition, ghost rejection
GenFit2-based Kalman filter
RAVE-based multivertex finding and fitting
Final Vertex finding
Hough transform seeding
Event generation
Improving TPC ionization simualtion
Kalman filter propagation
2 iterations
Pile up
Multi event generators
Full tracking simulation in 0-4 fm Au+Au collisions
sPHENIX simulation
sPHENIX simulation

## Slide 7: Calorimeters: in Simulation
EM calorimeter (EMCal) : 18 X0 W-SPACAL
Inner hadron calorimeter (Inner HCal) : .25 λ0 Al (Scint. Sampling)
sPHENIX coil and cryostat. (Magnet): 1.4 X0 Coil & Cryostat
Outer hadron calorimeter (Outer HCal) : 4 λ0 SS-Scint. sampling
Geant4 Land
24-GeV pion shower
EMCal
Inner HCal
Magnet
Outer HCal
Beam view of full calorimeters

## Slide 8: Simulation Setup: EMCal
10GeV, e+
2 cm
SPACAL Tower w/ fibers displayed
EMCal Half Sector
(fibers simulated but hidden from display)
full EMCal

## Slide 9: Simulation Setup: HCal
Baseline design
24-GeV pion shower
EMCal
Inner HCal
Magnet
Outer HCal
Beam view of full calorimeters
Calorimeter simulation & analysis chain: GEANT4 hit → Scintillation light model → Light collection model → Tower readout → Digitization → Calibrated tower energy → Clustering/Track matching/Jet finding

## Slide 10: Test Beam Verification [arXiv:1704.01461]
Geant4 World

## Slide 11: Test Beam Verification [arXiv:1704.01461]
EMCal energy resolution for EM shower in tower center
EMCal rejection for pion-
HCal energy response for pion-
New 2017 data
2016 data and submitted to IEEE TNS

## Slide 12: Au+Au background → Compact shower
EMCal
Inner HCal
Outer HCal

## Slide 13
EMCal radius (cm)
EMCal X (cm)
EMCal Y (cm)
← Moliere radius, 2cm
← 3x3 tower
95% containment
EMCal radius (cm)
Inner HCal radius (cm)
EMCal X (cm)
Inner HCal X (cm)
Inner Hcal Y (cm)
EMCal Y (cm)
← 3x3 tower
50% containment
← ~3x3 tower
60% containment
― Energy deposition (A.U.)
― Percentage outside radius
4 GeV Electrons in EMCal
4 GeV Pions in EMCal, that passed E/p electron-ID cut
EMCal
EMCal
Inner HCal
A.U./Leakage Ratio
A.U./Leakage Ratio
A.U./Leakage Ratio

## Slide 14: Performance simulations

## Slide 15: Performance : Single EM Showers
Beam test [arXiv:1704.01461] Full sPHENIX detector simulation
Applied cluster-position-based non-uniformity correction as used in test beam analysis
dE/E ~ 15%/ √(E) + 4% (meets sPHENIX goal)

## Slide 16: Performance : Photon in Full Event
Good linearity up to photon kinematic limit of sPHENIX
Good photon response shown in full event simulations

## Slide 17: Physics Performance : Electron-ID
Critical driving factor for EMCal design: Upsilon electron ID
Satisfied detector requirement (>90:1-pion rejection @ pT=4 GeV/c in central Au+Au collisions at 70% efficiency)
Updating Upsilon background and RAA projections
Pion rejection @ 90% efficiency (higher than spec.)
Upsilon RAA projections in sPHENIX proposal
Updating ...

## Slide 18: Performance : Jet Finding
Jets in p+p and central Au+Au collisions are also studied in full detector simulations
Jet finding followed by ATLAS style iterative background subtraction [10.1103/PhysRevC.86.024908]
Performance meeting sPHENIX spec.
Further improving underlying event subtraction and fake-jet rejection algorithm based on RHIC and LHC experiences

## Slide 19: Physics Performance : Jet Observables
Jet-balance/imbalance observables simulated in full detector events: day-1 measurement, resolution under control
On-going effort in understanding the details of the jet simulations and unfolding studies.
Expanding jet observables studied with the updated design and simulations
Di-jet transverse momentum asymmetry
γ-jet transverse momentum balance
Shape of observable well controlled
from truth → measured quantities
Promising for unfolding and sys. control

## Slide 20: b-quark jet
CMS work-point, Phys. Rev. Lett. 113, 132301 (2014)
sPHENIX simulation
b-jet + light jet: differential sensitivity to radiative VS collisional energy loss.

## Slide 21: Precision open bottom meson
drag
fluctuations
Diffusion coefficient DHQ
“Brownian” motion
 Langevin simu.
B-meson program: pT 2-10 GeV/c, precisely determine the bottom quark collectivity → clean access to DHQ
b

## Slide 22: Beyond sPHENIX

## Slide 23: Evolution of the PHENIX Interaction region
~2000
2017→2022, CD-0 @ 2016
≥2025
Time
PHENIX experiment
An EIC detector
16y+ operation
Broad spectrum of physics (QGP, Hadron Physics, DM)
170+ physics papers with 24k citations
Last run in this form 2016
Comprehensive central upgrade base on BaBar magnet
Rich jet and HF physics program → nature of QGP
Possible forward tracking, and calorimeter → Spin, CNM
Path of PHENIX upgrade leads to a capable EIC detector
Large coverage of tracking, calorimetry and PID
Open for new collaboration/new ideas
RHIC: A+A, spin-polarized p+p, spin-polarized p+A
EIC: e+p, e+A
arXiv:1501.06197 [nucl-ex]
arXiv:1402.1209 [nucl-ex]

## Slide 24: Evolving upgrade concepts
arXiv:1501.06197
CDR in preparation
arXiv:1402.1209
To RHIC PAC 2017

## Slide 25: EIC detector studies
Forward tracking resolution
(Haiwang Yu)
EIC LOI being updated this year. Many opportunity to contribute and design future of sPHENIX
DIS collision @ Q2 ≈ 100 (GeV/c)2

## Slide 26: Full detector EIC simulation in sPHENIX framework: Promise to stream readout EIC detector with sPHENIX DAQ
50 ub cross section @ L = 1034 cm-2 s-1
→
~100 Gbps (30 Gbps+ PID + headers) stream readout EIC without triggering
≈ sPHENIX DAQ disk rate
See my slide @ EIC stream readout meeting and sPHENIX cold-QCD TG meeting https://indico.bnl.gov/event/4464/contributions/20809/attachments/17998/22285/2018.04.02_EIC_Stream_Readout2.pdf

## Slide 27: How to get involved

## Slide 28: How to get involved
Always good to start with day-1 checklist
Discussion group:
  sPHENIX simulation meeting: https://indico.bnl.gov/categoryDisplay.py?categId=88
  Software and repository email list:
    https://lists.bnl.gov/mailman/listinfo/sphenix-software-l
    https://lists.bnl.gov/mailman/listinfo/sphenix-github-l
Documentation
  Software wiki: https://wiki.bnl.gov/sPHENIX/index.php/Software
  Doxygen software reference: https://www.phenix.bnl.gov/WWW/sPHENIX/doxygen/html/
Resource
  RCAF
    Works with both PHENIX and STAR(in testing) existing RCF account
    10 TB per user base disk associated with sPHENIX group tag: Register with this form .
  sPHENIX code repository: https://github.com/sPHENIX-Collaboration

## Slide 29: Framework: Fun4All
Based on PHENIX software framework, a.k.a. Fun4All
  Modular design, C++ based, 1 PB data / week PHENIX data analysis
Built-in Geant4 support Common macro run the simulation and standard analysis chain
Easy access for user modules in analysis : https://wiki.bnl.gov/sPHENIX/index.php/Example_of_using_DST_nodes

## Slide 30: Framework: Logistic
Repositories: https://github.com/sPHENIX-Collaboration
  analysis: which contains the analysis modules. Everyone who is a collaborator (request to join here) can update this repository directly.
  coresoftware: which contains the framework, the G4 simulation and the Event library to read raw data.
    Pull request & review required for updates
  macros: which contains macros to run the show.
    Pull request & review required for updates
Nightly build:
  Most recent software build for use on RCF daily (new builds)
  Weekly snapshot of software environment (ana builds)
Further information :
  https://wiki.bnl.gov/sPHENIX/index.php/Software

## Slide 31: Summary
sPHENIX has a robust simulation + reconstruction software
  Checked with test beam with detailed detector description
  Used in large studies in multiple campaigns
  Improving fidelity of simulation, optimizing speed of reconstruction
Current simulation show designed detector fit sPHENIX scientific goals
Many opportunity for Chinese collaborator to contribute
  Detector refinement
  Studies of physics opportunities : four topical groups
Join me this afternoon for a tutorial
Always start from here: day-1 checklist

## Slide 32: Extra Information

## Slide 33: Cold QCD
sPHENIX simulation p↑ + p → jet (h±) + X
√s = 510 GeV
Charge-track tagged jet asymmetry → Access Sivers effect
Charge-track asymmetry in jet → Access Transveristy @ large x
sPHENIX simulation
p↑ + p → jet (h±) + X, √s = 510 GeV
x1
arXiv:1602.03922

## Slide 34: Event generator
Standard inputs: HEPMC format
  Fun4AllHepMCInputManager -> HepMCNodeReader
Generators in
  Pythia8 for p+p: PHPythia8
  Pythia6 for p+p/e+p: PHPythia6
  Hijing for p+A, A+A
Additional event generator
  JEWEL/PHSartre/sHepGEN
  Suits of EIC event generators via EIC-Smear package
  Of-course single particle generator for testing
For your study, welcome to contribute your favorite generator or HepMC data sets:
  https://github.com/sPHENIX-Collaboration/coresoftware/tree/master/generators

## Slide 36: Inclusive b-jet RAA Performance
MVTX aiming first b-jet nuclear modification factor @ RHIC, covering ~15-40 GeV/c
  Mass dependence of parton energy loss
  Cleaner access to partonic kinematics
Uniqueness at RHIC (vs. LHC)
  Gluon splitting contribution is much less (~10%)

## Slide 37: EMCal: EM-shower energy resolution
Request:
Update with EMCal tower-by-tower calibration
Apply sPHENIX style
Joe Osborn (UMich), June 13 Sim meeting

## Slide 38: EMCal: Hadron rejection
Requests in priorities:
Update to sPHENIX plotting style
Produce Upsilon spectrum update with updated background
Use 2017 EMCal design and tracking simulations. Help on running?
Finalizing Upsilon R_AA projection?
Hadron rejection @ 90% electron eff. for embedded particle in 0-4.4 fm Au+Au collision
Work by Sasha Lebedev (ISU), quoted from Quarkonium-TG wiki, June-2017 Col. meeting
pT [GeV/c]
Pion rejection
pT [GeV/c]
Anti-proton Rejection
+
More in Sasha’s talk today.

## Slide 39: Performance : electron-ID in Au+Au
Updated and more detailed simulation show good safety margin on electron-ID performance on top of the baseline design (as required to reach Upsilon program physics goal)
Baseline performance, design goals
Sum all scintillator energy
1D SPACAL material with hits grouped into 2D SPACAL towers
2D projective SPACAL
Updated studies (Preliminary)
Sum all hadron taking account of hadron ratio
Full digitization (w/ Birk corrections)
Full tracking with silicon opt.
Fully implemented 2D SPACAL (tower/support structure)
1D projective SPACAL
Updated studies (Preliminary)
Sum all hadron taking account of hadron ratio
Full digitization (w/ Birk corrections)
Full tracking with silicon opt.
Ideally towering (no-tower boarder, no enclosure structure)
Reconstructed η and p
Reconstructed η and p