## Slide 1: Lattice design for the CEPC collider ring
Yiwei Wang, Yuanyuan Wei, Yuan Zhang, Dou Wang,
Sha Bai, Xiaohao Cui, Tianjian Bian, Chenghui Yu, Jie Gao
The Institute of High Energy Physics, Beijing
CEPC CDR internal review, 10 Feb. 2018

## Slide 2
Outline
Introduction
Lattice design of the collider ring
  Interaction region
  Arc region
  RF region
  Straight section region
Dynamic aperture
Performance with errors
Summary

## Slide 3
Introduction
The circumference of CEPC collider ring is 100 km.
In the RF region, the RF cavities are shared by two rings for H mode.
Twin-aperture of dipoles and quadrupoles is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
Compatible optics for H, W and Z modes
  For the W and Z mode, the optics except RF region is got by scaling down the magnet strength with energy.
  For H mode, all the cavities will be used and bunches will be filled in half ring.
  For W & Z modes, bunches will only pass half number of cavities and can be filled in full ring.
Notes: 2 fold symmetry

## Slide 4
Parameters of CEPC collider ring
D. Wang
 | Higgs | W | Z
Number of IPs | 2 |  | 
Energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
SR loss/turn (GeV) | 1.73 | 0.34 | 0.036
Half crossing angle (mrad) | 16.5 |  | 
Piwinski angle | 2.58 | 7.74 | 23.8
Ne/bunch (1010) | 15 | 15 | 8.0
Bunch number (bunch spacing) | 242 (0.68us) | 1220 (0.27us) | 12000 (25ns+10%gap)
Beam current (mA) | 17.4 | 87.9 | 461
SR power /beam (MW) | 30 | 30 | 16.5
Bending radius (km) | 10.6 |  | 
Momentum compaction (10-5) | 1.11 |  | 
IP x/y (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.001
Emittance x/y (nm) | 1.21/0.0031 | 0.54/0.0016 | 0.17/0.0016
Transverse IP (um) | 20.9/0.068 | 13.9/0.049 | 5.9/0.04
x/y/IP | 0.031/0.109 | 0.013/0.12 | 0.0041/0.072
VRF (GV) | 2.17 | 0.47 | 0.1
f RF (MHz) (harmonic) | 650 (216816) |  | 
Nature bunch length z (mm) | 2.72 | 2.98 | 2.42
Bunch length z (mm) | 3.26 | 6.53 | 8.5
HOM power/cavity (kw) | 0.54 (2cell) | 0.87(2cell) | 1.94(2cell)
Energy spread (%) | 0.1 | 0.066 | 0.038
Energy acceptance requirement (%) | 1.35 |  | 
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7
Photon number due to beamstrahlung | 0.29 | 0.44 | 0.55
Lifetime _simulation (min) | 100 |  | 
Lifetime (hour) | 0.67 (40 min) | 2 | 4
F (hour glass) | 0.89 | 0.94 | 0.99
Lmax/IP (1034cm-2s-1) | 2.93 | 11.5 | 32.1

## Slide 5
Linear optics of Interaction region
Provide local chromaticity correction of both plane
L*=2.2m, c=33mrad, GQD0=136T/m, GQF1=111T/m
IP upstream of IR: Ec < 120 keV within 400m, last bend Ec = 45 keV
IP downstream of IR: Ec < 300 keV within 250m, last bend Ec = 97 keV
The vertical emittance growth due to solenoid coupling is less than 4%.
Relaxed optics for injection can be re-matched easily as the modular design.
L*= 2.2m
x*= 0.36mm
y*= 1.5mm
GQD0-136T/m
GQF1111T/m
LQD0=2.0m
LQF1=1.48m
max deviation between two beamlines 9.7m
FT
CCY
CCX
CW
asymmetric IR layout*
*ref: K. Oide, ICHEP16.

## Slide 6: Nonlinearity correction of Interaction region
  Local chromaticity correction with sextupoles pairs separated by –I transportation
  up to 3rd order chromaticity corrected with main sextupoles, phase tuning and additional sextupole pair 2,3)
  higher order chromaticities can be corrected with higher order multipoles 3)
Ref: 2) Brinkmann 3) Y. Cai

## Slide 7: Nonlinearity correction of Interaction region
  Local chromaticity correction with sextupoles pairs separated by –I transportation
  all 3rd and 4th RDT due to sextupoles almost cancelled 1)
  tune shift dQ(Jx, Jy) due to finite length of main sextupoles corrected with additional weak sextupoles 3,4)
  Break down of -I due to energy deviation corrected with ARC sextupoles
    could be further optimized with odd dispersion scheme 5),
    Brinkmann sextupoles 2) or pair of decapoles 3)
Ref:
1) K. Brown
2) Brinkmann
3) Y. Cai
4) Anton
5) K. Oide
6) J. Bengttson’s

## Slide 8: Linear optics design of ARC region
-I
-I
  FODO cell, 90/90, non-interleaved sextupole scheme, period =5cells
Twin-aperture of dipoles and quadrupoles* is adopt in the arc region to reduce the their power. The distance between two beams is 0.35m.
SD
SD
SF
SF
magnets designed by F. Chen, M. Yang, X. Sun et al.
*Ref: A. Milanese,
PRAB 19, 112401 (2016)

## Slide 9: Nonlinearity correction of ARC region
  FODO cell, 90/90, non-interleaved sextupole scheme, period =5 cells
  tune shift dQ(Jx, Jy) is very small
    DA on momentum: large
  Chromaticity dQ() need to be corrected with many families
    DA off momentum: with many families to correct dQ()
  With 2 families of sextupoles in each 4 periods i.e. 20 cells
    all 3rd and 4th resonance driving terms (RDT) due to sextupoles cancelled, except small 4Qx, 2Qx+2Qy, 4Qy, 2Qx-2Qy
    break down of -I due to energy deviation cancelled
    thus cells numbers equal to 20*N in each ARC region

## Slide 10: FODO cell for cryo-module
Get a smallest average beta function to reduce the multi-bunch instability caused by RF cavities (compatible for Z mode)
  90/90 degree phase advance
  as short as possible distance between quadrupoles, but should be larger than a module length (12m)
  Filling factor of module is 75 %.
336 / 6 / 2RF stations / 2 sections / 2= 7 cells in each section
90/90 deg
Half cell: 13.7m+2.3m
max: 53.8 m
min: 9.5 m
cryo-module
quadrupole

## Slide 11: Optics design of RF region
Common RF cavities for e- and e+ ring (Higgs)
An electrostatic separator combined with a dipole magnet to avoid bending of incoming beam (ref: K. Oide, ICHEP16)
RF region divided into two sections for bypassing half numbers of cavities in Z mode
common RF cavities
combined magnet
Esep=1.8 MV/m
Lsep=50m
Ldrift=75m
x=10 cm at entrance of quad
Phase tuning
Phase tuning

## Slide 12: Optics design of Straight section region
The function of the straight section is phase advance tuning and injection.
  Independent magnets for two rings
  0.3m of longitudinal distance between two quadrupoles of two rings allows a larger size of quadrupoles
Phase tuning
Phase tuning
Injection
Bx=600 m at injection point
Injection section 66.7 m

## Slide 13: Injection
Bumped
Stored beam
Injected beam
Septum
2mm
X’
X
Acceptance >4sxc + 6sxi + S
Bump Height
For Higgs:
e_x = 1.21 nm.rad; e_inject = 3.58 nm.rad
sx = 0.85 mm, s_inject = 0.94 mm
Septum = 2 mm
Acceptance > 13 s
conventional off axis injection
4 kicker for local bump in the collider
by Xiaohao Cui

## Slide 14
Linear optics of the collider ring
  An optics fulfilling requirements of the parameters list, geometry, photon background and key hardware.
tune= 363.10 / 365.22 (near integer with two IPs)
natural chromaticity= -493 / -1544

## Slide 15
Energy sawtooth effects and correction
With only two RF stations, the energy sawtooth is around 0.35%
The closed orbit distortion in CEPC collider ring is around 1mm and becomes 1um after tapering the magnet strength with beam energy.

## Slide 16: Requirement of the dynamic aperture
Goal: 13 sx 12.5 sy  1.35%
  Requirement from injection*: 13 sx
  Requirement from beam beam (life time 100 min)#: 7.5 sx, 12.5 sy, 1.35 %
*X. Cui, # Yuan Zhang
Simulation of Lattice + Beamstrahlung + SR Fluctuation
x-100min: 7.5 sx
y-100min: 12.5 sy
z-100min: 1.35%

## Slide 17: Dynamic aperture optimization
Start point of the optimization
  Nonlinearity optimized term by term with 10 families of sextupoles in the IR and 4 families of sextupoles in the ARC.
Optimize dynamic aperture directly with MODE (Y. Zhang, IHEP)
  With 10 families of sextupoles in the IR, 32 families of sextupoles in ARC and 8 phase advances
Tracking in SAD w/ damping, fluctuation(100 samples), energy sawtooth and tapering 200 turns, 4 initial phases
by Y. Zhang et. al.
Achieved (without errors)@ Higgs : 15 sx 15 sy  1.5%
4 initial phases
initial phase=0

## Slide 18: Performance with errors
LOCO based on AT is used to correct distortion of closed orbit, beta, dispersion and coupling
About 1500 BPMs, horizontal and vertical correctors are respectively placed in the storage ring (4 per one betatron wave; IR is perfect )
  1. correct COD w/o sextupoles
  2. correct optics w/ sextupoles
  3. correct coupling
by Yuanyuan Wei
Component | x (mm) | y (mm) | z (mrad)
Dipole | 0.05 | 0.05 | 0.1
Quadrupole | 0.03 | 0.03 | 0.1
Sextupole | 0.03 | 0.03 | 0.1
Component | Field error
Dipole | 0.01%
Quadrupole | 0.02%

## Slide 19
  1. correct COD w/o sextupoles
Closed orbit distortion
COD  40/3 mm (x/y) before orbit correction except for IR region
COD  40/75 um (x/y) after orbit correction except for IR region
Need more corrector in the long drifts
before
after
50 samples

## Slide 20
  1. correct COD w/o sextupoles
Beta functions distortion
(β_err/β)max = 4% / 3.3% (x/y) before COD correction
(β_err/β)max = 3% / 2% (x/y) after COD correction
The vertical beta beat is larger than horizontal beta beat due to the fringe field effect of dipoles and quadrupoles.
X direction
y direction
50 samples

## Slide 21
2. correct optics w/ sextupoles
1/5 quadrupole ( around 600 out of 3000 quadrupoles) strengths are changed to restore beta functions
before
after
one sample
(β_err/β)max = 4% / 8% (x/y) before COD correction
(β_err/β)max = 1% / 1% (x/y) after COD correction except for IR region

## Slide 22
3. correct the coupling
Quadrupoles rotation and feed-down effects in the quadrupoles will generates betatron coupling and cause vertical dispersion.
Skew-Quads are installed in the sextupoles. Totally about 200 Skew-quads (1/5 sextupoles) are used in the coupling correction.
Before correction
emity/emitx=0.4%
After correction
emity/emitx=0.08%
one sample

## Slide 23: Summary
  Linear optics of the CEPC collider ring designed fulfilling requirements of the parameters list, geometry, photon background and key hardware.
Nonlinearity correction made to give a good start point of dynamic aperture optimization.
Further optimization of dynamic aperture is made with MODE and downhill simplex method.
Study of errors and correction made and the study of effects on dynamic aperture is under going.
  Translate corrected lattice from AT to SAD

## Slide 24
Thank you!