## Slide 1: Update on SPMT Electronics Simulation
Main contributors:
Tao Lin
Yan Zhang
2018/5/10

## Slide 2
The old version of LPMT electronics simulation software didn’t consider the joint simulation of multiple sub detectors.
The old framework is too complicated and has some unnecessary code replication, which affects the speed of operation.
Need to develop a new framework to resolve these problems.
Motivation

## Slide 3
Old electronics simulation work flow
New design
Outline
1. Update design
Electronics in real life
New framework prototype
New data structure
Status of algorithm
2. New framework
3. Status on electronics simulation

## Slide 4
Trigger Buffer
Pulse Buffer
Hit Buffer
Sniper Buffer
ReadoutAlg
check Trigger
Get trigger infor.
No Trig
TriggerSimAlg
Push trig to buffer
check Pulse
Get pulses
PMTSimAlg
UnpackingAlg
EvtMixingAlg
DetSim
BKG Root File
WaveFormSimAlg
has a trig
return ElecSim
if no enough pulses
if no enough hits
check hit
get hits
Push pulse to buffer
get event
Push hit to buffer
Trig DetSim
get event
Push event to buffer
Old Electronics Simulation work flow
Output file
Sniper Buffer
Push ElecSim to buffer
Root IO
Root IO

## Slide 5
New design
Use Trigger Buffer handle the Readout and Trigger Algorithm.
Trigger Algorithm invoke each trigger tool to generate a trigger.
If has a trigger, Readout Algorithm will be invoked.

## Slide 6
New framework prototype
Main components
• ElecSimAlg and ITriggerHandler (readout stage)
• TriggerSimAlg and ITriggerTool (trigger simulation)
• PMTSimAlg and IPMTTool (pmt simulation)
• ElecSimSvc: pulse buffer and trigger buffer.
Execution order:
• ElecSimTask -> TriggerSimTask -> PMTSimTask -> inputs
Create a new package (~ 1,500 LOC) •http://juno.ihep.ac.cn/svn/offline/trunk/Simulation/ElecSimV3/ElecSimAlg

## Slide 7
Electronics in Real Life

## Slide 8
Electronics in Real Life
Design by Lin Tao

## Slide 9
New data structure
enum PMTType: identify PMT type • kPMT_CD_Lpmt, kPMT_CD_Spmt, kPMT_CD
• kPMT_WP, kPMT_TT
enum TriggerType (same as PMT Type) • kTriggerLpmt, kTriggerSpmt, kTriggerCD (both L/S pmts)
• kTriggerWP, kTriggerTT
struct Trigger • TriggerType and TimeStamp
struct Pulse • pmtid, amplitude, TTS, hit time

## Slide 10
Status of algorithms
PMTSimAlg
• Mix events and generate pulses.
• Replace the original packages: EvtMixing, Unpacking, PMTSim.
• Get hits from SimPMTHit, and sorted by hittime.
• For Large PMT
• Generate pulses as several factors: Relative quantum efficiency, Single PE response, TTS and Time offset.
• Dark pulse: Add dark pulse as Poisson distribution in a time window.
• After pulse: Each pulse have a probability to generate a after pulse.

## Slide 11
Status of algorithms
TriggerSimAlg
• Read pulses and generate triggers, don’t modify the pulse buffer.
• If there are not enough pulses, invoke PMTSim.
• Invoke each trigger tool to generate a trigger.
• LPMT trigger scheme (Global Trigger) : Counting fired PMT number in a time window.
• SPMT trigger scheme: Self-trigger.
PulseBuffer
t（global time）
Pulse
300ns slip 25ns slip step
time window
firstPulseTime
buffer total length> 2000ns
Global Trigger

## Slide 12
Status of algorithms
ITriggerHandler (Waveform Simulation for LPMT)
• Select pulses in the readout window.
• With TriggerTime we open a time window and use all the pulse which belong to the window to do waveform simulation.
PulseBuffer
t（global time）
Pulse
buffer total length> 2000ns
firstPulseTime
preWaveSimWindow
postWaveSimWindow
200ns
800ns
TriggerTime
pulse to be converted

## Slide 13
Status of algorithms
ITriggerHandler (Waveform Simulation for LPMT)
• Generate waveform: Average 2000 single p.e. waveforms from experimental measurement.
• Other factors: Noise, Overshoot, Saturation
• FADC simulation:
• Sampling rate: 1 GHz,
• ADC resolution: 8 bit, 3 range (VULCAN); 12 bit, 2 range (Tsinghua).

## Slide 14
Status of algorithms
ElecSimAlg
• Generate readouts (by ITriggerHandler).
• Get a trigger first, then read pulses and remove used pulses.
• It’s possible to get ElecHeader with LPMT/SPMT events.
ElecSimSvc
• Manage trigger buffer and pulse buffer.
• Provide the PMT parameters service such as dark pulse rate, TTS etc.
• Provide time service.

## Slide 15: Summary
Design the new framework to simulate large and small PMT together.
Give a brief introduction of the work flow and data structure of the new framework.
Introduce the status of each algorithm.
Next to do:
• Testing the physical and computational performance of electronic simulation under the new framework, memory consumption.

## Slide 16: Thanks for your attention!