## Slide 1: Calibration strategy and MH sensitivity
Feiyang Zhang
2018-05-10

## Slide 2: Outline
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 3: Calibration device in sniper
20cm
20cm
Calibration system:
  1-D: Automatic Calibration Unit (ACU)
  2-D: Cable Loop System (CLS)
  3-D: Remotely Operated Vehicle (ROV)
  Outer surface: Guide Tube (GT)
Geometry in sniper:
  GT geometry is written into sniper as default option.
  ROV, source enclosure, quick connector and weights are written into sniper as alternative option.
  All these geometries can be enable or disable if necessary during simulation,
Quick connector
weights

## Slide 4: Radioactive source generator in sniper
  68Ge, 137Cs, 54Mn, 60Co, 40K
  e+: 68Ge, 22Na
  n: 241Am-Be, 241Am-C or Pu-C
Calibration sources
Usage
Use standard script “tut_detsim.py” by Lin Tao.
$ python tut_detsim.py --source_weight_QC \ # enable source enclosure and quick connector
--OffsetInX 1000 --OffsetInY 1000 --OffsetInZ 1000 \ # move source center at (1m,1m,1m)
gendecay --nuclear K40 --volume pSource # Use 40K (you can also use 68Ge, 137Cs..)
or
hepevt --exe AmC --volume pSource # Use AmC (you can also AmBe or PuC)

## Slide 5
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 6: Energy scale
Compton tail
Full absorption peak as measure.
60Co as energy scale: =1307 PE/MeV
Reconstructed energy for 68Ge: =0.964 MeV
Non-linearity:
Reconstruct energy for 54Mn, 137Cs, 40K, n-H, n-C, Am-C with same energy scale.
68Ge at CD center with source enclosure
60Co at CD center with source enclosure

## Slide 7: Gamma to e-/e+ converting
Gamma convert to e-/e+:
  Pair production
  Compton scattering
  Photoelectric
Gamma energy non-linearity can be deduced from non-linearity of primary e-/e+
The electron from annihilation gamma should also be considered.
One example of annihilation with e+ in flight
e-
e+
annihilation
e+
7 MeV
3 MeV
3 MeV
2 MeV
1.5 MeV
1.5 MeV
e-
e-
Residual energy
Pair production
e-
e+
annihilation
e+
0.511 MeV
0.511 MeV
e-
e-
Pair production
residual energy should be subtract.
0 MeV

## Slide 8: Model of gamma energy non-linearity
Residual energy
6.128±0.003 MeV
Energy bias to gamma = 0.03%
gamma energy: 6.13 MeV
Ref:
Liangjian Wen, et al., Ref: Daya Bay DocDB 8240-v2
Fengpeng An, et al (Daya Bay Collaboration): PRL 112, 061801(2014)
Empirical formula to describe electron non-linearity:
Construct model of gamma energy non-linearity with PDF and electron non-linearity:
Ekinetic distribution of primary e-/e+

## Slide 9: Bias of energy non-linearity correction
Bias < 0.15%
Bias of e+ after correction
68Ge
137Cs
54Mn
60Co
40K
n-H
n-C
241Am-C
n-Fe
Fit non-linearity of gamma to extract parameters.
Calculate bias between true and reconstructed energy of e+ from 1 to 8 MeV based on fit result.

## Slide 10
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 11: Calibration sources
Low Compton tail
The calibration mapping is constructed by
  ACU(21), CLS(219), and GT(168)
40K with source enclosure
~40000 events for one calibration point.
For GT calibration:
  Source is outer of CD surface.
  Used as points in inner CD.
Calibration points
40K with source enclosure

## Slide 12: Correction mapping
Corrected
with
Mean = 1261.4±0.1
Sigma = 37.58 ±0.11
ratio =
Spline function to describe the correction mapping
The resolution is sigma/mean = 2.98%
Mean PE of 1 MeV e+ at CD center is 1262
Mean bias is 0.05 % with visible energy 1 MeV of e+.

## Slide 13: Bias and energy resolution
Mean bias after correction
Energy resolution after correction
Mono energy e+ (1-8 MeV) uniformly distribution in CD.
Corrected it with non-uniformity correction mapping.
Use true position of event in MC simulation.
The overall bias is less than 0.1% from 1 to 8 MeV for e+.
Energy resolution:

## Slide 14: Combined with Vertex reconstruction
Energy resolution:
  3.25% @ 1MeV
We need better vertex reconstruction

## Slide 15: Assumption of vertex reconstruction
Resolution (cm) | a (%) | b(%) | 
5 | 2.89 | 0.65 | 3.07
10 | 2.94 | 0.74 | 3.17
12 | 2.95 | 0.78 | 3.20
15 | 2.95 | 0.84 | 3.24
20 | 3.07 | 0.83 | 3.34
25 | 3.16 | 0.82 | 3.43
30 | 3.18 | 0.86 | 3.46
35 | 3.27 | 0.83 | 3.53
40 | 3.32 | 0.84 | 3.58
45 | 3.36 | 0.87 | 3.64
50 | 3.35 | 0.94 | 3.67
Resolution (cm) | a (%) | b(%) | 
5 | 2.89 | 0.65 | 3.07
10 | 2.94 | 0.74 | 3.17
12 | 2.95 | 0.78 | 3.20
15 | 2.95 | 0.84 | 3.24
20 | 3.07 | 0.83 | 3.34
25 | 3.16 | 0.82 | 3.43
30 | 3.18 | 0.86 | 3.46
35 | 3.27 | 0.83 | 3.53
40 | 3.32 | 0.84 | 3.58
45 | 3.36 | 0.87 | 3.64
50 | 3.35 | 0.94 | 3.67
Energy resolution
Assume resolution of vertex reconstruction: 5,10,12,15,20,25,30,35,40,45,50 cm
Non-uniformity correction with the assumption, and calculate corresponding resolution.
Fit with to get parameter a and b.
Energy resolution is sensitive to vertex reconstruction.

## Slide 16
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 17: Procedure of study
Neutrino energy
Deposit energy
Visible energy
Detected energy
Prediction
Observation
IBD simulation in sniper
totalPE
PE at center
Detected energy
Calibration
Energy scale
Non-uniformity correction to center
Apply non-linearity
Response matrix
Energy resolution model
Energy smearing
fit
MH

## Slide 18
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 19: Probability of neutrino
Oscillation probability
Cross section

## Slide 20: Neutrino energy to deposit Energy
Neutrino events uniformly distribute in CD.
Get the corresponding deposit energy for every event.
Construct response matrix between neutrino energy and deposit energy.
Bins of matrix are 4000×4000.
Neutrino energy spectrum
Energy leakage
Response matrix between Ev and Edep

## Slide 21: Deposit energy to visible energy
Energy non-linearity obtained from calibration.
Non-linearity exists between deposit energy and Visible energy.

## Slide 22: Visible energy to detected energy
Construction of energy resolution model:
  e+ uniformly distribute in CD, with continuous energy from 1 to 8 MeV.
  Non-uniformity correction.
  Energy resolution as function of deposit energy.
  Fit it with to get “a” and “b”
“a” and “b” will be used to construct energy resolution model.
This method can only be used simulation.
Should try to obtain model of energy resolution from calibration in real experiment.

## Slide 23
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 24: Observation of IBD spectrum
Before correction
Simulation: IBD events uniformly distribute in CD.
100,000 events (~6 years data )for one experiment.
Correct them with correction mapping
Energy scale: 1307 PE/MeV (60Co)
Correction mapping
PE / energy scale

## Slide 25
Calibration strategy
  Calibration status in sniper
  Non-linearity correction
  Non-uniformity correction
MH sensitivity
  Prediction of IBD spectrum
  Observation of IBD spectrum in sniper
  fit and MH sensitivity
Summary

## Slide 26: Definition of and
MH discriminator is defined as:
is constructed to qualify the consistent of data and prediction:
Fit the IBD detected energy spectrum with normal hierarchy(NH) or inverted hierarchy(IH) predicted.

## Slide 27: Fit the IBD detected energy spectrum
Fit the IBD spectrum with prediction.
Number of bins is 200. So NDF = 200 -1 = 199.
for NH expected: 195 and for IH expected: 208.
is 13.
There is only one experiment (100,000 events for ~6 years data)
Simulate multiple times of experiment, and get the distribution of and .
NH is true

## Slide 28: and distribution
Simulate times of experiment: 170.
is 199.4 with right MH predicted , which seems good since the NDF is 199.
And =14.63
MH sensitivity is =3.82 refer to standard sensitivity definition in Yellow book.

## Slide 29: Summary
With Daya bay‘s model of energy non-linearity, it’s promising to make the bias less than 0.2%.
Combining ACU, CLS and GT, we can construct a correction mapping of non-uniformity. But this correction rely on vertex reconstruction, and we need better vertex reconstruction.
Considering non-linearity and non-uniformity correction, the MH sensitivity can reach to 3~4 σ.
But We need energy resolution model from calibration for prediction of IBD energy spectrum. That’s what we will consider for next step.

## Slide 30: Thank you！