## Slide 1
课题3：CMS端盖μ子探测器升级
CMS-MRPC探测器
王义
清华大学工程物理系

## Slide 2
端盖μ探测器升级
清华大学, 玻璃MRPC
RE3/1+RE4/1
In CMS PhaseII upgrade, station 3 and 4 of Muon system is intended to be constructed with RPC.
Requirement:
Rate >2kHz/cm2
Trapezoidal, space limit
Time resolution <100ps
Efficiency >95%
CMS端盖缪子探测器升级内容

## Slide 3
主要研究内容
根据物理条件要求及现场空间的限制，拟研制梯形MRPC。探测器长度达1米，上底宽度45cm，下底宽度55cm。由于我们研制的低电阻玻璃尺寸的限制，整个探测器由6个小梯形MRPC拼接而成，而整个探测器采用统一的PCB读出感应信号。每个MRPC包含5个气隙，气隙宽度为250微米，采用条形读出，读出条平均宽度为10mm。这种结构的优点是能够保证高的时间分辨，同时也能保证探测器的厚度在限定的范围内。
需要解决玻璃拼接，阻抗匹配，信号串扰及传输，探测器宇宙射线及粒子束流测试等关键技术问题。
同时还要研究高亮度实验中的气体污染问题，以保证探测器的长期稳定工作。
完成CMS前端缪子探测器ME3/1和ME4/1两个区的部分升级。

## Slide 4
主要进展
25 cm
20cm
27cm
拼接原型探测器
全尺寸MRPC
Gas gap number: 5
Gas gap width: 250 μm
Glass thickness: 0.7 mm
Glass bulk resistivity: ~ 1010 Ωcm
Mosaic interface: glass directly mosaic together
Strip number: 44
Strip shape: trapezoidal (6 mm/8 mm)
Strip interval: 3 mm
Strip length: 1 m

## Slide 5
Cluster size<1.3
Efficiency -> 95%
Time resolution ~60ps
计数率>40kHz/cm2
原型探测器的性能

## Slide 6
全尺寸测器的性能（@CERN 904）
NINOs signal
Cosmic ray test at CERN in Feb, 2017:
Gas component: 90% C2H2F4 + 5% i-C4H10 + 5% SF6.
Trigger PMT
Trigger PMT
Mosaic MRPC module

## Slide 7
全尺寸测器的性能（@HZDR）
Rate: 11 kHz/cm2.
Efficiency
Cut on S6:
Working gas :
90% C2H2F4 + 5% i-C4H10 + 5% SF6.

## Slide 8
Run005 ~ Run009
Run017 ~ Run021
全尺寸测器的性能（@HZDR）
时间分辨岁高压的变化
不同计数率下的时间分辨

## Slide 9
全尺寸测器的性能（@GIF++）
Chamber has been repaired at CERN in Sep, 2017
Working gas:
CMS gas: 95.2% C2H2F4 + 4.5% i-C4H10 + 0.3% SF6.

## Slide 10
There is no efficiency loss along with high rate. Efficiency always reaches about 94% at ± 6000V.
Rate[kHz/cm2] | Efficieny[%]
0 | 94.12
0.29 | 94.81
0.58 | 93.41
1.007 | 95
2.64 | 94.68
4.64 | 93.93
10.83 | 93.75
全尺寸测器的性能（@GIF++）

## Slide 11
Find a good technology to develop high rate, high time resolution and large area MRPC
30 MeV electron beam at HZDR at rate of 10kHz/cm2
Efficiency reaches 95% at ±6800V
Time resolution around 55ps.
Efficiency loss at mosaic interface is about 2%.
The real size mosaic MRPC can keep good performance with CMS dry gas.
Efficiency can reaches about 94% at ± 6000V at rate of 10kHz/cm2.
高计数率MRPC是一种全新的技术，在不同工作气体下的性能（如工作点，时间性能等），与已有普通浮法玻璃MRPC的完全不一样。
总结

## Slide 12
Next: 与新电子学联调
1、PETIROC2A: 单极性输入，快前放+ TDC
2、读出条两端读出，通过时间差得到击中位置

## Slide 13
Bakelite RPC 与PETIROC2A测试不成功
甄别阈值与CMS RPC老电子学一样，50fC, 效率下降的原因还不清楚。

## Slide 14
<100 μm Resolution (for momentum)
~ 340 m2 total active surface
250 μm Scintillating Fiber
524,000 SiPM Channels
PACIFIC – 64 channel SiPM readout ASIC
with 16 x 320 MHz digital outputs
> 12,000 Chips needed
> 2,500 Frontend Electronics Boards
LHCb China Group:
  Readout Electronics for Detector Performance Evaluation (> 20 Setups in SciFi Group)
  Co-design SciFi Frontend Electronics Boards
  SciFi Readout Electronics (PACIFIC) Quality Assurance System (for chips, and frontend boards)
  Manufacturing and testing all Frontend Boards (2,500 boards) in China
LHCb径迹探测器升级

## Slide 15
Automatically in FPGA firmware,
5 mins/ASIC, 13 mins/Frontend Boards
Basic Tests:
Power, I2C, Digital Output
Classify Tests
Linearity, Dynamic range, DC Baseline
Parameter Optimization (in to Database)
Configuration, DAC values (for baseline)
LHCb China Group (2018) finished:
  > 1500 PACIFIC ASICs tested
  20 Frontend Boards manufactured and tested
  4 Readout Electronics Quality Assurance System were set up at Heidelberg, Germany
2018 Summer To Do:
  ALL 12,000 PACIFIC ASICs test (with Spain group)
  ALL 2,500 Frontend Boards manufacture and test in China
  >5 Readout Electronics Quality Assurance System should be set up at Spain and Germany
LHCb SciFi – Scintillating Fiber Tracker

## Slide 16
Build new sequence for SciFi specific processing of 2017 Testbeam data, which allows for the tuning of simulation to data
16
Correlations between Y channels
Correlations between X channels
LHCb SciFi Tracker: software

## Slide 17
Wang Fuyue, Wang Yi. Performance study of new style mosaic MRPC. Chinese Physics C, 2016, 40(11) , 116006 . DOI：10.1088/1674-1137/40/11/116006.
Wang Fuyue, Han Dong and Wang Yi. Performance study of a Mosaic high rate MRPC. 2016 JINST 11 C09016
Lyu Pengfei, Wang Yi. et al. Gas related effects on multi-gap RPC performance in high luminosity experiments. 2016 JINST 11 C11041
Lyu Pengfei, Wang Yi. Development and performance of self-sealed MRPC. JINST，12，C03055
Yancheng Yu, Wang Yi. R&D of a real-size Mosaic MRPC within the framework of the CMS muon upgrade, JINST (已投稿）
一种新型的阻性板室探测器, 发明专利号：ZL201410190976.X
快时间响应射线探测器，实用新型，ZL 201520890740.7
文章和专利

## Slide 18: Thank You!