## Slide 1: Homework 1: R/Q Calculation
Calculate R/Q value of TM010 and TM110 mode of a 1.3 GHz pillbox cavity. The cavity length is half of the RF wavelength.

## Slide 2: Homework 2: Field Flatness Calculation
Calculate field flatness with cell frequency error of a 650 MHz 2-cell cavity. Pi-mode frequency of one cell is 649.8 MHz, and the other is 649.3 MHz. Cell-to-cell coupling factor k = 1.58 %. (Use RF circuit perturbation method)

## Slide 3: Homework 3: Cross Talk
Suppose a pickup is on the same side of the cavity beam tube as the input coupler. The accelerating mode signal directly coupled from the input coupler to the pickup rather than from the field of cavity is called “cross talk”.
Prove that the relative cross talk signal is much smaller (~ 1E-4) at 2 K than at room temperature. Explain the shape of the cross talk signal in the left.

## Slide 4: Homework 4: Linac Beam Injection Time
Calculate injection time (in terms of filling time τ) for a pulsed superconducting linac (on crest beam acceleration) to have same bunch energy in the bunch train.

## Slide 5: Homework 5: Robinson Instability
Calculate the growth rate of Robinson instability with CEPC Z-pole parameters. Suppose the cavity frequency is tuned 400 Hz above the RF frequency. Compare that with the radiation damping rate.
Parameters | Value | Unit
Beam current | 461 | mA
Beam energy | 45.5 | GeV
Energy loss / turn | 36 | MeV
Bunch number | 216816 | 
Revolution frequency | 2.99 | kHz
Longitudinal radiation damping time | 425 | ms
Synchrotron tune | 0.028 | 
RF frequency | 650 | MHz
Cavity number | 120 | 
Momentum compaction factor | 1.11E-5 | 
Cavity voltage | 2.9 | MV
Unloaded Q | 1.5E+10 | 
Loaded Q | 4.7E+4 | 
R/Q | 213 | Ohm