## Slide 1: Digitization & Tuning update
R. Farinelli – L. Lavezzi – NN. Miao – LL. Wang – LH. Wu
2018-06-14

## Slide 2: Status in March (reminder)
Shockley–Ramo theorem
i(t) = qe- x vdrift x Wloc
instantaneous current induced by a charge in motion on an electrode
APV25 simulation
RC circuit (t = 50 ns) + charge threshold
FULLY IMPLEMENTED
in standalone code (based on planar GEM)
Parameters we can tune
  noise (ADC)
  transparency (%)
  APV-25 threshold (ADC)
  conversion factor
Variables we must monitor
  cluster size
  cluster charge
  CC position resolution
  uTPC position resolution
  uTPC angle

## Slide 3: Tuning @ March 1st, 2018 (already “old story”)
Charge (ADC) vs angle (deg)
Within 30%
Cl.size vs angle (deg)
Perfect match!
CC resolution vs angle (deg)
Noise level = 0, 1, 5 ADC
APV threshold = 45 ADC
Conversion Factor = 30 ADC = 1fCc
Angle scan 0, 10, 20, 30, 45 deg
HV = 820 V
Fields = 1.5/3/3/5 kV/cm
With induction

## Slide 4: Tuning @ March 1st, 2018 (already “old story”)
Cl.size vs angle (deg)
Twice!!  work on it!
Added
missing clusterization
Fixed
induced current calculation
New
Old

## Slide 5
Now, June 2018
Conversion factor
remeasured in lab: 30 ADC = 1 fC
Threshold
In testbeams was 45 ADC
No more transparency + gain, but effective gain from histo
Parameters we can tune
  noise (ADC)
  transparency (%)
  APV-25 threshold (ADC)
  conversion factor

## Slide 6
Now, June 2018
GARFIELD computed WF, then not under control.
Let’s compute it with finite elements calculation
1st version: just one strip @ 1V; I actually used the field
I_curr = ele_ch * drift_velocity * Eloc
2nd version: one strip @1V AND the others @0V (Ramo’s theorem); I want to use the potential
Q_induced = ele_ch * DV
Weighting field

## Slide 7
Now, June 2018
After bug fixing of the ANSYS field maps we did new iffusion studies [NO MAG FIELD]
z (cm)
xEND- xSTART (cm)
xEND- xSTART (cm)
sigma(xEND- xSTART) cm)
OLD
NEW
less diffusion in drift gap
same in the other gaps
position

## Slide 8
Now, June 2018
z (cm)
xEND- xSTART (cm)
xEND- xSTART (cm)
mean (xEND- xSTART) cm)
OLD
NEW
shift in time smaller in drift gap BUT bigger smearing
shift in transf & induct gaps agrees with vD = 35 mm/ns
Time
sigma(xEND- xSTART) cm)
After bug fixing of the ANSYS field maps we did new iffusion studies [NO MAG FIELD]

## Slide 9
Angle scan
CHARGE
CL. SIZE
RESOL CC
simulated
simulated
simulated
experimental
experimental
experimental

## Slide 10
HV scan
CHARGE
CL. SIZE
RESOL CC
simulated
experimental
simulated
experimental
Fit with 2 Gaussians
Fit with 1 Gaussian

## Slide 11
Now, June 2018
(MC – EXP)/EXP
±30%
ANGLE SCAN

## Slide 12
Now, June 2018
(MC – EXP)/EXP
±30%
HV SCAN
charge
cl.size
resol CC